| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#19 TP#19 |
| Source:* | Vinod Choyi, InterDigital, vinod.choyi@interdigital.com Dale Seed, InterDigital, Dale.Seed@interdigital.com |
| Date:* | 2015-08-25 |
| Contact:* | As above |
| Reason for Change/s:* | Use Case and Requirements for Dyanmic Authorization Policy Provisioning |
| CR against: Release* | REL-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0019 Dynamic Authorization |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes a use case and corresponding requirements for dynamic authorization policy provisioning

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 5	Use Cases

## Use case of Dynamic Authorization Policy Provisioning

### Description

In a oneM2M System the Platform, Gateways and Devices interact each other in the way of many-to-many, furthermore many of these relations may be dynamic and temporary. So the access control mechanism used by the M2M System  needs to be flexible and efficient and authorization policies that support such dynamic authorization must be tailored accordingly and provisioned to the various authorization components.

In this use case, provisioning of dynamic authorization policies to the various dynamic authorization components is described. An administrator that is authorized uses the Dynamic Authorization Policy Retrieval Point (DA-PRP) to define, create and modify appropriate dynamic authorization policies associated with each of the dynamic authorization components. The DA-PRP then provisions the appropriate policies to the DA-PDP, DA-PEP and information to the DA-PIP on a regular basis.

### Actors

The entities involved in the use case are shown in Figure 5.3.2-1 and described as follows:

M2M Platform: It represents an infrastructure entity that interacts with M2M Gateways  /Devices and M2M Application for providing common functionalities. In this use case the M2M Platform provides the ability to provision dynamic ruthorization policies by implementing a Dynamic Authorization – Policy Retrieval Point (DA-PRP).

M2M Gateway: It represents a gateway that is responsible for hosting a resource. In addition, the M2M Gateway is responsible for implementing the Dynamic Authorization - Policy Enforcement (DA-PEP), Dynamic Authorization - Policy Decision Point (DA-PDP) and Dynamic Authorization - Policy Information Point (DA-PIP) functions.

M2M Device: It represents a sensor application or a sensor device that is responsible for measuring sensor data and hosting a resource on an M2M Gateway.

Figure 5.3.2-1: Entities involved in provisioning of Dynamic Authorization policies

### Pre-Conditions

M2M Platform that implements the DA-PRP, has access to a policy database that is configured with dynamic authorization rules

It is assumed that the communications between the M2M Platform and the M2M Gateway occurs over a secure communications channel.

It is assumed that the communications between the M2M Device and the M2M Gateway occurs over a secure communications channel.

### Normal Flow

Procedure for provisioning of dynamic authorization policies:

- An administrator that has authorized access to the M2M Platform configures appropriate policies that are to be provisioned using a DA-PRP

- The DA-PRP at the platform, provisions appropriate decision policies to the DA-PDP, enforcement policies to the DA-PEP and information to the DA-PIP. The provisioning process is performed periodically.

### Potential Requirements

- The M2M system shall support provisioning of dynamic authorization policies.

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?