| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#19 TP#19 |
| Source:* | Vinod Choyi, InterDigital, vinod.choyi@interdigital.com Dale Seed, InterDigital, Dale.Seed@interdigital.com |
| Date:* | 2015-08-25 |
| Contact:* | As above |
| Reason for Change/s:* | Use case and requirements for Dynamic Authorization |
| CR against: Release* | REL-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0019 Dynamic Authorization |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes a use case and proposed requirements for service layer dynamic authorization.

### - Start of changes to Use Cases -

# 5	Use Cases

## Use case of Dynamic Authorization

### Description

In a oneM2M System the Platform, Gateways and Devices interact with each other in the way of many-to-many, furthermore many of these relations may be dynamic and temporary. So the access control mechanism used by the M2M System shall be flexible and efficient.

In this use case an M2M Device would like to perform CRUD operations on resource(s) hosted on an M2M Gateway. The M2M device may be registered with the M2M Gateway or may even be completely unknown to it. Even if the M2M Device is registered to the Gateway, it is deemed that the Device is restricted from being able to perform one or more of the CRUD operations on the resource based on a traditional static access control policy. Dynamic authorization enables a previously restricted M2M Device to be able to perform newer operations on resource(s) hosted at the M2M Gateway. Dynamic authorization checks may be dictated based on dynamic authorization policies which may dictate the types of checks (e.g. higher-level of authentication checks, payment based authorization, platform validation checks etc.) that are performed. The authorization provided may be for a finite period of time and may be added to the static access control policy.

### Actors

The entities involved in the use case are shown in Figure 5.3.2-1 and described as follows:

M2M Gateway: It represents a gateway that is responsible for hosting a resource. In addition, the M2M Gateway is responsible for implementing the Dynamic Authorization – Policy Administration Point (DA-PAP), Dynamic Authorization Policy Enforcement (DA-PEP), Dynamic Authorization Policy Decision (DA-PDP) functions and storing Policy Information Point (DA-PIP).

M2M Device: It represents a sensor application or a sensor device that is responsible for measuring sensor data and hsoting a resource on an M2M Gateway.

Figure 5.3.2-1: Entities involved in Dynamic Authorization

### Pre-Conditions

M2M Gateway is provisioned with appropriate dynamic authorization policies based on which, it decides on the dynamic authorization checks that will have to be performed.

It is assumed that the communications between the M2M Device and the M2M Gateway occurs over a secure communications channel.

### Normal Flow

Procedure for dynamic authorization:

- An M2M Device requests to perform a CRUD operation on a resource hosted on the M2M Gateway

- The M2M Gateway determines that the M2M Device does not have the appropriate authorization based on a check with the static ACPs.

- The DA-PDP at the M2M Gateway then consults its dynamic authorization polices in order to determine if the M2M Device can be provided with authorization. If dynamic authorization can be carried out, then the M2M Gateway determines the types of authorization checks that will have to performed with the M2M Device.

- The  M2M Gateway in conjunction with the M2M Device performs one or more dynamic authorization checks (e.g. multi-factor authentication checks, platform validation checks, payment-based authorization, subscription etc..)

- If the authorization checks have been successfully completed then the M2M Gateway updates the relevant entries within the DA-PEP in order that the M2M Device is able to perform one or more CRUD operations on a resource for finite amount of time. Additionally, in certain cases, the ACP may be updated to include the M2M Device and the resource / operations that it is allowed to perform based on the dynamic authorization results.

- The M2M Gateway provides a response to the M2M device indicating the authorization that was provided to it.

### Potential Requirements

- The M2M system shall support dynamic authorization functions (PEP, PDP, PIP, PAP) to reside at the same resource hosting function.

- The M2M system shall support various authorization checks (e.g. multi-factor authentication, platform validation, payment authorization etc..) in order to enable dynamic authorization.

- The M2M system shall support the update of static ACP based on dynamic authorization results

### ---End of changes to Use Cases ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?