| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#19 TP#19 |
| Source:* | Vinod Choyi, InterDigital, vinod.choyi@interdigital.com Dale Seed, InterDigital, Dale.Seed@interdigital.com |
| Date:* | 2015-08-25 |
| Contact:* | As above |
| Reason for Change/s:* | Proposal solution for data security |
| CR against: Release* | REL-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 End-to-End Security |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution provides a solution for providing security of data for use in oneM2M.

-- START CHANGE --

## 8.x	A Solution for providing security of data “at-rest”

## 8.x.2	General procedure for securing data “at-rest”

The generic procedure of securing data “at-rest” is illustrated in figure 8.x.2-1 and described as follows:

Figure 8.x.2-1: Hosting secure data

- The Originator of data would like to provide protection (integrity /authenticity and / or confidentiality) to the data that it generates and hosts onto a Hosting CSE.

  - Data is generated by an originator

  - It also generates appropriate credential(s) for protecting the data. Alternatively, the Originator may not generate the credential(s) but instead request credential(s) from a Credential Registry.

  - The originator then either encrypts, integrity protects or performs both to the data using the credential(s) that it generated

  - The data originator may optionally provide access control rule(s) associated with the credential(s)

- The Originator establishes a secure communications channel with a Credential Registry (CR)

- The Originator then requests to register the credential(s) that it generated with the CR along with optional access control rule(s)

- The CR registers the credential(s)

  - The CR generates or creates unique Credential-Id(s)

  - The CR associates the Credential-Id(s) with respective credential(s) and stores them securely

  - The CR sets an expiration to the credential registration

  - The CR also associates access control rules to the credential(s) that were either provided by the originator or created by the CR.

- The CR sends a response containing the associated Credential-Id(s) to the Originator

- The Originator then associates the credential-Id(s) with the respective protected data

- The Originator establishes a secure communications channel with a Hosting CSE (HCSE)

- The Originator sends a request to register and host the protected data along with the associated Credential-Id(s) with the HCSE.

- The HCSE checks to ensure that the Originator is authorized to perform registration of protected data. If the Originator is deemed to be authorized then the HCSE registers and hosts the data along with the associated Credential-Id(s)

- The HCSE sends a response indicating “Success”

It should be noted that the CR function may be implemented as part of the CSE or as part of a centralized entity (e.g. Trusted-Third Party)

### ---End of changes ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?