| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 19 |
| Source:* | Vinod Choyi, Interdigital, vinod.choyi@interdigital.com |
| Date:* | 2015-09-05 |
| Contact:* | Same as above |
| Reason for Change/s:* | Identifying threats to data security |
| CR against: Release* | oneM2M R2 |
| CR against: WI* | X TR-0008 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0008-Security |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality X New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO X This CR is a mirror CR? YES NO X if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In an oneM2M system, entities may require service layer messaging in order to communicate data / content with another entity that may be multiple hops away. Messages that carry data / content may traverse multiple intermediate entities before the message reaches the final destination (receiver). An entity that generates, owns or hosts data would like to make sure that the integrity and confidentiality of the data is maintained from the originator to the receiver and hosted securely so that only authorized entities are able to view, process and modify the data.

### -----------------------Start of change 1-------------------------------------------

# 7	Security Vulnerabilities and Threats

## 7.xx Eavesdropping of data

| Threat ID | xx |
| --- | --- |
| Overview | Eavesdropping of data that is hosted on M2M entities (e.g. M2M service entities such as CSE) by un-authorized entities and copied. |
| Issue | Leakage and discovery of private data could lead to monetary and privacy loss and the leaked data may be used to perform additional attacks. |
| Description | Discovery may be achieved e.g. by reading the contents of memory locations or data stored within a datastore at the hosting entity. The methods of attack may include remote hacking and illicit use of management or maintenance interfaces or non-malicious access by the hosting entity, which is not authorized to access the data. The data may be e.g. sensor data or M2M service-related operational data |
| Impacted Use Cases | All |
| Affected Security domain | Application domain security; Intra Common Services domain security; Inter Common Services domain security |
| Affected Stakeholders | M2M Application Service Provider; Manufacturer of M2M System and its components; M2M Service Provider; System Administrator; User/Consumer. |
| Architecture impact | M2M Service infrastructure |

## 7.xy Un-authorized modification of data

| Threat ID | xy |
| --- | --- |
| Overview | Unauthorized modification of data that is hosted on M2M entities (e.g. M2M service entities such as CSE) by un-authorized entities. |
| Issue | Unauthorized modification of data could render the data useless or could lead to major ramifications to applications that uses the modified data. Unauthorized modification of m2m system data could lead to a denial-of-service of the M2M service. |
| Description | Unauthorized modification of data may be achieved e.g. by modifying the contents of memory locations or stored within a datastore at the hosting entity. The methods of attack include remote hacking and illicit use of management or maintenance interfaces or non-malicious access by the hosting entity, which is not authorized to modify the data. The data may be e.g. sensor data or M2M service-related operational data. |
| Impacted Use Cases | All |
| Affected Security domain | Application domain security; Intra Common Services domain security; Inter Common Services domain security |
| Affected Stakeholders | M2M Application Service Provider; Manufacturer of M2M System and its components; M2M Service Provider; System Administrator; User/Consumer. |
| Architecture impact | M2M Service infrastructure |

### -----------------------End of change 1 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?