| Input Contribution |
| --- |
| Meeting ID* | TP# 20 - SEC 20 |
| Title:* | SEC-2015-xxxx-TR-0012_Determining_Security_Requirements_based_on_Security_Profile |
| Source:* | vinod.choyi@interdigital.com dale.seed@interdigital.com |
| Uploaded Date:* | 2015-10-30 |
| Document(s) Impacted* | TR-0012 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TR-0012 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Introduction

This contribution proposes the use of a Security Profile (SP) in conjunction with a Device and or Application Profile in order to determine the security requirements and features associated with an entity.

### ---------------------------------------------------------------------------------------------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]			oneM2M TS-0001 “Functional Architecture”

[i.3]			oneM2M TS-0003 “Security Solutions”

[i.4]	oneM2M TS-0011 “Common Terminology”

# 8.5	Proposal for determining detailed Security Requirements, Features and associated Algorithms

## 8.5.1	Security Determination Process

#### 8.5.1.2	Overall Description

This section provides description on mechanisms that can be employed for determining the appropriate security requirements, features, and algorithms and associated credentials in order that the security mechanisms that are employed are adequate but at the same time efficient for the type of service offered by the entity and also does not drain valuable resources from the entity.

8.5.1.3				Detailed Description

Table 8.5.1.3-1 illustrates Entity Profile (EP) associated with an entity (e.g. AE1). The EP may be obtained or provided explicitly during the registration phase. It may be obtained as part of the M2M Subscription Profile associated with an entity. The EP provides a very high-level security requirement of the Entity. It may be used to derive and generate a more granular security requirement as illustrated in Figure 8.5.1.3-4. However, since the profile of the entity does not provide details of the device, the selection of the features may not be appropriate from a performance perspective.

It is

| Entity Profile | Values |
| --- | --- |
| Class of Service | Healthcare |
| Type of Service | Real-time |
| Impact | Critical (Life and Limb) |
| Security Level | High |

Table 8.5.1.3-1 Entity Profile of an Entity (e.g. AE1)

An example Device Profile (DP) is illustrated in Table 8.5.1.3-2. Using the DP as well as the EP, a more appropriate security requirements and features may be generated. So, a low-powered, low-memory device that only provides a service that requires “low” Security, then the security function(s), the algorithms selected and the key sizes may be selected appropriately. E.g. the message authentication mechanism selected may be HMAC-SHA1 with 160 bit keys whereas an entity with more processing and memory and requiring a higher security would be provisioned with 256 bit keys that may be used with HMAC-SHA2 mechanism.

| Device Capability | Values |
| --- | --- |
| Processing Capability | 900 MHz |
| RAM | 500 Kb |
| Flash | 1MB |
| Battery | 5.0 Micro-W/MHz |
| Wireless Capability | Bluetooth, WiFi |
| Sleep Mode | Sleep / Deep-Sleep |
| Secure Environment | Yes |
| Trusted Platform Module (TPM) | No |
| OS / version | Android / Kitkat |

Table 8.5.1.3-2 Device Profile of an Entity (e.g. AE1)

An example Security Profile (SP) is illustrated in Table 8.5.1.3-3. Even if both the EP and DP are available, in certain cases, it may not be enough to determine, for example, whether end-to-end security is required or if data at-rest security is required or not. In such cases, it would be preferable to be provided with an SP.

| Security Requirement | Within Security domain (at HCSE or RCSE) | End-to-End |
| --- | --- | --- |
| Message Originator Authenticity / Integrity | High | Very High |
| Message Re-play protection | High | Very High |
| Non-repudiation capability | Low | Low |
| Message Confidentiality | Medium | Medium |
| Data Confidentiality in Transit | High | High |
| Data Confidentiality at Rest | Medium | High |
| Data Integrity in Transit | High | Very High |
| Data Integrity at Rest | Medium | Very High |
| Service Availability | High | Very High |
| Data Availability | High | Very High |

Table 8.5.1.3-3 Entity Profile of an Entity (e.g. AE1)

An example security features that have been determined based upon the information provided in the SP, DP and EP is illustrated in Table 8.5.1.3-4.

| Entity ID | Security Features | Within Security Domain | End-to-End |
| --- | --- | --- | --- |
|  |  | Algorithms | Sizes | Protocol(s) | Algorithms | Sizes |
| AE1 | Message Originator Authenticity / Integrity | HMAC-SHA-2 | 256 / 512 | (D)TLS, JWS | HMAC-SHA-2 | 256 / 512 |
|  | Message Replay Protection | Nonce | 256 | N/A | Timestamp / Nonce + Sequence Number | 256 bits |
|  | Non-Repudiation | None |  | N/A | None |  |
|  | Message Confidentiality | AES | 112 | (D)TLS | AES | 192 |
|  | Confidentiality of Data in Transit | AES | 192 | (D)TLS, JWE | AES | 192 |
|  | Confidentiality of Data at Rest | AES | 256 | N/A | AES | 256 |
|  | Integrity of Data in Transit | HMAC-SHA-2 | 256 | (D)TLS, JWS | HMAC-SHA-2 | 256 |
|  | Integrity of Data at Rest | HMAC-SHA-512 | 512 | N/A | HMAC-SHA-512 | 512 |
|  | Authentication Mechanism | Symmetric Key | 256 | (D)TLS | Symmetric Key | 256 |
|  | Un-Authenticated use | YES |  |  |  |  |
|  | Authentication Process | Direct |  |  |  |  |
|  | Presence of Secure Element | YES |  |  |  |  |
|  | Integrity of Data |  |  |  |  |  |

Table 8.5.1.3-4: An example of detailed security features determined based on SP, EP and DP