| Input Contribution |
| --- |
| Meeting ID* | TP# 20 - SEC 20 |
| Title:* | SEC-2015-xxxx-TR-0012_End_to_End_Security_Credential_Generation_Process |
| Source:* | vinod.choyi@interdigital.com dale.seed@interdigital.com |
| Uploaded Date:* | 2015-10-30 |
| Document(s) Impacted* | TR-0012 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TR-0012 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Introduction

This contribution proposes the architecture for generation of end-to-end message protection mechanisms and associated credentials using symmetric keying.

### ---------------------------------------------------------------------------------------------------

## 2.2	Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

[i.2]			oneM2M TS-0001 “Functional Architecture”

[i.3]			oneM2M TS-0003 “Security Solutions”

[i.4]	oneM2M TS-0011 “Common Terminology”

[i.5]	IETF RFC 7518: “JSON Web Algorithms (JWA)”, 2015

[i.6]	IETF RFC 7526: “JSON Web Encryption (JWE)”, 2015

[i.7]		IETF RFC 7527: “JSON Web Key (JWK)”, 2015

[i.8]				IETF RFC 7525: “JSON Web Signature (JWS)”, 2015

[i.9]				IETF RFC 5869: “HMAC-based Extract-and-Expand Key Derivation Function (HKDF)”, 2010

# 8.4	A Solution for providing End-to-End Message Authentication using Symmetric Key

## 8.4.1	End-to-End Security Credential(s) Generation Process

#### 8.4.1.2	Overall Description

This section provides description on mechanisms that can be employed for generation of credential(s) that are to be used for end-to-end security. Based on security requirements associated with an Entity (e.g. AE), appropriate end-to-end security credentials may be generated.

8.4.1.3				Detailed Description

Table 8.4.1.3-1 illustrates the end-to-end security requirements that have been determined and provided by the entity (e.g. AE1) or determined based on a security profile associated with AE1. The table illustrates that AE1 provides or requires the following:

- End-to-End message authentication using a Message Integrity Code (MIC)

- Also provides for or requires the ability to verify the integrity of data in-transit

- End-to-End message confidentiality in transit and thereby also provides for end-to-end data confidentiality in-transit.

| Security Requirement | End-to-End |
| --- | --- |
| Message Originator Authenticity / Integrity | Message Integrity Code (MIC): 256 bits |
| Message Re-play protection | Nonce / Random / Time Component |
| Non-repudiation capability | None |
| Message Confidentiality | Encryption: 256 bit encryption |
| Confidentiality of Data in Transit | Encryption: 256 bit encryption |
| Confidentiality of Data at Rest | None |
| Integrity of Data in Transit | Message Integrity Code (MIC): 256 bits |
| Integrity of Data at Rest | None |

Table 8.4.1.3-1 End-to-End Security Requirements

Based on the higher-level requirements appropriate end-to-end credentials may be generated using either bootstrapping process (preferable approach) or by using pre-provisioned end-to-end credentials. Illustrated in Figure 8.4.1.3-1 is a high-level key generation process.

As part of the “Generation of End-to-End Key Generation” Phase, the enrolee and the enrolment target generates End-to-End credentials using the Kpsa or Km as the master key in order to generate the End-to-End master key. If the enrolee is an AE, and the Enrolment Target is a CSE, then an end-to-end master credential, Ke2e_AE_CSE_master is generated. Alternatively, if the target is a MAF, then the Km would be used as the master key for the generating the End-to-End master key. An Example of End-to-End Key Generation using RFC 5809 is provided below:

Ke2e_AE_CSE_master = HMAC-Hash (Salt, Kpsa_AE_CSE) or

Ke2e_AE_MAF_master = HMAC-Hash (Salt, Km_AE_MAF)

Using the generated end-to-end master key, the associated end-to-end message authentication and or end-to-end message confidentiality keys are generated in the following manner:

T(0) = empty string (zero length)

Ke2e_AE_CSE_msg_auth = T(1) = HMAC-Hash (Ke2e_AE_CSE_master, T(0) | “E2E Message Authentication Key”| 0x01)

Ke2e_AE_CSE_msg_conf = T(2) = HMAC-Hash (Ke2e_AE_CSE_master, T(1)| “E2E Message Confidentiality Key”|0x02)

This process is repeated by each Enrolee and associated Enrolment Target based on a unique Enrollee-EnrolmentTarget_Ke2e_master that is shared between the Enrolee and the Enrolment Target (e.g. AE and CSE specific end-to-end keys).

Figure: 8.4.1.3-1: End-to-End Key Generation Phase

An example list of generated keys illustrated in Table 8.4.1.3-2:

| Security | Symmetric Keys Generated and Used | Parameters |
| --- | --- | --- |
| Message Originator Authenticity / Integrity | Ke2e_EntityA_EntityN_msg_auth | None |
| Message Re-play protection | Ke2e_EntityA_EntityN_msg_auth | Nonce / Time / Seq# |
| Non-repudiation capability | N/A | N/A |
| Message Confidentiality | Ke2e_EntityA_EntityN_msg_conf | IV |
| Confidentiality of Data in Transit | Ke2e_EntityA_EntityN_msg_conf | IV |
| Confidentiality of Data at Rest | None | None |
| Integrity of Data in Transit | Ke2e_EntityA_EntityN_msg_auth | Nonce / Time / Seq# |
| Integrity of Data at Rest | None | None |

Table 8.4.1.3-2: Depicting example keys that generated and associated parameters