| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#20 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2015-11-04 |
| Contact:* | As above |
| Reason for Change/s:* | Provides a high level description of the end-to-end security framework for a single-envelope security session, in which the envelope contains all key parameters needed for intended entities to process the secured payload in the envelope. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenace / < Work Portion number(optional)> STE Small Technical Enhancements / < Work Portion number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 and v0.6.0 |
| Clauses/Sub Clauses* | Clause 6.2.2 “ESF Security Layer for Single-Envelope Security Session-Type (ESF-S1)”, Clause 7.x.2 “Requirements for the ESF-S1 Reference Points” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution is one of a series on the End-to-End Security Framework (ESF). For details on this series, see introduction to SEC-2015-06xx-CR_TR-0012_ESF_Intro.

The present contribution proposes high level details for End-to-End Security Framework for ESF-S1 (One-way Single envelope) security sessions: ESF-S1 is based on the ESF reference model – the ESF reference model is described in proposed text for clause 6.2.2 in contribution “SEC-2015-06xx-CR_TR-0012_ESF_Ref_Model”.

ESF-S1 envelopes are comprised of

- Key establishment parameter: sufficient for the Target ESF End-Point(s) (EEPs) to compute or obtain the keys for securing the payload, and

- Secured payload: protected using the keys computed or obtained using the key establishment parameters.

This contribution proposes text for

- Clause 6.2.2.1	“ESF-S1 High Level Architecture”: The ESF-S1 call flow including a figure and descriptive text

- Clause 7.x.2 “ESF-S1 Requirements”, including list of proposed “crypto algorithm classes” for key establishment and payload security.

This contribution provides high level architecture and requirements only. Further architecture-level details are left for consideration in clause 8 “Description and Analysis of Available Options”.

NOTE TO RAPPORTEUR: The references in the text currently use short labels (e.g. [RFC6749]), and the assignment of proper reference labels (e.g. [i.7]) is currently left to the rapporteur. The references are currently highlighted in yellow, to assist in finding the references within the proposed text.

R01: editorial changes.

### -----------------------Start of change 1-------------------------------------------

##### 6.2.2.2	 ESF-S1 Processing flow

ESF-S1 supports an envelope having a single Source EEP and one or more Target EEPs.

Figure 6.2.2.1-1 shows the processing flow when using this session type.

Figure 6.2.2.1-1 Processing flow for single envelope session type (S1).

- EEPs can interact with Facilitators to provide the Facilitators with long-term parameters (that is, parameters with long lifetime) and/or short-term parameters (that is, parameters with a short lifetime). This step is not expected to be mandatory.

  - (Optional). EEPs could provide interact with one or more Facilitators to provide long-term parameters (that is, parameters with long lifetime) that the other EEPs can use for either for

    - Generating S1 session envelopes, as Source EEPs, or

    - Processing received envelopes, as Target EEPs.

Example long-term parameters include

    - List of supported Key Establishment Algorithm-Sets (keAlgSets)

    - List of supported Payload Security Algorithm-Sets (psAlgSets)

    - Certificates

    - Security Profile

This interaction is expected to happen relatively infrequently – possibly only once in the lifetime of the EEP. The Facilitator(s) store the parameters and make them available for retrieval.

Editor’s note: access to the parameters may be controlled

  - (Optional). EEPs could provide interact with one or more Facilitators to update short-term parameters that can be provided to other EEPs for either for

    - Generating S1 session envelopes, as Source EEPs, or

    - Processing received envelopes, as Target EEPs.

Example, short-term parameters include

    - Random values with short lifetime; these might be used as challenges for authentication.

    - Secret keys with short lifetime; these might be used as challenges for authentication.

The Facilitator(s) store the parameters and make them available for retrieval.

This interactions are expected to happen relatively infrequently – possibly only once in the lifetime of the EEP.

Editor’s note: access to the parameters may be controlled

- The Source EEP provides the Security Layer Functions with

  - Target Data, and

  - (Optional) Security profile applicable to the Target Data,

  - Editor’s note: The security profile text might need expanding.

  - Identifiers for the intended Target EEPs. This could include individual identifiers and group identifiers.

This triggers the resulting call flow.

- Source EEP Key Establishment processing:

- Editor’s note: It could be appropriate to discuss here how the Source EEP determines the minimum security levels to be applied and what session type should be applied. It is worth discussion where the decision is made – Preparation Function, Security Function etc.. Interaction with security profiles should be considered.

  - (Optional) The Source EEP could retrieve the Target EEP(s)’ long-term and/or short-term parameters from the Facilitator(s).

Editor’s note: access to the parameters may be controlled

Editor’s note: How the Key Establishment identifies the appropriate Facilitators to contact is FFS.

  - The Source EEP selects one or more Key Establishment Algorithm-Sets (keAlgSet) and Payload Security Algorithm-Set (psAlgSet).

  - NOTE: Multiple keAlgSets could be needed only in some (but not all) scenarios involving multiple Target EEPs.

  - The selection of Algorithm Sets could be influenced by

    - The combinations of keAlgSets and psAlgSets  supported by the Source EEP.

    - Preferences configured to the Source EEP .

    - The combinations of keAlgSets and psAlgSets   supported by the Target EEP(s), which may have been either configured to the Source EEP or retrieved by the Source EEP from the Facilitators in (optional) step 3.a.

The choices of keAlgSet(s) and psAlgSet are somewhat dependent on each other; in particular, if the psAlgSet includes encryption and/or symmetric-key based integrity protection of the target data, then the keAlgSet(s)  must include an algorithm for generating a secret key to be used for this protection. A high level overview of possible psAlgSet  Options is found in clause 7.x.2.2 “ESF-S1 Payload Security Requirements”. A high level overview of possible keAlgSet options is found in clause 7.x.2.3 “ESF-S1 Key Establishment Requirements”.

  - The Source EEP applies the selected keAlgSet(s), which can include

  - Proof of the Source EEP’s identity,

  - Proof of the integrity of the selected keAlgSet(s) and psAlgSet, and

  - Generation of keys for processing the target data.

  - (Optional) The Source EEP provides the Facilitator(s) with updated Short-term Key establishment parameters. This may include configuring access controls at the Facilitator to limit access only to the set of intended Target EEPs.

  - Source EEP Payload Security processing. The Source EEP applies the selected psAlgSet to the input payload using the key(s) provided by the Source EEP, resulting in the ESF-treated target data.

  - Source EEP Envelope Serialization: The Source EF serializes the keAlgSet(s), psAlgSet, key establishment parameters and ESF-treated target data into an envelope.

- The envelope is obtained by the Target EEP(s). The Security Layer does not address how the Target EEP(s) obtain the envelope.

NOTE: The following discussion shows processing at one of the potentially multiple Target EEPs.

  - Target EEP Envelope Serialization processing: The Target EF extracts the keAlgSet(s), psAlgSet, key establishment parameters and ESF-treated target data from the received envelope.

- Target EEP Key Establishment processing: In the case that there are multiple Key Establishment Algorithm Sets present, the Target EEP identifies a Key Establishment Algorithm Set that it expects to process successfully.

  - (Optional) The Target EEP could retrieve the Source EEP’s long-term and/or short-term parameters from the Facilitator(s). The Facilitator(s) could authorize access based on configured access controls.

  - The Target EEP applies the selected Key Establishment Algorithm Set, which can include

  - Verifying the identity of Source EEP,

  - Verifying the selected keAlgSet(s) and psAlgSet, and

  - Generation of keys for processing the input payload.

  - Target EEP Payload Security processing : The Target EEP applies the selected psAlgSet  to the secured payload using the established key(s), resulting in the verified target data.

  - The Target EEP outputs:

  - The verified target data, and

  - Source EEP’s identity.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

#### 7.x.2 	ESF-S1 Requirements

##### 7.x.2.1	ESF-S1 Macro-Considerations

In addition to the macro-considerations in clause 7.x.1.1 “ESF Security Layer Macro-Considerations”, the following ESF-S1-specific macro-considerations are proposed:

Editor’s note: there are currently no ESF-S1-specific macro-considerations. Members are invited to provide ESF-S1-specific macro-considerations. If there are no ESF-S1-specific macro-considerations then this clause can be deleted.

##### 7.x.2.2	ESF-S1 Payload Security  Requirements

A Payload Security Algorithm Class (psAlgCl) describes the type of protection that is afforded the input payload; suggested Payload Security Algorithm Classes for oneM2M Release 2 are listed in Table 7.x.2.2-1 “List of ESF-S1 Payload Security Algorithm Class (AlgCl) options”. This list is not necessarily exhaustive, and other options could be available.

Editor’s note: members are invited to provide other options for consideration.

The selection of algorithms for each AlgCl is discussed in clause 8 “Description and Analysis of Available Options”.

Editor’s note: Should advantages and disadvantages of each Algorithm Class be documented in the present document or TR-0008 [TR0008]?

| Payload Security Algorithm Class | Example mechanism | Brief Description | Target Data | Keys that must be established |
| --- | --- | --- | --- | --- |
| Symmetric integrity protection only | MIC | Source EEP and Target EEP(s) use a symmetric key for integrity protection, but not confidentiality. Target EEPs can impersonate the Source EEP. For this psAlgCl, ESF does not perform encryption. | AAD only | Payload security processing requires a symmetric envelope master key established between the Source EEP and Target EEP(s) |
| Symmetric confidentiality and integrity protection | AEAD | Source EEP and Target EEP(s) use a symmetric key for confidentiality and integrity protection. Target EEPs can impersonate the Source EEP | Plaintext + (optional) AAD |  |
| Symmetric confidentiality and non-repudiation protection | AEAD + Digital Signature | Source EEP and Target EEP(s) use a symmetric key for confidentiality and digital signature for non-repudiation. Target EEPs cannot impersonate the Source EEP. Use of Authenticated Encryption is suggested. | Plaintext + (optional) AAD | Payload security processing requires a symmetric envelope master key established between the Source EEP and Target EEP(s); additional the Source EEP uses a digital signature private signing key and the Target EEP(s) use a digital signature public verification key. |
| Non-repudiation protection only | Digital Signature | Source EEP and Target EEP(s) use a digital signature for non-repudiation. For this psAlgCl, ESF does not perform encryption. | AAD only | Source EEP uses a digital signature private signing key and the Target EEP(s) use a digital signature public verification key. |

Table 7.x.2.2-1 List of ESF-S1 Payload Security Algorithm Class (psAlgCl) options.

##### 7.x.2.3	ESF-S1 Key Establishment Requirements

The psAlgCl in Table 7.x.2.2-1 “List of ESF-S1 Payload Security Algorithm Class (AlgCl) options” which require a digital signature public verification key are:

- AEAD + Digital Signature, and

- Digital Signature.

If one of these psAlgCl are used, then a digital signature public verification key is provided for additional verification of the input payload. The digital signature public verification key could be provided in a certificate communicated as key establishment parameter in envelope or via Facilitator. The Target EEP verifies the certificate prior to verifying the digital signature on the target data.

The psAlgCl in Table 7.x.2.2-1 “List of ESF-S1 Payload Security Algorithm Class (psAlgCl) options” which require an envelope master key are:

- Symmetric integrity protection

- Symmetric confidentiality and integrity protection, and

- Symmetric confidentiality and integrity protection + non-repudiation.

- A Key Establishment Algorithm Class (keAlgCl) describes the type of key establishment mechanisms used to establish an envelope master key; suggested Key Establishment Algorithm Classes for oneM2M Release 2 are listed in Table 7.x.2.3-1 “List of ESF-S1 Key Establishment Key Establishment Algorithm Class (AlgCl) options”. This list is not necessarily exhaustive, and other options could be available. This list is not intended to constrain the options considered for establishing an envelope master key.

Editor’s note: Should advantages and disadvantages of each Algorithm Class be documented in the present document or TR-0008 [TR0008]?

| Name | Brief Description |
| --- | --- |
| Trusted Third Party (TTP) | The Source EEP requests a Facilitator to store the envelope master key with an associated set of permissions. The Facilitator could optionally generate the envelope master key for the Source EEP. The Source EEP and Facilitator agree on a unique envelope master key identifier for the envelope master key, and this envelope master key identifier is provided in the envelope. After the Target EEP retrieves the envelope, then the Target EEP provides the envelope master key identifier to the Facilitator. If the Target EEP has the necessary permissions, then the Facilitator provides the envelope master key to the Target EEP. This requires a high degree of trust in the Facilitator, and communication with the Facilitator (form both the Source EEP and Target EEP) must be mutually authenticated and secured. |
| Pre-Provisioned Shared Key | The envelope master key is provided to the Source EEP and Target EEP(s) via mechanisms not specified by oneM2M (e.g. manual input, pre-provisioning). |
| Key Encryption | The Source EEP selects a set of Target EEPs for which the Source EEP knows a public encryption key of the Target EEP (for example, the public encryption keys could be in certificates, or Identity Based Encryption might be applied) or the Source EEP shares a symmetric key encryption key (KEK). For each Target EEP, then Source EEP encrypts the envelope master key using either the public encryption key or KEK and includes the resulting encrypted envelope master key in the envelope. The envelope includes an encrypted envelope master key for each Target EEP. After the Target EEP retrieves the envelope, then the Target EEP uses its private decryption key or KEK (shared with the Source EEP) to decrypt its encrypted envelope master key and obtain the envelope master key. The mechanism could optionally authenticate the Source EEP; e.g by including a digital signature that can be verified using a certificate of the Source EEP. |
| Key Agreement | (This approach can work only if there is a single Target EEP). The Source EEP and Target EEP applies a key agreement protocol to establish a shared key. For example, the Source EEP could use a Diffie-Hellman protocol [ReferenceNeeded] using a public key in a certificate of the Target EEP. The mechanism could optionally authenticate the Source EEP; e.g. by including a digital signature that can be verified using a certificate of the Source EEP. |

Table 7.x.2.3-1 List of ESF-S1 Key Establishment Algorithm Class (AlgCl) options which could be considered for establishing an envelope master key.

##### 7.x.2.4	ESF-S1-Specific ESF Facilitation Requirements

Proposed ESF-S1-specific Requirements. In addition to the generic requirements in clause 7.x.1.3 “Generic ESF Key Establishment Requirements”, the following ESF-S1-specific requirements are proposed:

- ESF Facilitation shall support Facilitators acting as a repository of long-term key parameters associated with an ESF End-Point which could including

  - List of supported ksAlgSets.

  - List of supported psAlgSets.

  - List of Certificates or public keys.

These parameters could be used in the Key Encryption, Key Agreement and Digital Signature Algorithm Classes in Table 7.x.2.3-1 “List of ESF-S1 Key Establishment Algorithm Class (AlgCl) options”

- ESF Facilitation may support Facilitator acting as a repository of the latest provided short-term key parameters associated with an ESF End-Point, which could including

  - A short-lifetime randomly-generated, non-secret value – e.g. for use as challenges in authentication or for adding non-secret entropy to key generation.

  - A short-lifetime public key value – e.g. EC-DH public key for adding perfect forward secrecy (PFS).

NOTE: The case of using a short-lifetime secret value – e.g. for use as adding secret entropy to key generation – is already covered by the first ESF Facilitation requirement “The reference point supports EEPs obtaining symmetric (secret) keys through interaction with trusted Facilitators” in clause 7.x.1.3 “Generic ESF Key Establishment Requirements”.

These parameters could be used in the Key Encryption, Key Agreement and Digital Signature Algorithm Classes in Table 7.x.2.3-1 “List of ESF-S1 Key Establishment Algorithm Class (AlgCl) options”

##### 7.x.2.5	ESF-S1 Envelope Serialization Requirements

Proposed ESF-S1 Envelope Serialization requirements. In addition to the generic requirements in clause 7.x.1.5 “Generic ESF Envelope Serialization Requirements”, the following ESF-S1-specific Envelope Serialization requirements are proposed:

- The ESF-S1 Envelope Serialization supports representing secured payloads for the Payload Security Algorithm Classes in clause 7.x.2.2 “ESF-S1 Payload Security Requirements”.

- The ESF-S1 Envelope Serialization supports representing key establishment parameters for the Key Establishment Algorithm Classes in clause 7.x.2.3 “ESF-S1 Payload Security Requirements”.

- The ESF-S1 Envelope Serialization supports representing the keAlgSet and psAlgSet”.

JSON Representations. The IETF JOSE specifications [references] can provide a JSON representation of the ESF-S1 secured payload and key establishment parameters. The generic envelope serialization requirements and the proposed ESF-S1 Envelope requirements could be satisfied by be an envelope which is a JSON element comprised of

- An identifier for the security session type (in this case indicating S1), followed by

- One or more JOSE data elements containing the ESF-S1 key establishment parameters and ESF-S1 secured payload.

XML Representations. The W3C XML-SIG [i.26] and XML-ENC [i.28] can provide a XML representation of the ESF-S1 secured payload and key establishment parameters. The generic envelope serialization requirements and the proposed ESF-S1 Envelope requirements could be satisfied by be an envelope which is a XML element comprised of

- An identifier for the security session type (in this case indicating S1), followed by

- One or more XML-SIG and/or XML-ENC data elements containing the ESF-S1 secured payload and key establishment parameters.

Detailed proposed specification for JSON serialization and XML serialization are provided in clause 8.

Editor’s note: The above sentence anticipates detailed specifications will be provided in clause 8. If detailed specifications are not provided, then the above sentence should be deleted.

### -----------------------End of change 2---------------------------------------------

### Add the following references to clause 2.2. “Informative references”

### -----------------------Start of Changes to References Section -------------

[RFC5166] 	IETF RFC 5166: “An Interface and Algorithms for Authenticated Encryption”, 2008

### -----------------------End of Changes to References Section -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations and acronyms

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

End-to-End Security: Provides for securing messages that can traverse multiple hops between communication entities. Securing of messages involves mutually authenticating the end entities. Securing of messages also involves providing confidentiality and integrity protection of messages in order that end entities are assured that the messages have not been altered or eavesdropped by un-authorized entities.

End-to-End Authentication: Provides an entity with the ability to validate another entity’s identity that was supplied as part of the message. The communicating entities can be multiple hops away.

Canonical:	A unique and unambiguous representation of data [i.17]

Canonicalization:	The process of converting a legal representation of data into its canonical form.

Object-based security:	technology embeds application data within a secure object that can be safely handled by untrusted entities [i.19]

End-to-End Data Integrity Protection: Provides the ability for an entity to integrity protect data.. The integrity protected data can be transported over multiple hops consisting of trusted or untrusted communication entities. An authorized consumer of the data is able to verify the integrity of data and is also able to verify the originator of the data. Such a protection mechanism would ensure that the data is integrity protected “at-rest” and “in-transit” even when handled by intermediate nodes.

End-to-End Data Confidentiality Protection: Provides the ability for an entity to provide for confidentiality protection of data. The confidentiality protected data can be transported over multiple hops consisting of trusted or untrusted communication entities. Only authorized entities can decrypt the confidentiality protected data. Such a protection mechanism would ensure that the data is confidentiality protected “at-rest” and “in-transit” even when handled by intermediate nodes.

Authenticated Encryption with Associated Data: An algorithm providing confidentiality for the plaintext and a way to check its integrity and authenticity while providing the ability to check the integrity and authenticity of some associated data. In this context: plaintext refers to data that is authenticated and encrypted; and associated data refers to data that is authenticated, but not encrypted. See [RFC5116] for further details.

Editor’s Note: the definitions are subject to further refinement.

NOTE:	This may contain additional information.

## 3.4	Acronyms

For the purposes of the present document, the abbreviations [2] apply:

AMI	Advanced Metering Infrastructure

AEAD	Authenticated Encryption with Associated Data

DAP	Data Aggregation Point

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---