| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#20 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2015-11-02 |
| Contact:* | As above |
| Reason for Change/s:* | Provides the ESF Preparation Layer and ESF Integration Layer Processing for ESF Target Data Class 2 protecting the Content parameter of requests and responses. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenace / < Work Portion number(optional)> STE Small Technical Enhancements / < Work Portion number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 and v0.7.0 |
| Clauses/Sub Clauses* | New Clause 6.3.2 “ESF Specifications for ESF Target Data Class 2” |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution is one of a series on the End-to-End Security Framework (ESF). For details on this series, see introduction to SEC-2015-0633-CR_TR-0012_ESF_Intro.

The present contribution provides the ESF Preparation Layer and ESF Integration Layer Processing for ESF Target Data Class 2 which protects the Content parameter of requests and responses.

NOTE TO RAPPORTEUR: The references in the text currently use short labels (e.g. [RFC6749]), and the assignment of proper reference labels (e.g. [i.7]) is currently left to the rapporteur. The references are currently highlighted in yellow, to assist in finding the references within the proposed text.

### -----------------------Start of change 1-------------------------------------------

### 6.3.2	ESF Specifications for ESF Target Data Class 2

#### 6.3.2.1	Profile for ESF Target Data Class 2

Table 6.3.2.1-1 “Profile for ESF Target Data Class 2” contains the profile for ESF Target Data Class 2.

| Aspect | Description |
| --- | --- |
| ESF Target Data Class Identifier | 2 |
| Input item | A request or response |
| Target data | A serialization of the Content parameter of the input request or response |
| Treated Item | The input request or response with the original Content parameter replaced by the envelope produced by the ESF Security Layer. |
| EEP Constraints | The present document allows an EEP to be the Originator or Hosting CSE of the input request or response or any other CSE on the oneM2M path between the Originator and Hosting CSE of the input request or response. |
| Security Layer Constraints | There can be only one receiving EEP. |

Table 6.3.2.1-1 Profile for ESF Target Data Class 2

#### 6.3.2.2	ESF Target Data Class 2 Processing at the Sending EEP

The follow steps occur at a Sending EEP when applying this ESF Target Data Class to an outbound request or response

- The EEP’s Preparation Function extracts the Content parameter of the request or response, and serializes the Content parameter to form the target data.

- The EEP’s Preparation Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Target data, and

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating an envelope.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then at the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two outbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the envelope and applicable ESF Target Data Class identifier to the EEP’s Integration Function. The envelope is serialized as is XML or JSON.

- The EEP’s Integration Function forms the ESF-treated request or response from the input request or response by updating values of the following parameters

  - Content:  The original value is replaced with the envelope received from the ESF Security Function.

  - Resource Type: replacing this with a reserved identifier for ESF-protected Content parameter.

- The EEP’s Integration Function passes the ESF-treated request or response to the next step in processing outbound messages.

#### 6.3.2.3	ESF Target Data Class 2 Processing at the Receiving EEP

The follow steps occur at a Receiving EEP when applying this ESF Target Data Class to an inbound request or response

- The EEP’s Integration Layer parses the received message to identify the sending EEP and extract

  - Content: comprises the envelope. The envelope is serialized as is XML or JSON.

  - Resource Type: a reserved identifier for protected requests and responses protected by ESF Target Data Class 2.

- The EEP’s Integration Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Envelope.

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating a verified target data. This processing includes verification that the provided ESF Target Data Class identifier is correct.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then at the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two inbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the EEP’s Preparation Layer with

  - Verified target data, comprising a serialization of the original value of the Content parameter.

  - There is no additional data for this ESF Target Data Class

- The EEP’s Preparation Function

  - Parses the target data to form the value of the verified Content parameter.

  - (If the Content parameter contains a resource) Determines the resource type of the verified Content parameter.

  - Forms the verified request or response by updating values of the following parameters

- Content:  The value in the received request or response is replaced with the value received from the ESF Security Function in the target data.

- (if the verified  Content parameter contains a resource) Resource Type: replacing this with the resource type of the resource in the verified Content parameter.

- The EEP’s Preparation Function passes the verified request or response to the next step in processing inbound messages.

### -----------------------End of change 1---------------------------------------------