| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#20 |
| Source:* | Datang |
| Date:* | 2015-11-09 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Reason for Change/s:* | Providing more detail about the procedure of evaluating heterogeneous access control policies and some editorial changes. |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0016 and v0.4.1 |
| Clauses/Sub Clauses* | 7.3.1 Proposal 1: Solution of Supporting Heterogeneous Access Control Policies |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR proposes provides more detail about the procedure of evaluating heterogeneous access control policies and some editorial changes

### -----------------------Start of change 1-------------------------------------------

# 7	Supporting user specified access control policies

## 7.1	Issues

According to the description in clause 9.6.2 of oneM2M TS-0001 [1] and in clause 7.1 of oneM2M TS-0003 [2], the current authorization solution does not support heterogeneous access control policies. As it is difficult to predicate all the authorization requirements of the oneM2M system and then design a versatile authorization system to satisfy all authorization requirements, it is reasonable for the oneM2M access control system to support user-defined access control mechanisms and/or access control policy languages..

## 7.2	Solutions

### 7.2.1	Proposal 1: Solution of Supporting Heterogeneous Access Control Policies

#### 7.2.1.1	Introduction

This clause describes a solution that extends the current oneM2M authorization system to support heterogeneous access control policies.

In the oneM2M authorization system there are two types of access control policies. One type is evaluated in PDP, another type is enforced in PEP such as privacy related access control policies. Access control policies enforced in PEP is also called obligation policy.

#### 7.2.1.2	Redefined Resource Type accessControlPolicy

The redefined <accessControlPolicy> resource is shown in the Figure 7.2.1.2-1.

Figure 7.2.1.2-1: Redefined <accessControlPolicy> resource

In the redefined <accessControlPolicy> resource the modified and the new defined attributes are specified in table 7.2.1.2-1.

Table 7.2.1.2-2: New defined/modified attributes of <accessControlPolicy> resource

| Attributes of <accessControlPolicy> | Multiplicity | RW/ RO/ WO | Description | <accessControlPolicyAnnc> Attributes |
| --- | --- | --- | --- | --- |
| privileges | 0..1 | RW | A set of access control rules that applies to resources referencing this <accessControlPolicy> resource using the accessControlPolicyID attribute. | MA |
| policyRef | 0..1 | RW | A reference to an access control policy, from which access control policy can be retrieved. | MA |
| policyCategory | 0..1 | RW | PDP uses this attribute for selecting a suitable policy evaluator to evaluate the access control policy specified in privileges or policyRef attribute. | MA |
| policyType | 1 | RW | This attribute indicates the access control policy specified in policyRef attribute should be evaluated in a PDP or in a PEP. | MA |

#### 7.2.1.2	Generic Procedure of Evaluating Heterogeneous  Access Control Policies

The generic procedure of evaluating heterogeneous access control policies is shown in figure 7.2.1.2-1 and described as follows:

- The process in PRP:

The PRP generates two policy sets named as ACPSet and ObligationSet respectively. The ACPSet is used for keeping the access control policies enforced by a PDP. The ObligationSet is used for keeping the obligation policies enforced by a PEP.

The PRP retrieves all applicable access control policies according to an access control policy request.

The PRP puts the applicable policies that should be enforced by the PDP into the ACPSet, and puts the applicable policies that should be enforced by the PEP into the ObligationSet.

The PRP returns both ACPSet and ObligationSet back to the PDP via an access control policy response.

- The process in PDP:

The PDP evaluates an access control decision request against the policies stored in the ACPSet, and makes an access control decision.

If the result of policy evaluation is “permit” and the ObligationSet is not empty, the PDP should return both the access control decision and the ObligationSet back to the PEP, otherwise only the access control decision should be returned back to the PEP via an access control decision response.

- The process in PEP:

The PEP enforces the access control decision, and fulfills the obligation policies in the ObligationSet if they accompany the access control decision.

Figure 7.2.1.2-1: Generic procedure of evaluating heterogeneous access control policies

### -----------------------End of change 1---------------------------------------------