| Input Contribution |
| --- |
| Meeting ID* | SEC 20 |
| Title:* | TS-0016 AE discovery and selection |
| Source:* | Sungcheol Park, KT, sungcheol.park@kt.com |
| Uploaded Date:* | 2015-11-11 |
| Document(s) Impacted* | WI-0021; TS-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TS-0016 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 1	Introduction

This contribution provides a proposal for Application Entity discovery and selection. The document(TS-0016) has getSecureEnvironment, getSEFunctions and getSecureEnvironment, but there is no functions for AEs. A field domain node may have one or more SEs, and SE may be removable. So we need to get a list of available SE, to select a SE, and to use the functions of the SE. A SE may have one or more AE. An AE issuer may create, activate, deactivate, delete AE. And each AE may be issued by different issuers. So each AE has different sensitive functions. And also, CSE need to check what AEs are available when a new SE connected. Because of these, an application for an AE needs to get a list of available AE, to select AE, and to use the functions of the AE.

A SE may has its sensitive functions to access control of SE and to management AEs. For example, An access control function of SE may permit based on its access control policy and data. And remote application management function may load, activate and delete AEs.

An AE may has its dedicated sensitive functions, such as access control function, application dedicated cipher function and sensitive application data management function.

# 2	Proposal

## 7.X	AE Discovery and Selection

### 7.X.1	getApplicationEntity

#### 7X.1.1	Description

This service provides a list of available AE provided by a given SE. A SE may have one or more AEs. A SE may be inserted and be removed physically. Application provider which issued AEs may create, update and delete the AEs. Because of these, CSE or an application for the AE need to check available AEs.

#### 7.X.1.2	Pre-Conditions

M2M-SE-ID is known to the calling entity (getSecureEnvironment).

#### 7.X.1.3	Signature – getApplicationEntity

Table 7.3.1.3-1: getApplicationEntity

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| seId | IN | NO | M2M-SE-Identifier |
| applicationId | IN | NO | Application Identifier (App-ID) for the AE |
| responseType | OUT | NO | Response types: List of available Application Entities include their M2M-AE-IDs and their provided security level No Application Entity available (but SE exists) Application Entities do not exist |

### 7.X.2	getAEFunctions

#### 7.X.2.1	Description

This service provides a list of available sensitive functions provided by a given AE. Unlike getSEFunctions is related with the functions of SE, getAEFunctions is related with dedicated functions to the AE. For example, a mobile TV application shall get permission to access the SE from the access control function of the SE, and then the application should request the multimedia content decryption to the decoding function of the AE.

#### 7.X.2.2	Pre-Conditions

M2M-AE-ID is known to the calling entity (getApplicationEntity).

#### 7.X.2.3	Signature – getAEFunctions

Table 7.3.2.3-1: getAEFunctions

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | NO | M2M-AE-Identifier |
| applicationId | IN | NO | Application Identifier (App-ID) for the AE |
| responseType | OUT | NO | Response types: List of available sensitive functions No sensitive function available (but AE exists) AEs do not exist |

### 7.X.3	selectApplicationEntity

#### 7.X.3.1	Description

Selects a particular Application Entity available within the present entity.

#### 7.X.3.2	Pre-Conditions

Not applicable.

#### 7.X.3.3	Signature – selectApplicationEntity

Table 7.4.1.3-1: selectApplicationEntity

| Parameter name | Direction | Optional | Description |
| --- | --- | --- | --- |
| aeId | IN | conditional | M2M-AE-ID |
| secLevel | IN | conditional | Types: AE with highest available security level to be selected AE with a particular security level to be selected |
| responseType | OUT | NO | Response types: Security level of selected AE together with aeId Security level or selected AE does not exist |
| Note: conditional is to be interpreted as mandatory if no other conditional parameter does exist. |