| Input Contribution |
| --- |
| Meeting ID* | SEC 20 |
| Title:* | TS-0016 profile management |
| Source:* | Sungcheol Park, KT, sungcheol.park@kt.com |
| Uploaded Date:* | 2015-11-12 |
| Document(s) Impacted* | WI-0021; TS-0016 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | For discussion and decision to be included into TS-0016 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 1	Introduction

This contribution provides a proposal for a profile resource.

# 2	Proposal

### 7.X.1	<Profile> resource

SEs or AE_SECs provide a service to store and protect profile data. A profile is the representation of parameters and data for its application, keys, and load files. The responsibility for defining which SE/AE_SEC can be used as target SEs/AE_SECs for customizing the SE/AE_SEC rests with the SE/AE_SEC issuer. Hence, the AE_SEC issuer defines business rules for each SE/AE_SEC offering in terms of which are acceptable SE/AE_SECs to use for each application for the SE/AE_SEC.

Editor’s note 1: The intention is to have this resource stored in the SE, which assumes presence of a CSE_SEC inside the SE. The figure 5.2-1 does not currently have a CSE-SEC. This conflict first needs to be resolved .

Figure 7.5-1: <profile>representation

Attributes in < profile > are shown in table 7.5-1.

Table 7.5-1: Attributes of < profile > resource

| Attributes of <profile> | Multiplicity | RW/ RO/ WO | Description | <profile> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created, and the lastModifiedTime value is updated when the resource is updated. | NA |
| creator | 1 | RO | The issuer identification of the profile. | NA |
| profileType | 1 | RO | Profile type: SE Profile: SE profiles template or image that describes every SE which will be or has been customized. AE_SEC Profile: AE_SEC Profiles contain the scripts necessary to customize the application, including the data preparation. The AE_SEC profiles contain the scripts as well as the data element references and key references required for script execution. | NA |
| conflictRules | 1 | RO | The rules which the profile must satisfy before being utilized. | NA |
| cryptoEngine | 0..1 | RO | Describes characteristics of the cryptographic engine in terms of key type and algorithm support. | NA |
| key | 1..n | RO | Specify key definition inheriting features of specified Key Profile. | NA |
| profileFunction | 0..n | RO | SE/AE_SEC defined script functions which will be used by the script fragments. | NA |
| profileData | 0..n | RO | Externally provided parameters and data used by the scripts defined for SE/AE_SEC. | NA |
| secureChannel | 0..1 | RO | Valid only if the application is a Security Domain | NA |
| lifeCycles | 1 | RW | The life cycle status of the SE/AE_SEC (created, activated and deactivated) which are defined by the SE/AE_SEC issuers. | NA |
| codes | 0..n | RO | Describes the different load files where the applet code for the application can be found. | NA |
| accessPrivileges | 1 | RO | Access control policies and data to control access to the profile of SE/AE_SEC. | NA |

### 7.X.2	<profile> Resource Procedures

#### 7.X.2.1	CREATE <profile>

This procedure shall be used for creating a <profile> resource.

Table 7.6.2.1-1: <profile> CREATE

| <profile> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs and Mca |
| Information in Request message | Following parameters shall exist within the Create request: Operation To: The ID of SE/AE_SEC where the <profile> resource is intended to be Created From: the profile issuer Content: <profile> Name: name of profile |
| Processing at Originator before sending Request | Establish security association between the profile issuer and SE/AE_SEC Requests from an profile issuer includes its ID. |
| Processing at Receiver | Check accessPrivileges and validate request. Download profile file and install it. |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

#### 7.6.2.2	RETRIEVE < profile >

This procedure shall be used for retrieving a < profile > resource.

Table 7.6.2.2-1: < profile > RETRIEVE

| <sensitiveDataObject> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs and Mca |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: Operation To: The ID of SE/AE_SEC where the <profile> resource has From: the profile issuer |
| Processing at Originator before sending Request | Establish security association between the profile issuer and SE/AE_SEC Requests from an profile issuer includes its ID |
| Processing at Receiver | Check accessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = Sensitive Data |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

#### 7.X.2.3	UPDATE <profile>

This procedure shall be used for updating the attributes and actual data of a < profile > resource.

Table 7.6.2.3-1: <profile> UPDATE

| <profile> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs and Mca |
| Information in Request message | Following parameters shall exist within the UPDATE request: Operation To: The ID of SE/AE_SEC where the <profile> resource has From: the profile issuer Content: <profile> Name: name of profile Content |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an profile issuer includes its ID |
| Processing at Receiver | Check accessPrivileges and validate request. Set enableSatus as activate or deactivated |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = R; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

#### 7.X.2.4	DELETE <profile>

This procedure shall be used for deleting a <profile> resource.

Table 7.6.2.4-1: <profile> DELETE

| <profile> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs and Mca |
| Information in Request message | Following parameters shall exist within the DELETE request: Operation To: The ID of SE/AE_SEC where the <profile> resource has From: the profile issuer Name: name of profile |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an profile issuer includes its ID |
| Processing at Receiver | Check accessPrivileges and validate request. Delete profile |
| Information in Response message | Response status codes: ack; successful operation = DELETE; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |