| CHANGE REQUEST |
| --- |
| Meeting:* | SEC20.5 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-01-14 |
| Contact:* | As above |
| Reason for Change/s:* | TS-0003 Stage 2 text for End-to-End Key establishment using certificates (E2EKey) |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and v1.3 |
| Clauses/Sub Clauses* | 3, 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

See presentation SEC-2015-0668R02-E2E_Attribute_and_Primitive_Security.

Corresponding changes for TS-0001 are provided in ARC-2016-0006-TS-0001_CR_End-to-End_Security.

### -----------------------Start of change 1-------------------------------------------

## 8.x	End-to-End Key Establishment using Certificates (E2EKey)

### 8.x.1	Purpose of E2EKey

End-to-End Certificate-based Key Establishment (E2EKey) provides an interoperable framework for two end-points to use certificates for establishing a secret symmetric key called pairwiseE2EKey from which symmetric keys are derived for use in other end-to-end security frameworks such as End-to-End Security of Data (ESData) or End-to-End Security of Primitives (ESPrim).

Applicable use cases and requirements are discussed in TR-0012 [i.TR0012].

The present document specifies the E2EKey messages and associated processing for E2EKey. The transport of E2EKey messages is specified in TS-0001 [1].

### 8.x.2	E2EKey Architecture

#### 8.x.2.1 E2EKey Reference Model

The entities in the E2EKey reference model are the E2EKey Initiating End-Point which initiates the procedure and the single E2EKey Terminating End-Point with which the E2EKey Initiating End-Point intends to establish a pairwiseE2EKey.

NOTE: Within the scope of clause 8.x, terms including the word “E2EKey” can be shortened by removing “E2EKey” to facilitate readability. For example, “E2EKey Initiating End-Point” is often shortened to “Initiating End-Point”.

The E2EKey Procedure consists of the Initiating End-Point and Terminating End-Point exchanging a sequence of E2EKey Messages and apply processing based on those E2EKey Messages. If the E2EKey Procedure is successful, then the Initiating End-Point and Terminating End-Point export a pairwiseE2EKey based on the parameters exchanged in the E2EKey Messages.

There is no inherent restriction on which entities may be an Initiating End-point; these end-points may be entities inside a oneM2M system (that is, AEs and CSEs) or entities outside of a oneM2M system (for example, entities which are part of a system that interworks with oneM2M).

The only restriction on entities which may be Terminating End-Points is that the Terminating End-Point shall be able to receive the unsolicited E2EKey Message initiating the E2EKey Procedure. Since TS-0001 [1] specifies the transport of E2EKey messages, TS-0001 also specifies which entities may be Target End-Points.

#### 8.x.2.2 E2EKey Procedure Message Flow

The E2EKey Messages shall be transported as specified in TS-0001 [1]; for example, the <e2EKeyCSE> resource may be used.

The E2EKey Messages shall contain the TLS v1.2 [5] parameters defined in Table 8.x.2.2-1 “E2EKey Message definitions”.

The E2EKey Messages shall be generated and processed according to TLS v1.2 [5].

The E2EKey Procedure message flow is shown in Figure 8.x.2.2-1 “E2EKey Procedure message flow”, and described in the following text.

Figure 8.x.2.2-1: E2EKey Procedure message flow

- The E2EKey endpoints shall be provisioned with private key and certificates described in clause 8.1.2.3 "Credential Configuration for Certificate-Based Security Frameworks". The certificates of the Initiating End-Point and terminating End-Points shall conform to clause 10.1 “Certificate-Based Security Framework Details”.

- The Initiating End-Point and Terminating End-Point shall be configured with the information needed for the authentication and identification of the Terminating End-Point and Initiating End-Point respectively:

The Initiating End-Point is commanded to initiate the E2EKey Procedure, and the command includes the following arguments:

The Terminating End-Point’s certificate information: as described in clause 8.1.2.4 "Information Needed for Certificate Authentication of another Entity".

The Terminating End-Point’s identity. This identity is used for

  - Determining where E2EKey Message 1 is sent, and

  - Associating with the established pairwiseE2EKey.

The Terminating End-Point shall be configured with the following arguments describing Initiating Entity authorized to perform the E2EKey Procedure:

The Initiating End-Point’s certificate information: as described in clause 8.1.2.4 "Information Needed for Certificate Authentication of another Entity".

  - In the case where the Initiating End-Point’s certificate is a raw public key certificate, the Terminating End-Point shall also be configured with an identity to associate with the established pairwiseE2EKey.

The End-Points may be configured in any order.

Editor’s note: Clause 8.1.2.4 “Information Needed for Certificate Authentication of another Entity” currently addresses SAEFs only. Clause 8.1.2.4 requires changing to cover E2EKey. These changes are mostly editorial.

- The Initiating End-Point shall generate E2EKey Message 1.

- The Initiating Entity shall send E2EKey Message 1 to the Terminating End-Point identified in step 2.

- The Terminating Entity shall process E2EKey Message 1, and generate E2EKey Message 2.

- The Terminating Entity shall send E2EKey Message 2 to the Initiating End-Point.

- The Initiating Entity shall process E2EKey Message 2, and generate E2EKey Message 3.

- The Initiating Entity shall send E2EKey Message 3 to the Terminating End-Point.

- The Terminating Entity shall process E2EKey Message 3, generate E2EKey Message 4, and export the pairwiseE2EKey using TLS Exporter specification (RFC 5705) [18] as described in clause 10.3.1 “TLS Key Export Details”. The

Editor’s note: It will be necessary to add the TLS export details for E2EKey in clause 10.3.2. This is a stage 3 detail.

- The Terminating Entity shall send E2EKey Message 4 to the Initiating End-Point.

- The Initiating Entity shall process E2EKey Message, and export the pairwiseE2EKey using TLS Exporter specification (RFC 5705) [18] as described in clause 10.3.1 “TLS Key Export Details”.

Table 8.x.2.2-1: E2EKey Message definitions

| E2EKey Message | Sending End-Point | TLSv1.2 Parameter (success case) [5] | Informative Description (normative description is in TL2v1.2 specification [5]) |
| --- | --- | --- | --- |
| 1 | Initiating | ClientHello | List of allowed ciphersuites, random value, indicator to export pairwiseE2EKey |
| 2 | Terminating | ServerHello | Selected ciphersuite, random value, indicator to export pairwiseE2EKey |
|  |  | Certificate | Terminating End-Point’s certificate |
|  |  | ServerKeyExchange | Key exchange parameters generated by the Terminating End-Point. The content of this parameter is dependent on selected ciphersuite |
|  |  | CertificateRequest | Instructs the Initiating End-Point to authenticate itself with a certificate |
|  |  | ServerHelloDone | Indicates the end of the message |
| 3 | Initiating | Certificate | Initiating End-Point’s certificate |
|  |  | ClientKeyExchange | Key exchange parameters generated by the Initiating End-Point. The content of this parameter is dependent on selected ciphersuite |
|  |  | Finished | MIC on all preceding parameters exchanged in the procedure. The MIC is generated using session secrets established using the preceding parameters. |
| 4 | Terminating | Finished | MIC on all preceding parameters exchanged in the procedure. The MIC is generated using session secrets. |

The TLS ciphersuites used for the E2EKey Procedure shall conform to clause 10.2.3 “TLS and DTLS Ciphersuites for Certificate-Based Security Frameworks”.

### -----------------------End of change 1---------------------------------------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in oneM2M-TR-0004 [2] and the following apply:

AE-ID Certificate: certificate with a certificate chain to a trust anchor certificate and containing an AE-ID in the subjectAltName extension

NOTE:	An AE_ID certificate can be used to verify that an entity has been assigned the AE-ID in the certificate.

association configuration: phase of a Security Association Establishment Framework in which the entity establishing the Security Association (and the Central Key Distribution Server, in the case of Centralized Security Frameworks), are provided with identities (and any other relevant credentials) to ensure that the security association is established between the intended entities

association security handshake: phase of a Security Association Framework in which the security association endpoints perform mutual authentication

bootstrap credential: pre-provisioned credential enabling mutual authentication of the Enrolee and the M2M Enrolment function

bootstrap credential configuration: phase of a Security Bootstrap Framework in which the Bootstrap Credentials are pre-provisioned to the Enrolee and the M2M Enrolment function

bootstrap enrolment handshake: phase of a Security Bootstrap Framework in which the Enrolee and M2M Enrolment Function perform mutual authentication

bootstrap instruction configuration: phase of a Security Bootstrap Framework in which the Enrolee and M2M Enrolment Function are provided with identities (and any other relevant credentials) to enable the M2M Enrolment function to establish a Master Credential between the intended Enrolee and M2M Authentication Function

bootstrap server function [13]: BSF is hosted in a network element under the control of a Mobile Network Operator. BSF, HSS, and UEs participate in GBA in which a shared secret is established between the network and a UE by running the bootstrapping procedure

NOTE:	The shared secret can be used between NAFs and UEs, for example, for authentication purposes.

bootstrapping transaction identifier [13]: bootstrapping transaction identifier (B-TID) is used to bind the subscriber identity to the keying material in GBA reference points Ua, Ub and Zn

CA-Certificate [i.6]: certificate created by one certification authority (CA) certifying the public key of another CA

certificate: See Public Key Certificate.

certificate chain: sequence of one or more CA-certificates, where: the Public Verification Key in each CA-certificate is certified in the previous CA-certificate; and the public key of the first CA-Certificate is trusted a priori

NOTE:	Trust in the public key in each CA-certificate can be based on trust in the previous CA-Certificate.

certificate name: unique identifier in a name field of a Certificate (e.g. in the X.509 "Subject" or "Subject Alternative Name" attribute)

certificate verification: process necessary to trust an entity's Certificate

certification authority [i.6]: responsible for establishing and vouching for the authenticity of public keys

NOTE:	[This] includes binding public keys to distinguished names through signed certificates, managing certificate serial numbers, and certificate revocation.

credential configuration: phase of a Security Association Establishment Framework in which the Credentials necessary for the Security Association Establishment Framework are configured to the relevant entities and functions

Credential-ID type-ID: portion of a Credential-ID indicating the type of credential being identified

CSE-ID certificate: certificate with a certificate chain to a root of trust and containing a CSE-ID in the subjectAltName extension

NOTE:	A CSE_ID certificate can be used to verify that an entity has been assigned the CSE-ID in the certificate.

device certificate: certificate with a certificate chain to a root of trust and containing at least one globally unique hardware instance identifier in the subjectAltName extension

NOTE:	A device certificate can be used to verify that an entity is executing on the identified hardware instance.

digital signature [i.7]: information is signed by appending to it an enciphered summary of the information

NOTE:	The summary is produced by means of a one-way hash function, while the enciphering is carried out using the private key of the signer.

E2EKey Initiating End-Point: The E2EKey end-point which initiates the E2EKey Procedure.

E2EKey Messages: messages exchanged between the E2EKey Initiating End-Point and E2EKey Terminating End-Point as part of End-to-End Certificate-based Key Establishment.

E2EKey Procedure: a sequence of exchanged E2EKey Messages and processing based on those E2EKey Messages, for the purposes of End-to-End Certificate-based Key Establishment.

E2EKey Terminating End-Point:  The E2EKey end-point which the E2EKey Initiating End-Point intends to perform the E2EKey Procedure.

End-to-End Certificate-based Key Establishment: an interoperable framework for two end-points to use certificates for establishing end-to-end secret symmetric keys for use in other end-to-end security frameworks such as End-to-End Security of Data (ESData) or End-to-End Security of Primitives (ESPrim).

enrolee: AE or CSE that requires remote provisioning of a symmetric key to be shared with an enrolment target

enrolment key: symmetric key established between an Enrolee and M2M Enrolment Function following successful mutual authentication

NOTE:	A symmetric key to be shared by the Enrolee and an Enrolment Target may be derived (at the Enrolee and M2M Enrolment Function) from the currently valid Enrolment Key, and the M2M Enrolment Function subsequently securely delivers the symmetric key to the Enrolment Target.

enrolment key generation: phase of remote security provisioning Framework in which the Enrolee and M2M Enrolment function establish an Enrolment Key and Enrolment Key identifier

enrolment phase: step in the lifecycle of an M2M equipment where it becomes provisioned for operation with a specific M2M Service Provider

enrolment target: M2M Authentication Function, CSE, or AE with whom an Enrolee wishes to establish a symmetric key (master credential or pre-provisioned secure connection key) using remote security provisioning

entity identifier: CSE-ID (or AE-ID respectively) of a CSE (or AE respectively)

FQDN certificate: certificate with a certificate chain to a root of trust and containing an FQDN

generic bootstrap architecture: set of 3GPP and 3GPP2 specifications providing security features and a mechanism to bootstrap authentication and key agreement for application security from the 3GPP and 3GPP2 underlying network authentication mechanisms

message integrity code: tag computed from a message and a symmetric key, and attached to a message

NOTE 1:	The purpose of a messages integrity code is to facilitate, without the use of any additional mechanisms, assurances regarding both the source of a message and its integrity.

NOTE 2:	A Message Integrity Code is sometimes called a "Message Authentication Code" - we have used "Message Integrity Code" since the abbreviation of "Message Authentication Code" (MAC) might be misunderstood to refer to "Media Access Control". The definition is based on text from [i.6] (p323).

M2M secure connection key: key shared between two CSEs of M2M Nodes (e.g. ASN/MN-CSE and IN-CSE) in order to secure the communication between those two entities

NOTE:	This M2M Secure Connection Key results from a successful M2M Security Association Establishment procedure.

MAF handshake: phase of a Security Association Establishment Framework in which an entity and the MAF perform mutual authentication and generate a Symmetric Key which can then be used in the Association Security Handshake for mutual authentication between that entity and other entities

master credentials: credentials used to mutually authenticate between an ASN/MN-CSE and the MAF. This is done to secure access to the infrastructure of an M2M Service Provider

NOTE:	The Master Credentials are either pre-provisioned or remotely provisioned (without relying on those credentials).

Online Certificate Status Protocol: A protocol for requesting a report on the status of one or more X.509 certificates (IETF RFC 6960 [35])

operational phase: period in the lifecycle of an M2M equipment where it is actually used for providing M2M services

policy decision point [i.5]: system entity that evaluates applicable policy and renders an authorization decision

policy enforcement point [i.5]: system entity that performs access control, by making decision requests and enforcing authorization decisions

policy information point [i.5]: system entity that acts as a source of attribute values

policy retrieval point: system entity that retrieves applicable policy or policy set

pre-provisioned secure connection key: Symmetric Key that is pre-provisioned to two entities (which may be AEs or CSEs) to be used for mutual authentication of those entities in Security Association Establishment

pre-provisioned secure connection key identifier: Identifier for a Pre-Provisioned Secure Connection Key

pre-provisioned symmetric enrolee key: Symmetric Key that is pre-provisioned to the Enrolee and M2M Enrolment Function

pre-provisioned symmetric enrolee key identifier: Identifier for a Pre-Provisioned Symmetric Enrolee Key

private signing key: secret key that can generate signatures that can be verified using a corresponding Public Verification Key

public key certificate: electronic document that uses a digital signature to bind a public key with an identity

NOTE:	[i.6] A public-key certificate is a data structure consisting of a data part and a signature part. The data part contains cleartext data including, as a minimum, a public [verification] key and a string identifying the part (subject entity) to be associated therewith. The signature part consists of the digital signature of a certification authority over the data part, thereby binding the subject entity's identity to the specified public key.

public key certificate flavour: name describing the usage of a public key certificate within the scope of oneM2M

public key infrastructure: set of hardware, software, people, policies, and procedures needed to create, manage, distribute, use, store, and revoke Public Key Certificates. For more details, see [i.6].

public verification key: credential that can verify digital signatures generated by a corresponding Private Signing Key, but which cannot be used to generate digital signatures

raw public key certificate: certificate comprising only the SubjectPublicKeyInfo structure of an X.509 certificate that carries the parameters necessary to describe the public key [37]

relative enrolment key identifier: part of the enrolment key identifier that is unique within the context of  a M2M Enrolment Function

security association establishment: sequential processing of credential configuration, association configuration and association security handshake between two entities

NOTE:	Credential configuration and/or association configuration can not be performed if those steps have already been executed before.

security association establishment framework: Security Framework for Security Association Establishment

security bootstrap framework: Security Framework for Remote security provisioning: a mechanism for remotely provisioning a Master Credential and Master Credential Identifier to a Enrolee and an M2M Authentication Function

secure environment: a logical entity that protects Sensitive Data and Sensitive Functions from tampering, unauthorized monitoring or execution and that provides access to these Sensitive Data and Sensitive Functions to authorized oneM2M entities

security framework: set of procedures providing Security Association Establishment or Remote security provisioning

sensitive function: function processed within the secure environment requiring protection from unauthorized monitoring, tampering or execution and that is operating on sensitive data, e.g. derivation of keys from M2M long-term service-layer keys and cryptographic algorithms

self-signed certificate: Public Key Certificate that is signed by the same entity whose identity it certifies

symmetric key: secret key that is shared between two entities

trust anchor certificate: a certificate that is trusted a priori

X.509: ITU-T recommendation for a Public Key Infrastructure

## 3.2	Symbols

For the purposes of the present document, the following symbols apply:

||	Concatenation

## 3.3	Abbreviations

For the purposes of the present document, the abbreviations given in oneM2M TR-0004 [i.2] and the following abbreviations apply:

3GPP2	3rd Generation Partnership Project 2

AAA	Authentication, Authorization and Accounting

ABAC	Attribte Based Access Control

ACP	AccessControlPolicy Instance

AE-ID	Application Entity Identifier

ASN-CSE	CSE which resides in the Application Service Node

BSF	Bootstrapping Server Function

B-TID		Bootstrapping Transaction Identifier

CA	Certification Authority

CIDR	Classless Inter-Domain Routing

CoAP	Constrained Application Protocol

CSE-ID	Common Service Entity Identifier

DTLS	Datagram Transport Layer Security (Protocol)

E2EKey	End-to-End Certificate-based Key Establishment.

Enrolee-ID	Enrollee Identity

ETSI	European Telecommunications Standards Institute

FQDN	Fully Qualified Domain Name

GBA_ME	ME-based GBA

GBA_U	GBA with UICC-based enhancements

GUSS	GBA User Security Settings

HLR	Home Location Register

HSS	Home Subscriber System

HTTP	HyperText Transfer Protocol

HW	Hardware

ID	Identifier

IdA	Identifier for entity A

IdB	Identifier for entity B

IN-CSE	CSE which resides in the Infrastructure Node

IPv4	Internet Protocol version 4

IPv6	Internet Protocol version 6

Kc	M2M Secure Connection Key

KcId 	M2M Secure Connection Key identifier

Ke	Enrolment Key

KeId	Enrolment Key Identifier

Km	Master Credential

KmId	Master Credential Identifier

Kpm	pre-provisioned credential for Master Credential provisioning

KpmId	pre-provisioned credential for Master Credential provisioning Identifier

Kpsa	provisioned credential for M2M Security Association Establishment

KpsaId	provisioned credential for M2M Security Association Establishment Identifier

Ks	temporary Key material referred to in GBA

Ks_(ext/int)_NAF	Derived key in GBA_ME or Derived key in GBA_U which remains on UICC

Ks..NAF	Abbreviation of Ks_(int/ext)_NAF

Ks_NAF	Derived key in the ME

Ks_ext_NAF 	Derived key in GBA_U sent to the ME

Ks_int_NAF	Derived key in GBA_U which remains on UICC

M2M-SP	M2M Service Provider

MAF	M2M Authentication Function

MAF-ID	M2M Authentication Function Identifier

Mca	Reference Point for M2M Communication with AE

Mcc	Reference Point for M2M Communication with CSE

Mcc'	Reference Point for M2M Communication with CSE of different M2M Service Provider

Mcn	Reference Point for M2M Communication with NSE

MEF	M2M Enrolment Function

MIC	Message Integrity Code

MN-CSE	CSE which resides in the Middle Node

NAF	Network Application Function

OCSP	Online Certificate Status Protocol

PDP	Policy Decision Point

PEP	Policy Enforcement Point

PIP	Policy Information Point

PKI	Public Key Infrastructure

PRP	Policy Retrieval Point

RSPF	Remote Security Provisioning Framework

SAEF	Security Association Establishment Framework

SE	Secure Environment

SW	Software

TEE	Trusted Execution Environment

TLS	Transport Layer Security (Protocol)

(D)TLS-PSK	(D)TLS Pre-Shared Key (ciphersuites)

UE	(3GPP) User Equipment

UNSP	Underlying Network Service Provider

USS	User Security Settings

URI	Uniform Resource Identifier

XACML	eXtensible Access Control Markup Language

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---