| CHANGE REQUEST |
| --- |
| Meeting:* | SEC21 |
| Source:* | Giesecke & Devrient |
| Date:* | 2015-01-11 |
| Contact:* | Dirk.Wacker[at]gi-de.com, Giesecke & Devrient |
| Reason for Change/s:* | Pseudo CR to add missing features to TS-0016 |
| CR against: Release* | 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0016 v0.3.0 |
| Clauses/Sub Clauses* | 7.7 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This pseudo-CR introduces a Cipher resource within the Secure Environment together with its associated procedures.

### -----------------------Start of change 1-------------------------------------------

### 7.7.1	<Cipher> resource

Secure Environments provide a service for cryptographic operations. A <Cipher> resource shall represent sensitive data and related information owned by a creator as shown in figure 7.6-1.

Figure 7.7.1-1: <Cipher> representation

Attributes in <Cipher> are shown in table 7.7.1-1.

Table 7.7-1: Attributes of <Cipher> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| creator | 1 | RO | The AE-ID of the AE creating the resource. | NA |
| currentByteSize | 1 | RO | Current size in bytes of sensitive data. | NA |
| sensitiveData | 1 | RW | Contains sensitive data and required information to access and manage sensitive data owned by a dedicated creator | NA |
| seAccessPrivileges | 1 | WO | Is used to control access to the resource. | NA |
| algorithm | 1 | RO | Contains the algorithm type of the resource instance | NA |
| Mode | 1 | RW | Specifies the mode of the Cipher instance, either encrypt or decrypt. | NA |
| keyData | 1 | WO | Contains the value of a key | NA |
| keyInformation | 0..1 | RW | Contains information about a key like a certificate | NA |

Editor’s note: It is to be investigated if references to keys are possible and how access control of theses keys could then be realized.

It is to be investigated if virtual resources should be used.

The following types are defined for the algorithm attribute:

- ALG_AEAD_AES_128_GCM: The AEAD_AES_128_GCM authenticated encryption algorithm works as specified in [RFC5116], using AES-128 as the block cipher, by providing the key, nonce, and plaintext, and associated data to that mode of operation.

- ALG_AEAD_AES_256_GCM: This algorithm is identical to AEAD_AES_128_GCM, but with the following differences: K_LEN is 32 octets, instead of 16 octets, and AES-256 GCM is used instead of AES-128 GCM.

- ALG_AEAD_AES_128_CCM: The AEAD_AES_128_CCM authenticated encryption algorithm works as specified in [RFC5116], using AES-128 as the block cipher, by providing the key, nonce, associated data, and plaintext to that mode of operation.

- ALG_AEAD_AES_256_CCM: This algorithm is identical to AEAD_AES_128_CCM, but with the following differences: K_LEN is 32 octets, instead of 16, and AES-256 CCM is used instead of AES-128 CCM.

- ALG_AES_BLOCK_128_CBC_NOPAD : Cipher algorithm ALG_AES_BLOCK_128_CBC_NOPAD provides a cipher using AES with block size 128 in CBC mode and does not pad input data.

- ALG_AES_BLOCK_128_ECB_NOPAD : Cipher algorithm ALG_AES_BLOCK_128_ECB_NOPAD provides a cipher using AES with block size 128 in ECB mode and does not pad input data.

- ALG_AES_CBC_ISO9797_M1: Cipher algorithm ALG_AES_CBC_ISO9797_M1 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the ISO 9797 method 1 scheme.

- ALG_AES_CBC_ISO9797_M2: Cipher algorithm ALG_AES_CBC_ISO9797_M2 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the ISO 9797 method 2 (ISO 7816-4, EMV'96) scheme.

- ALG_AES_CBC_PKCS5: Cipher algorithm ALG_AES_CBC_PKCS5 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the PKCS#5 scheme.

- ALG_AES_CTR: Cipher algorithm ALG_AES_CTR provides a cipher using AES in counter (CTR) mode.

- ALG_AES_ECB_ISO9797_M1: Cipher algorithm ALG_AES_ECB_ISO9797_M1 provides a cipher using AES with block size 128 in ECB mode, and pads input data according to the ISO 9797 method 1 scheme.

- ALG_AES_ECB_ISO9797_M2: Cipher algorithm ALG_AES_ECB_ISO9797_M2 provides a cipher using AES with block size 128 in ECB mode, and pads input data according to the ISO 9797 method 2 (ISO 7816-4, EMV'96) scheme.

- ALG_AES_ECB_PKCS5: Cipher algorithm ALG_AES_ECB_PKCS5 provides a cipher using AES with block size 128 in ECB mode, and pads input data according to the PKCS#5 scheme.

- ALG_DES_CBC_ISO9797_M1: Cipher algorithm ALG_DES_CBC_ISO9797_M1 provides a cipher using DES in CBC mode or triple DES in outer CBC mode, and pads input data according to the ISO 9797 method 1 scheme.

- ALG_DES_CBC_ISO9797_M2: Cipher algorithm ALG_DES_CBC_ISO9797_M2 provides a cipher using DES in CBC mode or triple DES in outer CBC mode, and pads input data according to the ISO 9797 method 2 (ISO 7816-4, EMV'96) scheme.

- ALG_DES_CBC_NOPAD: Cipher algorithm ALG_DES_CBC_NOPAD provides a cipher using DES in CBC mode or triple DES in outer CBC mode, and does not pad input data.

- ALG_DES_CBC_PKCS5: Cipher algorithm ALG_DES_CBC_PKCS5 provides a cipher using DES in CBC mode or triple DES in outer CBC mode, and pads input data according to the PKCS#5 scheme.

- ALG_DES_ECB_ISO9797_M1: Cipher algorithm ALG_DES_ECB_ISO9797_M1 provides a cipher using DES in ECB mode, and pads input data according to the ISO 9797 method 1 scheme.

- ALG_DES_ECB_ISO9797_M2: Cipher algorithm ALG_DES_ECB_ISO9797_M2 provides a cipher using DES in ECB mode, and pads input data according to the ISO 9797 method 2 (ISO 7816-4, EMV'96) scheme.

- ALG_DES_ECB_NOPAD:  Cipher algorithm ALG_DES_ECB_NOPAD provides a cipher using DES in ECB mode, and does not pad input data.

- ALG_DES_ECB_PKCS5: Cipher algorithm ALG_DES_ECB_PKCS5 provides a cipher using DES in ECB mode, and pads input data according to the PKCS#5 scheme.

- ALG_KOREAN_SEED_CBC_NOPAD: Cipher algorithm ALG_KOREAN_SEED_CBC_NOPAD provides a cipher using the Korean SEED algorithm specified in the Korean SEED Algorithm specification provided by KISA, Korea Information Security Agency in CBC mode and does not pad input data.

- ALG_KOREAN_SEED_ECB_NOPAD: Cipher algorithm ALG_KOREAN_SEED_ECB_NOPAD provides a cipher using the Korean SEED algorithm specified in the Korean SEED Algorithm specification provided by KISA, Korea Information Security Agency in ECB mode and does not pad input data.

- ALG_RSA_NOPAD: Cipher algorithm ALG_RSA_NOPAD provides a cipher using RSA and does not pad input data.

- ALG_RSA_PKCS1: Cipher algorithm ALG_RSA_PKCS1 provides a cipher using RSA, and pads input data according to the PKCS#1 (v1.5) scheme.

- ALG_RSA_PKCS1_OAEP: Cipher algorithm ALG_RSA_PKCS1_OAEP provides a cipher using RSA, and pads input data according to the PKCS#1-OAEP scheme (IEEE 1363-2000).

Editor’s note: It need to be investigated, which algorithms are needed for oneM2M specifications.

#### 7.7.1.1	<Cipher> Resource Procedures

##### 7.7.1.1.1	CREATE <Cipher>

This procedure shall be used for creating a <Cipher>  resource.

Table 7.7.1.1.1-1: <Cipher> CREATE

| <Cipher> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the Create request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Content: algorithm, mode, keyData and keyInformation |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

If keyData contains ‘generateKey’ a key according algorithm is generated and written in keyData, in such a case keyInformation is filled with the public part of the generated key.

##### 7.7.1.1.2	RETRIEVE <Cipher>

This procedure shall be used for retrieving the generated output from all/last input data of the <Cipher> resource. This procedure must be called to complete the cipher operation.

Table 7.7.1.1.2-1: <Cipher> RETRIEVE

| <Cipher> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = sensitiveData (either encrypted or decrypted, depending on the mode) |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.1.1.3	UPDATE <Cipher>

This procedure shall be used for updating the <Cipher> resource with data to encrypt or decrypt. It may be necessary to use this procedure several times until all data is transmitted.

Table 7.7.1.1.3-1: <Cipher> UPDATE

| <Cipher> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the UPDATE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Name Content = sensitiveData (to encrypt or decrypt), keyInformation, mode |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = R; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.1.1.4	DELETE <Cipher>

This procedure shall be used for deleting a <Cipher> resource.

Table 7.7.1.1.4-1: <Cipher> DELETE

| <Cipher> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the DELETE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = DELETE; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

### 7.7.2	<Rand> resource

A <Rand> resource shall represent random data owned by a creator as shown in figure 7.7.2-1.

Figure 7.7.2-1: <Rand> representation

Attributes in <Rand> are shown in table 7.7.2-1.

Table 7.7.2-1: Attributes of <Rand> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| creator | 1 | RO | The AE-ID of the AE creating the resource. | NA |
| randomData | 1 | RO | Contains random data which can be retrieved by the creator | NA |
| seAccessPrivileges | 1 | WO | Is used to control access to the resource. | NA |
| rngType | 1 | WO | A SE can comprise several RNGs, like pseudo RNGs, physical RNGs, Hybrid RNGs, each one even with different properties. The one requested is given by this attribute | NA |
| requestedDataSize | 1 | RW | Requested amount of randomData in Bytes | NA |

#### 7.7.2.1	<Rand> Resource Procedures

##### 7.7.2.1.1	CREATE <Rand>

This procedure shall be used for creating a <Rand>  resource.

Table 7.7.2.1.1-1: <Rand> CREATE

| <Rand> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the Create request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Content: rngType |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

##### 7.7.2.1.2	RETRIEVE <Rand>

This procedure shall be used for retrieving the random numbers.

Table 7.7.2.1.2-1: <Retrieve> RETRIEVE

| <Cipher> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = randomData |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.2.1.3	UPDATE <Rand>

This procedure shall be used for setting the amount of random data which is requested.

Table 7.7.1.1.3-1: <Rand> UPDATE

| <Rand> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the UPDATE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Name Content = requestedDataSize |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = U; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.2.1.4	DELETE <Rand>

This procedure shall be used for deleting a <Rand> resource.

Table 7.7.2.1.4-1: <Rand> DELETE

| <Cipher> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the DELETE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = DELETE; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

### 7.7.3	<Hash> resource

Secure Environments provide a service for calculating hashes. A <Hash> resource shall represent sensitive data and related information owned by a creator as shown in figure 7.7.3-1.

Figure 7.7.3-1: <Hash> representation

Attributes in <Hash> are shown in table 7.7.3-1.

Table 7.7.3-1: Attributes of <Hash> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| creator | 1 | RO | The AE-ID of the AE creating the resource. | NA |
| seAccessPrivileges | 1 | WO | Is used to control access to the resource. | NA |
| algorithm | 1 | WO | Specfies the algorithm for the hash | NA |
| message | 1 | RW | The message which is to be hashed | NA |
| hash | 1 | RO | Is the calculated Hash | NA |

The following types are defined as algorithm types: SHA256, SHA384, SHA512

#### 7.7.3.1	<Hash> Resource Procedures

##### 7.7.3.1.1	CREATE <Hash>

This procedure shall be used for creating a <Hash>  resource.

Table 7.7.3.1.1-1: <Hash> CREATE

| <Cipher> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the Create request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Content: algorithm |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

##### 7.7.3.1.2	RETRIEVE <Hash>

This procedure shall be used for retrieving the calculated hash. This procedure must be called to complete the hash operation.

Table 7.7.3.1.2-1: <Hash> RETRIEVE

| <Hash> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = hash |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.3.1.3	UPDATE <Hash>

This procedure shall be used for updating the <Hash> resource with data to be hashed.

Table 7.7.3.1.3-1: <Hash> UPDATE

| <Hash> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the UPDATE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Name Content = message |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = U; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.3.1.4	DELETE <Hash>

This procedure shall be used for deleting a <Hash> resource.

Table 7.7.3.1.4-1: <Hash> DELETE

| <Hash> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the DELETE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = DELETE; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

Editor’s note: It is to be discussed, if this resource should be merged with the <Cipher> resource.

### 7.7.4	<Signature> resource

Secure Environments provide a service for signing messages and verifying signatures. A <Signature> resource shall represent sensitive data and related information owned by a creator as shown in figure 7.7.4-1.

Figure 7.7.4-1: <Signature> representation

Attributes in <Signature> are shown in table 7.7.4-1.

Table 7.7.4-1: Attributes of <Signature> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description | <sensitiveDataObjectAnnc> (MA/OA/NA) |
| --- | --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. | NA |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. | NA |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. | NA |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. | NA |
| creator | 1 | RO | The AE-ID of the AE creating the resource. | NA |
| message | 1 | RW | Message either to be signed or to be used to verify a signature, this could be alternatively a hash value | NA |
| seAccessPrivileges | 1 | WO | Is used to control access to the resource. | NA |
| algorithm | 1 | RO | Contains the algorithm type of the resource instance | NA |
| mode | 1 | RW | Specifies the mode of the Signature instance, either sign or verify. | NA |
| keyData | 1 | WO | Contains the value of the key | NA |
| keyInformation | 0..1 | RW | Contains information about the key like a certificate | NA |
| signature | 1 | RW | Contains the signature either to be calculated or to be verified | NA |

The following types are defined for the algorithm attribute:

ALG_AES_CMAC_128 : Signature algorithm ALG_AES_CMAC_128 generates a 16-byte Cipher-based MAC (CMAC) using AES with blocksize 128 in CBC mode with ISO9797_M2 padding scheme.

ALG_AES_MAC_128_NOPAD :Signature algorithm ALG_AES_MAC_128_NOPAD generates a 16-byte MAC using AES with blocksize 128 in CBC mode and does not pad input data.

ALG_DES_MAC4_ISO9797_1_M1_ALG3 : Signature algorithm ALG_DES_MAC4_ISO9797_1_M1_ALG3 generates a 4-byte MAC using triple DES with a 2-key DES3 key according to ISO9797-1 MAC algorithm 3 with method 1, where input data is padded using method 1 and the data is processed as described in MAC Algorithm 3 of the ISO 9797-1 specification.

ALG_DES_MAC4_ISO9797_1_M2_ALG3 : Signature algorithm ALG_DES_MAC4_ISO9797_1_M2_ALG3 generates a 4-byte MAC using triple DES with a 2-key DES3 key according to ISO9797-1 MAC algorithm 3 with method 2 (also EMV'96, EMV'2000), where input data is padded using method 2 and the data is processed as described in MAC Algorithm 3 of the ISO 9797-1 specification.

ALG_DES_MAC4_ISO9797_M1 :Signature algorithm ALG_DES_MAC4_ISO9797_M1 generates a 4-byte MAC (most significant 4 bytes of encrypted block) using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC4_ISO9797_M2 :Signature algorithm ALG_DES_MAC4_ISO9797_M2 generates a 4-byte MAC (most significant 4 bytes of encrypted block) using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC4_NOPAD : Signature algorithm ALG_DES_MAC4_NOPAD generates a 4-byte MAC (most significant 4 bytes of encrypted block) using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC4_PKCS5 :Signature algorithm ALG_DES_MAC4_PKCS5 generates a 4-byte MAC (most significant 4 bytes of encrypted block) using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC8_ISO9797_1_M1_ALG3 :Signature algorithm ALG_DES_MAC8_ISO9797_1_M1_ALG3 generates an 8-byte MAC using triple DES with a 2-key DES3 key according to ISO9797-1 MAC algorithm 3 with method 1, where input data is padded using method 1 and the data is processed as described in MAC Algorithm 3 of the ISO 9797-1 specification.

ALG_DES_MAC8_ISO9797_1_M2_ALG3 :Signature algorithm ALG_DES_MAC8_ISO9797_1_M2_ALG3 generates an 8-byte MAC using triple DES with a 2-key DES3 key according to ISO9797-1 MAC algorithm 3 with method 2 (also EMV'96, EMV'2000), where input data is padded using method 2 and the data is processed as described in MAC Algorithm 3 of the ISO 9797-1 specification.

ALG_DES_MAC8_ISO9797_M1 :Signature algorithm ALG_DES_MAC8_ISO9797_M1 generates an 8-byte MAC using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC8_ISO9797_M2 :Signature algorithm ALG_DES_MAC8_ISO9797_M2 generates an 8-byte MAC using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC8_NOPAD :Signature algorithm ALG_DES_MAC8_NOPAD generates an 8-byte MAC using DES in CBC mode or triple DES in outer CBC mode.

ALG_DES_MAC8_PKCS5 :Signature algorithm ALG_DES_MAC8_PKCS5 generates an 8-byte MAC using DES in CBC mode or triple DES in outer CBC mode.

ALG_DSA_SHA : Signature algorithm ALG_DSA_SHA generates a 20-byte SHA digest and signs/verifies the digests using DSA.

ALG_ECDSA_SHA :Signature algorithm ALG_ECDSA_SHA generates a 20-byte SHA digest and signs/verifies the digest using ECDSA.

ALG_ECDSA_SHA_224 :Signature algorithm ALG_ECDSA_SHA_224 generates a 28-byte SHA-224 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-224 curve specified in the Digital Signature Standards specification[NIST FIPS PUB 186-2].

ALG_ECDSA_SHA_256 :Signature algorithm ALG_ECDSA_SHA_256 generates a 32-byte SHA-256 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-256 curve specified in the Digital Signature Standards specification[NIST FIPS PUB 186-2].

ALG_ECDSA_SHA_384 :Signature algorithm ALG_ECDSA_SHA_384 generates a 48-byte SHA-384 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-384 curve specified in the Digital Signature Standards specification[NIST FIPS PUB 186-2].

ALG_ECDSA_SHA_512 :Signature algorithm ALG_ECDSA_SHA_512 generates a 64-byte SHA-512 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-521 curve specified in the Digital Signature Standards specification[NIST FIPS PUB 186-2].

ALG_HMAC_MD5 :HMAC message authentication algorithm ALG_HMAC_MD5 This algorithm generates an HMAC following the steps found in RFC: 2104 using MD5 as the hashing algorithm.

ALG_HMAC_RIPEMD160 :HMAC message authentication algorithm ALG_HMAC_RIPEMD160 This algorithm generates an HMAC following the steps found in RFC: 2104 using RIPEMD160 as the hashing algorithm.

ALG_HMAC_SHA_256 :HMAC message authentication algorithm ALG_HMAC_SHA_256 This algorithm generates an HMAC following the steps found in RFC: 2104 using SHA-256 as the hashing algorithm.

ALG_HMAC_SHA_384 :HMAC message authentication algorithm ALG_HMAC_SHA_384 This algorithm generates an HMAC following the steps found in RFC: 2104 using SHA-384 as the hashing algorithm.

ALG_HMAC_SHA_512 :HMAC message authentication algorithm ALG_HMAC_SHA_512 This algorithm generates an HMAC following the steps found in RFC: 2104 using SHA-512 as the hashing algorithm.

ALG_HMAC_SHA1 :

HMAC message authentication algorithm ALG_HMAC_SHA1 This algorithm generates an HMAC following the steps found in RFC: 2104 using SHA1 as the hashing algorithm.

ALG_KOREAN_SEED_MAC_NOPAD : Signature algorithm ALG_KOREAN_SEED_MAC_NOPAD generates an 16-byte MAC using Korean SEED in CBC mode.

ALG_RSA_MD5_PKCS1 :Signature algorithm ALG_RSA_MD5_PKCS1 generates a 16-byte MD5 digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_MD5_PKCS1_PSS :Signature algorithm ALG_RSA_MD5_PKCS1_PSS generates a 16-byte MD5 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_MD5_RFC2409 : Signature algorithm ALG_RSA_MD5_RFC2409 generates a 16-byte MD5 digest, pads the digest according to the RFC2409 scheme, and encrypts it using RSA.

ALG_RSA_RIPEMD160_ISO9796 : Signature algorithm ALG_RSA_RIPEMD160_ISO9796 generates a 20-byte RIPE MD-160 digest, pads the digest according to the ISO 9796 scheme, and encrypts it using RSA.

ALG_RSA_RIPEMD160_ISO9796_MR :Signature algorithmALG_RSA_RIPEMD160_ISO9796_MR generates 20-byte RIPE MD-160 digest, pads it according to the ISO9796-2 specification and encrypts using RSA.

ALG_RSA_RIPEMD160_PKCS1 :Signature algorithm ALG_RSA_RIPEMD160_PKCS1 generates a 20-byte RIPE MD-160 digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_RIPEMD160_PKCS1_PSS : Signature algorithm ALG_RSA_RIPEMD160_PKCS1_PSS generates a 20-byte RIPE MD-160 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_SHA_224_PKCS1 :Signature algorithm ALG_RSA_SHA_224_PKCS1 generates a 28-byte SHA digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_SHA_224_PKCS1_PSS :Signature algorithm ALG_RSA_SHA_224_PKCS1_PSS generates a 28-byte SHA-224 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_SHA_256_PKCS1 :Signature algorithm ALG_RSA_SHA_256_PKCS1 generates a 32-byte SHA digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_SHA_256_PKCS1_PSS :Signature algorithm ALG_RSA_SHA_256_PKCS1_PSS generates a 32-byte SHA-256 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_SHA_384_PKCS1 :Signature algorithm ALG_RSA_SHA_384_PKCS1 generates a 48-byte SHA digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_SHA_384_PKCS1_PSS :Signature algorithm ALG_RSA_SHA_384_PKCS1_PSS generates a 48-byte SHA-384 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_SHA_512_PKCS1 :Signature algorithm ALG_RSA_SHA_512_PKCS1 generates a 64-byte SHA digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_SHA_512_PKCS1_PSS ;Signature algorithm ALG_RSA_SHA_512_PKCS1_PSS generates a 64-byte SHA-512 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_SHA_ISO9796 :Signature algorithm ALG_RSA_SHA_ISO9796 generates a 20-byte SHA digest, pads the digest according to the ISO 9796-2 scheme as specified in EMV '96 and EMV 2000, and encrypts it using RSA.

ALG_RSA_SHA_ISO9796_MR :Signature algorithmALG_RSA_SHA_ISO9796_MR generates 20-byte SHA-1 digest, pads it according to the ISO9796-2 specification and encrypts using RSA.

ALG_RSA_SHA_PKCS1 :Signature algorithm ALG_RSA_SHA_PKCS1 generates a 20-byte SHA digest, pads the digest according to the PKCS#1 (v1.5) scheme, and encrypts it using RSA.

ALG_RSA_SHA_PKCS1_PSS :Signature algorithm ALG_RSA_SHA_PKCS1_PSS generates a 20-byte SHA-1 digest, pads it according to the PKCS#1-PSS scheme (IEEE 1363-2000), and encrypts it using RSA.

ALG_RSA_SHA_RFC2409 :Signature algorithm ALG_RSA_SHA_RFC2409 generates a 20-byte SHA digest, pads the digest according to the RFC2409 scheme, and encrypts it using RSA.

SIG_CIPHER_AES_CMAC128 :Cipher algorithm SIG_CIPHER_AES_CMAC128 choice for the cipherAlgorithm parameter of the getInstance(byte, byte, byte, boolean) method.

#### 7.7.4.1	<Signature> Resource Procedures

##### 7.7.4.1.1	CREATE <Signature>

This procedure shall be used for creating a <Signature> resource.

Table 7.7.4.1.1-1: <Signature> CREATE

| <Signature> CREATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the Create request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Content: algorithm, mode, keyData and keyInformation |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = CREATE; Unsuccessful Operation = C; Request Identifier |
| Processing at Originator after receiving Response | n/a |
| Exceptions | According to [2] |

If keyData contains ‘generateKey’ a key according algorithm is generated and written in keyData, in such a case keyInformation is filled with the public part of the generated key.

##### 7.7.4.1.2	RETRIEVE <Signature>

This procedure shall be used for retrieving either the calculated signature of the <Signature> resource or the result of the verification of a signature.

Table 7.7.4.1.2-1: <Signature> RETRIEVE

| <Cipher> RETRIEVE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the RETRIEVE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = RETRIEVE; Unsuccessful Operation = R; Request Identifier Content = signature (in case of sign mode) |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.4.1.3	UPDATE <Signature>

This procedure shall be used for updating the <Signature> resource with the message to be signed or to be verified and in the case of verification the signature to be verified.

Table 7.7.4.1.3-1: <Signature> UPDATE

| <Signature> UPDATE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the UPDATE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier Content = message, signature (in case of signature verification), keyInformation, mode |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = UPDATE; Unsuccessful Operation = U; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

##### 7.7.1.1.4	DELETE <Signature>

This procedure shall be used for deleting a <Signature> resource.

Table 7.7.1.1.4-1: <Signature> DELETE

| <Signature> DELETE request message parameters |
| --- |
| Associated Reference Point | Mcs |
| Information in Request message | Following parameters shall exist within the DELETE request: Operation To: contains M2M-SE-ID or M2M-AE-ID From Registree AE Request Identifier |
| Processing at Originator before sending Request | Establish security association between creator and SE Requests from an AE includes their AE-ID |
| Processing at Receiver | Check seAccessPrivileges and validate request |
| Information in Response message | Response status codes: ack; successful operation = DELETED; Unsuccessful Operation = D; Request Identifier |
| Processing at Originator after receiving Response | As defined in [2] |
| Exceptions | As defined in [2] |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of Changes to References Section -------------

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

## 2.2	Informative references

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

### -----------------------End of Changes to References  -------------

### -Start of changes to Definitions Symbols Abbreviations Acronyms -

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

<defined term>: <definition>

<defined term>[N]: <definition>

## 3.2	Symbols

<symbol>	<Explanation>

## 3.3	Abbreviations and Acronyms

<ABBREVIATION/ACRONYM>	<Explanation>

### ---End of changes to Definitions, Symbols, Abbreviations, Acronyms ---

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?