| Input Contribution |
| --- |
| Meeting ID* | SEC#21 |
| Title:* | TS-0003 Distributed Authorization Resource Procedures |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Uploaded Date:* | 2016-01-18 |
| Document(s) Impacted* | TS-0003-V1.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0003. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1	Introduction

This contribution proposes the solution for distribute authorization.

2	Proposal

### 7.x.3	Resource Type-Specific Procedures

#### 7.x.3.1	Retrieve <policyDecisionPoint>

This procedure is used to trigger a PDP process that is bound to a <policyDecisionPoint> virtual resource.

Originator: The Originator should request to obtain an access control decision by using RETRIEVE operation on a <policyDecisionPoint> virtual resource from the Receiver. The Originator is a CSE.

Receiver: The Receiver should check if the Originator has RETRIEVE permission on the <policyDecisionPoint> virtual resource. Upon successful validation, the Receiver should make an access control decision based on access control policies. If there is no process bound to the <policyDecisionPoint> virtual resource, the Receiver should respond with an error.

Table 7.x.3.1-1: <policyDecisionPoint> RETRIEVE

| <policyDecisionPoint> RETRIEVE |
| --- |
| Associated Reference Points | Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following additions: From: Identifier of the CSE that initiates the Request To: Address of the <policyDecisionPoint> virtual resource Content: The representation of the decision request. The parameters contained in it are listed in table 7.x.3.1-2 |
| Processing at Originator before sending Request | The Originator should create a decision request according to an access request. The Originator should request to obtain a decision by using the RETRIEVE operation on a <policyDecisionPoint> virtual resource which is the child resource of a <authorization> resource of the Receiver. The access control decision request should be included in the Content parameter of the Request message. The Originator should be a CSE |
| Processing at Receiver | The Receiver should perform the following operations: Check if the Originator has RETRIEVE permission on the <policyDecisionPoint> virtual resource Check the validity of the provided parameters Check if the <policyDecisionPoint> virtual resource is bound to a PDP process. Upon successful validation, passing the access control decision request to the PDP process. The PDP process contact a PRP to obtain applicable access control policies, and may also contact a PIP to obtain some access control attributes, and then make an access control decision. The Receiver should create an access control decision response according to the access control decision and respond to the Originator. The access control decision response should be included in the Content parameter of the Response message. |
| Information in Response message | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following additions: Content: The representation of the access control decision response. The parameters contained in it are listed in table 7.x.3.1-3 |
| Processing at Originator after receiving Response | The Originator should enforce the access control decision, i.e. either permit or deny the access to resource |
| Exceptions | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following: There is no PDP process bound to the <policyDecisionPoint> virtual resource The provided content of the access control decision request is not in line with the specified structure |

# Table 7.x.3.1-2: Parameters of content in the access control decision request message

| Parameter | Description | Mandatory/ Optional | Usage in access control mechanism |
| --- | --- | --- | --- |
| To | URI of target resource | M | Selection of access control policies associated with the target resource and selection of access control rules in an access control policy |
| From | Identifier representing the originator of the request | M | Evaluated against accessControlOriginators in access control rules |
| Operation | Requested operation | M | Evaluated against accessControlOperations in access control rules |
| Attribute Names | List of attribute names directly under the target resource | O | Evaluated against permittedAttributes in access control rules |
| Child Resource Types | List of child resource types directly under the target resource | O | Evaluated against permittedChildResources in access control rules |
| Role IDs | List of role identifiers | O | Used in role based access control |
| Token IDs | List of token identifiers | O | Used for retrieve tokens |
| Tokens | List of tokens | O | Used in token based access control |
| Advice Demand | A Boolean value shows the demand of returning permitted attribute names and child resource types | O | Determine if the permitted attribute names and permitted child resource types should be included in the respond |
| NOTE: This parameter is for use in future Release(s). |

# Table 7.x.3.1-3: Parameters of content in the access control decision response message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| Decision | Result of access control policy evaluation | M |
| Status Code | A code represents what error occurred during evaluation of the decision request | O |
| Status Message | A free-form description of the status code | O |
| Permitted Attribute Names | List of permitted attribute names | O |
| Permitted Child Resource Types | List of permitted child resources types | O |

#### 7.x.3.2	Retrieve <policyRetrievalPoint>

This procedure is used to trigger a PRP process that is bound to a <policyRetrievalPoint> virtual resource.

Originator: The Originator should request to obtain access control policies by using RETRIEVE operation on a <policyRetrievalPoint> virtual resource from the Receiver. The Originator is a CSE.

Receiver: The Receiver should check if the Originator has RETRIEVE permission on the <policyRetrievalPoint> virtual resource. Upon successful validation, the Receiver should retrieve all applicable access control policies. If there is no process bound to the <policyRetrievalPoint> virtual resource, the Receiver should respond with an error.

Table 6.2.2.3.7-1: <policyRetrievalPoint> RETRIEVE

| <policyRetrievalPoint> RETRIEVE |
| --- |
| Associated Reference Points | Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following additions: From: Identifier of the CSE that initiates the Request To: The address of the <policyRetrievalPoint> virtual resource Content: The representation of the policy request. The parameters contained in it are listed in table 7.x.3.2-2 |
| Processing at Originator before sending Request | The Originator should create an access control policy request according to an access control decision request. The Originator should request to obtain access control policies by using the RETRIEVE operation on a <policyRetrievalPoint> virtual resource which is the child resource of a <authorization> resource of the Receiver. The access control policy request should be included in the Content parameter of the Request message. The Originator should be a CSE |
| Processing at Receiver | The Receiver should perform the following operations: Check if the Originator has RETRIEVE permission on the <policyRetrievalPoint> virtual resource Check the validity of the provided parameters Check if the <policyRetrievalPoint> virtual resource is bound to a PRP process. Upon successful validation, passing the access control policy request to the PRP process. The PRP process retrieves all applicable access control policies according to the access control policy request. The Receiver should create an access control policy response using the retrieved access control policies and respond to the Originator. The access control policy response should be included in the Content parameter of the Response message. |
| Information in Response message | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following additions: Content: The representation of the policy response. The parameters contained in it are listed in table 7.x.3.2-3 |
| Processing at Originator after receiving Response | The Originator should evaluate the access control decision request using the retrieved the access control policies. |
| Exceptions | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following: There is no PRP process bound to the <policyRetrievalPoint> virtual resource The provided content of the access control policy request is not in line with the specified structure |

# Table 7.x.3.2-2: Parameters of content in the policy request message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| To | URI of target resource | M |
| From | Identifier representing the originator of the request | M |

# Table 7.x.3.2-3: Parameters of content in the policy response message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| Policy Combining Algorithm | Specifying what algorithm shall be used for arriving at an authorization decision given the individual results of evaluation of a set of policies. | M |
| Policies | A set of policies that shall be used to evaluate the access control decision request | M |

#### 7.x.3.3	Retrieve <policyInformationPoint>

This procedure is used to trigger a PIP process that is bound to a <policyInformationPoint> virtual resource.

Originator: The Originator should request to obtain access control attributes by using RETRIEVE operation on a <policyInformationPoint> virtual resource from the Receiver. The Originator is a CSE.

Receiver: The Receiver should check if the Originator has RETRIEVE permission on the <policyInformationPoint> virtual resource. Upon successful validation, the Receiver should obtain the requested attributes. If there is no process bound to the <policyInformationPoint> virtual resource, the Receiver should respond with an error.

Table 6.2.2.3.8-1: <policyInformationPoint> RETRIEVE

| <policyInformationPoint> RETRIEVE |
| --- |
| Associated Reference Points | Mcc and Mcc' |
| Information in Request message | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following additions: From: Identifier of the CSE that initiates the Request To: The address of the <policyInformationPoint> virtual resource Content: The representation of the attribute request. The parameters contained in it are listed in table 7.x.3.3-2 |
| Processing at Originator before sending Request | The Originator should create an access control attribute request according to an access request. The Originator should request to obtain an access control attributes by using the RETRIEVE operation on a <policyInformationPoint> virtual resource which is the child resource of a <authorization> resource of the Receiver. The access control attribute request should be included in the Content parameter of the Request message. The Originator should be a CSE |
| Processing at Receiver | The Receiver should perform the following operations: Check if the Originator has RETRIEVE permission on the <policyInformationPoint> virtual resource Check the validity of the provided parameters Check if the <policyInformationPoint> virtual resource is bound to a PIP process. Upon successful validation, passing the access control attribute request to the PIP process. The PIP process obtains the requested access control attributes according to the access control attribute request. The Receiver should create an access control attribute response using the obtained access control attributes and respond to the Originator. The access control attribute response should be included in the Content parameter of the Response message. |
| Information in Response message | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following additions: Content: The representation of the attribute response. The parameters contained in it are listed in table 7.x.3.3-3 |
| Processing at Originator after receiving Response | The Originator should evaluate the access control decision request using the retrieved the access control policies and access control attributes |
| Exceptions | According to clause 10.1.2 of oneM2M TS-0001 [1] with the following: There is no PIP process bound to the <policyInformationPoint> virtual resource The provided content of the access control attribute request is not in line with the specified structure |

# Table 7.x.3.3-2: Parameters of content in the attribute request message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| From | Identifier representing the originator of the request | M |
| Role ID or Token ID | Identifier of a role or token | M |

# Table 7.x.3.3-3: Parameters of content in the attribute response message

| Parameter | Description | Mandatory/ Optional |
| --- | --- | --- |
| Role or token resource attriburtes | Attributes of a role or token resource | M |