| CHANGE REQUEST |
| --- |
| Meeting:* | SEC#21 |
| Source:* | Gemalto |
| Date:* | 2016-01-16 |
| Contact:* | François Ennesser (francois.ennesser@gemalto.com) |
| Reason for Change/s:* | A clean-up of TR-0012 required before freezing |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0012 v0.8.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# 3	Definitions, symbols, abbreviations  and acronyms

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in [i.2] and the following apply:

M2M Trust Enabler Function (TEF): It is a trusted third-party entity that can provide services such as credential generation, registration and provisioning in order to enable secure data protection and access.

End-to-End Security: Provides for securing messages that can traverse multiple hops between communication entities. Securing of messages involves mutually authenticating the end entities. Securing of messages also involves providing confidentiality and integrity protection of messages in order that end entities are assured that the messages have not been altered or eavesdropped by un-authorized entities (including intermediary nodes involved in the transmission).

End-to-End Authentication: Provides an entity with the ability to validate another entity’s identity that was supplied as part of the message. The communicating entities can be multiple hops away.

Canonical:	A unique and unambiguous representation of data [i.17]

Canonicalization:	The process of converting a legal representation of data into its canonical form.

Object-based security:	technology that embeds application data within a secure object that can be safely handled by untrusted entities [i.19]

End-to-End Data Integrity Protection: Provides the ability for an entity to integrity protect data.. The integrity protected data can be transported over multiple hops consisting of trusted or untrusted communication entities. An authorized consumer of the data is able to verify the integrity of data and is also able to verify the originator of the data. Such a protection mechanism would ensure that the data is integrity protected “at-rest” and “in-transit” even when handled by intermediate nodes.

End-to-End Data Confidentiality Protection: Provides the ability for an entity  to provide for confidentiality protection of data. The confidentiality protected data can be transported over multiple hops consisting of trusted or untrusted communication entities. Only authorized entities can decrypt the confidentiality protected data. Such a protection mechanism would ensure that the data is confidentiality protected “at-rest” and “in-transit” even when handled by intermediate nodes.

Authenticated Encryption with Associated Data: An algorithm providing confidentiality for the plaintext and a way to check its integrity and authenticity while providing the ability to check the integrity and authenticity of some associated data. In this context: plaintext refers to data that is authenticated and encrypted; and associated data refers to data that is authenticated, but not encrypted. See [i.30] for further details.

Editor’s Note: the definitions are subject to further refinement.

Editor’s Note: a definition  for Group Authentication is needed.

NOTE:	This may contain additional information.

## 6.2	End-to-End Security Framework (ESF) Proposal 1

This clause proposes the End-to-End Security Framework (ESF) that provides protection to minimize the number of CSEs that are required to be trusted to maintain the integrity and/or confidentiality of communications in a oneM2M network. ESF includes support for group authentication, which providing mechanisms for improving the efficiency of establishing end-to-end security between members in a group.

The requirements applicable to ESF are provided in SEC-028 through to SEC-033, SEC-036, SEC-046 and SEC-047 of TS-0002 [2].

### 6.2.1		End-to-End Security Framework Introduction

Introduction to the ESF Security Layer. The ESF Security Layer, proposed to be specified in TS-0003 [3] defines the following processes:

- Key establishment.

- Transforming target data into ESF-treated target data, or the reverse, using established keys. The target data is comprised of plaintext (data to be encrypted and integrity protected) and/or additional authenticated data (to be integrity protected only).

- Serializing (e.g. using JSON or XML) key establishment parameters and/or ESF-treated target data. The serialization is called an envelope.

What is ESF? There is no inherent restriction on how the ESF Security Layer can be used – it can be used by entities inside or outside of a oneM2M system. However, the End-to-End Security Framework (ESF) specifies how the ESF Security Layer is used when one or both of the ESF Security Layer end-points is a CSE or AE. These additional processing details depend on the target data class to be secured, listed in Table 6.2.1-1 “List of ESF target data classes”. The target data class specific details are proposed to be specified in TS-0001 [TS0001].

NOTE 1: The list of supported ESF target data classes is limited for this release. Further ESF target data classes could be added in the future releases.

| Input Item | Target data | Details in Clause: |
| --- | --- | --- |
|  | Plaintext | Additional Authenticated Data (AAD) |  |
| Request or response | Entire Request or response | None | 6.3.1 |
| Request or response | Content parameter | None | 6.3.2 |
| <contentInstance> resource | content attribute | None | 6.3.3 |

Table 6.2.1-1 List of ESF target data classes

NOTE: The currently-defined ESF target data classes do not use the Additional Authenticated Data. The option to use Additional Authenticated Data has been included in the ESF Security Layer so that future ESF target data classes can use Additional Authenticated Data without requiring an update to the ESF Security Layer specifications.

The ESF functionality within a CSE or AE is called an ESF End-Point (EEP). The ESF reference model partitions the functionality into three protocol layers; shown in Figure 6.2.1-1 “High Level ESF Reference model”.

Figure 6.2.1-1 High Level ESF Reference model. Control data (e.g. security parameters) are not shown.

The three protocol layers in the high level ESF reference model are:

- ESF Preparation Layer:

  - A sending EEP, given an input item, extracts the appropriate target data. The input items are either oneM2M messages or oneM2M resources. The target data is provided to the ESF security layer, in a format independent of the target data class, for transforming into an envelope. The input item is forwarded to the ESF Integration Layer for composing the ESF-treated item.

  - A receiving EEP reconstitutes a verified input item from the verified target data received from the ESF Security Layer and the ESF-treated item and ESF target data identifier received from the sending EEP.

The processing at this layer depends on the ESF target data class.

- ESF Security Layer: transforms the target data into an envelope, or the reverse. The processing at this layer does not depend on the target data class. Further details are in clause 6.2.2 “ESF Security Layer High Level Description”.

- ESF Integration Layer:

  - A sending EEP forms the ESF-treated item from the input item received from the ESF Preparation Layer, and the envelope received from the ESF Security Layer.

  - A receiving EEP obtains the ESF-treated item via the Mcc and/or Mca reference points, and extracts the envelope. The envelope is provided to the ESF security layer for transforming back to the verified target data. The ESF-treated item is provided to the ESF Preparation layer for reconstituting the verified input item.

The processing at this layer depends on the ESF target data class.

The ESF Preparation Layer and ESF Integration Layer are tightly dependent on each other, since they both depend on ESF target data class, however the ESF Security Layer processing is independent of those layers. Aside from the dependence of key generation on the ESF target data identifier, the security processing is independent of the ESF target data. This independence allows a single ESF Security Layer end-point implementation to be used for all ESF target data classes. Three security session types are proposed for the ESF Security Layer (for more details, see clause 6.2.2 “ESF Security Layer Overview”). Each of the supported ESF target data classes can be protected using any of the ESF security session types.

In which oneM2M specifications are the ESF layers proposed to be detailed? The functional architecture of the ESF Preparation Layer and ESF Integration Layer are proposed to be specified in TS-0001 [1], with protocol-level details proposed to be specified TS-0004 [TS0004]. As stated at the beginning of the present clause, the ESF Security Layer details are proposed to be specified in TS-0003 [3].

Editor’s note: Is this an appropriate place to discuss how ESF secured resource portions or primitives can be recursively secured within other ESF secured resource portions or primitives? For example, the content, attribute may be secured end-to-end as using ESF target data class 3 at an ADN-AE for consumption by an IN-AE; and the primitive or primitive binding creating the content on the IN-CSE could be secured end-to-end (from ADN-AE to IN-CSE) using ESF target data class 1.

### ESF Security Layer High Level Architecture

#### 6.2.2.1	ESF Security Layer Overview

The Security Layer supports the three security session types listed in Table 6.2.2.1-1.

| Term | Abbr | Security Session Comprises | State Lifetime | Details in clause: |
| --- | --- | --- | --- | --- |
| One-way Single envelope security session | ESF-S1 | One envelope sent in one direction. Provides all crypto parameters necessary to establish the keys securing the payload. Other than credentials, no state is stored | Stateless | 6.2.2.2 |
| Two-way Single Envelope security session | ESF-S2 | Envelopes securing request and corresponding response. Request envelope provides all crypto parameters necessary to establish the key plus secured payload. Other than credentials, no state is stored | Initiator stores state until response received. Target stores state until. response sent | No further details provided |
| Two-way Multi-envelope security session | ESF-Sm | Handshake exchange followed by any number of envelopes containing secured payloads (sent in either direction) | Initiator and Target store state until session is terminated or expires | 6.2.2.3 |

Table 6.2.2.1-1 List of security session types in the ESF reference model.

For each security session type the ESF Security Layer processing can be partitioned into:

- Key Establishment processing: includes

  - negotiating the cryptographic algorithms to be used for key establishment and payload security, and

  - establishing keys for securing payloads and. KEF

- Payload Security processing: applying security mechanisms transforming the target data into the ESF-treated target data, or the reverse, using the established keys.

- Envelope Serialization processing: responsible for representing exchanged data (key establishment parameters, and ESF-treated target data) in an envelope: a common serialization independent of the security session type.

#### 6.2.2.2	ESF-S1 Processing flow

ESF-S1 supports an envelope having a single Source EEP and one or more Target EEPs.

Figure 6.2.2.1-1 shows the processing flow when using this session type.

Figure 6.2.2.1-1 Processing flow for single envelope session type (S1).

NOTE: Figure changed: MAF changed to MEF

- EEPs can interact with Facilitators to provide the Facilitators with long-term parameters (that is, parameters with long lifetime) and/or short-term parameters (that is, parameters with a short lifetime). This step is not expected to be mandatory.

  - (Optional). EEPs could provide interaction with one or more Facilitators to provide long-term parameters (that is, parameters with long lifetime) that the other EEPs can use either for

    - Generating S1 session envelopes, as Source EEPs, or

    - Processing received envelopes, as Target EEPs.

Example long-term parameters include

    - List of supported Key Establishment Algorithm-Sets (keAlgSets)

    - List of supported Payload Security Algorithm-Sets (psAlgSets)

    - Certificates

    - Security Profile

This interaction is expected to happen relatively infrequently – possibly only once in the lifetime of the EEP. The Facilitator(s) store the parameters and make them available for retrieval.

Editor’s note: access to the parameters may be controlled

  - (Optional). EEPs could provide interaction with one or more Facilitators to update short-term parameters that can be provided to other EEPs either for

    - Generating S1 session envelopes, as Source EEPs, or

    - Processing received envelopes, as Target EEPs.

Example, short-term parameters include

    - Random values with short lifetime; these might be used as challenges for authentication.

    - Secret keys with short lifetime; these might be used as challenges for authentication.

The Facilitator(s) store the parameters and make them available for retrieval.

This interactions are expected to happen relatively infrequently – possibly only once in the lifetime of the EEP.

Editor’s note: access to the parameters may be controlled

- The Source EEP provides the Security Layer Functions with

  - Target Data, and

  - (Optional) Security profile applicable to the Target Data,

Editor’s note: The security profile text might need expanding.

  - Identifiers for the intended Target EEPs. This could include individual identifiers and group identifiers.

This triggers the resulting call flow.

- Source EEP Key Establishment processing:

Editor’s note: It could be appropriate to discuss here how the Source EEP determines the minimum security levels to be applied and what session type should be applied. It is worth discussion where the decision is made – Preparation Function, Security Function etc.. Interaction with security profiles should be considered.

  - (Optional) The Source EEP could retrieve the Target EEP(s)’ long-term and/or short-term parameters from the Facilitator(s).

Editor’s note: access to the parameters may be controlled

Editor’s note: How the Key Establishment identifies the appropriate Facilitators to contact is FFS. (may just be provisioned in CSE, with overriding option by AE, in this release?)

  - The Source EEP selects one or more Key Establishment Algorithm-Sets (keAlgSet) and Payload Security Algorithm-Set (psAlgSet).

NOTE: Multiple keAlgSets could be needed only in some (but not all) scenarios involving multiple Target EEPs.

The selection of Algorithm Sets could be influenced by

    - The combinations of keAlgSets and psAlgSets  supported by the Source EEP.

    - Preferences configured to the Source EEP .

    - The combinations of keAlgSets and psAlgSets   supported by the Target EEP(s), which may have been either configured to the Source EEP or retrieved by the Source EEP from the Facilitators in (optional) step 3.a.

The choices of keAlgSet(s) and psAlgSet are somewhat dependent on each other; in particular, if the psAlgSet includes encryption and/or symmetric-key based integrity protection of the target data, then the keAlgSet(s)  must include an algorithm for generating a secret key to be used for this protection. A high level overview of possible psAlgSet  Options is found in clause 7.4.2.2 “ESF-S1 Payload Security Requirements”. A high level overview of possible keAlgSet options is found in clause 7.4.2.3 “ESF-S1 Key Establishment Requirements”.

  - The Source EEP applies the selected keAlgSet(s), which can include

    - Proof of the Source EEP’s identity,

    - Proof of the integrity of the selected keAlgSet(s) and psAlgSet, and

    - Generation of keys for processing the target data.

  - (Optional) The Source EEP provides the Facilitator(s) with updated Short-term Key establishment parameters. This may include configuring access controls at the Facilitator to limit access only to the set of intended Target EEPs.

- Source EEP Payload Security processing. The Source EEP applies the selected psAlgSet to the input payload using the key(s) provided by the Source EEP, resulting in the ESF-treated target data.

- Source EEP Envelope Serialization: The Source EF serializes the keAlgSet(s), psAlgSet, key establishment parameters and ESF-treated target data into an envelope.

- The envelope is obtained by the Target EEP(s). The Security Layer does not address how the Target EEP(s) obtain the envelope.

NOTE: The following discussion shows processing at one of the potentially multiple Target EEPs.

- Target EEP Envelope Serialization processing: The Target EF extracts the keAlgSet(s), psAlgSet, key establishment parameters and ESF-treated target data from the received envelope.

- Target EEP Key Establishment processing: In the case that there are multiple Key Establishment Algorithm Sets present, the Target EEP identifies a Key Establishment Algorithm Set that it expects to process successfully.

  - (Optional) The Target EEP could retrieve the Source EEP’s long-term and/or short-term parameters from the Facilitator(s). The Facilitator(s) could authorize access based on configured access controls.

  - The Target EEP applies the selected Key Establishment Algorithm Set, which can include

    - Verifying the identity of Source EEP,

    - Verifying the selected keAlgSet(s) and psAlgSet, and

    - Generation of keys for processing the input payload.

- Target EEP Payload Security processing : The Target EEP applies the selected psAlgSet  to the secured payload using the established key(s), resulting in the verified target data.

- The Target EEP outputs:

  - The verified target data, and

  - Source EEP’s identity.

#### 6.2.2.3	ESF-Sm Processing Flow

The ESF-Sm reference model allows establishing multi-envelope sessions between a single Initiating EEP (analogous to a TLS/DTLS Client) and a single Terminating EEP (analogous to a TLS/DTLS Server).

An ESF-SM security session has two phases:

- ESF-Sm handshake phase: in which the Initiating EEP and Terminating EEP – optionally assisted by Facilitator(s), and under the influence of a security profile – accomplish the following:

  - Negotiating a key establishment cryptographic algorithms and payload security cryptographic algorithms.

  - Apply the negotiated key establishment cryptographic algorithms to

    - Authenticate the Terminating EEP,

    - (Optionally) Authenticate the Initiating EEP,

    - Establish secret session keys to be used in for payload security.

A processing flow would depend on the handshake details, and the handshake details are beyond the scope of a high level description. For this reason, a processing flow is not provided.

- ESF-Sm payload security phase, in which the sending EEP (which can be the Initiating EEP and Terminating EEP) apply the negotiated payload security cryptographic algorithms transform the target data into ESF-treated target data which is then serialized in an envelope. At the receiving EEP, the ESF-treated target data is extracted from the envelope and the negotiated payload security cryptographic algorithms transform the ESF-treated target data into verified target data.  Due to the simplicity of this processing, a processing flow diagram is not provided.

## 6.3	ESF Preparation Layer and ESF Integration Layer Processing

### 6.3.1	ESF Specifications for ESF Target Data Class 1

#### 6.3.1.1	Profile for ESF Target Data Class 1

Table 6.3.1.1-1 “Profile for ESF Target Data Class 1” contains the profile for ESF Target Data Class 1.

| Aspect | Description |
| --- | --- |
| ESF Target Data Class Identifier | 1 |
| Input item | A request or response |
| Target data | A serialization of the entire request or response |
| Treated Item | A new encapsulating request or response whose Content parameter is the envelope produced by the ESF Security Layer. The Originator and Hosting CSE of the encapsulating message are the ESF End-Points for this message. |
| EEP Constraints | The present document allows an EEP to be the Originator or Hosting CSE of the input message or any other CSE on the oneM2M path between the Originator and Hosting CSE of the input message. |
| Security Layer Constraints | There can be only one Target EEP. |
| Target Data-class specific parameters for ESF Policy | Parameters for the encapsulating message (e.g. To, From) |

Table 6.3.1.1-1 Profile for ESF Target Data Class 1

#### 6.3.1.2	ESF Target Data Class 1 Processing at the Sending EEP

The following steps occur at a Sending EEP when applying this ESF Target Data Class to an outbound request or response

- The EEP’s Preparation Function serializes the request or response into a binary data object.

- The EEP’s Preparation Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Target data set to the binary data object and

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating an envelope.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two outbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the envelope and applicable ESF Target Data Class identifier to the EEP’s Integration Function. The envelope is serialized as is XML or JSON.

- The EEP’s Integration Function forms a request or response (according to if the protected message was a request or response) including the envelope in the content:

- The EEP’s Integration Function passes the request or response to the next step in processing outbound messages.

#### 6.3.1.3	ESF Target Data Class 1 Processing at the Receiving EEP

The following steps occur at a Receiving EEP when applying this ESF Target Data Class to an inbound request or response

- The EEP’s Integration Layer parses the received message to identify the sending EEP and extract the envelope which is the Content parameter of the message. The envelope is serialized as is XML or JSON.

- The EEP’s Integration Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Envelope.

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating a verified target data. This processing includes verification that the provided ESF Target Data Class identifier is correct.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two inbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the verified target data and to the EEP’s Preparation Layer.

- The EEP’s Preparation Function parses the binary data object to form the verified request or response.

- The EEP’s Preparation Function passes the request or response to the next step in processing inbound messages.

### 6.3.2	ESF Specifications for ESF Target Data Class 2

#### 6.3.2.1	Profile for ESF Target Data Class 2

Table 6.3.2.1-1 “Profile for ESF Target Data Class 2” contains the profile for ESF Target Data Class 2.

| Aspect | Description |
| --- | --- |
| ESF Target Data Class Identifier | 2 |
| Input item | A request or response |
| Target data | A serialization of the Content parameter of the input request or response |
| Treated Item | The input request or response with the original Content parameter replaced by the envelope produced by the ESF Security Layer. |
| EEP Constraints | The present document allows an EEP to be the Originator or Hosting CSE of the input request or response or any other CSE on the oneM2M path between the Originator and Hosting CSE of the input request or response. |
| Security Layer Constraints | There can be only one receiving EEP. |

Table 6.3.2.1-1 Profile for ESF Target Data Class 2

#### 6.3.2.2	ESF Target Data Class 2 Processing at the Sending EEP

The following steps occur at a Sending EEP when applying this ESF Target Data Class to an outbound request or response

- The EEP’s Preparation Function extracts the Content parameter of the request or response, and serializes the Content parameter to form the target data.

- The EEP’s Preparation Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Target data, and

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating an envelope.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two outbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the envelope and applicable ESF Target Data Class identifier to the EEP’s Integration Function. The envelope is serialized as is XML or JSON.

- The EEP’s Integration Function forms the ESF-treated request or response from the input request or response by updating values of the following parameters

  - Content:  The original value is replaced with the envelope received from the ESF Security Function.

  - Resource Type: replacing this with a reserved identifier for ESF-protected Content parameter.

- The EEP’s Integration Function passes the ESF-treated request or response to the next step in processing outbound messages.

#### 6.3.2.3	ESF Target Data Class 2 Processing at the Receiving EEP

The following steps occur at a Receiving EEP when applying this ESF Target Data Class to an inbound request or response

- The EEP’s Integration Layer parses the received message to identify the sending EEP and extract

  - Content: comprises the envelope. The envelope is serialized as is XML or JSON.

  - Resource Type: a reserved identifier for protected requests and responses protected by ESF Target Data Class 2.

- The EEP’s Integration Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Envelope.

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating a verified target data. This processing includes verification that the provided ESF Target Data Class identifier is correct.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two inbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the EEP’s Preparation Layer with

  - Verified target data, comprising a serialization of the original value of the Content parameter.

  - There is no additional data for this ESF Target Data Class

- The EEP’s Preparation Function

  - Parses the target data to form the value of the verified Content parameter.

  - (If the Content parameter contains a resource) Determines the resource type of the verified Content parameter.

  - Forms the verified request or response by updating values of the following parameters

- Content:  The value in the received request or response is replaced with the value received from the ESF Security Function in the target data.

- (if the verified  Content parameter contains a resource) Resource Type: replacing this with the resource type of the resource in the verified Content parameter.

- The EEP’s Preparation Function passes the verified request or response to the next step in processing inbound messages.

### 6.3.3	ESF Specifications for ESF Target Data Class 3

#### 6.3.3.1	Profile for ESF Target Data Class 3

Table 6.3.3.1-1 “Profile for ESF Target Data Class 3” contains the profile for ESF Target Data Class 3.

| Aspect | Description |
| --- | --- |
| ESF Target Data Class Identifier | 3 |
| Input item | A <contentInstance> resource |
| Target data | A serialization of The content attribute in the input <contentInstance> resource. (Optionally) A contentInfo attribute if it is applicable to the input <contentInstance> resource, regardless of whether the contentInfo attribute is explicitly included in input <contentInstance> resource, or whether ontologyRef is inherited from the parent of the input <contentInstance> resource. (Optionally) An ontologyRef attribute applicable to the input <contentInstance> resource, regardless of whether the ontologyRef attribute is explicitly included in input <contentInstance> resource, or whether ontologyRef is inherited from the parent of the input <contentInstance> resource. |
| Treated Item | The input <contentInstance> resource, with the original content attribute value replaced by the envelope produced by the ESF Security Layer. |
| EEP Constraints | The EEPS could be any entities on the data path of the content attribute value - including CSEs, AEs or an entities in another system with which oneM2M interworks. |
| Security Layer Constraints | Multiple Target EEPs are allowed. |

Table 6.3.3.1-1 Profile for ESF Target Data Class 3

#### 6.3.3.2	ESF Target Data Class 3 Processing at the Sending EEP

The following steps occur at a Sending EEP when applying this ESF Target Data Class to an outbound <contentInstance> resource.

- The EEP’s Preparation Function processes the outbound  <contentInstance>

  - The EEP’s Preparation Function parses the outbound <contentInstance> the extract the attributes to be protected, which comprises:

    - The content attribute.

    - (Optionally) The contentInfo attribute.

    - (Optionally) The ontologyRef attribute.

  - The EEP’s Preparation Function serializes these attributes to form the target data.

- The EEP’s Preparation Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Target data.

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating an ESF envelope.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two outbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the envelope and applicable ESF Target Data Class identifier to the EEP’s Integration Function. The ESF envelope is serialized as in XML or JSON.

- The EEP’s Integration Function forms the ESF-treated <contentInstance> from the input <contentInstance> by updating values of the following attributes

  - content:  The original value is replaced with the ESF envelope received from the ESF Security Function.

- The EEP’s Integration Function passes the ESF-treated resource to the next step in processing outbound resources.

#### 6.3.3.3	ESF Target Data Class 3 Processing at the Receiving EEP

The following steps occur at a Receiving EEP when applying this ESF Target Data Class to an inbound request or response

- The EEP’s Integration Layer parses the received message to identify the sending EEP and extract

  - content:  comprising the ESF envelope received from the ESF Security Function.

- The EEP’s Integration Function passes to the EEPs Security Function

  - The applicable ESF Target Data Class identifier.

  - Envelope.

  - There is no additional data for this ESF Target Data Class.

- The EEPs Security Function applies the applicable processing according to the security session type, generating a verified target data. This processing includes verification that the provided ESF Target Data Class identifier is correct.

NOTE: If ESF-Sm is applied, and the security session is not yet established, then the ESF-Sm handshake phase must be applied prior to transmitting any target data. Consequently, the first two inbound envelopes in this case will typically contain handshake phase key exchange parameters, and not the message.

- The EEPs Security Function provides the EEP’s Preparation Layer with

  - Verified target data, comprising a serialization of the original value of the content, (optionally) contentInfo and (Optionally) ontologyRef.

  - There is no additional data for this ESF Target Data Class

- The EEP’s Preparation Function

  - Parses the verified target data to form the verified values of content, (optionally) contentInfo and (Optionally) ontologyRef.

  - Forms the verified resource by updating values of the following attributes

    - Content:  The value in the received resource is replaced with the value of content received from the ESF Security Function in the target data.

    - contentInfo: If the verified target data contains contentInfo, then this value replaces the value received in the verified target data.

    - ontologyRef: If the verified target data contains ontologyRef, then this value replaces the value received in the verified target data.

- The EEP’s Preparation Function passes the verified resource to the next step in processing inbound resources.

# 7	Requirements and Principles

<Text>

## 7.1	Assumptions

Editor’s note: this clause provides assumptions.

<Text>

## 7.2	Requirements on the Entities

Editor’s note: this clause provides high level requirements for the entities in the architecture .

<Text>

## 7.3	Requirements on the Reference Points

Editor’s note: this clause provides some requirements for the reference points between the entities in the architecture

## 7.4 	End-to-End Security Framework (ESF) Security Layer Requirements

Editor’s Note: how to fix this clause to the structure of section 7 is FFS.

Clause 7.4 proposes detailed requirements for the ESF Security Layer. These requirements are intended only for use in design and analysis of components of ESF as part of the work represented in this TR.

Clause 7.4.1 proposes requirements which are independent of the security session type. Clauses 7.4.2, 7.4.3, 7.4.4 proposes requirements specific to the security session types ESF-S1, ESF-S2 and ESF-Sm respectively.

### 7.4.1	Generic Requirements for the ESF Security Layer

#### 7.4.1.1	Generic ESF Security Layer Macro-Considerations

“Macro-considerations” are considerations or requirements for the ESF Security Layer that are not specific to the Facilitation, Key Establishment, Payload Security or Envelope Serialization processing of the ESF Security Layer.

The following is a list of proposed macro-considerations for the ESF Security Layer which are independent of security session type:

- The ESF Security Layer supports ESF End-Point implementations with ESF Key Establishment processing in a secure environment providing established keys to ESF Payload Security processing outside the secure environment.

Proposed macro-considerations for individual security session types are found in clauses 7.4. 2.1 (for ESF-S1), 7.4.3.1 (for ESF-S2), and 7.4.4.1 (for ESF-Sm).

#### 7.4.1.2	Generic ESF Payload Security Requirements

The following is a list of proposed requirements for the ESF Payload Security processing which are independent of the security session type:

- ESF Payload Security supports protecting the payload using a symmetric (secret) key established using the corresponding ESF Key Establishment reference points.

- ESF Payload Security supports encryption of the input payload using a symmetric key.

- ESF Payload Security supports integrity protection of the input payload using a symmetric key.

- ESF Payload Security supports a range of crypto algorithms, to enable migrating to another secure cryptographic algorithms in the event that cryptographic algorithms are found to be insecure or are otherwise deprecated.

- ESF Payload Security is not required to maintain state between security sessions.

Proposed ESF Payload Security requirements for individual security session types are found in clauses 7.4.2.2 (for ESF-S1), 7.4.3.2 (for ESF-S2), and 7.4.4.2 (for ESF-Sm).

#### 7.4.1.3	Generic ESF Key Establishment Requirements

The following is a list of proposed requirements for the ESF Key Establishment processing which are independent of the security session type:

- ESF Key Establishment provides a mechanism for negotiating an appropriate set of cryptographic algorithms and credentials. This could be influenced by

  - Cryptographic algorithms supported by the EEPs

  - Credentials of the EEPs.

  - A Security Profile relevant to the target data.

- ESF Key Establishment supports authenticated key establishment based on a symmetric (secret) key provisioned by means unspecified by oneM2M specifications.

- ESF Key Establishment supports authenticated key establishment based on a symmetric (secret) key obtained through interaction with a trusted Facilitator.

NOTE: The role of Facilitator in this case could be played by an M2M Authentication Function (MAF) or M2M Enrolment Function (MEF).

- ESF Key Establishment supports key establishment using certificates.

- ESF Key Establishment supports mutual authentication.

- ESF Key Establishment could support one-way authentication of the source/initiator EEP or target/responder EEP.

- ESF Key Establishment ensures that there is only a very low probability that keys established for one security session are identical to keys established for a different security session – regardless of the security session type of both security sessions.

- ESF Key Establishment ensures keys established for one security session type cannot be used in another security session type; e.g. the keys established for a single-envelope security session cannot be used for a multi-envelope security session.

- ESF Key Establishment ensures that there is only a very low probability that keys established for one ESF target data class are identical to keys established for a different ESF target data class.

- ESF Key Establishment maintains minimal state between security sessions.

Proposed ESF Key Establishment requirements for individual security session types are found in clauses 7.4.2.3 (for ESF-S1), 7.4.3.3 (for ESF-S2), and 7.4.4.3 (for ESF-Sm).

#### 7.4.1.4	Generic ESF Facilitation Requirements

ESF Facilitation is independent of the security session type. The following is a list of proposed requirements for the ESF Facilitation which are independent of the security session type:

- ESF Facilitation is independent of the security session type (S1, S2 or Sm)

- ESF Facilitation supports being secured from the ESF End-Point to the Facilitator.

- ESF Facilitation supports mutual authentication of the ESF End-Point and the Facilitator.

- A Facilitator may apply access control.

- ESF Facilitation supports EEPs obtaining symmetric (secret) keys through interaction with trusted Facilitators.

NOTE: The role of Facilitator in this case could be played by an M2M Authentication Function (MAF) or M2M Enrolment Function (MEF).

- ESF Facilitation supports Facilitators acting as a repository of certificates or public keys associated with an ESF End-Point.

- ESF Facilitation supports Facilitators acting as a repository of Security Profiles.

Proposed ESF Facilitation requirements imposed by individual security session types are found in clauses 7.4.2.4 (for ESF-S1), 7.4.3.4 (for ESF-S2), and 7.4.4.4 (for ESF-Sm).

#### 7.4.1.5	Generic ESF Envelope Serialization Requirements

The following is a list of proposed ESF Envelope Serialization requirements which are independent of the security session type:

- The envelope serialization is independent of the security session type (S1, S2 or Sm) and type of input data (resource portion or primitive).

- The envelope serialization identifies the security session type (S1, S2 or Sm)

- The envelope serialization identifies the target data class.

- The envelope serialization is compatible with oneM2M resource and primitive representations (JSON and XML are supported at the time of writing).

- The envelope serialization shall allow simple identification of envelopes within oneM2M resources representations (JSON and XML are supported at the time of writing).

Proposed ESF Envelope Serialization requirements for individual security session types are found in clauses 7.4.2.5 (for ESF-S1), 7.4.3.5 (for ESF-S2), and 7.4.4.5 (for ESF-Sm).

### 7.4.2	ESF-S1 Requirements

#### 7.4.2.1	ESF-S1 Macro-Considerations

In addition to the macro-considerations in clause 7.4.1.1 “ESF Security Layer Macro-Considerations”, the following ESF-S1-specific macro-considerations are proposed:

Editor’s note: there are currently no ESF-S1-specific macro-considerations. Members are invited to provide ESF-S1-specific macro-considerations. If there are no ESF-S1-specific macro-considerations then this clause can be deleted.

#### 7.4.2.2	ESF-S1 Payload Security  Requirements

A Payload Security Algorithm Class (psAlgCl) describes the type of protection that is afforded the input payload; suggested Payload Security Algorithm Classes for oneM2M Release 2 are listed in Table 7.4.2.2-1 “List of ESF-S1 Payload Security Algorithm Class (AlgCl) options”. This list is not necessarily exhaustive, and other options could be available.

Editor’s note: members are invited to provide other options for consideration.

The selection of algorithms for each AlgCl is discussed in clause 8 “Description and Analysis of Available Options”.

Editor’s note: Should advantages and disadvantages of each Algorithm Class be documented in the present document or TR-0008 [TR0008]?

| Payload Security Algorithm Class | Example mechanism | Brief Description | Target Data | Keys that must be established |
| --- | --- | --- | --- | --- |
| Symmetric integrity protection only | MIC | Source EEP and Target EEP(s) use a symmetric key for integrity protection, but not confidentiality. Target EEPs can impersonate the Source EEP. For this psAlgCl, ESF does not perform encryption. | AAD only | Payload security processing requires a symmetric envelope master key established between the Source EEP and Target EEP(s) |
| Symmetric confidentiality and integrity protection | AEAD | Source EEP and Target EEP(s) use a symmetric key for confidentiality and integrity protection. Target EEPs can impersonate the Source EEP | Plaintext + (optional) AAD |  |
| Symmetric confidentiality and non-repudiation protection | AEAD + Digital Signature | Source EEP and Target EEP(s) use a symmetric key for confidentiality and digital signature for non-repudiation. Target EEPs cannot impersonate the Source EEP. Use of Authenticated Encryption is suggested. | Plaintext + (optional) AAD | Payload security processing requires a symmetric envelope master key established between the Source EEP and Target EEP(s); additionally the Source EEP uses a digital signature private signing key and the Target EEP(s) use a digital signature public verification key. |
| Non-repudiation protection only | Digital Signature | Source EEP and Target EEP(s) use a digital signature for non-repudiation. For this psAlgCl, ESF does not perform encryption. | AAD only | Source EEP uses a digital signature private signing key and the Target EEP(s) use a digital signature public verification key. |

Table 7.4.2.2-1 List of ESF-S1 Payload Security Algorithm Class (psAlgCl) options.

#### 7.4.2.3	ESF-S1 Key Establishment Requirements

The psAlgCl in Table 7.4.2.2-1 “List of ESF-S1 Payload Security Algorithm Class (AlgCl) options” which require a digital signature public verification key are:

- AEAD + Digital Signature, and

- Digital Signature.

If one of these psAlgCl are used, then a digital signature public verification key is provided for additional verification of the input payload. The digital signature public verification key could be provided in a certificate communicated as key establishment parameter in envelope or via Facilitator. The Target EEP verifies the certificate prior to verifying the digital signature on the target data.

The psAlgCl in Table 7.4.2.2-1 “List of ESF-S1 Payload Security Algorithm Class (psAlgCl) options” which require an envelope master key are:

- Symmetric integrity protection

- Symmetric confidentiality and integrity protection, and

- Symmetric confidentiality and integrity protection + non-repudiation.

A Key Establishment Algorithm Class (keAlgCl) describes the type of key establishment mechanisms used to establish an envelope master key; suggested Key Establishment Algorithm Classes for oneM2M Release 2 are listed in Table 7.4.2.3-1 “List of ESF-S1 Key Establishment Key Establishment Algorithm Class (AlgCl) options”. This list is not necessarily exhaustive, and other options could be available. This list is not intended to constrain the options considered for establishing an envelope master key.

Editor’s note: Should advantages and disadvantages of each Algorithm Class be documented in the present document or TR-0008 [TR0008]?

| Name | Brief Description |
| --- | --- |
| Trusted Third Party (TTP) | The Source EEP requests a Facilitator to store the envelope master key with an associated set of permissions. The Facilitator could optionally generate the envelope master key for the Source EEP. The Source EEP and Facilitator agree on a unique envelope master key identifier for the envelope master key, and this envelope master key identifier is provided in the envelope. After the Target EEP retrieves the envelope, then the Target EEP provides the envelope master key identifier to the Facilitator. If the Target EEP has the necessary permissions, then the Facilitator provides the envelope master key to the Target EEP. This requires a high degree of trust in the Facilitator, and communication with the Facilitator (from both the Source EEP and Target EEP) must be mutually authenticated and secured. |
| Pre-Provisioned Shared Key | The envelope master key is provided to the Source EEP and Target EEP(s) via mechanisms not specified by oneM2M (e.g. manual input, pre-provisioning). |
| Key Encryption | The Source EEP selects a set of Target EEPs for which the Source EEP knows a public encryption key of the Target EEP (for example, the public encryption keys could be in certificates, or Identity Based Encryption might be applied) or the Source EEP shares a symmetric key encryption key (KEK). For each Target EEP, then Source EEP encrypts the envelope master key using either the public encryption key or KEK and includes the resulting encrypted envelope master key in the envelope. The envelope includes an encrypted envelope master key for each Target EEP. After the Target EEP retrieves the envelope, then the Target EEP uses its private decryption key or KEK (shared with the Source EEP) to decrypt its encrypted envelope master key and obtain the envelope master key. The mechanism could optionally authenticate the Source EEP; e.g by including a digital signature that can be verified using a certificate of the Source EEP. |
| Key Agreement | (This approach can work only if there is a single Target EEP). The Source EEP and Target EEP applies a key agreement protocol to establish a shared key. For example, the Source EEP could use a Diffie-Hellman protocol [ReferenceNeeded] using a public key in a certificate of the Target EEP. The mechanism could optionally authenticate the Source EEP; e.g. by including a digital signature that can be verified using a certificate of the Source EEP. |

Table 7.4.2.3-1 List of ESF-S1 Key Establishment Algorithm Class (AlgCl) options which could be considered for establishing an envelope master key.

#### 7.4.2.4	ESF-S1-Specific ESF Facilitation Requirements

Proposed ESF-S1-specific Requirements. In addition to the generic requirements in clause 7.4.1.3 “Generic ESF Key Establishment Requirements”, the following ESF-S1-specific requirements are proposed:

- ESF Facilitation shall support Facilitators acting as a repository of long-term key parameters associated with an ESF End-Point which could include

  - List of supported ksAlgSets.

  - List of supported psAlgSets.

  - List of Certificates or public keys.

These parameters could be used in the Key Encryption, Key Agreement and Digital Signature Algorithm Classes in Table 7.4.2.3-1 “List of ESF-S1 Key Establishment Algorithm Class (AlgCl) options”

- ESF Facilitation may support Facilitator acting as a repository of the latest provided short-term key parameters associated with an ESF End-Point, which could include

  - A short-lifetime randomly-generated, non-secret value – e.g. for use as challenges in authentication or for adding non-secret entropy to key generation.

  - A short-lifetime public key value – e.g. EC-DH public key for adding perfect forward secrecy (PFS).

NOTE: The case of using a short-lifetime secret value – e.g. for use as adding secret entropy to key generation – is already covered by the first ESF Facilitation requirement “The reference point supports EEPs obtaining symmetric (secret) keys through interaction with trusted Facilitators” in clause 7.4.1.3 “Generic ESF Key Establishment Requirements”.

These parameters could be used in the Key Encryption, Key Agreement and Digital Signature Algorithm Classes in Table 7.4.2.3-1 “List of ESF-S1 Key Establishment Algorithm Class (AlgCl) options”

#### 7.4.2.5	ESF-S1 Envelope Serialization Requirements

Proposed ESF-S1 Envelope Serialization requirements. In addition to the generic requirements in clause 7.4.1.5 “Generic ESF Envelope Serialization Requirements”, the following ESF-S1-specific Envelope Serialization requirements are proposed:

- The ESF-S1 Envelope Serialization supports representing secured payloads for the Payload Security Algorithm Classes in clause 7.4.2.2 “ESF-S1 Payload Security Requirements”.

- The ESF-S1 Envelope Serialization supports representing key establishment parameters for the Key Establishment Algorithm Classes in clause 7.4.2.3 “ESF-S1 Payload Security Requirements”.

- The ESF-S1 Envelope Serialization supports representing the keAlgSet and psAlgSet”.

JSON Representations. The IETF JOSE specifications [references] can provide a JSON representation of the ESF-S1 secured payload and key establishment parameters. The generic envelope serialization requirements and the proposed ESF-S1 Envelope requirements could be satisfied by an envelope which is a JSON element comprised of

- An identifier for the security session type (in this case indicating S1), followed by

- One or more JOSE data elements containing the ESF-S1 key establishment parameters and ESF-S1 secured payload.

XML Representations. The W3C XML-SIG [i.26] and XML-ENC [i.28] can provide a XML representation of the ESF-S1 secured payload and key establishment parameters. The generic envelope serialization requirements and the proposed ESF-S1 Envelope requirements could be satisfied by an envelope which is a XML element comprised of

- An identifier for the security session type (in this case indicating S1), followed by

- One or more XML-SIG and/or XML-ENC data elements containing the ESF-S1 secured payload and key establishment parameters.

Detailed proposed specification for JSON serialization and XML serialization are provided in clause 8.

Editor’s note: The above sentence anticipates detailed specifications will be provided in clause 8. If detailed specifications are not provided, then the above sentence should be deleted.

### 7.4.4	ESF-Sm Requirements

#### 7.4.4.1	ESF-Sm Macro-Considerations

In addition to the generic considerations in clause 7.4.1.1 “ESF Security Layer Macro-Considerations”, the following ESF-S1-specific macro-considerations: are proposed

- The ESF-Sm security layer shall support a signaling messages including the ability to end an existing ESF-Sm session. An example of such a signaling messages are the alert messages of TLS v1.2 (see RFC 5246 [i.31]) and DTLS v1.2 (see RFC 6347 [i.32]).

Editor’s note: Members are invited to provide further ESF-S1-specific macro-considerations.

#### 7.4.4.2	ESF-Sm Payload Security Requirements

Proposed ESF-Sm Payload Security Requirements. In addition to the generic requirements in clause 7.4.1.2 “Generic Payload Security Requirements”, the following ESF-Sm-specific Payload Security requirements are proposed:

- Replay detection shall be supported by ESF-Sm.

Possible ESF-Sm Payload Security Solutions.

Encryption and Integrity protection can be provided by either

- A combination of an encryption algorithm and an independent MIC algorithm.

- An Authenticated Encryption with Associated Data (AEAD) algorithm.

Replay detection can be provided by including a sequence number which is protected by the integrity protection calculation.

All of the above mechanisms are supported by appropriate choices of ciphersuites for TLS v1.2 in RFC 5246 [i.31] and DTLS v1.2 in RFC 6347 [i.32]. The selection of appropriate ciphersuites is discussed in clause 8 “Description and Analysis of Available Options”.

TLS assumes a reliable transport (such as TCP); consequently, TLS cannot be used in all oneM2M scenarios. DTLS does not assume a reliable transport; consequently, DTLS can be used in all oneM2M scenarios. For this reason, DTLS is preferable to TLS.

There are other security protocols which could provide the functionality required for ESF-Sm Payload Security, however these are not as widely used as TLS and DTLS.

Recommendation: DTLS v1.2 record payload protection is the recommended solution for ESF-Sm Payload Security.

#### 7.4.4.3	ESF-Sm Key Establishment Requirements

Proposed ESF-Sm Key Establishment Requirements. In addition to the generic requirements in clause 7.4.1.3 “Generic ESF Key Establishment Requirements”, the following ESF-Sm-specific Key Establishment requirements are proposed:

- Perfect Forward Secrecy countermeasures (e.g. the ephemeral Diffie-Hellman protocol or ephemeral Elliptic Curve Diffie-Hellman protocol) is required to be supported by ESF-Sm and optional to be used.

- Replay detection of ESF-Sm Key Establishment handshake messages is required to be supported by ESF-Sm Key Establishment and required to be used.

This list is not necessarily exhaustive, and other options could be available. This list is not intended to constrain the options considered for establishing symmetric (secret) keys for use in the EF-Sm Payload Security reference point.

Possible ESF-Sm Key Establishment Solutions. All of the above mechanisms are supported by appropriate choices of ciphersuites for TLS v1.2 (see RFC 5246 [i.31]) and DTLS v1.2 (see RFC 6347 [i.32]). The selection of appropriate ciphersuites is discussed in clause 8 “Description and Analysis of Available Options”.

TLS assumes a reliable transport (such as TCP); consequently, TLS cannot be used in all oneM2M scenarios. DTLS does not assume a reliable transport; consequently, DTLS can be used in all oneM2M scenarios. For this reason, DTLS is preferable to TLS.

There are other security protocols which could provide the functionality required for ESF-Sm Payload Security, however these are not as widely used as TLS and DTLS.

Recommendation: The DTLS v1.2 handshake is the recommended solution for ESF-Sm key establishment.

#### 7.4.4.4	ESF-Sm-Specific ESF Facilitation Requirements

There are no ESF-Sm-specific requirements proposed in addition to the generic requirements in clause 7.4.1.3 “Generic ESF Facilitation Requirements”.

NOTE: In theory, ESF-Sm could support a Facilitator enabling an faster ESF-S1 key establishment by acting as a repository of the latest provided short-term, non-secret key establishment parameters associated with an ESF End-Point. Such short-term parameters could include

  - A short-lifetime secret value – e.g. for use as adding secret entropy to key generation. This options requires trusting the Facilitator to maintain the confidentiality of the value.

  - A short-lifetime public key value – e.g. EC-DH public key for adding perfect forward secrecy (PFS).

There is a problem, because the DTLS v1.2 handshake (recommended for ESF-Sm Key Establishment handshake) does not support integrating such parameters into a faster key exchange. If DTLS v1.2 handshake is used, then storing short-term, non-secret key establishment parameters for ESF-Sm Key Establishment provides no value. For this reason, there is no proposal to store short-term, non-secret key establishment parameters for ESF-Sm key establishment.

#### 7.4.4.5	ESF-Sm Envelope Requirements

Solutions providing ESF-Sm Key Establishment and Payload Security. The discussion in previous clauses indicates the following:

- The DTLS v1.2 handshake (see RFC 6347 [i.32]) is the preferred existing solution providing the functionality required for ESF-Sm Key Establishment key establishment (see clause 6.2.2.4).

- The DTLS v1.2 record payload protection is the preferred existing solution providing the functionality required for ESF-Sm Payload Security payload security (see clause 6.2.2.3).

Consequently, DTLS v1.2 is a preferable solution for ESF-Sm Key Establishment and ESF-Sm Payload Security.

However, DTLS messages are binary data, while resources and primitives use a JSON or XML representation. This prevents using the binary DTLS messages directly in a resource or primitive

Proposed ESF-Sm Envelope requirements. In addition to the generic requirements in clause 7.4.1.5 “Generic ESF Envelope Requirements”, the following ESF-Sm-specific Envelope requirements are proposed:

- ESF-Sm Envelope is required to support transporting DTLS records, where these records contain

  - DTLS handshake messages, providing the ESF-Sm Key Establishment functionality

  - DTLS protected payloads, providing the ESF-Sm Payload Security functionality. Since DTLS allows tunneling DTLS handshake messages inside an established DTLS session, the DTLS protected payloads can provide the ESF-Sm Key Establishment functionality.

- ESF-Sm Envelope is required to encode binary DTLS records in an ASCII character space allowed by the values in JSON and XML data elements.

JSON Representations. The generic envelope serialization requirements and the proposed ESF-Sm Envelope requirements could be satisfied by an envelope which is a JSON element comprised of

- An identifier for the security session type (in this case indicating Sm), and

- A JSON data element containing a base64 encoding [i.33] of a DTLS message.

XML Representations. The generic envelope serialization requirements and the proposed ESF-Sm Envelope requirements could be satisfied by an envelope which is a XML element comprised of

- An identifier for the security session type (in this case indicating Sm), and

- A XML data element containing a base64 encoding [i.33] of a DTLS message.

Detailed proposals for JSON serialization and XML serialization are provided in clause 8 “Description and Analysis of Available Options”.

# 8	Available Options

## 8.1	Review of Existing Technology

### 8.1.1	Review of Object-Based Security Technology

#### 8.1.1.1	Introduction to Object-Based Security Technology

NOTE: this clause borrows heavily from the introduction to [i.19].

Channel-based security technologies such as IPsec [i.15], Transport Layer Security (TLS) [6] and Data gram TLS (DTLS) [7] create a secure channel at the IP layer or transport layer over which data can flow. In protocols with application-layer intermediaries, channel-based security protocols would protect messages from attackers between intermediaries, but not from the intermediaries themselves.

In the present oneM2M security specifications, the only protection afforded by oneM2M messages is provided by the channel-based TLS or DTLS. Some of the use cases in clause 5 require protecting messages from CSEs acting as intermediaries, and the existing oneM2M security mechanisms cannot offer this protection.  Additional technology is required.

Object-based security technologies (see definitions) embed data within “secure object” that can be safely handled by untrusted intermediaries in the scenarios discussed above. Clause 8.1.1 provides a review of well-known standardized object-based security technologies including

- Secure/Multipurpose Internet Mail Extensions (S/MIME) [i.17] was proposed as a mechanism for providing an email with end-to-end security protection in the presence of untrusted Mail Transfer Agents en route to its destination. S/MIME provides confidentiality, integrity, and data origin authentication. S/MIME assumes a hierarchical PKI. These specifications are discussed in clause 8.1.1.2.

- OpenPGP [i.16] provides security services similar to S/MIME. Open PGP supports both hierarchical PKIs (as used in S/MIME) and a decentralized PKI known as a “Web-of-Trust” [i.22]. OpenPGP is discussed in clause 8.1.1.3.

- The XML security specifications XML Signature [i.28] and XML Encryption [i.26] can be applied to any content type, with the result represented in an XML object. These mechanisms are used by several security token systems (e.g., Security Assertion Markup Language (SAML) [i.12), and the Common Alerting Protocol (CAP) emergency alerting format [i.10]. XML security discussed in clause 8.1.1.4.

- The IETF JSON Object Signing and Encryption (JOSE) working group [i.5] has been chartered to develop a secure object format based on JSON with roughly equivalent features to the XML security specifications in the preceding bullet. JSON Security is discussed in clause 8.1.1.5.

In addition to a high level description of the protocols, the following issues are considered:

oneM2M Protocol Binding support for natively identifying the object-based security protocol media type. Internet media types [i.13] are identified by a string, such as "application/xml", registered in the IANA Media Types registry [i.3]. All the above object-based security protocols use one of the registered media types. Note that the media types currently supported by oneM2M systems are defined in clause 6.7 of TS-0004 [i.2].

- HTTP [i.20]: HTTP natively supports identification of all registered media string-based identifiers, including the media type for the above object-based security protocols.

- CoAP [i.21]: CoAP In order to minimize the overhead of using the string-based media type identifiers, CoAP natively recognizes only the small set of Internet media types recorded in the "CoAP Content-Formats" sub-registry of the IANA "CoRE Parameters" registry (see [i.2]). Recognition of the object-based security protocol media type in CoAP is examined on a case by case basis.

- MQTT [i.11]: MQTT leaves identification of the media type to the application layer. For all choices of object-based security protocol, oneM2M would be required to specify how the object-based security protocol media type is identified when MQTT is used.

Formatting and Parsing Complexity: some of the above object-based security protocols include complex rules for formatting and parsing of messages. This is worth consideration, because application developers that lack the tools or motivation to handle complex rules are likely to avoid developing applications using such security protocols. Execution environments could provide function calls that apply complex formatting and/or parsing on behalf of AEs– thus reducing the burden on the application developers.  However, it is unclear if the scope of oneM2M includes defining function calls. Consequently, it is unclear if the formatting and parsing complexity is a factor in making decisions. This review (clause 8.1.1) only reports on the formatting and parsing complexity; the review avoids drawing any recommendations based on the complexity.

Canonicalization: Consider a scenario where a signed object of some media type (e.g. XML) is parsed at an intermediary server, with the information later reconstructed same media type before being forwarded to another entity. For many media types, there are multiple legitimate equivalent serializations (representations) of the original signed object, so the second serialization of the object may differ slightly from the original serialization in the object. If the serializations differ, then a signature on the original serialization of the object would no longer apply for the second serialization– even though the serializations are logically equivalent. Consequently, an entity who receives the second serialization of the object cannot use the original signature to verify the origin of the object.

For example, in XML the nature of the whitespace may not convey any meaning – so the intermediary server may reconstruct XML with different whitespace to the original serialization. Similarly, the order of attributes in XML does not convey any meaning, so the intermediary server may reconstruct XML with attributes in a different order to the original serialization. In both cases, a signature on the original serialization of the object would no longer apply for the second serialization– even though the serializations are logically equivalent.

To address this issue, some media types define a canonical form that is uniquely and unambiguously representable in the environment where the signature is created and the environment where the signature will be verified. The process of producing the canonical form from a particular serialization is called canonicalization.

Canonicalization has the advantage that signatures can always be verified, even if the object gets parsed and reconstructed by an intermediary. This benefit does not come for free, since canonicalization can add to the complexity of formatting and parsing. Furthermore, if the original serialization of the object is always sent with the digital signature, then the complexity of canonicalization provides no technical benefit. Consequently, canonicalization can be an advantage in some scenarios and disadvantage in others.

In summary: canonicalization is required in scenarios where the object is parsed and reconstructed at an intermediate server. However, if objects are not parsed and reconstructed then canonicalization simply adds an un-necessary and complex step. This review (clause 8.1.1) only reports whether the object-based security technologies provide canonicalization; the review does not investigate which scenarios warrant canonicalization, and avoids drawing any recommendations based on the support for canonicalization.

#### 8.1.1.2	Secure/Multipurpose Internet Mail Extensions (S/MIME)

##### 8.1.1.2.1	High Level Description of S/MIME

NOTE: This description borrows heavily from the S/MIME specification [i.17].

S/MIME [i.17] (Secure/Multipurpose Internet Mail Extensions) provides a consistent way to send and receive secure MIME data.  S/MIME provides authentication, message integrity and non-repudiation of origin (using digital signatures), and data confidentiality (using encryption).  As a supplementary service, S/MIME provides for message compression.

S/MIME is not restricted to mail; it can be used with any transport mechanism that transports MIME data, such as HTTP or SIP. As such, S/MIME takes advantage of the object-based features of MIME and allows secure messages to be exchanged in mixed-transport systems.

S/MIME defines the creation and processing of a MIME body part that has been cryptographically enhanced according to the Cryptographic Message Syntax (CMS) [i.18]. CMS is used to digitally sign, digest, authenticate, or encrypt arbitrary message content. The CMS values are generated using ASN.1 [i.23], using BER-encoding (Basic Encoding Rules) [i.24].

##### 8.1.1.2.2	Considerations regarding of S/MIME

###### 8.1.1.2.2.1	CoAP identification of S/MIME media types

S/MIME [i.17] registers the internet media type identifiers “application/pkcs7-mime” and “application/pkcs7-signature” in the IANA Media Types registry [i.3].

At the time of writing, the S/MIME media types are not in the “CoAP Content-Formats” registry [i.2], so CoAP cannot natively identify the S/MIME media types. If oneM2M decides to use S/MIME, then oneM2M will need to specify how the CoAP binding indicates that S/MIME has been used.

###### 8.1.1.2.2.2	Formatting, Parsing and Canonicalization Complexity for S/MIME

Recall that S/MIME uses CMS which in turn uses ASN.1 [i.23], with BER-encoding (Basic Encoding Rules) [i.24].

[i.19] states the following opinion regarding the use of ASN.1

“In recent years, usage of ASN.1 has decreased (along with other binary encodings for general objects), while more applications have come to rely on text-based formats such as the Extensible Markup Language (XML) [W3C.REC-xml] or the JavaScript Object Notation (JSON) [RFC7159].

“Many current applications thus have much more robust support for processing objects in these text-based formats than ASN.1 objects; indeed, many lack the ability to process ASN.1 objects at all.”

S/MIME provides simple guidance for canonicalization of text. Otherwise, S/MIME does not impose any canonicalization rules, but requires that the original MIME entity is already canonicalized according to the media type and subtype of the original MIME entity. The complexity of this canonicalization then depends on the media type of the original MIME entity.

For example, if S/MIME is used to secure XML, then XML canonicalization must be applied (see clause 8.1.1.4.2.3). XML Security also requires canonicalization, so the overhead of canonicalization is the same where S/MIME or XML security is applied.

#### 8.1.1.3	OpenPGP

##### 8.1.1.3.1	High Level Description of OpenPGP

The OpenPGP message format specification [i.16] uses a combination of strong public-key and symmetric cryptography to provide security services for electronic communications and data storage. These services include confidentiality, key management, authentication, and digital signatures.

OpenPGP supports both hierarchical PKIs (as used with S/MIME) and a decentralized PKI known as a “Web-of-Trust”. The web-of-trust model is mostly useful for authenticating people, but has not gained significant momentum.

##### 8.1.1.3.2	Considerations for OpenPGP

###### 8.1.1.3.2.1	CoAP identification of the OpenPGP media type

MIME Security with OpenPGP [i.14] defines three content types in the IANA Media Types registry [i.3] for implementing security and privacy with OpenPGP: "application/pgp-encrypted", "application/pgp-signature" and "application/pgp-keys".

At the time of writing, the OpenPGP media types are not in the “CoAP Content-Formats” registry [i.2], so CoAP cannot natively identify the OpenPGP media types. If oneM2M decides to use OpenPGP, then oneM2M will need to specify how the CoAP binding indicates that OpenPGP has been used.

###### 8.1.1.3.2.2	Formatting, Parsing and Canonicalization Complexity for OpenPGP

OpenPGP messages are ASCII radix-64 representations of binary data. The data elements have (type, length, value) format with registered types recorded at IANA Pretty Good Privacy (PGP) registry [i.4].

The opinion about binary encodings in clause 8.1.1.2.2.1 “Formatting and Parsing Complexity for S/MIME” would also be relevant to OpenPGP formatting and parsing.

OpenPGP provides simple guidance for canonicalization of text, and all other data is treated as binary data.

#### 8.1.1.4	XML Security

##### 8.1.1.4.1	High Level Description of XML Security

XML security specifications are generated by the W3C’s XML Security Working Group [i.27] in the form of “W3C recommendations”. The latest recommendations, published in in 2013, are described below - (the descriptions borrow heavily from the respective documents).

- XML Encryption Syntax and Processing Version 1.1 [i.26] specifies how to encrypt data and represent the result in XML. The result of encrypting data is an XML Encryption EncryptedData element that contains (via one of its children's content) or identifies (via a URI reference) the cipher data. The data may be in a variety of formats, including octet streams and other unstructured data, or structured data formats such as XML documents, an XML element, or XML element content.

- XML Signature Syntax and Processing Version 1.1 [i.28] provides integrity, message authentication, and/or signer authentication services for data of any type, whether located within the XML that includes the signature or elsewhere. An XML Signature may be applied to the content of one or more resources. Enveloped or enveloping signatures are over data within the same XML document as the signature; detached signatures are over data external to the signature element.

- XML Signature Properties [i.29] defines a namespace and three properties to be used in XML Signatures: a Profile Property (a URI) identifying how in the signature is to be used (e.g. constraining the choice of algorithms); a Role Property (a URI) specifying an application specific role for the signature; and an Identifier Property enabling use cases where a unique identifier needs to be associated with the signature.

NOTE: There are a variety of additional technical reports on “XML Security 2.0”, but these have status of “WG Notes”, and are not endorsed as “W3C Recommendations”.

XML Encryption and XML Signatures can be applied to provide desired combinations of confidentiality, integrity, message authentication, and/or signer authentication.

##### 8.1.1.4.2	Considerations for XML Security

###### 8.1.1.4.2.1	CoAP identification of the XML Security media type

The output of XML encryption and XML signatures are represented in XML. XML parsers processing the XML will be able to identify the XML encryption elements and XML signature elements. Consequently, an oneM2M Protocol binding can support transporting XML encryption and XML signatures provided the protocol can identify the XML media type.

XML uses the media type “application/xml” in the IANA Media Types registry [i.3].

CoAP identities the XML media type using the CoAP Content-Format ID “41” (see [i.2]).

###### 8.1.1.4.2.2	Formatting, Parsing and Canonicalization Complexity for XML Security

XML formatting and parsing is relatively easy and well supported. However, the need for XML canonicalization [i.25] in XML Encryption and XML Signatures introduces significant complexity.

The JOSE use cases document [i.19] expresses this opinion on formatting and parsing complexity for XML Security:

In practice, however, XML-based secure object formats introduce similar levels of complexity to ASN.1 (e.g., due to the need for XML canonicalization), so developers that lack the tools or motivation to handle ASN.1 aren’t likely to use XML security either.”

This quote should be interpreted as an opinion, rather than technical fact, but it worthy of consideration.

###### 8.1.1.4.2.3	Canonicalization and XML Security

Canonical XML is specified in recommendation [i.25]. XML encryption and XML Signature convert all XML to the Canonical XML prior to applying cryptographic processes. See clause 8.1.1.4.2.2 for discussion on the impact of canonicalization on formatting and parsing complexity for XML security.

#### 8.1.1.5	JSON Security

##### 8.1.1.5.1	High Level Description of JSON Security

The IETF JSON Object Signing and Encryption (JOSE) working group [JOSE] has been chartered to develop a secure object format based on JSON. The JOSE working group has published the following documents:

- JOSE use cases and requirements. [i.19]. The use cases include security tokens, OAuth, OpenID Connect, XMPP, emergency alerting, constrained devices (including object security for CoAP).

- JSON Web Algorithms (JWA) [i.6] registers cryptographic algorithms and identifiers to be used with JOSE specifications.

- [i.8] JSON Web Key (JWK) defines JSON-based data structures that represent a cryptographic key (JWK) and a set of JWKs (JWK set).”

- [i.7] JSON Web Encryption (JWE) represents encrypted content using JSON based data structures. The JWE cryptographic mechanisms encrypt and provide integrity protection for an arbitrary sequence of octets.

- [i.9] JSON Web Signature (JWS) represents content secured with digital signatures or Message Authentication Codes (MACs) using JSON-based data structures. The JWS cryptographic mechanisms provide integrity protection for an arbitrary sequence of octets.”

The JOSE cookbook [i.5] provides a representative set of examples of protecting content using JOSE.

The secured objects produced using JOSE specifications can use either a JSON serialization or a compact, URL-safe text serialization (intended for space constrained environments such as HTTP Authorization headers and URI query parameters).

##### 8.1.1.5.2	Considerations for JSON Security

###### 8.1.1.5.2.1	CoAP identification of the JSON Security media type

The output of JWK, JWE and JWS can use a JSON serialization. JSON parsers processing the JSON will be able to identify the JWK, JWE and JWS elements. Consequently, an oneM2M Protocol binding can identify JWK, JWE and JWS provided the protocol can identify the JSON media type.

JSON uses the media type “application/json” in the IANA Media Types registry [i.3].

CoAP identities the JSON media type using the CoAP Content-Format ID “50” (see [i.2]).

###### 8.1.1.5.2.2	Formatting, Parsing and Canonicalization Complexity for JSON Security

The formatting and parsing complexity of XML is comparable to the formatting and parsing complexity of JSON; formatting and parsing is relatively easy and well supported. JWK, JWE and JWS do not use canonicalization, which makes the formatting and parsing of JWK, JWE and JWS less complex than formatting and parsing for XML Security (which requires canonicalization).

## 8.2   Group Authentication

### 8.2.1  Group Authentication Solution 1

Figure 8.2.2-1 illustrates the sequence of events when using the group authentication solution 1 for the static group which corresponding to Clause 6.1.1. In this description, "Entity Ax" or "Entity Ay" corresponds to either a CSE or AE in a group, "Entity B" corresponds to MN-CSE, and "Entity C" corresponds to IN-CSE.

Credential Configuration: The Provisioned Credential for M2M Security Association Establishment (Kpsaxm, Kpsaym, Kpsami, Kpsaxi, and Kpsayi) and the corresponding Provisioned Credential for M2M Security Association Establishment Identifier, denoted KpsaxmId, KpsaymId, KpsamiId, KpsaxiId, and KpsayiId are provisioned to both entities either with pre-provisioning or remote provisioning.

NOTE 1: The provisioning (by definition) uses mechanisms not specified by oneM2M. The remote provisioning is performed thanks to Security Bootstrap Frameworks described in clause 8.3 in TS0003 [5].

NOTE 2: Entity Ax, Entity Ay, Entity B, and Entity C shall be configured with the information needed for the authentication and identification during the Inner/Outer Group Authentication and Group Security Association Handshake. For instance, Entity Ax is configured with Entity B identity (IdB) associated with the Provisioned Credential for M2M Security Association Establishment identifier KpsaxmId to establish security context by using Kpsaxm. Entity Ax is to use this identity IdB for Entity B authenticating using the related arguments. This identity is also used to route the (D)TLS exchange.

Inner Group Authentication:

- Each Entity Ax (or Ay) in a group and the Entity B perform a (D)TLS-PSK handshake [8] to establish a secure session:

Take Entity Ax as example:

  - The "psk_identity" parameter [8] is set to the value of the Provisioned Credential for M2M Security Association Establishment identifier KpsaxmId between the Entity Ax and the Entity B.

  - The "psk" parameter [8] is set to the value of the Provisioned Credential for M2M Security Association Establishment Kpsaxm between the Entity Ax and the Entity B.

- The Entity Ax and the Entity B authenticate each other by verifying Message Integrity Codes (MIC) which was generated using the symmetric key (Kpsaxm) to make mutual authentication.

NOTE 3: Each Entity in a group shall perform inner group authentication with the Entity B.

NOTE 4: This is just an example to use (D)TLS-PSK here, it is not limited to (D)TLS-PSK only.

Outer Group Authentication: Due to the successful Inner Group Authentication, Entity B could be on behalf of all entities in the group to make mutual authentication with the Entity C.

- The Entity B and Entity C perform a (D)TLS-PSK handshake [8] to establish a secure session:

  - The "psk_identity" parameter [8] is set to the value of the Provisioned Credential for M2M Security Association Establishment identifier KpsamiId between the Entity B and the Entity C.

  - The "psk" parameter [8] is set to the value of the Provisioned Credential for M2M Security Association Establishment Kpsami between the Entity B and the Entity C.

- The Entity B and Entity C authenticate each other by verifying Message Integrity Codes (MIC) which was generated using the symmetric key (Kpsami) to make mutual authentication. After that, each Entity in the group has carried out the authentication with the help of the Entity B.

- The Entity C generates the M2M Group Secure Connection Key for each Entity in the group. Especially, in the IN’s database, there is a mapping between the identifier of MN (e.g. IdB) and each Entity’s identifier (e.g. IdAx) in the group. For instance, Entity C generates Ksx for Entity Ax from the Provisioned Credential (Kpsaxi) between the Ax and C, a random number (Rand) and the identifier of Ax (IdAx). Moreover, Entity C sets the Group Secure Connection Key Identifier (KsxId) equal to KpsaxiId, and stores the M2M Group Secure Connection Key (Ksx) and the related Identifier (KsxId).

NOTE 5: The derivation of the M2M Group Secure Connection Key, e.g. Ksx := HMAC-SHA-256(Kpsaxi, “oneM2M Group Secure Connection Key derivation” ||  Enrolee-Ax-ID || Rand), where Kpsaxi is the value of the Provisioned Credential between the Enrolee Ax and the IN; Rand is a random number generated by the Entity C; Enrolee Ax’s CSE-ID or AE-ID (Enrolee-Ai-ID), which shall be encoded to an octet string according to UTF-8 encoding rules as specified in IETF RFC 3629 [11] and apply Normalization Form KC (NFKC) as specified in [9]; HMAC-SHA-256 is defined in RFC 2014 [10].

Group Security Association Handshake: The Group Security Association Handshake enables the establishment of the M2M Group Secure Connection Key (e.g. Ksx) and the associated Key Identifier (e.g. KsxId) shared between each Entity Ax (or Ay) in the group and the Entity C.

Take Entity Ax as example:

- Entity C sends the random number (Rand) to Entity B.

- Entity B forwards the Rand to the Entity Ax.

- Entity Ax generates the M2M Group Secure Connection Key (Ksx) from the Provisioned Credential (Kpsaxi) between the Entity Ax and the Entity C, the random number (Rand) and the identifier of Ai (IdA), sets the Group Secure Connection Key Identifier (KsxId) is KpsaxiId, and stores the M2M Group Secure Connection Key (Ksx) and the related Identifier (KsxId). After that, Entity Ax sends the Service Request Message to Entity B.

- Entity B forwards the Service Request Message to Entity C.

NOTE 6: The Service Request Message is sent by the entity in a given group when the entity requires the IN to provide the services.

- Upon the Service Request Message, Entity B forwards this message to IN.

NOTE 7: After each Entity in a group (e.g. Ax) sets up security association with IN using the same key (e.g. Ksx), each Entity could be seen as authenticated when the security association works, since the mutual authentication between each Entity (e.g. Ax) and the IN is fulfilled through the proof of possessing the M2M Group Secure Connection Key (e.g. Ksx).

Figure: 8.2.2-1: The sequence of events When using Group Authentication Solution 1

## 8.3	A Solution for providing security of data “at-rest”

### 8.3.1	General procedure for hosting and accessing secure data

The generic procedure for hosting and accessing securedata is illustrated in figure 8.3.2-1 and described as follows:

Figure 8.3.2-1: Hosting and accessing secure data

Editor’s note: The above flow has to be further investigated.

- The Originator of data (AE) would like to provide protection (integrity /authenticity and / or confidentiality) to the data that it generates and hosts onto a Hosting CSE.

  - Data is generated by an originator

  - It also generates appropriate credential(s) for protecting the data. Alternatively, the Originator may not generate the credential(s) but instead request credential(s) from a Credential Registry.

  - The originator then either encrypts, integrity protects or performs both to the data using the credential(s) that it generated

  - The data originator may optionally provide access control rule(s) associated with the credential(s)

- The Originator establishes a secure communications channel with an M2M Trust Enabler Function (TEF)

- The Originator then requests to register the credential(s) that it generated with the TEF along with optional access control rule(s), that are used to govern an entity’s access to the credentials

- The TEF registers the credential(s)

  - The TEF generates or creates unique Credential-Id(s)

  - The TEF associates the Credential-Id(s) with respective credential(s) and stores them securely

  - The TEF sets an expiration to the credential registration

  - The TEF also associates access control rules to the credential(s) that were either provided by the originator or created by the TEF.

- The TEF sends a response containing the associated Credential-Id(s) to the Originator

- The Originator then associates the Credential-Id(s) with the respective protected data

- The Originator establishes a secure communications channel with a Hosting CSE (HCSE)

- The Originator sends a request to register and host the protected data along with the associated Credential-Id(s) with the HCSE.

- The HCSE checks to ensure that the Originator is authorized to perform registration of protected data. If the Originator is deemed to be authorized then the HCSE registers and hosts the data along with the associated Credential-Id(s)

- The HCSE sends a response indicating “Success”

- A Client application (AE) that would like to access the secure data produced by an Orignator AE, performs a security association establishment process with the HCSE

- The Client AE would like to retrieve the protected data that was created by the Originator AE and therefore sends a request to the HCSE

- The HCSE checks to see if the Client AE is authorized to perform retrieval of the protected data

- If the Client AE has been authorized then the HCSE sends the protected data along with the Credential-Id(s) associated with the protected data to the Client AE.

- The Client AE establishes a secure communications channel with the TEF

- The Client AE requests to retrieve the credential(s) by sending the respective Credential-Id(s) to the TEF

- The TEF checks to see if the Client AE has been authorized to retrieve the credential(s) identified by the respective Credential-Id(s)

- If the Client AE has been authorized then the TEF responds with the corresponding credential(a) using the secure channel

- The Client AE uses the credential(s) in order to verify the integrity / authenticity and / or decrypt the data if it has been encrypted using appropriate credential(s)

It should be noted that the TEF function may be implemented as part of the CSE or as part of a centralized entity (e.g. MEFy)

### 8.3.2	Bootstrapped procedure for providing data security

#### 8.3.2.1	Overall Description

This section provides detailed description on mechanisms that can be employed for providing security of data both “at-rest” and “in-transit” in an end-to-end manner. If an entity (e.g. AE) has a trust relationship with an M2M Trust Enabling Function (TEF), then that trust can be leveraged in order to generate credentials for integrity / authenticity and or confidentiality of data. Here, the term “data” is used in a generic manner may represent an oneM2M resource, which may be a system resource (e.g. <mgmtObj>) resource or application generated data or instances of application generated data (e.g. <contentInstance>).

#### 8.3.2.2	Detailed Description

Figure 8.3.2.2-1 illustrates a message between entities involved in data generation, data hosting, and generating credentials for data security as well consumer of protected data. The functional roles associated with each entity is further described below:

##### Originator (AE1):

- Has a trust relationship with a M2M Trust Enabler Function (TEF) and associated credentials

- Ability to generate data security-specific credentials based on a bootstrapping procedure with the TEF

- Ability to request registration of Credential-Id with a TEF and associated ACPs

- Generates protected (integrity and or encrypted) data or data instances (contentInstances) using the data-security-specific credentials

- Has a trust relationship with a Hosting (HCSE) and establish a secure communications channel with the HCSE

- Ability to request hosting of protected data onto a HCSE

##### Hosting CSE (HCSE):

- Has a trust relationship with an Originator AE1 and also a separate trust relationship with Client application AE2 and associated credentials

- Ability to process request by Originator AE1 for hosting of protected data and the ability to host protect data and data instances.

- Ability to process a Retrieve request by a Client application AE2 for protected data or data instances

##### Trust Enabler Function (TEF):

- Has a trust relationship with an Originator AE1 and also a separate trust relationship with Client application AE2 and associated credentials

- Ability to process request by Originator AE1 for performing a bootstrapping process and generate data-security-specific credentials.

- Ability to perform Credential-Id registration request from Originator AE1

- Ability to process a Retrieve request by a Client application AE2 for data-security-specific credential(s)

##### Client (AE2):

- Has a trust relationship with a M2M Trust Enabler Function (TEF) and associated credentials

- Has a trust relationship with a HCSE and associated credentials in order to establish a secure connection with it.

- Ability to request a “Retrieve” operation on protected data hosted on a HCSE

- Ability to request “Retrieve” operation for credentials identified by a Credential-Id with a TEF

- Ability to verify authenticity / integrity of data or data instances and or the ability to decrypt the data or data instances obtained from HCSE using the credentials that were retrieved from TEF.

The detailed messaging steps are provided below:

- The bootstrapping process described within TS-0003 (Release 1) specifications is further enhanced by using the bootstrapping process in order to derive “data security”-specific credentials. The shared credential KpmId / Kpm between an AE and a MEF or a TEF is used to generate session credentials KeId / Ke, as described in TS-0003 (Release 1). The credential Ke is then used to generate data security-specific credentials between the AE and the TEF. Similar mechanisms may be used if the bootstrapping process is used between an AE and CSE leveraging existing security association between AE and CSE. The security association identified by KpsaId / Kpsa as described in oneM2M TS-0003. The Kpsa is then used instead of Ke. Similarly, KmId / Km that is used for establishing security association between an AE and MAF may be used to generate data security credentials between AE and MAF. It must be noted that a more preferable approach is for the AE and TEF to generate the data security credentials.

- A Salt that is a random value that is used as part of the key generation mechanism may have been shared during the bootstrapping process or may computed as a hash value of the initial communications between the AE and the TEF during the bootstrapping process. The Salt may be a cryptographic representation of the channel that is bound between AE1 and the TEF. The channel may be a secure connection established using TLS or DTLS. As part of the “Data Security Credential Generation” process, the AE1 (Enrolee) and the TEF (Enrollment Target) generates data security credentials using the Ke, (Ke_AE1-TEF refers the Ke that is associated between AE1 and TEF) as the master key in order to generate the data security master key, K_AE1_TEF_data_sec_master. Alternatively, if the target is a MAF, then the Km would be used as the master key for the generating the data security master key. An Example of data security Key Generation using RFC 5869 [i.9], where the Enrollee is AE and the Enrollment Target  is TEF, is provided below:

K_AE1_TEF_data_sec_master = HMAC-Hash (Salt, Ke_AE1_TEF)

T(0) = empty string (zero length)

Once the K_AE1_TEF_data_sec_master has been generated it is then used for Key Expansion in order to generate unique data authenticity and data confidentiality keys. In some cases, only a single key is generated if the data authenticity as well confidentiality is provided by an algorithm such as the AEAD (e.g. AES-CCM or AES-GCM)

K_AE1_TEF_data_auth = T(1) = HMAC-Hash (K_AE1_TEF_data_sec_master, T(0) | “Data Authenticity and Integrity”| 0x01)

The K_AE1_TEF_data_auth key is used for providing data authenticity and data integrity and is referred to as data authenticity or data integrity key.

K_AE1_TEF_data_conf = T(2) = HMAC-Hash (K_AE1_TEF_data_sec_master, T(1)| “Data  Confidentiality Key”|0x02)

The K_AE1_TEF_data_conf key is used for providing data confidentiality and is referred to as the data confidentiality key.

In certain cases, the Kpsa_AE1_CSE1 (which is the Kpsa between AE1 and CSE1) is used instead of Ke_AE1_TEF, and the process described above is used to generate unique keys for data security protection, namely, data authentication / integrity and data confidentiality. Kpsa is used if a CSE is used by the AE as the data security credential registry in place of a TEF.

In certain other cases, only a single session key, K_AE1_TEF_data_auth_conf that is generated from Ke or Kpsa or Kpm is used for providing both data authenticity as well as data confidentiality, when used with AEAD class of algorithms.

- The TEF performs a similar process of key generation. The negotiation of the algorithm, key generation mechanisms, types and number of keys to be generated etc.. are assumed to have been performed during step 0, when the bootstrapping process was carried out between AE1 and TEF.

- AE1 generates content / data, where each instance of the content / data may be protected by unique set of data  authenticity and data confidentiality keys or all instances of the content is protected by a single data authenticity key and by a single data confidentiality key. An example key generation where only a single data authenticity and a data confidentiality key for a container that may contain multiple content instances is generated is shown below:

K_AE1_Container-x_data_auth = HMAC-Hash (K_AE1_TEF_data_auth, “Data Authenticity and Integrity”| “Container-x”| Nonce or creationTime) and

K_AE1_Container-x_data_conf = HMAC-Hash (K_AE1_TEF_data_conf, “Data Confidentiality”| “Container-x”| Nonce or creationTime)

Alternatively for each instances of content within a container, a unique set of keys may be generated:

K_AE1_ContentInstance-x_data_auth = HMAC-Hash (K_AE1_TEF_data_auth, “Data Authenticity and Integrity”| “Container-x”| Nonce or creationTime) and

K_AE1_ContentInstance-x_data_conf = HMAC-Hash (K_AE1_TEF_data_conf, “Data Confidentiality”| “ContentInstance”| Nonce or creationTime)

The content is encrypted and or integrity protected using the above generated keys. For encrypting the content a random IV may be generated by AE1 and uses it along with the encryption algorithm and the content (data) in order to generate the encrypted content (R1-EC, the encrypted resource).

If content instance are being encrypted separately, then each content instance has a unique confidentiality key and a new IV is generated each time an encryption process is carried out generating an encrypted content instance; therefore each content instance has an associated separate encrypted content instance.

For integrity protecting or adding authenticity to content / data, a random Nonce along with Time component is used in order to generate an Authentication Tag (AT) of the content.

If each content instance is being protected separately then each content instance has an associated AT. In the case of providing data authenticity in certain cases, it may be preferable to use a single key for generating each individual ATs.

The encrypted content may be represented as the modified oneM2M container or <contentInstance> resource as depicted in Figure 8.3.3.2-2. Alternatively, The encrypted content R1-EC that is created may be based upon the JSON Web Encryption (JWE) specified in [i.6], while the R1-AT that is created may be based upon the JSON Web Signature specified in [i.8]. The appropriate algorithms may be represented in the form as specified in the JSON Web Algorithms (JWA) standards [i.5].

As a general case, each key that is generated and used is associated with a unique Credential-Id. The Credential-Id may be generated by the AE1 or provided by the TEF to AE1. In certain cases, the Credential-Id may carry characteristics of the content id or content instance id and the type of credential. An example of a Credential-id may be of the form:

K_AE1_Container-x_data_conf-Id@TEF.com, which is associated with the key, K_AE1_Container-x_data_conf

- AE1 registers the Credential-Id with the TEF. The AE1 Requests to create a Credential resource identified by a Credential-Id and associated Access Control Policies (ACP). The Credential-Id may alternatively be generated and provided by the TEF in order to avoid collision of Credential-Ids that are associated with the TEF. Collisions of Credential-Ids may be avoided if a hash is carried out of the generated id by AE1:

H1 = Hash (K_AE1_Container-x_data_conf-Id)

Credential-Id = H1@TEF.com

- The TEF checks to ensure that AE1 has been authorized to register the credentials with the TEF also verifies the Credential-Id as well as optional Cryptographic Parameters (CryptoParams) that may have been included. The TEF then creates a <credential> resource type and populates it with the necessary attributes, such as, the <accessControlPolicy> values.

- The TEF sends a Response that indicates successful creation of the Credential (<credential>) resource to AE1.

- AE1 and HCSE establishes a secure connection as per TS-0003 security solutions using (D)TLS.

- AE1 Requests to create a secure resource R1, that is encrypted (encrypted resource denoted as: R1-EC) and integrity protected using R1-AT. AE1 also provides the necessary CryptoParams, Credential-Id. The CryptoParams details the type of algorithm to be used, the length of the keys, mechanisms on how the protection is to be carried out etc. The Credential-Id may be part of the CryptoParams or may be sent as separate child resource associated with R1. AE1 also includes the associated ACPs. The ACP may be integrity protected.

- HCSE verifies the request and checks to ensure that AE1 has been authorized to create a resource at HCSE

- HCSE responds with a success message.

- At some point a client (AE2) would like to retrieve R1. The AE2 and HCSE performs a mutual authentication and sets up a secure connection using (D)TLS.

- AE2 sends a Request to “Retrieve” the resource R1, to HCSE. Mechanisms involved in discovering R1 is outside the scope and it is assumed that the AE2 is able to discover the location of a secure version of R1.

- HCSE verifies the authorization of whether AE2 is allowed to perform a retrieve operation using the information within the ACP that was created by AE1.

- The HCSE sends a Response containing the R1-EC, EC-AT as well as R1-CryptoParams. The R1-EC may be represented using e.g. JSON-based notation, JWE, while the EC-AT may be represented using JWS and the R1-CryptoParams may be represented using JWA. Alternatively, both the EC-AT and R1-EC may be represented as JWE especially if the algorithm used for encryption and integrity protection is based on AEAD algorithm (e.g. AES-GCM, AES-CCM). Alternatively, the encrypted content, R1-EC as well the R1-AT may be represented as an oneM2M resource along with the appropriate CryptoParams.

- If the Credential-Id was included as part of the CryptoParams, AE2 extracts the Credential-Id from it.

- The AE2 and TEF performs mutual authentication and sets up a secure connection using (D)TLS.

- AE2 sends a Request message to the TEF in order to perform a retrieve operation by including the Credential-Id as the resource-id within the message. The Credential-Id may be sent using e.g. JSON-based notation such as JWK or using the oneM2M resource structure. The AE2 may also extract a Salt or Nonce from the CryptoParams that is associated with the resource R1 (data). AE2 may also send the Salt or Nonce along with the Credential-Id in order to retrieve resource-specific credentials.

- TEF verifies authorization of AE2 based on the ACP that was created by the AE1 during the credential registration process in 2.

- If AE2 is authorized to retrieve, then the TEF computes the resource-specific credentials sends the credentials over a secure channel to the AE2. In addition the TEF may also send usage info, on how the credentials may be used and the associated algorithms that are to be used. The AE2 may already have possession of the usage info that it obtained from the HCSE as part of the CryptoParams. However, in certain cases where a container may contain a number of contentInstance resources and each with its own encrypted contentInstance and authentication tags and associated credentials then the TEF may be able to provide additional guidance on how the credentials may be used in order to verify contentInstance integrity as well how it may be used to decrypt the contentInstances. If the Salt is sent by then the TEF may generate the:

K_AE1_TEF_data_sec_master, which is then provisioned to the AE2. The AE2 uses the K_AE1_TEF_data_sec_master in order to generate container-specific or contentInstance-specific credentials. The mechanisms to generate K_AE1_TEF_data_auth and K_AE1_TEF_data_conf and associated container or contentInstance-specific credentials may follow similar to the mechanisms detailed earlier.

Alternatively, the TEF may provision either K_AE1_TEF_data_auth and / or K_AE1_TEF_data_conf to the AE2, which then generates the container-specific or contentInstance-specific credentials. In other cases, the TEF may only provision just the container-specific or contentInstance-specific credential(s) to the AE2. The AE2 does not perform any key generation since it is provisioned with the keys and thereby limiting the AE2 from having cryptographic access to specific container or contentInstance(s). It should be noted that for each of the keys the associated Nonce(s) and or creation time associated with the container or content instances may have to be provided to the TEF. In certain cases, when the AE1 performs registration of the credential process in step 4, the AE1 may include the CryptoParams associated with the Credential-Id with the TEF.

From a performance and security perspective, the more preferred approach may be for the TEF to only provision the K_AE1_TEF_data_auth and / or K_AE1_TEF_data_conf to the AE2. It should be noted that all the credentials have an associated life-time associated with it. After the expiration of lifetime, new credentials may have to be generated.

- Using the credentials AE2 verifies the integrity using R1-AT and decrypts R1 using the provisioned or generated container or contentInstance credentials.

Figure 8.3.2.2-1: Message flow depicting hosting and retrieval of protected content

An example of a protected <contentInstance> is depicted in Figure 8.3.2.2-2. The contentInstance has an encryptedContent as a child resource and associated cryptoParams, the cryptographic parameters that are to be used in order to be able to decrypt the contentInstance. In addition, an authenticationTag or digitalSignature resource and associated cryptoParams, the parameters that are to be used in order to be able to verify the authentication tag or digital signature are added to the existing contentInstance resource.

Figure 8.3.2.2-2: Resource structure of a protected <contentInstance>

## 8.4	A Solution for providing End-to-End Message Authentication using Symmetric Key

### 8.4.1	End-to-End Security Credential(s) Generation Process

#### 8.4.1.1	Overall Description

This section provides description on mechanisms that can be employed for generation of credential(s) that are to be used for end-to-end security. Based on security requirements associated with an Entity (e.g. AE), appropriate end-to-end security credentials may be generated.

#### 8.4.1.2	Detailed Description

Table 8.4.1.2-1 illustrates the end-to-end security requirements that have been determined and provided by the entity (e.g. AE1) or determined based on a security profile associated with AE1. The table illustrates that AE1 provides or requires the following:

- End-to-End message authentication using a Message Integrity Code (MIC)

- Also provides for or requires the ability to verify the integrity of data in-transit

- End-to-End message confidentiality in transit and thereby also provides for end-to-end data confidentiality in-transit.

| Security Requirement | End-to-End |
| --- | --- |
| Message Originator Authenticity / Integrity | Message Integrity Code (MIC): 256 bits |
| Message Re-play protection | Nonce / Random / Time Component |
| Non-repudiation capability | None |
| Message Confidentiality | Encryption: 256 bit encryption |
| Confidentiality of Data in Transit | Encryption: 256 bit encryption |
| Confidentiality of Data at Rest | None |
| Integrity of Data in Transit | Message Integrity Code (MIC): 256 bits |
| Integrity of Data at Rest | None |

Table 8.4.1.2-1 End-to-End Security Requirements

Based on the higher-level requirements appropriate end-to-end credentials may be generated using either bootstrapping process (preferable approach) or by using pre-provisioned end-to-end credentials. Illustrated in Figure 8.4.1.2-1 is a high-level key generation process.

As part of the “Generation of End-to-End Key Generation” Phase, the enrolee and the enrolment target generates End-to-End credentials using the Kpsa as the master key in order to generate the End-to-End master key. If the enrolee is an AE, and the Enrolment Target is a CSE, then an end-to-end master credential, Ke2e_AE_CSE_master is generated. An Example of End-to-End Key Generation using RFC 5869 is provided below:

Ke2e_AE_CSE_master = HMAC-Hash (Salt, Kpsa_AE_CSE)

Using the generated end-to-end master key, the associated end-to-end message authentication and or end-to-end message confidentiality keys are generated in the following manner:

T(0) = empty string (zero length)

Ke2e_AE_CSE_msg_auth = T(1) = HMAC-Hash (Ke2e_AE_CSE_master, T(0) | “E2E Message Authentication Key”| 0x01)

Ke2e_AE_CSE_msg_conf = T(2) = HMAC-Hash (Ke2e_AE_CSE_master, T(1)| “E2E Message Confidentiality Key”|0x02)

This process is repeated by each Enrolee and associated Enrolment Target based on a unique Enrollee-EnrolmentTarget_Ke2e_master that is shared between the Enrolee and the Enrolment Target (e.g. AE and CSE specific end-to-end keys).

Figure: 8.4.1.2-1: End-to-End Key Generation Phase

An example list of generated keys illustrated in Table 8.4.1.2-2:

| Security | Symmetric Keys Generated and Used | Parameters |
| --- | --- | --- |
| Message Originator Authenticity / Integrity | Ke2e_EntityA_EntityN_msg_auth | None |
| Message Re-play protection | Ke2e_EntityA_EntityN_msg_auth | Nonce / Time / Seq# |
| Non-repudiation capability | N/A | N/A |
| Message Confidentiality | Ke2e_EntityA_EntityN_msg_conf | IV |
| Confidentiality of Data in Transit | Ke2e_EntityA_EntityN_msg_conf | IV |
| Confidentiality of Data at Rest | None | None |
| Integrity of Data in Transit | Ke2e_EntityA_EntityN_msg_auth | Nonce / Time / Seq# |
| Integrity of Data at Rest | None | None |

Table 8.4.1.2-2: Depicting example keys that generated and associated parameters

## 8.5	Proposal for determining detailed Security Requirements, Features and associated Algorithms

### 8.5.1	Security Determination Process

#### 8.5.1.1	Overall Description

This section provides description on mechanisms that can be employed for determining the appropriate security requirements, features, and algorithms and associated credentials in order that the security mechanisms that are employed are adequate but at the same time efficient for the type of service offered by the entity and also does not drain valuable resources from the entity.

#### 8.5.1.2	Detailed Description

Table 8.5.1.2-1 illustrates Entity Profile (EP) associated with an entity (e.g. AE1). The EP may be obtained or provided explicitly during the registration phase. It may be obtained as part of the M2M Subscription Profile associated with an entity. The EP provides a very high-level security requirement of the Entity. It may be used to derive and generate a more granular security requirement as illustrated in Figure 8.5.1.3-4. However, since the profile of the entity does not provide details of the device, the selection of the features may not be appropriate from a performance perspective.

| Entity Profile | Values |
| --- | --- |
| Class of Service | Healthcare |
| Type of Service | Real-time |
| Impact | Critical (Life and Limb) |
| Security Level | High |

Table 8.5.1.2-1 Entity Profile of an Entity (e.g. AE1)

An example Device Profile (DP) is illustrated in Table 8.5.1.2-2. Using the DP as well as the EP, a more appropriate security requirements and features may be generated. So, a low-powered, low-memory device that only provides a service that requires “low” Security, then the security function(s), the algorithms selected and the key sizes may be selected appropriately. E.g. the message authentication mechanism selected may be HMAC-SHA1 with 160 bit keys whereas an entity with more processing and memory and requiring a higher security would be provisioned with 256 bit keys that may be used with HMAC-SHA2 mechanism.

| Device Capability | Values |
| --- | --- |
| Processing Capability | 900 MHz |
| RAM | 500 Kb |
| Flash | 1MB |
| Battery | 5.0 Micro-W/MHz |
| Wireless Capability | Bluetooth, WiFi |
| Sleep Mode | Sleep / Deep-Sleep |
| Secure Environment | Yes |
| OS / version | Android / Kitkat |

Table 8.5.1.2-2 Device Profile of an Entity (e.g. AE1)

An example Security Profile (SP) is illustrated in Table 8.5.1.2-3. Even if both the EP and DP are available, in certain cases, it may not be enough to determine, for example, whether end-to-end security is required or if data at-rest security is required or not. In such cases, it would be preferable to be provided with an SP.

| Security Requirement | Within Security domain (at HCSE or RCSE) | End-to-End |
| --- | --- | --- |
| Message Originator Authenticity / Integrity | High | Very High |
| Message Re-play protection | High | Very High |
| Non-repudiation capability | Low | Low |
| Message Confidentiality | Medium | Medium |
| Data Confidentiality in Transit | High | High |
| Data Confidentiality at Rest | Medium | High |
| Data Integrity in Transit | High | Very High |
| Data Integrity at Rest | Medium | Very High |
| Service Availability | High | Very High |
| Data Availability | High | Very High |

Table 8.5.1.2-3 Security Profile of an Entity (e.g. AE1)

An example security features that have been determined based upon the information provided in the SP, DP and EP is illustrated in Table 8.5.1.2-4.

| Entity ID | Security Features | Within Security Domain | End-to-End |
| --- | --- | --- | --- |
|  |  | Algorithms | Sizes | Protocol(s) | Algorithms | Sizes |
| AE1 | Message Originator Authenticity / Integrity | HMAC-SHA-2 | 256 / 512 | (D)TLS, JWS | HMAC-SHA-2 | 256 / 512 |
|  | Message Replay Protection | Nonce | 256 | N/A | Timestamp / Nonce + Sequence Number | 256 bits |
|  | Non-Repudiation | None |  | N/A | None |  |
|  | Message Confidentiality | AES | 112 | (D)TLS | AES | 192 |
|  | Confidentiality of Data in Transit | AES | 192 | (D)TLS, JWE | AES | 192 |
|  | Confidentiality of Data at Rest | AES | 256 | N/A | AES | 256 |
|  | Integrity of Data in Transit | HMAC-SHA-2 | 256 | (D)TLS, JWS | HMAC-SHA-2 | 256 |
|  | Integrity of Data at Rest | HMAC-SHA-512 | 512 | N/A | HMAC-SHA-512 | 512 |
|  | Authentication Mechanism | Symmetric Key | 256 | (D)TLS | Symmetric Key | 256 |
|  | Authentication Process | Direct |  |  |  |  |
|  | Presence of Secure Element | YES |  |  |  |  |

Table 8.5.1.2-4: An example of detailed security features determined based on SP, EP and DP

# 9	Procedures for Recommended Options

Editor’s note: this clause provides detailed description of the recommended combination(s) of individual end-to-end authenticated key exchange, group end-to-end  authenticated key exchange and end-to-end message security.

<Text>

# 10	Conclusions and recommendations

Editor’s Note: This clause will capture agreed conclusions and recommendations.

# Annex <A>: Problem Statement for needing End-to-End Data Security

## A.1	Introduction

The general protection afforded to data / content is only while the content is “in transit” between two “trusted” entities by means of transport-layer protocol (e.g. TLS / DTLS). There is no notion of protection of content while hosted at an entity (at rest). The implication is that the content (object) protection, if at all performed, must be done at the application layer. The problem with the application layer content protection approach is multi-fold:

- Applications do not provide a uniform mechanism for application data / content protection. Application layer protection only provides for the actual application data protection and not the resources associated with the oneM2M service layer.

- Service Layer resources are not protected.

- A separate application layer protocol for securing content must be performed, which may be far more cumbersome

- In certain scenarios, in order for a service layer to be able to provide value-added services, the content may have to be stored in its un-encrypted form

### Use-case 1

Illustrated in Figure 1 is a use-case where there are 4 entities involved: an AE1, a Hosting CSE (CES1), an IN-CSE and a hacker application or even a non-malicious function. The AE1 created a resource within a CSE1 at service layer which stores attributes and content / content instances. In this use case, two attributes are provided as examples: Attribute 1 and Attribute 2. It is assumed that the AE1 and CSE1 have mutually authenticated one another and used a secure communications channel prior to performing the “create resource” operation. At some point, a hacking application exploits a vulnerability within the CSE1 through an IN-CSE. It is possible that the hacking application may be able to reach the CSE1 without having to go through an IN-CSE, however, because of the diversity of protocol support (e.g. open ports and services that run) on the IN-CSE, it may make a very good entry point for a hacking application. Once the hacker is able to access the CSE1, it steals the content stored within the AE1 resource. It is a classic attack without the need for much sophistication. One way to mitigate such an attack is to encrypt the whole disk or use encryption on a per-file basis. However, the content may have to be processed at the SL and decrypted at a transit node on the communication path, where the content becomes vulnerable to an attack. Another mechanism is to protect the content using JSON-based object signing and encryption mechanisms. But there is no framework to enable the use of such mechanisms for protecting SL resources. An additional issue is that, the CSE1’s platform is not trustworthy and therefore secure processes may not be carried out. Also, if a root key is broken, then it exposes the data from all the AEs stored on the CSE1. In short, the security of an application data or user’s confidential data is off-loaded to an entity that the user or application does not have much control of and the trustworthiness of the platform is based on the trust the user has of the SP. Additionally, when the CSE1 is de-commissioned the data remains within the CSE1 and protected only by a file-based encryption, which may be broken easily by an obsolete operating system protecting the resources. The threats can be summaried as follows:

- Unauthorized access by an entity to data / content at rest

- Unauthorized access to data / content by an intermediate node (e.g. CSE) during transit

- Unauthroized access to system specific resources during rest or transit

A summary of the issues is provided here:

- Lack of a confidentiality protection mechanism at the hosting entity (e.g. CSE), when the content is at rest.

- Lack of a mechanism to hide the content even from the CSE (e.g. a less-trustworthy CSE)

- Each hop (e.g. transit CSE) has an un-encrypted access to the content once the data comes through a TLS/DTLS tunnel, when transferring content to a Client.

Figure 1: Un-authorized access to a data / content

### Use-case 2

The use case illustrated in Figure 2involves six entities: AE1 that generates the content, AE2 and AE3 are Client applications that consume the content produced by AE1. The content is hosted on CSE1 without any integrity protection. Similar to the above mentioned case, an attacker may exploit vulnerabilities either at the IN-CSE or CSE1 and modifies the resource and / or the resource structure, e.g. attributes and / or content(s). The figure illustrates a scenario where an attacker is able to perform an un-authorized modification of AE1’s attribute, Attribute 1. AE2 that is subscribed to AE1’s resource obtains the modified copy of the resource. In cases, where the resource obtained from AE1 is used to make critical decisions or operations by AE2 then it may have major ramifications. At a later point, the attacker deletes the Attribute 2 and adds new Attribute 3 and 4, essentially the attacker is not only changing the resource, but also the structure of the resource. An AE3 that is subscribed to the resource has a completely different resource tree than what was created by AE1. The threats can be summaried as follows:

- Unauthorized modification of data / content at rest

- Unauthorized modification of data / content by an intermediate node (e.g. CSE) during transit

- Unauthroized modification of system specific resources during rest or transit

Summary of the issues are listed below:

- There is no mechanism to provide integrity protection to a resource

- There is no mechanism to provide integrity protection to the structure of the resource

- There is no mechanism to provide integrity protection to system critical resources (e.g. ACPs, m2mSubscriptionProfile, managementObject resources etc.)

Figure 2: Un-authorized modification of data / content

# Annex <B>: Use case for remote attestation

Editor’s Note: Figure(s) will be provided later for better explanation.

## B.1		Description

In a oneM2M System, a simple application deployment where sensors provide a flow of messages from peripheric ADNs, relayed by MNs and finally up to a central IN is not always possible due to 1) lack of connectivity or 2) inneficient use of network bandwidth.

The lack of connectivity can be seen as a complete loss of connectivity or as the result of an unacceptably high network latency between the ADN and the IN. An example would be a car automation system. The sensor and the M2M Gateway are both part of the car. The processing has to be done inside the car such that the result is immediately available. When connectivity allows, the results can be shared with other vehicles or road infrastructure. For critical information (ie: speed), the receivers need a way to verify the correctness of the result (ie: a platoon of vehicles adjusting their speeds to match). This relates to OSR-022, which states a certain independence of Field Nodes when disconnected from the Infrastrcture:

| OSR-022 | When some of the components of a M2M Solution are not available (e.g. WAN connection lost), the oneM2M System shall be able to support the normal operation of components of the M2M Solution that are available. | Implemented in Rel-1 |
| --- | --- | --- |

Data aggregation is an example where the centralized approach leads to inneficient use of bandwidth. Although the IN is much more powerful than a sensor, it is not practical to aggregate millions (or billions) of data points from each individual ADN. A middleground would be to distribute the computation across the MNs and reduce the data flows to manageable sizes as they approach the collection point (IN). More explicity, as messages flow from sensors through MNs, the MNs peform a computation based on these inputs (ie: max, average) and expose a smaller, virtual resource to the next MNs and ultimately to the IN. This distributed map-reduce helps makes the data collection practical. For critical applications (compute maximum of temperatures to trigger alarm), the receiver needs a way to verify the correctness of the result. This enables a secure fulfilment of the Semantics Mashup Requirements MSH-01 to MSH-05:

| MSH-001 | The oneM2M System shall provide the capability to host processing functions for mash-up. | Targeted for Release 2 |
| --- | --- | --- |
| MSH-002 | The oneM2M System shall enable M2M Applications to provide processing functions for mash-up. | Targeted for Release 2 |
| MSH-003 | The oneM2M System itself may provide pre-provisioned or dynamically created processing functions for mash-up. | Targeted for Release 2 |
| MSH-004 | The oneM2M System shall be able to create and execute mash-ups based on processing functions. | Targeted for Release 2 |
| MSH-005 | The oneM2M System shall be able to expose mash-ups as resources e.g. virtual devices. | Targeted for Release 2 |

More generally, the previous examples show the value of an application design where the M2M Gateway can process the data from the originating sensor (constrained M2M device) on its way to the receiver (IN, another M2M Gateway, or M2M Device). For such a design to be useful, the receiver needs to be able to verify that the MN correctly processed the right data, thus providing end-to-end assurance of data and computation integrity.

## B.2 Actors

The actors in this use case are the sensor (ADN-AE), the middle-node (MN-AE, or prover) and another node (ASN-AE, or verifier).

ADN-AE(s): One or multiple sensors act as the data source. They usually are constrained M2M Devices (ADN-AE). They are equipped with a TPM capable of  digitally signing the data.

MN-AE: Is an application running on the MN that receives the inputs from the sensors and computes a function over them.

ASN-AE: Is another node that receives the output from the MN-AE and wishes an assurance that the result is correct (correct inputs and correct computation).

## B.3 Pre-conditions

The sensors are equipped with TPMs (ie: they are tamper-proof  and can cryptographically sign messages).

## B.4 Normal flow

Setup

- The Application Service Provider creates the application, deploys and configures it on MN-AE and  on ASN-AE.

Operation

- (Optional) Setup between ASN-AE and  ADN-AE that might be needed to protect against replay attacks.

- The sensor generates data, signs it, and sends it to the MN-AE.

- The MN-AE computes the result of the function over the sensor data and a proof. It sends the result along with the proof to the ASN-AE.

- The ASN-AE verifies the proof and based on  the outcome accepts or rejects the result.

## B.5 Potential requirements

The potential requirements match the security requirements SER-044 and SER-050:

| SER-044 | For M2M Application Service data, that are processed by an M2M Application B in a M2M entity (e.g. M2M Gateway) on its path from an originator A to the recipient M2M Application C, the oneM2M System shall provide means that enable the recipient to verify both: integrity of the data received by the M2M Application B from the originator A and, at the same time that the M2M Application B that has processed the data has not been compromized. | Targeted for Release 2 |
| --- | --- | --- |
| SER-050 | The oneM2M System shall enable pre-defined conditions to be protected from unauthorized modification. | Targeted for Release 2 |

In the case of SER-050, the predefined conditions are the instructions that comprise the AE program itself. In that sense, satisfying SER-044 also satisfies SER-050.

# Comments

No such a clause

No such a clause