| CHANGE REQUEST |
| --- |
| Meeting:* | SEC22.2 |
| Source:* | Datang |
| Date:* | 2016-04-21 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Reason for Change/s:* | CR for Role Based Access Control |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0023 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and v2.0.1 |
| Clauses/Sub Clauses* | 7.4 Role Based Access Control |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes the role based authorization architecture and procedures.

### -----------------------Start of change 1-------------------------------------------

## 7.4	Role Based Access Control

### 7.4.1	Role Based Access Control Architecture

Figure 7.4-1 provides a high level overview of the role based access control architecture in the oneM2M System. The entities related to role issuance and role based access control are described as follows:

- Authorization Authority: It is responsible for assigning roles to Originators through creating <role> and/or <token> resources in Role and/or Token Repositories.

- Role Repository: It is a CSE that is responsible for storing <role> resources.

- Token Repository: It is a CSE that is responsible for storing <token> resources.

# Figure 7.4-1. Role based access control architecture

The generic procedure of this architecture is described as follows:

Step 001:	An Originator may apply for a role from an Authorization Authority.

Step 002:	The Authorization Authority shall check if the requested role can be assigned to the Originator. If it is permitted, the Authorization Authority shall issue the requested role to the Originator. A token that holds the assigned role may also be issued.

Step 003:	The Authorization Authority may create a <role> and/or a <token> resource in a Role Repository and/or a Token Repository, from which the Originator’s role assignment information can be retrieved.

Step 004:	The Originator may retrieve the assigned roles and/or tokens from Role and/or Token Repositories in order to get detailed information about the assigned roles and/or tokens.

Step 005:	The Originator sends an access request to the target resource in the Hosting CSE. The request shall contain the role information that may be the Role-IDs, Tokens or Token-IDs.

Step 006:	The Hosting CSE may send an access control decision request to a PDP.

Step 007:	The PDP shall retrieve the Originator’s role assignment information according to the Role-IDs and/or Token-IDs from the Role and/or Token Repositories.

Step 008:	The PDP shall verify the Originator’s roles and/or tokens and then make an access control decision according to the access control policies and roles.

NOTE 1:	Some steps described here may not be needed in some applications, e.g. a Role Authority may directly issue roles and/or tokens to an Originator without step 1, or the Originator already have the role information from the Authorization Authority, and does not need to do the step 4.

### 7.4.2	Role Issuing Procedure

The general procedure of issuing a role to an Originator is shown in the Figure 7.4.2-1 and described as follows:

# Figure 7.4.2-1: Procedure of issuing a role

- The Originator shall send a role application request via a <role> CREATE request to an Authorization Authority. Besides the parameters specified in clause 8.1.2 of TS-0001 [1], the Role-ID that the Originator wants to apply for shall be contained in the role application request.

- The Authorization Authority shall check if the applied role can be assigned to the Originator according to the role assignment policies that are however out of scope of present document. After passing the role assignment policy check, the Authorization Authority shall assign the role to the Originator. A valid role assignment process shall include a <role> and/or <token> resource creation.

- If a token that hold the role assigned to the Originator has been issued, the Authorization Authority shall create a <token> resource in a Token Repository. The <token> CREATE request shall provide the mandatory and optional attributes as specified in clause 9.6.39 of TS-0001 [1].

- The Authorization Authority shall create a <role> resource in an Authorization Repository. The <role> CREATE request shall provide the mandatory and optional attributes as specified in clause 9.6.38 of TS-0001 [1].

- The Authorization Authority shall return the result of role assignment back to the Originator. The returned information may be Role-ID, content of <role> resource, address of <role> resource, Token-ID, content of <token> resource or address of <token> resource.

- If the address of a <token> resource is provided, the Originator may use it to retrieve the <token> resource in order to obtain detailed information about the token.

- If the address of a <role> resource is provided, the Originator may use it to retrieve the <role> resource in order to obtain detailed information about the role.

### 7.4.3	Role Based Access Control Procedure

The general procedure of using a role in an authorization process is shown in the Figure 7.4.3-1 and described as follows:

# Figure 7.4.3-1: Role based access control procedure

- The Originator may select applicable Role-IDs, Token-IDs, or tokens according to the App-IDs attribute of <role> or <token> resources, and include them into the request sent to the Hosting CSE.

- The PEP in the Hosting CSE shall generate access control decision request according to the request of the Originator, and send the request to a PDP. The Role-IDs, Token-IDs, or tokens received from the Originator shall be included in the request.

- In case of Role-IDs or Token-IDs, the PDP shall send role or token information request with a Role-ID or Token-ID to a PIP in order to get the role or information, and the PIP shall further send a <role> or <token> resource retrieve request to the Role or Token Repository. The PDP may directly send <role> or <token> resource retrieve request to the Role or Token Repository instead of via a PIP.

- The Role Repository shall retrieve the <role> or <token> resource and return the attributes of <role> or <token> resource back to the PIP or directly back to the PDP, and the PIP shall further return the retrieved attributes back to the PDP.

- The PDP shall verify the received roles and/or tokens, the verification shall include: if the role/token is issued by a valid Role/Token Authority, if holder of the role/token is equal to the Originator, and if the role/token is still valid. Only valid roles/tokens shall be used for access control.

- The PDP shall evaluate the access request of the Originator using access control policies and Role-IDs for making an access control decision as described in clause 7.1.

- The PDP shall return the access control decision back to the PEP.

- The Hosting CSE shall enforce the access control decision, i.e. either perform the resource access on behalf the Originator or deny the resource access.

- The Hosting CSE shall return the result of resource access back to the Originator.

### -----------------------End of change 1-------------------------------------------