| Input Contribution |
| --- |
| Meeting ID* | SEC 23 |
| Title:* | Stage 3 plan for E2E Security |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcom.com |
| Uploaded Date:* | 2016-05-16 |
| Document(s) Impacted* | TS-0003 rel 2, TS-0004 rel 2. |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | No action |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

The table below lists the expected changes to TS-0003 and TS-0004 to provide the stage 3 text for end-to-end security. Changes related to use of notification is addressed in “Stage 3 plan for Security use of Notification”. Some notes about the table:

- TS-0003 is called the “SEC” specification, with corresponding text shown in dark red font.

- TS-0004 is called the “PRO” specification, with corresponding text shown in red font.

- The cells in the column for “Expected Relative Difficulty” are coloured to highlight tasks expected to have “High” and “Medium” relative difficulty.

Within the scope of this contribution, there are no changes expected for TS-0008 and TS-0009 – although there are changes to TS-0008 and TS-0009 for end-to-end security which are addressed in “Stage 3 plan for Security use of Notification”.

It is inevitable that additional changes in other clauses will be necessary, but this table provides a high level view of the work to be done. This list excludes minor editorial text alignments, addressing of remaining Editor’s notes and possible addition of text related to error handling.

Qualcomm will provide these CRs. This document is expected to be a living document, with subsequent revisions updating the status of the changes. If no status is provided, the task has not been started.

| Topic | Item Type | Item | Expected Relative Difficulty | Target Spec | Impacted clauses | Status |
| --- | --- | --- | --- | --- | --- | --- |
| e2eSecurity Capabilities | Resource attribute | Components and purpose | Low | SEC | See SEC-2016-0096 | submitted |
|  |  | Processing | - | SEC | 8.4.2 should be sufficient already | n/a |
|  |  | Format | Medium | PRO | PRO-2016-0183 | submitted |
| ESPrim | Generic Procedures | Originator | Medium | PRO | 7.2.2 Generic procedures. | Generating/ processing ESPrim Objects PRO-2016-207 | submitted |
|  |  | Receiver | High | PRO |  |  | submitted |
|  | Common Operations | Originator | High | PRO | 7.3 Common Operations. |  | submitted |
|  |  | Hosting CSE | High | PRO |  |  | submitted |
|  | E2ERandObject | Components and purpose | Low | SEC | See SEC-2016-0099 | submitted |
|  |  | Processing | - | SEC | 8.4.2 should be sufficient already | n/a |
|  |  | Format | Low | PRO | PRO-2016-0183R01 | n/a |
|  | Session key generation algorithms | Processing | Low | SEC | 10 | PH |
| ESData | ESData Envelope | Format | Medium | PRO | PRO-2016-0183 | submitted |
|  |  | Processing | Medium | SEC | See SEC-2016-0099 | submitted |
|  | Attribute | contentInfo format | Low | PRO | 6.3.4.2.28 “EncodingType” | submitted |

Color key for status:

Author Assigned

Drafting

Submitted

Submitted: in discussion

Agreed/Complete