| CHANGE REQUEST |
| --- |
| Meeting:* | SEC 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-05-16 |
| Contact:* | As above |
| Reason for Change/s:* | Provides structure of e2eSecInfo resource attribute |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.0.1 |
| Clauses/Sub Clauses* | New 8.4.3.1.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR defines parameters and attributes used in End-to-End security frameworks. All changes are clarifications of existing features. This CR references a recently approved SEC-2016-0099R02 “CR TS-0003 R2 ESPrim Stage 3”.

R00 Changes (with R01 changes shown inline):

- parameter definitions

  - receiverE2ERandObject (R01: this was moved to SEC-2016-0099R02).

  - originator2ERandObject  (R01: this was moved to SEC-2016-0099R02).

  - The e2eSecInfo attribute occurs in the <CSEBase>, <remoteCSE> and <AE> resource types. TS-0001 (R2) says that the e2eSecInfo attribute is described in TS-0003. This CR provides the TS-0003 text describing e2eSecInfo

### -----------------------Start of change 2-------------------------------------------

#### 8.4.3.1.3	e2eSecInfo resource attribute definition

The e2eSecInfo attribute occurs in the <CSEBase>, <remoteCSE> and <AE> resource types. The structure of the e2eSecInfo resource attribute is shown in Table 8.4.3.1.3-1. This parameter is used in establishing sessionESPrimKey as part of End-to-End Security of Primitives (ESPrim), described in clause 8.4.2. The data types are specified in TS-0004 [4].

Table 8.4.3.1.3-1: Structure of the e2eSecInfo attribute

| Element Path | Multiplicity | Description |
| --- | --- | --- |
| supportedE2ESecurityFeatures | 1 | A list of Security Usage Identifiers (SUIDs) for the End-to-End Security Features supported by the CSE or AE associated with the <CSEBase>, <remoteCSE> or <AE> resource containing the e2eSecInfo resource attribute. |
| e2ECertificates | 0..1 | A list of certificates associated with the CSE or AE associated with the <CSEBase>, <remoteCSE> or <AE> resource containing the e2eSecInfo resource attribute. |
| sharedReceiverE2ERandObject | 0..1 | A receiverE2ERandObject parameter (see clause 8.4.3.1.2) generated by the CSE or AE associated with the <CSEBase>, <remoteCSE> or <AE> resource containing the e2eSecInfo resource attribute. |

### -----------------------End of change 2-------------------------------------------