| CHANGE REQUEST |
| --- |
| Meeting:* | SEC23 |
| Source:* | Datang |
| Date:* | 2016-05-15 |
| Contact:* | Wei Zhou, Datang, zhouwei@catt.cn Hui Xu, Datang, xuhui@catt.cn |
| Reason for Change/s:* | TS-0003 CR Token Structure |
| CR against: Release* | 2 |
| CR against: WI* | Active WI MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003-V2.1.0 |
| Clauses/Sub Clauses* | 7.3.2.4 Token Structure |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes the role based authorization architecture and procedures.

### -----------------------Start of change 1-------------------------------------------

#### 7.3.2.4	Token Structure

A token is used to carry authorization information that can be roles assigned to the token holder or access control policies applicable to the token holder. The structure of token is shown in figure 7.3.3.1-1, it contains the following data fields:

- version: version of the token.

- tokenID: unique ID of the token.

- issuer: ID of the token issuer.

- holder: ID of the token holder.

- notBefore: token valid from this time.

- notAfter: token expired after this time.

- tokenName: optional, human readable name of the token.

- appIDs: optional, list of App-IDs that are used for determining what M2M applications this token are used for.

- audience: optional, list of CSE-IDs of the CSEs expected to accept the token.

- permissions: permissions associated with the token. Its format is shown in table 7.2.4.1-1.

- extension: used for store other information, e.g. application-specific information.

# Figure 7.2.4.1-1: Structure of token

A token shall be protected by the ESData security mechanism. A token shall be signed, encrypted or signed and encrypted.

# Table 7.2.4.1-1: Structure of token permission

| Element Path | Multiplicity | Description | Note |
| --- | --- | --- | --- |
| resourceIDs | 0..1 | The resources to which this permission applies. If not present, then the privilege applies to all resources |  |
| privileges | 0..1 | A set of access control rules applicable to the identified resources (for the identified holder) | At least one of these must be present |
| roleIDs | I 0..1 | A set of roleIDs applicable to the identified resources (for the identified holder) |  |

### -----------------------End of change 1-------------------------------------------

# Comments

Reference?