| CHANGE REQUEST |
| --- |
| Meeting:* | SEC23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-05-16 |
| Contact:* | As above |
| Reason for Change/s:* | Provides the protocol specification of oneM2M JSON Web Tokens (JWTs) for use in Token-based authorization |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0019 Dynamic Authorization MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.1.1 |
| Clauses/Sub Clauses* | 2.1, 2.2, New 7.3.2.6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR provides the protocol specification of oneM2M JSON Web Tokens (JWTs) for use in Token-based authorization. JWTs are specified in IETF RFC 7519. This CR references text introduced in SEC-2016-0108 “CR TS-0003 Token Evaluation”.

### -----------------------Start of change 1-------------------------------------------

#### 7.3.2.6	oneM2M JSON Web Tokens (JWTs)

##### 7.3.2.6.1	Introduction to oneM2M JWTs

oneM2M specifies a JSON Web Tokens (JWTs) representation (RFC 7519 [RFC7519]) for Tokens used in oneM2M. A JWT compliant with the present clause is called a oneM2M JWT.

Background: A JWT uses either the JSON Web Signature (JWS) Compact Representation, or JSON Web Encryption (JWE) Compact Representation,  specified in IETF RFC 7515 [RFC7515] and  IETF RFC 7519 [RFC7519]. The JWT specification RFC 7519 [RFC7519] also defines an unsecured JWT which is a JWS using the "alg" Header Parameter value "none" and with the empty string for its JWS Signature value”.

The JWT specification defines a JSON element which is the structure of the payload of the JWS or JWE when used as a JWT. This payload comprises a set of JWT claims, with RFC 7519 [RFC7519] standardizing an initial set of JWT claim names.  IANA maintains a registry of JWT claim names [IANA-JWT].

##### 7.3.2.6.2	oneM2M JWT Profile

oneM2M JWT Claims: Table 7.3.2.6.2-1 provides the mapping from the JWT claim names in a oneM2M JWT map to the elements of the m2m:tokenObject complex data type described in TS-0004 [4]. Where available, JWT claim names registered with IANA [i.IANA-JWT] have been used. TS-0004 [4] specifies which elements are mandatory and which elements are optional.

Table 7.3.2.6.2-1: The oneM2M JWT claim set and mapping to Token Object elements

| Token Object Element Path | JSON element name | Where is this JSON element name defined? | Additional specification |
| --- | --- | --- | --- |
| version | “tkvr” | TS-0004 [4] short names |  |
| tokenID | “jti” | RFC 7519 [RFC7519] | tokenID shall conform to the m2m:tokenID data type |
| issuer | “iss” | RFC 7519 [RFC7519] |  |
| holder | “azp” | OpenID Connect Core 1.0 [OpenIDConnectCore] |  |
| notBefore | “nbf” | RFC 7519 [RFC7519] |  |
| notAfter | “exp” | RFC 7519 [RFC7519] |  |
| tokenName | “tknm” | TS-0004 [4] short names |  |
| audience | “aud” | RFC 7519 [RFC7519] |  |
| permissions | “tkps” | TS-0004 [4] short names | The permissions “tkps” claim is a complex data type defined in TS-0004 [4]. The permissions element shall use the JSON representation. |
| extension | “tkex” | TS-0004 [4] short names |  |

oneM2M JWT Security Profile. The JWS Compact Representation and JWE Compact Representation are both supported by ESData (see clause 8.5.3). A oneM2M JWT may use any ESData security class: Encryption-only, Signature-only or Nested-Sign-then-encrypt. A oneM2M JWT may use any algorithm supported by ESData for the JWS Compact Representation and JWE Compact Representation.

A oneM2M JWT may be an unsecured JWT, in which case the oneM2M JWT is considered to use the unsecured ESData security class.

RFC7519 [RFC7519] discusses security considerations of JWTs, and operators of Token Issuers (Dynamic Authorization Servers and Authorization Authorities) should consult that text when deciding on ESData security class and algorithms.

Editor’s note: we need some text about risks of using unsecured JWT.

JOSE header parameters of oneM2M JWTs. When the Encryption-only ESData security class is used, then

- The JOSE header of the JWE shall include the “typ” parameters set to “JWT”.

- The JOSE header of the JWE shall not include the “cty” parameter.

When the Signature -only ESData security class is used, then

- The JOSE header of the JWS shall include the “typ” parameters set to “JWT”.

- The JOSE header of the JWS shall not include the “cty” parameter.

When the Nested-Sign-then-encrypt ESData security class is used, then the JWT claims are the payload of a JWS, and the JWS becomes the payload of a JWE. In this case,

- The JOSE header of both the JWS and the JWE shall include the “typ” header parameters set to “JWT”.

- The JOSE header of the JWE shall include the “cty” parameter set to be "JWT", to indicate that a Nested JWT is carried in this JWT.

- The JOSE header of the JWS shall not include the “cty” parameter.

##### 7.3.2.6.3	oneM2M JWT Procedures

Configuring CSEs for verifying from a Token Issuer.  In order for a CSE to verify oneM2M JWTs issued by a particular Token Issuer, the CSE shall be provided with the following information in a secure manner

- The combinations of ESData Security classes and algorithms permitted by the Token Issuer.

- Credentials for verifying Tokens conforming to those ESData Security classes and algorithms, noting that no credentials are needed for verifying tokens using the unsecured ESData Security class.

The present specification does not provide any mechanisms for providing this information to the CSE. The present specification does not define data structures for storing this information on the CSE.

Editor’s note: some text might be needed about storing the credentials securely.

Creating a oneM2M JWT: When a Token Issuer is triggerd to create a token, then the Token issuer shall perform the following steps

- The Token Issuer shall form a Token Object of data type m2m:tokenObject.

- The Token Issuer shall create the corresponding oneM2M JWT claim set using the mapping in Table 7.3.2.6.2-1.

- The Token Issuer shall select an ESData Security Class, algorithms and corresponding credentials. This step may also be performed before step 1) or between steps 1) and 2).

- The Token Issuer shall create oneM2M JWT using the oneM2M JWT claims, ESData Security Class, algorithms and corresponding credentials. This step uses the process described for JWTs in RFC7519 [RFC7519].

The resulting oneM2M JWT has data type m2m:dynAuthJWT.

Validating a oneM2M JWT: When a CSE receives a oneM2M JWT for use in an access decision, then the CSE shall perform the following steps

- The CSE shall validate that the oneM2M JWT conforms to the m2m:dynAuthJWT data type.

- The CSE shall validate the security of the oneM2M JWT as described in clause 7.3.2.5, using the JWT-specific details in RFC7519 [RFC7519] and configured credentials (if required). A CSE shall discard a oneM2M JWT which uses a ESData Security class or algorithms which are not permitted by the Token Issuer.

- The Token Issuer shall create a Token object from the oneM2M JWT claim set using the mapping in Table 7.3.2.6.2-1.

- The CSE shall validate the Token content in the JWT claims as described in clause 7.3.2.5.

The permissions in the “tkps” JWT claim can now be processed as described in clause 7.3.2.5.

### ----------------------------End of change 1----------------------------------

Note: clause 7.3.2.5 was recently introduced in SEC-2016-0108

### ------------Add the following normative references to clause 2.1  -------------

[RFC7519]  IETF RFC 7516: “JSON Web Token (JWT)”, 2015

[OpenIDConnectCore] OpenID Foundation, “OpenID Connect Core 1.0”, 2014

### ------------End of changes to clause 2.1  -------------

### ------------Add the following informative references to clause 2.2  -------------

[i.IANA-JWT] IANA JSON Web Token (JWT) registry, http://www.iana.org/assignments/jwt/jwt.xhtml

### ------------End of changes to clause 2.2  -------------