| CHANGE REQUEST |
| --- |
| Meeting:* | SEC24 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Date:* | 2016-07-20 |
| Contact:* | As above |
| Reason for Change/s:* | Updates to Certificate Profiles |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0016 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0003 and 2.3.0 |
| Clauses/Sub Clauses* | 10.1.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR adds some missing details on certificate profiles defined in clause 10.1.1 of TS-0003. It provides the allowed values for the keyUsage and extKeyUsage Extensions.

### -----------------------Start of change 1-------------------------------------------

## 10.1	Certificate-Based Security Framework Details

### 10.1.1	Certificate Profiles

#### 10.1.1.0	General

NOTE:	These certificate profiles are compliant with the CoAP specification IETF RFC 7252 [38].

#### 10.1.1.1	Common Certificate Details

All certificates shall conform to the following profile:

Certificates shall conform to IETF RFC 5280 [34].

The certificate shall include a SubjectPublicKeyInfo that indicates an algorithm of id-ecPublicKey with namedCurves secp256r1 [34]; this curve is equivalent to the NIST P-256 curve [39].

Editor’s note: algorithm-ids and parameters for RSA encryption and RSA signatures are required.

The public key format shall be uncompressed [46].

The hash algorithm shall be SHA-256.

The key usage extension shall be included. Table 10.1.1.1-1 specifies the allowed values for the key usage extension according to the intended usage of the certificate.

Table 10.1.1.1-1: Allowed values for the keyUsage Extension [34] according to the intended usage of the certificate

| keyUsage bits | CA Certificates (10.1.1.3) | ESData Encryption Key Management (8.5.3.2) | ESData Signature (8.5.3.3) | Other Certificates |
| --- | --- | --- | --- | --- |
|  |  | RSA | ECDH-ES | RSA, ECDSA |  |
| digitalSignature | 0 | 0 | 0 | 1 | 1 |
| nonrepudiation (also called contentCommitment) | 0 | 0 | 0 | 0 or 1 | 0 or 1 |
| keyEncipherment | 0 | 1 | 0 | 0 | 0 |
| dataEncipherment | 0 | 0 | 0 | 0 | 0 |
| keyAgreement | 0 | 0 | 1 | 0 | 0 |
| keyCertSign | 1 | 0 | 0 | 0 | 0 |
| cRLSign | 0 or 1 | 0 | 0 | 0 | 0 |
| encipherOnly | 0 | 0 | 0 | 0 | 0 |
| decipherOnly | 0 | 0 | 0 | 0 | 0 |

The extended key usage extension shall be included in certificates issued to CSEs and AEs. Table 10.1.1.1-1 specifies the allowed values for the key usage extension according to the intended usage of the certificate

Table 10.1.1.1-2: Allowed values for the extKeyUsage Extension [34] according to the intended usage of certificates issued to AEs and CSEs

| Certificate Usage | keyPurposeID |
| --- | --- |
| Certificates used in TSL or DTLS handshakes (MEF Interface, SAEF, ESCertKE) | id-kp-oneM2MTLSAuth ::= TBD |
| ESData Encryption Key Management (8.5.3.2) | id-kp-oneM2MESDataEnc ::= TBD |
| ESData Signature (8.5.3.3) | id-kp-oneM2MESDataSig ::= TBD |

#### 10.1.1.2	Raw Public Key Certificate Profile

Raw public key certificates shall conform to clause 10.1.1.1 "Common Certificate Details" and IETF RFC 7250 [37].

#### 10.1.1.3	Details Common to Certificates with Certificate Chains

Certificates with Certificate Chains shall conform to the following description:

These certificates shall conform to clause 10.1.1.1 "Common Certificate Details".

Certificates shall be signed with ECDSA using secp256r1, and the signature shall use SHA-256.

Certificate chains should limit the number of intermediate CA certificates to avoid having a negative impact in constrained environments.

### -----------------------End of change 1-------------------------------------------