| Input Contribution |
| --- |
| Meeting ID* | SEC 27 |
| Title:* | Use case for Security Developer’s Guide TR-0038 |
| Source:* | Norihiro Okui, KDDI, no-okui@kddi.com |
| Uploaded Date:* | 2017-02-16 |
| Document(s) Impacted* | TR-0038 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | include the text proposed in this contribution into TR-0038. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution provides an usecase for security developer guide. The usecase is based on remote light control usecase which is described in TR-0025.

======== Text proposed for TR-0038 starts here =============================

# Use case

This guide is based on a home lighting use case involving lights in a home that can be remotely controlled by a user's smartphone leveraging the capabilities of oneM2M. An overview of the use case is shown in figure 5.1. The main components are introduced as follows:

- The lights are deployed in a home and are attached to a home gateway.

- The home gateway communicates with a cloud service platform allowing the lights to be controlled remotely by the smartphone.

- The cloud service platform supports a set of services to enable the smartphone to more easily control the lights in the home. Some examples of services include registration, discovery, data management, group management, subscription/notification etc

- The smartphone hosts an application used to remotely control the lights in the home and supports the following capabilities:

  - Discovery of lights deployed in the home.

  - Sending commands to change light states i.e. ON and OFF.

  - Retrieval of light states.

- M2M Authentication Function (MAF) is used when employing MAF-based Security Association Establishment (SAE) between field nodes and infrastructure nodes. When using Pre-Shared Key or Certificate-based SAE, the MAF is not required.

Figure 5.1 Overview of remote lights control use case