| Input Contribution |
| --- |
| Meeting ID* | SEC 27 |
| Title:* | Functional architecture for Security Developer’s Guide TR-0038 |
| Source:* | Norihiro Okui, KDDI, no-okui@kddi.com |
| Uploaded Date:* | 2017-02-16 |
| Document(s) Impacted* | TR-0038 v0.0.1 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | include the text proposed in this contribution into TR-0038. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution provides a functional architecture for security developer guide.

======== Text proposed for TR-0038 starts here =============================

# 6	Functional architecture

This clause describes how the different components of this use case can be represented by corresponding oneM2M architectural entities as shown in figure 6.1.

Figure 6.1 oneM2M functional architecture of remote door locks control use case

An IN-CSE is hosted in the cloud by the oneM2M Service Provider and a MN-CSE is hosted on the Home Gateway. Applications and MAF used in the current use case are classified as follows:

- ADN-AE1: an application embedded in Front Door Lock with capabilities to control Front Door Lock and interact with the home gateway MN-CSE through Mca reference point;

- ADN-AE2: an application embedded in Back Door Lock with capabilities to control Back Door Lock and interact with the home gateway MN-CSE through Mca reference point;

- ADN-AE3: an application embedded in the smartphone device with capabilities to interact directly with the oneM2M service platform IN-CSE through Mca reference point used to remotely control Front Door Lock and Back Door Lock;

- MN-AE: a gateway application embedded into the home gateway that interacts with the MN-CSE through Mca reference point.

- MAF: M2M Authentication Function assigns symmetric keys to MAF clients on the IN-CSE and the ADN-AE3 through Mmaf reference point.