| Input Contribution |
| --- |
| Meeting ID* | SEC #28 |
| Title:* | Remote Security Provisioning Issue for Decentralized Authentication |
| Source:* | Jie Shi, Huawei, shi.jie1@huawei.com Guilin Wang, Huawei, wang.guilin@huawei.com Yanjiang Yang, Huawei, yang.yanjiang@huawei.com |
| Date:* | 2017-03-15 |
| Input related to* | TR-0041 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS-0003 |
| Decision requested or recommendation:* | It is proposed to agree the content in this contribution |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### ----------------------start of change 1 ----------------------------------------------

# 6	Issues and Requirements

Editor’s Note: This clause provides some use cases and/or some general description about security issues related to decentralized authentication.

6.1 Decentralized Authentication Requirement

Clause 6.5 of TR-0026, Vehicular Domain Enabler, is “Use Cases for Electronic Toll Collection (ETC) service”. Two security requirements are set out in 6.5.10 of TR-0026 as follows:

…

- The M2M System shall enable each of many M2M devices to perform mutual authentication with each of many M2M gateways.

- The M2M System shall enable mutual authentication of M2M devices and M2M gateways in a timely manner.

Fulfilling these two requirements demands an efficient and flexible decentralized authentication solution for peer-to-peer communications.

6.2 Remote Security Provisioning Issue for Decentralized Authentication

In order to perform decentralized authentication, the M2M System needs to provide mechanism of remote security provisioning to entities that require authentication.

### ----------------------end of change 1 -------------------------------------------------