| CHANGE REQUEST |
| --- |
| Meeting ID:* | SEC 29 |
| Source:* | Yanjiang Yang, Huawei, yang.yanjiang@huawei.com Jie Shi, Huawei, shi.jie1@huawei.com Guilin Wang, Huawei, wang.guilin@huawei.com |
| Date:* | 2017-05-23 |
| Reason for Change/s:* | Algorithm details for the existing solutions |
| CR against: Release* | <Release> Only ONE Release shall be indicated |
| CR against: WI* | Active WI-0066 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TR-0041 and V0.2.0 |
| Clauses * | 7.1.2 and 7.1.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TR-0041 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present CR proposes algorithm details for the existing solution of decentralized authentication.

### -----------------------Start of change 1-------------------------------------------

# 7	Solutions

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 7.1.2 Detailed Solution

In this framework, an IBC credential is provisioned to each entity, and two entities authenticate each other using (D)TLS handshake with PSK ciphersuite.

Figure 7.1.2-1 shows the sequence of events in this decentralized authentication framework using IBC credentials, wherein “Entity A” and “Entity B” could be either a CSE or an AE.

Figure 7.1.2-1: The sequence of events in decentralized authentication using IBC credentials

Credential Configuration: IBC credentials (IdA, SkA, MPK) and (IdB, SkB, MPK) are provisioned to entity A and entity B respectively, where IdA and IdB are the identities of entity A and entity B respectively, SkA and SkB are the private keys corresponding to IdA and IdB respectively, and the MPK is the master public key which is a public system parameter. Details of IBC credentials and their use in (D(TLS)-PSK handshake will be given in Clause 7.1.3.

Association Security Handshake: The entities shall perform a (D)TLS PSK handshake with IBC credentials to establish a secure session. The details are described as follows, where unless specified, TLS messages remain the same as in the original (D)TLS PSK handshake.

- Entity A initiates TLS with B using a TLS PSK ciphersuite, i.e., Entity A sends a TLS ClientHello message with PSK ciphersuite to entity B.

- Entity B returns TLS message ServerKeyExchange, in which the psk_identity_hint in ServerKeyExchange is set to IdB.

- After receiving ServerKeyExchange message, entity A retrieves IdB, computes a key K = KeyGen(IdB, SkA, MPK) and sets TLS psk parameter to be K, which will be used to authenticate entity B. Here, the function KeyGen can be implemented using different techniques, and two particular implementations are described shortly.

- Entity A sends TLS message ClientKeyExchange and Finished, where the psk_identity in ClientKeyExchange is set to IdA;

- After receiving ClientKeyExchange, entity B retrieves IdA, computes a Key K = KeyGen(IdA, SkB, MPK), and sets TLS psk parameter to be K, which will be used to authenticate entity A. Here, the function KeyGen can be implemented using different techniques, and two particular implementations are described shortly.

- Entity B sends TLS message Finished to A and completes the TLS PSK handshake.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 7.1.3 Algorithmic Details

The IBC credential and the KeyGen algorithm based on the Elliptic Curve-Based Certificateless Signatures specified in [i.2] is provided.

7.1.3.1 Master Public Key

PKG, equivalent to KMS (Key Management Service) in [i.2], is responsible for establishing MPK and MSK in a setup phase. MPK includes the Static Parameters and the Community Parameters defined in Clause 4 of [i.2]. For the purpose of exposition, the relevant Static Parameters in [i.2] are listed in the following table.

Table 7.1.3.1-1 Static Parameters

| N | A security parameter; the size in bits of the prime p over which elliptic curve cryptography is to be performed. |
| --- | --- |
| P | A prime number of size n bits. The finite field with p elements is denoted F_p |
| E | An elliptic curve defined over F_p, having a subgroup of prime order q |
| B | An element of F_p, where E is defined by the formula y^2 = x^3 - 3*x + B modulo p |
| G | A point on the elliptic curve E that generates the subgroup of order q |
| Q | The prime q is defined to be the order of G in E over F_p |
| hash | A cryptographic hash function mapping arbitrary strings to strings of N octets, where N = Ceiling(n/8) is the number of octets output by the hash function |

The Community Parameters in [i.2] are KPAK, which is the KMS Public Authentication Key. KPAK is derived from the KSAK (KMS Secret Authentication Key) in KMS as KPAK = [KSAK]G, where the KSAK is chosen to be a random secret non-zero integer modulo q and is kept secret to the KMS. The MSK is KSAK.

As a result, MPK = (n, p, E, B, G, q, Hash, KPAK) and MSK = (KSAK).

7.1.3.2 IBC Credential

In Clause 5.1 [1.2], user key material is defined as a (SSK, PVT) pair, where SSK is Secret Signing Key and PVT is Public Validation Token. The SSK is kept secret, but the PVT does not need to be kept secret. The algorithm to generate (SSK, PVT) pair is defined in Clause 5.1.1 of [i.2] and specified as follows.

Let IDU  be the identifier of an entity U. A (SSKU, PVTU) pair is constructed from IDA by KMS through the following procedures:

- Choose vU, a random (ephemeral) non-zero element of F_q;

- Compute PVTU = [vU]G;

- Compute a hash value HSU = hash(G || KPAK || IDU|| PVTU), an N-octet integer;

- Compute SSKU = (KSAK + HSU * vU) modulo q;

- If either the SSKU or HSU is zero modulo q, the KMS erases the SSKU and aborts or restart the procedure with a fresh value of vU;

- Output the (SSKU, PVTU) pair. The KMS then erases the value v.

Given (SSKU, PVTU) for entity U, the IBC credential (IdU, SkU, MPK) for entity U is specified to be IdU = (IDU, PVTU) and SkU = SSKU.

7.1.3.2 KeyGen Algorithm

Let entity A and entity B in Figure 7.1.2-1 have IBC credentials (IdA = (IDA,PVTA), SkA = SSKA, MPK) and (IdB = (IDB,PVTB), SkB = SSKB, MPK), respectively, where PVTA = [vA]G, SSKA = KSAK + HSA*vA modulo q, PVTB = [vB]G, SSKB = KSAK + HSB*vB modulo q, with vA and vB being two random non-zero element of F_q, HSA =  hash(G||KPAK||IDA||PVTA) and HSB = hash(G||KPAK||IDB||PVTB).  The key generation function is defined as follows.

KeyGen for A

Input: IdB = (IDB, PVTB), SkA = (KSAK + HSA*vA) modulo q, MPK

Output: KA – an elliptic curve point

- Parse IdB into IDB and PVTB;

- Compute HSB = hash(G||KPAK||IDB||PVTB);

- Compute TMP = KPAK + [HSB]PVTB;

- Compute KA = [SSKA]TMP;

- Output KA.

KeyGen for B

Input: IdA = (IDA,PVTA), SkB = (KSAK + HSB*vB) modulo q, MPK

Output: KB – an elliptic curve point

- Parse IdA into IDA and PVTA;

- Compute HSA = hash(G||KPAK||IDA||PVTA);

- Compute TMP = KPAK + [HSA]PVTA;

- Compute KB = [SSKB]TMP;

- Output KB.

Note: It is obvious that KA = KB, as KA = [SSKA]TMP = [SSKA](KPAK + [HSB]PVTB) = [(KSAK + HSA*vA][ KSAK + HSB*vB]G and KB = [SSKB]TMP = [SSKB](KPAK + [HSA]PVTA) = [(KSAK + HSB*vB][ KSAK + HSA*vA]G;

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 7.1.4 Evaluation

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?