| Input Contribution |
| --- |
| Meeting ID* | TP#34 |
| Title:* | TR-0050 Key issue 2 of Security Area #1 |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn |
| Date:* | 2018-03-12 |
| Input related to* | WI-0077 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0055 Attribute Based Access Control Policy, V0_1_0 |
| Decision requested or recommendation:* | Approve the proposed text into the TR. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes a key issue for the “Security Area #1: Attribute Based Access Control Policy”.

### -----------------------Start of change 1---------------------------------------------

## 6.2	Key Issues

### 6.2.x	Key Issue #1.y: Support more policy combining algorithms

#### 6.2.x.1	Key issue details

Since the access control policy scheme used in oneM2M System is based on Access Control List (ACL), the logical relationship between the data elements in accessControlOriginators parameter is “OR”, i.e. “permit-override”. This limits the expressive capability of access control policy. For example, it cannot specify that an AE/CSE that has a role can perform an operation on a resource because the logical relationship between the AE/CSE and the role in current access control scheme is “OR”.

Multiple access control policies can be associated to one resource in oneM2M System. Currently, only one policy combining algorithm, i.e. “permit-override”, is supported. It seems that more policy combining algorithms should be supported. For example, when multiple stakeholders are involved, there could be a case that requires one can access a resource only when it is permitted by all access control policies specified by the different stakeholders respectively. In this case a policy combining algorithm “deny-override” should be supported. This algorithm specifies that an access request can be permitted only when it is permitted by all applicable access control policies.

Current access control scheme cannot specify a blacklist. In some access control scenarios using blacklists may be more appropriate than a white list, e.g. to exclude a small set of subjects.

#### 6.2.x.1	Potential security requirements

The oneM2M system should enable more access control policy combining algorithms such as OR and/or NOT.

### 6.2.m	Key Issue #1.m: <key issue name>

Editor's Note: Key issues within the security area are not in any particular order but they are added incrementally (m = 1, 2, 3…) when new key issue is identified.

#### 6.2.m.1	Key issue details

Editor's Note: This clause will describe the key issue.

<Text>

#### 6.2.m.2	Potential security requirements

Editor's Note: This clause will describe the potential requirements arising from the key issue.

<Text>

### -----------------------End of change 2---------------------------------------------