| Input Contribution |
| --- |
| Meeting ID* | TP#34 |
| Title:* | TR-0050 Key issue 1 of Security Area #2 |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn |
| Date:* | 2018-03-12 |
| Input related to* | WI-0077 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0055 Attribute Based Access Control Policy, V0_1_0 |
| Decision requested or recommendation:* | Approve the proposed text into the TR. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes a key issue for the “Security Area #2: Enhanced Privacy Policy Enforcement”.

### -----------------------Start of change 1---------------------------------------------

## 6.2	Key Issues

Editor's Note: This clause will contain the key issues that need to be addressed on each security area.

### 6.2.x	Key Issue #1.y: Support privacy policy

#### 6.2.x.1	Key issue details

Privacy Policy is an access control policy used to prevent the disclosure of privacy information to unauthorized persons. In many cases privacy policies may act as filters that filter out privacy information in the original data before the data is transferred to the requesters instead of reject the request.

Privacy policy can be enforced in different ways based on the access control architecture adopted by a system. A typical way is that the privacy is integrated with normal access control policy. Another way is that the privacy policy is implemented as a separately access control policy that will filter out the data that is concerned by the privacy policy from the data that has been agreed by the normal access control policy.

For the first method, the privacy policy could be implemented by the existing access control policy in the oneM2M System. The drawback of this method is that if any data is concerned by the privacy policy, the whole request will be rejected. If the privacy policy is implemented as a data filter, the privacy policy will only need to filter out the data concerned by the privacy policy instead of blocking the whole request. The second method may be more convenience than the first method in some application scenarios. This approach may be more convenient, especially if the privacy policy is allowed to change dynamically. For example, privacy policy is generated according to user’s privacy preference.

In oneM2M System, privacy policies are supported through Privacy Policy Management Architecture (PPM) in oneM2M System. The PPM may acts as a PDP or PRP or DAS Server. When the PPM acts as a PDP or DAS Server, the returned value is an access control; decision. When the PPM acts as a PRP, the returned value is an access control policy. In any cases, the access control policies only used for making access control decisions. None of them can be used for data filter purpose. Therefore, the current oneM2M privacy protection mechanism belongs to the first privacy policy enforcement mechanism mentioned above.

As we discussed in the previous discussion, this privacy policy enforcement approach is more suitable for many scenarios.

In order to support this new privacy policy enforcement mechanism, the following implementation issues should be addressed:

Privacy policy scheme that specifies the privacy policy that acts as a filter.

How the privacy policy is provisioned to the privacy policy enforcement point, i.e. the Hosting CSE.

How the privacy policy is enforced in the privacy policy enforcement point, i.e. the Hosting CSE.

#### 6.2.x.1	Potential security requirements

The oneM2M System should be able to filter out privacy-related data before sending data to the Originator.

The oneM2M System should be able to enforce privacy policies in the hosing CSE.

The oneM2M System should be able to provide privacy policies to the hosting CSE.

### 6.2.m	Key Issue #1.m: <key issue name>

Editor's Note: Key issues within the security area are not in any particular order but they are added incrementally (m = 1, 2, 3…) when new key issue is identified.

#### 6.2.m.1	Key issue details

Editor's Note: This clause will describe the key issue.

<Text>

#### 6.2.m.2	Potential security requirements

Editor's Note: This clause will describe the potential requirements arising from the key issue.

<Text>

### -----------------------End of change 2---------------------------------------------