| Input Contribution |
| --- |
| Meeting ID* | TP#34 |
| Title:* | TR-0050 Key issue 1 of Security Area #3 |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn |
| Date:* | 2018-03-12 |
| Input related to* | WI-0077 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0055 Attribute Based Access Control Policy, V0_1_0 |
| Decision requested or recommendation:* | Approve the proposed text into the TR. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes a key issue for the “Security Area #3: Heterogeneous Access Control Policy Integration”.

### -----------------------Start of change 1---------------------------------------------

## 8.2	Key Issues

### 8.2.x	Key Issue #3.y: Heterogeneous access control policy integration

#### 8.2.x.1	Key issue details

This TR investigates some newly defined access control policies that may enhance current oneM2M access control system, e.g. the attributed based access control policy developed in clause 6 and the privacy policy developed in clause 7. In order to support the newly defined access control policies, the following issues should be addressed:

How the newly defined access control policies are stored in oneM2M System.

How the newly defined access control policies are used in oneM2M System.

How the newly defined access control policies can work with the existing access control policies in oneM2M System.

#### 8.2.x.2	Potential security requirements

The enhanced access control system should be backward compatible with the existing access control system.

### 8.2.m	Key Issue #3.m: <key issue name>

Editor's Note: Key issues within the security area are not in any particular order but they are added incrementally (m = 1, 2, 3…) when new key issue is identified.

#### 8.2.m.1	Key issue details

Editor's Note: This clause will describe the key issue.

<Text>

#### 8.2.m.2	Potential security requirements

Editor's Note: This clause will describe the potential requirements arising from the key issue.

<Text>

### -----------------------End of change 2---------------------------------------------