| CHANGE REQUEST |
| --- |
| Meeting ID:* | SEC 34.2 |
| Source:* | François Ennesser, Gemalto, francois.ennesser@gemalto.com |
| Date:* | 2018-04-02 |
| Reason for Change/s:* | TS-0016 finalisation |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active WI-0021 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0016 v0.9.0 |
| Clauses * | 9, 7.3.0, 7.2.2-4, 7.5.2.0 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

At TP 34 we identified the need to reformat the lists in Clause 9 as tables to align with TS-0004, and to add the reference to the XSD file defining the common resource types that are applicable to the Mcs interface.

### -----------------------Start of change 1-------------------------------------------

### 7.3.0	Overview

An <SE> resource shall represent information about a Secure Environment available in a node. There could be multiple <SE> resources in one node.

One Secure Environment may be represented in the <CSEbase> resource and multiple <AE> resources of that node. Concurrent accesses to the Secure Environment are resolved in the SE abstraction layer.

Common data types applicable to the Mcs interface are inherited from TS-0004 [14].

## The data types for the specific resource attributes specified in this clause are listed in the following subclauses and defined in the following file:

## SENV-commonTypes-v0_9_0.xsd

## Applicable values for resource attributes and for enumerating Mcs resources are detailed in clause 9. Short names for attributes and resource types are provided in clause 10.

The <SE> resource shall contain the child resources specified in table 7.3.0-1.

Table 7.3.0-1: Child resources of <SE> resource

| Child Resources of <SE> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| memory | <mgmtObj> as defined in the specialization [memory] | 0..1 | This resource provides the non volatile memory information of the Secure Environment. See clause D.4. of [2] |
| firmware | <mgmtObj> as defined in the specialization [firmware] | 0..n | This resource describes the information about the firmware of the Secure Environment include name, version etc. See clause D.2 of [2]. |
| software | <mgmtObj> as defined in the specialization [software] | 0..n | This resource describes the information about the software of the Secure Environment. See clause D.3 of [2]. |
| deviceInfo | <mgmtObj> as defined in the specialization [deviceInfo] | 0..n | The resource contains information about the Secure Environment, like identity, manufacturer and model number, if applicable. See clause D.8 of [2]. |
| SEReboot | <mgmtObj> as defined in the specialization [SEReboot] | 0..n | The resource is the place to reboot the Secure Environment, if it is a rebootable hardware. In the case of secure elements there would be two resources, one for a cold reset and one for a warm reset of the secure element, defined in ISO/IEC 7816-3 [7]. |
| accessControlPolicy | <accessControlPolicy> | 0..n | The Access Control Policies (ACPs) shall be used by the SE to control access to the resources |
| sensitiveDataObject | <sensitiveDataObject> | 0..n | See clause 7.4.1 |
| cipher | <cipher> | 0..n | See clause 7.5.1 |
| rand | <rand> | 0..n | See clause 7.5.2 |
| hash | <hash> | 0..n | See clause 7.5.3 |
| signature | <signature> | 0..n | See clause 7.5.4 |
| secureConnection | <secureConnection> | 0..n | See clause 7.6.1 |
| identity | <identity> | 0..n | See clause 7.7.1 |

The <SE> resource shall contain the attributes specified in table 7.3.0-2.

Table 7.3.0-2: Attributes of <SE> resource

| Attributes of <SE> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| creationTime | 1 | RO | Time/date of creation of the resource. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. |
| SEType | 0..1 | RO | See table 7.2.1-2 |
| m2mSeID | 1 | WO | See tables 7.2.1-1 and 7.2.1-2 |
| securityLevel | 1 | WO | See clause 6.2 |
| supportedResourceType | 1 (L) | RW | List of the resource types which are supported in the SE. |
| e2eSecInfo | 0..1 (L) | RW | Indicates the end-to-end security capabilities |
| hostedCSELink | 0..1 | RW | This attribute allows to find the <CSEBase> resource representing the CSE that is residing on the Secure Environment that is represented by this <se> resource. The attribute contains the resource ID of that <CSEBase> resource. |
| hostedAELinks | 0..1 (L) | RW | This attribute allows to find the AEs hosted by this Secure Environment. The attribute contains a list of resource identifiers of <AE> resources representing the AEs residing on the specific Secure Environment that is represented by the current <se> resource. |

Table 7.3.0-3: Data types of <SE> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| SEType | O | O | senv:SEType |
| securityLevel | M | NP | senv:securityLevel |
| m2mSeID | M | NP | m2m:ID |
| supportedResourceType | O | O | m2m:resourceType |
| e2eSecInfo | O | O | m2m:e2eSecInfo |
| hostedCSELink | O | O | m2m:ID |
| hostedAELinks | O | O | m2m:ID |

### 7.3.1	Resource SEReboot

The [SEReboot] resource shall be used to reboot a Secure Environment. The [SEReboot] resource is a specialization of the <mgmtObj> resource.

The [SEReboot] resource shall contain the child resources specified in table 7.3.1-1.

Table 7.3.1-1: Child resources of [SEReboot] resource

| Child Resources of [SEReboot] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 of oneM2M TS-0001 [2] where the type of this resource is described. |
| [variable] | <semanticDescriptor> | 0..n | See clause 9.6.30 of oneM2M TS-0001 [2]. |

The [SEReboot] resource shall contain the attributes specified in table 7.3.1-2.

Table 7.3.1-2: Attributes of [SEReboot] resource

| Attributes of [seReboot] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| resourceName | 1 | WO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| parentID | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| expirationTime | 1 | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| creationTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| Labels | 0..1(L) | RW | See clause 9.6.1.3 of oneM2M TS-0001 [2]. |
| mgmtDefinition | 1 | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. This attribute shall have the fixed value "seReboot". |
| objectIDs | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| objectPaths | 0..1 (L) | WO | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| Description | 0..1 | RW | See clause 9.6.15 of oneM2M TS-0001 [2]. |
| rebootType | 1 | RO | The type of reboot supported by the Secure Environment. This attribute is a specialization of [objectAttribute] attribute. Type of reboots could be such as Cold Reset or Warm Reset as defined in ISO/IEC 7816-3 [7]. |
| SEReboot | 1 | RW | The action that allows rebooting the device. The action is triggered by assigning value "TRUE" to this attribute. This attribute is a specialization of [objectAttribute] attribute. |

Table 7.3.1-3: Data types of <SEReboot> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| RebootType | M | NP | senv:RebootType |
| SEReboot | O | O | xs:boolean |

## 7.4	Sensitive Data Storage

### 7.4.1	<sensitiveDataObject> resource

Secure Environments shall provide a service to store and protect sensitive data. Sensitive data objects are represented as SE-resources and are created and managed within the Secure Environment. Requests to SE-resources are using absolute addressing. A <sensitiveDataObject> resource shall represent sensitive data and related information owned by a creator.

Attributes in <sensitiveDataObject> are shown in table 7.4-1.

Table 7.4-1: Attributes of <sensitiveDataObject> resource

| Attributes of <sensitiveDataObject> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| Creator | 1 | RO | The AE-ID or CSE-ID of the AE or CSE creating the resource. |
| currentByteSize | 1 | RO | Current size in bytes of sensitive data. |
| sensitiveData | 1 | RW | Contains sensitive data and required information to access and manage sensitive data owned by a dedicated creator |
| accessControlPolicyID | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs value is configured, the accessControlPolicyIDs of the parent resource shall be applied for privilege checking. |

Table 7.4-2: Data types of <sensitiveDataObject> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| currentByteSize | M | NP | xs:nonNegativeInteger |
| sensitiveData | O | O | xs:byte |
| creator | M | NP | m2m:ID |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 7.2.2	Differences between Mcs and Mcc/Mca reference points

The Mcs reference point is a simple variant of the Mcc/Mca reference points specifying the interaction of CSEs and AEs with secure environments.

An <SE> resource shall represent information about a Secure Environment available in a node. There could be multiple <SE> resources in one node. Secure Environments are represented in <CSEbase> resources and <AE> resources as <SE> child resources.

The present document has no further impact on the specification oneM2M TS-0001 [2] and has no impact on the specification oneM2M TS-0004 [14]. However, the Mcs reference point uses much of the specification in oneM2M TS-0004 [14] and in particular allows use of the WebSocket binding in oneM2M TS-0020 [18]. Though the other bindings, i.e. the HTTP binding in oneM2M TS-0008 [15], the CoAP binding in oneM2M TS-0009 [16] and the MQTT binding in oneM2M TS-0010 [17], remain applicable, they are not so relevant in the context of a node implementation.

The Mcs reference point incorporates the following concepts from the Mcc/Mca reference points:

The concept of operations acting on resources.

The resource addressing from Mcc/Mca is used.

The universal attributes and some common attributes of resources.

The Mcs reference point differs from Mcc/Mca in the following ways:

The CSE/AE can only communicate directly with the secure environment – there are no transited CSEs. Only Blocking Mode communication method is supported.

The <subscription> resource and NOTIFY operations are not supported.

The registration is conducted by the creation of the <SE> child resource in the corresponding <CSEbase> resource or <AE> resource, respectively. An AE needs to be registered at the CSE to be able to access the SE.

The Mcs interface involves AE or CSE located on the same node as the SE abstraction layer, hence Security Association Establishment does not apply as such and can be superseded by implementation dependent mechanisms.

There are no announced resources.

## Common data types are inherited from clause 6.3 of [14]. The present document does not mention optional common attributes that are not used over Mcs.

## 7.2.3	Namespaces used for resource and data types

Representations of resources applicable to the Mcs Interface employ the namespace identifier "senv:" for global XML elements associated with a resource type. Data types of the attributes and complex-type elements of these resource types may use any of the name space identifiers listed in table 7.2.3-1

Any data types of XML elements defined for use in present document shall be one of name spaces in table 7.2.4-1.

Table 7.2.3-1: Namespaces applicable to resource types defined in the present document

| Name space | Prefix | Name space definition | Types defined in |
| --- | --- | --- | --- |
| Secure Environment | senv: | http://www.onem2m.org/xml/secureEnvironment | the present document and TS-0003 [2] |
| oneM2M protocol CDT | m2m: | http://www.onem2m.org/xml/protocol | TS-0004 [3] |
| Device Configuration | dcfg: | http://www.onem2m.org/xml/deviceConfig | TS-0022 [9] |

## 7.2.4	Mcs Resource type definitions

The files defining the resource types of Mcs specific resources are given in table 7.2.4-1.

Table 7.2.4-1: Resource type definitions

| Resource Type | XSD File Name |
| --- | --- |
| algorithmSpecificParameter | SENV-algorithmSpecificParameter-v0_9_0.xsd |
| cipher | SENV-cipher-v0_9_0.xsd |
| connectionInstance | SENV-connectionInstance-v0_9_0.xsd |
| hash | SENV-hash-v0_9_0.xsd |
| identity | SENV-identity-v0_9_0.xsd |
| Rand | SENV-rand-v0_9_0.xsd |
| secureConnection | SENV-secureConnection-v0_9_0.xsd |
| sensitiveDataObject | SENV-sensitiveDataObject-v0_9_0.xsd |
| SEReboot | SENV-SEReboot-v0_9_0.xsd |
| SE | SENV-SE-v0_9_0.xsd |
| signature | SENV-signature-v0_9_0.xsd |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 7.5	Sensitive Cryptographic Functions

### 7.5.1	<cipher> resource

#### 7.5.1.0	Introduction

Secure Environments shall provide a service for cryptographic operations. A <cipher> resource shall represent sensitive data and related information owned by a creator.

The <cipher> resource shall contain the child resources specified in table 7.5.1-1.

Table 7.5.1-1: Child resources of <cipher> resource

| Child Resources of <cipher> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| encrypt | <encrypt> | 1 | See clause 7.5.1.2 |
| decrypt | <decrypt> | 1 | See clause 7.5.1.3 |
| generateKey | <generateKey> | 0..1 | See clause 7.5.1.4 |
| algorithmSpecificParameter | <algorithmSpecificParameter> | 0..1 | See clause 7.5.1.5 |

Attributes in <cipher> are shown in table 7.5.1-2.

Table 7.5.1-2: Attributes of <cipher> resource

| Attributes of <signature> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| sensitiveData | 0..1 | RW | Message to be either encrypted or decrypted . |
| currentByteSize | 1 | RW | Current size in bytes of sensitive data. |
| maxByteSize | 1 | RO | Maximum size in bytes of sensitive data. |
| algorithm | 1 | WO | Contains the algorithm type of the resource instance. |
| keyData | 0..1 | WO | Contains the value of the key. |
| calculatedData | 0..1 | RO | Contains the result of a cipher operation. |

Table 7.5.1-3: Data types of <cipher> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| sensitiveData | O | O | xs:byte |
| algorithm | M | NP | senv:cipherAlgotrithm |
| keyData | O | NP | xs:byte |
| currentByteSize | O | O | xs:nonNegativeInteger |
| maxByteSize | M | NP | xs:nonNegativeInteger |
| calculatedData | NP | NP | xs:byte |

The following types are defined for the algorithm attribute:

ALG_AEAD_AES_128_GCM: The AEAD_AES_128_GCM authenticated encryption algorithm works as specified in IETF RFC 5116 [8], using AES-128 as the block cipher, by providing the key, nonce, and plaintext, and associated data to that mode of operation.

ALG_AEAD_AES_256_GCM: This algorithm is identical to AEAD_AES_128_GCM, but with the following differences: K_LEN is 32 octets, instead of 16 octets, and AES-256 GCM is used instead of AES-128 GCM.

ALG_AEAD_AES_128_CCM: The AEAD_AES_128_CCM authenticated encryption algorithm works as specified in IETF RFC 5116 [8], using AES-128 as the block cipher, by providing the key, nonce, associated data, and plaintext to that mode of operation.

ALG_AEAD_AES_256_CCM: This algorithm is identical to AEAD_AES_128_CCM, but with the following differences: K_LEN is 32 octets, instead of 16, and AES-256 CCM is used instead of AES-128 CCM.

ALG_AEAD_AES_128_CCM_8: The AEAD_AES_128_CCM_8 authenticated encryption algorithm is identical to the AEAD_AES_128_CCM algorithm (see section 5.3 of IETF RFC 5116 [8]), except that it uses 8 octets for authentication, instead  of the full 16 octets used by AEAD_AES_128_CCM (see Section 6.1 of IETF RFC 6655 [9]).

ALG_AEAD_AES_256_CCM_8: The AEAD_AES_256_CCM_8 authenticated encryption algorithm is identical to the AEAD_AES_256_CCM algorithm (see section 5.4 of IETF RFC 5116 [8]), except that it uses 8 octets for authentication, instead of the full 16 octets used by AEAD_AES_256_CCM (see section 6.2 of IETF RFC 6655 [9]).

ALG_AES_BLOCK_128_CBC_NOPAD : Cipher algorithm ALG_AES_BLOCK_128_CBC_NOPAD provides a cipher using AES with block size 128 in CBC mode and does not pad input data.

ALG_AES_CBC_ISO9797_M1: Cipher algorithm ALG_AES_CBC_ISO9797_M1 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the ISO 9797 [10] method 1 scheme.

ALG_AES_CBC_ISO9797_M2: Cipher algorithm ALG_AES_CBC_ISO9797_M2 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the ISO 9797 [10] method 2 (ISO 7816-4 [i.3], EMV'96) scheme.

ALG_AES_CBC_PKCS5: Cipher algorithm ALG_AES_CBC_PKCS5 provides a cipher using AES with block size 128 in CBC mode, and pads input data according to the PKCS#5 scheme.

[...]

#### 7.5.1.5	<algorithmSpecificParameter> Resource

The <algorithmSpecificParameter> contains parameter required for the different algorithm.

The <algorithmSpecificParameter> resource shall inherit the same access control policies of the parent <cipher> resource, and shall not have its own accessControlPolicyIDs attribute.

Attributes in <algorithmSpecificParameter> are shown in table 7.5.1.5-1.

Table 7.5.1.5-1: Attributes of <algorithmSpecificParameter> resource

| Attributes of <algorithmSpecificParameter> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| initialVector | 0..1 | RW | AES algorithms, except for ALG_AES_CMAC_128, in CBC mode expect a 16-byte parameter value for the initialization vector (IV). |
| nonce | 0..1 | RW | a value for the nonce as expected by AEAD algorithm |
| associatedData | 0..1 | RW | The associated data for AEAD algorithm, which contains the data to be authenticated, but not encrypted. |
| label | 0..1 | RW | "EXPORTER-oneM2M-Bootstrap" for TLS Key Export for Enrolment Key. "EXPORTER-oneM2M-Connection" for TLS Key Export for M2M Secure Connection Key. |

Table 7.5.1.5-2: Data types of <algorithmSpecificParameter> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| initialVector | O | O | xs:byte |
| nonce | O | O | xs:byte |
| associatedData | O | O | xs:byte |
| label | O | O | senv:cipherLabel |

### 7.5.2	<rand> resource

#### 7.5.2.0	Introduction

A <rand> resource shall represent random data owned by a creator.

The <rand> resource shall contain the child resources specified in table 7.5.2.0-1.

Table 7.5.2.0-1: Child resources of <rand> resource

| Child Resources of <rand> | Child Resource Type | Multiplicity | Description | <randAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| generateRand | <generateRand> | 1 | See clause 7.5.2.2 | None |

Attributes in <rand> are shown in table 7.5.2.0-2.

Table 7.5.2.0-2: Attributes of <rand> resource

| Attributes of <rand> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| randomData | 0..1 | RO | Contains random data which can be retrieved by the creator |
| rngType | 1 | WO | The following types of RNGs can be requested according to ISO/IEC 18031 [13]: pseudo RNG or true (physical) RNG |
| requestedDataSize | 0..1 | RW | Requested amount of randomData in Bytes |

Table 7.5.2.0-3: Data types of <rand> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| randomData | NP | NP | xs:byte |
| rngType | M | NP | senv:rngType |
| requestedDataSize | O | O | xs:nonNegativeInteger |

### [...]

### 7.5.3	<hash> resource

#### 7.5.3.0	Introduction

Secure Environments shall provide a service for calculating hashes. A <hash> resource shall represent sensitive data and related information owned by a creator.

The <hash> resource shall contain the child resources specified in table 7.5.3-1.

Table 7.5.3-1: Child resources of <hash> resource

| Child Resources of <hash> | Child Resource Type | Multiplicity | Description | <hashAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| calculateHash | <calculateHash> | 1 | See clause 7.5.3.2 | None |

Attributes in <hash> are shown in table 7.5.3-2.

Table 7.5.3-2: Attributes of <hash> resource

| Attributes of <hash> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| algorithm | 1 | WO | Specfies the algorithm for the hash |
| message | 0..1 | RW | The message which is to be hashed |
| hashValue | 0..1 | RO | Is the calculated Hash |

Table 7.5.3-3: Data types of <hash> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| algorithm | M | NP | senv:hashAlgorithm |
| message | O | O | xs:byte |
| hashValue | NP | NP | xs:byte |

The following types are defined as algorithm types:

SHA256;

SHA384;

SHA512.

[...]

### 7.5.4	<signature> resource

#### 7.5.4.0	Introduction

Secure Environments shall provide a service for signing messages and verifying signatures. A <signature> resource shall represent sensitive data and related information owned by a creator.

The <signature> resource shall contain the child resources specified in table 7.5.4-1.

Table 7.5.4-1: Child resources of <signature> resource

| Child Resources of <signature> | Child Resource Type | Multiplicity | Description | <signatureAnnc> Child Resource Types |
| --- | --- | --- | --- | --- |
| calculateSignature | <calculateSignature> | 1 | See clause 7.5.4.2 | None |
| verifySignature | <verifySignature> | 1 | See clause 7.5.4.3 | None |
| generateKey | <generateKey> | 0..1 | See clause 7.5.4.4 | None |

Attributes in <Signature> are shown in table 7.5.4-2.

Table 7.5.4-2: Attributes of <signature> resource

| Attributes of <signature> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| message | 0..1 | RW | Message either to be signed or to be used to verify a signature, this could be alternatively a hash value. |
| algorithm | 1 | WO | Contains the algorithm type of the resource instance. |
| keyData | 0..1 | WO | Contains the value of the key. |
| keyInformation | 0..1 | RW | Contains information about the key like a certificate. |
| signature | 0..1 | RW | Contains the signature either to be calculated or to be verified. |
| verificationResult | 0..1 | RO | Contains the result of a signature verification operation.(TRUE or FALSE) |

Table 7.5.4-3: Data types of <signature> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| message | O | O | xs:byte |
| algorithm | M | NP | senv:signatureAlgorithm |
| keyData | O | NP | xs:byte |
| keyInformation | O | O | xs:anyType |
| signature | O | O | xs:byte |
| verificationResult | NP | NP | xs:boolean |

The following types are defined for the algorithm attribute:

ALG_AES_CMAC_128 : Signature algorithm ALG_AES_CMAC_128 generates a 16-byte Cipher-based MAC (CMAC) using AES with blocksize 128 in CBC mode with ISO9797_M2 padding scheme.

ALG_AES_MAC_128_NOPAD :Signature algorithm ALG_AES_MAC_128_NOPAD generates a 16-byte MAC using AES with blocksize 128 in CBC mode and does not pad input data.

ALG_ECDSA_SHA_256 :Signature algorithm ALG_ECDSA_SHA_256 generates a 32-byte SHA-256 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-256 curve specified in the Digital Signature Standards specification NIST FIPS PUB 186-2 [11].

ALG_ECDSA_SHA_384 :Signature algorithm ALG_ECDSA_SHA_384 generates a 48-byte SHA-384 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-384 curve specified in the Digital Signature Standards specification NIST FIPS PUB 186-2 [11].

ALG_ECDSA_SHA_512 :Signature algorithm ALG_ECDSA_SHA_512 generates a 64-byte SHA-512 digest and signs/verifies the digest using ECDSA with the curve defined in the ECKey parameters - such as the P-521 curve specified in the Digital Signature Standards specification NIST FIPS PUB 186-2 [11].

ALG_HMAC_SHA_256 :HMAC message authentication algorithm ALG_HMAC_SHA_256 This algorithm generates an HMAC following the steps found in IETF RFC 2104 [12] using SHA-256 as the hashing algorithm.

ALG_HMAC_SHA_384 :HMAC message authentication algorithm ALG_HMAC_SHA_384 This algorithm generates an HMAC following the steps found in IETF RFC 2104 [12] using SHA-384 as the hashing algorithm.

ALG_HMAC_SHA_512 :HMAC message authentication algorithm ALG_HMAC_SHA_512 This algorithm generates an HMAC following the steps found in IETF RFC 2104 [12] using SHA-512 as the hashing algorithm.

### ------------------------End of change 3 -------------------------------------------

### -----------------------Start of change 4 -------------------------------------------

## 7.6	Secure Connection Establishment

### 7.6.1	<secureConnection> resource

Secure Environments shall provide a service to AEs or CSEs to establish a secure connection to a dedicated communication partner. The <secureConnection> resource shall represent the services offered by the Secure Environment to enable the establishment of a secure connection to a communication partner. The services include the following:

generation of key material within the secure environment that can be used for the establishment of a secure connection by the requesting entity (creator) outside of the secure environment;

acting as secure connection endpoint and sending the data provided by the requesting entity (creator) from within the secure environment with the key material generated and kept inside the secure environment.

The <secureConnection> resource shall contain the child resources specified in table 7.6.1-1.

Table 7.6.1-1: Child resources of <secureConnection> resource

| Child Resources of <secureConnection> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| connectionInstance | <connectionInstance> | 0..n | See clause 7.6.3 |
| generateKey | <generateKey> | 0..1 | See clause 7.6.7 |

Attributes in <secureConnection> are shown in table 7.6.1-2.

Table 7.6.1-2: Attributes of <secureConnection> resource

| Attributes of <secureConnection> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| maxNrOfInstances | 0..1 | RO | Maximum number of direct child <connectionInstance> resources in the <secureConnection> resource. |
| currentNrOfInstances | 0..1 | RW | Current number of direct child <connectionInstance> resource in the <secureConnection> resource. It is limited by the maxNrOfInstances. |
| connectionType | 1 | RW | Contains the type of connection that has to be supported. Supported types are: TLS; DTLS; SMS; E2EKey. |
| keyData | 0..1 | WO | Contains the key material. |
| keyInformation | 0..1 | RW | Specifies the additional information required for the key and the ciphersuite, e.g. Certificates, rootkeys, the public part of keyData. |
| cipherSuite | 0..1 | RW | Specifies the ciphersuites that are supported. Supported cipher suites are given in oneM2M TS-0003 [1]. |

Table 7.6.1-3: Data types of <secureConnection> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| maxNrOfInstances | M | NP | xs:nonNegativeInteger |
| currentNrOfInstances | O | O | xs:nonNegativeInteger |
| connectionType | M | NP | senv:connectionTypeID |
| keyData | O | NP | xs:byte |
| keyInformation | O | O | xs:anyType |
| cipherSuite | O | O | dcfg:TLSCiphersuites |

[...]

### 7.6.3	<connectionInstance> resource

The <connectionInstance> resource represents a data instance in the <secureConnection> resource.

The <connectionInstance> resource inherits the same access control policies of the parent <secureConection> resource, and does not have its own accessControlPolicyIDs attribute.

The services shall include the following:

generation of key material within the secure environment that can be used for the establishment of a secure connection by the requesting entity (creator) outside of the secure environment;

acting as secure connection endpoint and sending the data provided by the requesting entity (creator) from within the secure environment with the key material generated and kept inside the secure environment.

The <connectionInstance> resource shall contain the child resources specified in table 7.6.3-1.

Table 7.6.3-1: Child resources of <connectionInstance> resource

| Child Resources of <connectionInstance> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| algorithmSpecificParameter | <algorithmSpecificParameter> | 0..1 | See clause 7.5.1.5 |
| connect | <connect> | 1 | See clause 7.6.5 |
| send | <send> | 1 | See clause 7.6.6 |

Attributes in <connectionInstance> are shown in table 7.6.3-2.

Table 7.6.3-2: Attributes of <connectionInstance> resource

| Attributes of <connectionInstance> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| destinationURI | 1 | RW | Specifies the end point to which the secure connection shall be established. |
| outgoingPayloadData | 0..1 | RW | Contains the data that has to be sent via the established secure connection. |
| incomingPayloadData | 0..1 | RO | Contains the data received via the established secure connection. |
| negotiatedKey | 0..1 | RO | Contains the negotiated key e.g. the pairwiseE2EKey using TLS Exporter specification (IETF RFC 5705 [6]). |
| negotiatedCipherSuite | 0..1 | RO | Is the cipher suite negotiated between the Secure Environment and the remote entity. |

Table 7.6.3-3: Data types of <connectionInstance> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| destinationURI | M | O | xs:anyURI |
| outgoingPayloadData | O | O | xs:byte |
| incomingPayloadData | NP | NP | xs:byte |
| negotiatedKey | O | NP | xs:byte |
| negotiatedCipherSuite | O | NP | dcfg:TLSCiphersuites |

[...]

## 7.7	Authentication and Identification

### 7.7.1	<identity> resource

Secure Environments shall provide a service to AEs or CSEs to establish an Identity and provide authentication of this Identity. The <identity> resource shall represent the services offered by the Secure Environment to enable the establishment of a secure Identity. The services include the following:

generation of an Identity and associated key material within the secure environment;

using the associated key material for authenticating the generated Identity.

The <identity> resource shall contain the child resources specified in table 7.7-1.

Table 7.7.1-1: Child resources of <identity> resource

| Child Resources of <identity> | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| authenticate | <authenticate> | 0..1 | See clause 7.7.3 |
| generateKey | <generateKey> | 0..1 | See clause 7.7.4 |

Attributes in <Identity> are shown in table 7.7.1-2.

Table 7.7.1-2: Attributes of <identity> resource

| Attributes of <identity> | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | Defines the resource type. |
| resourceID | 1 | RO | Defines an identifier for the resource. This attribute shall be provided by the creator. The creator shall assign a resourceID which is unique within its context. |
| resourceName | 1 | WO | This attribute is the name for the resource that is used for 'hierarchical addressing method' to represent the parent-child relationships of resources. |
| parentID | 1 | RO | This attribute is the resourceID of the parent of this resource. |
| expirationTime | 1 | RW | Time/date after which the resource will be deleted by the Hosting CSE. |
| accessControlPolicyIDs | 0..1 (L) | RW | Is used to control access to the resource. If no accessControlPolicyIDs are provided at the time of creation, the accessControlPolicyIDs of the parent resource is linked to this attribute. |
| creationTime | 1 | RO | Time/date of creation of the resource. The creationTime is set by the CSE hosting the SE when the resource is created. |
| lastModifiedTime | 1 | RO | Last modification time/date of the resource. This attribute is mandatory. The lastModifiedTime value is set by the Hosting CSE when the resource is created,and the lastModifiedTime value is updated when the resource is updated. |
| idName | 1 | WO | Contains the name of the identity. |
| keyData | 0..1 | WO | Contains the value of a key. |
| idData | 0..1 | RW | Contains information associated to the identity and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others public key material, protocol identifier, certificates. |
| originatorAuthenticationData | 0..1 | RW | Contains information provided by the Originator and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others nonces, certificates, signatures. |
| receiverAuthenticationData | 0..1 | RO | Contains information provided by the Receiver and which is necessary for the authentication protocol. The detailed structure depends on the authentication protocol and could comprise among others nonces, certificates, signatures. |

Table 7.7.1-3: Data types of <identity> resource specific attributes

| Name | Request Optionality | Data type |
| --- | --- | --- |
|  | Create | Update |  |
| idName | M | NP | xs:string |
| keyData | O | NP | xs:byte |
| idData | O | O | xs:anyType |
| originatorAuthenticationData | O | O | xs:anyType |
| receiverAuthenticationData | NP | NP | xs:anyType |

### -----------------------End of change 4 -------------------------------------------

### -----------------------Start of change 5 -------------------------------------------

# 9	Resource type definitions for the Mcs reference point

## 9.1	Mcs specific enumeration values of m2m:resourceType

The following values are defined specifically for the Mcs interface, as an extension to applicable values inherited from TS-0004 [14]:

Table 9.1-1: Mcs enumeration values

| Value | Resource type |
| --- | --- |
| 20001 | algorithmSpecificParameter |
| 20002 | cipher |
| 20003 | connectionInstance |
| 20004 | hash |
| 20005 | identity |
| 20007 | rand |
| 20008 | secureConnection |
| 20009 | sensitiveDataObject |
| 20010 | SEReboot |
| 20011 | SE |
| 20012 | signature |

## 9.2	senv:SEType

The values in table 9.2-1 are defined as per table 7.2.1-2:

Table 9.2-1: SEType defined values

| Value | Meaning |
| --- | --- |
| 1 | UICC as per ETSI |
| 2 | GlobalPlatform Secure Element |
| 3 | TEE as per GlobalPlatform |
| 4 | Software cryptographic library |

## 9.3	senv:securityLevel

Thevalues in table 9.3-1 are defined as per clause 6.2:

Table 9.3-1: securityLevel defined values

| Value | Meaning |
| --- | --- |
| 1 | Low security |
| 2 | Medium security |
| 3 | High Security |

## 9.4	senv:rebootType

The values in table 9.4-1 are defined:

Table 9.4-1: rebootType defined values

| Value | Meaning |
| --- | --- |
| 1 | Cold Reset as defined in ISO/IEC 7816-3 [7] |
| 2 | Warm Reset as defined in ISO/IEC 7816-3 [7] |

## 9.5	senv:cipherLabel

The values in table 9.5-1 are defined:

Table 9.5-1: cipherLabel defined values

| Value | Meaning |
| --- | --- |
| 1 | EXPORTER-oneM2M-Bootstrap |
| 2 | EXPORTER-oneM2M-Connection |

## 9.6	senv:cipherAlgorithm

The values in Table 9.6-1 are defined:

NOTE:	Values for AEAD algorithms were taken from IANA with an offset of 1000. Values for other algorithms were taken from JavaCard API.

Table 9.6-1: cipherAlgorithm defined values

| Value | Meaning |
| --- | --- |
| 1001 | ALG_AEAD_AES_128_GCM |
| 1002 | ALG_AEAD_AES_256_GCM |
| 1003 | ALG_AEAD_AES_128_CCM |
| 1004 | ALG_AEAD_AES_256_CCM |
| 1018 | ALG_AEAD_AES_128_CCM_8 |
| 1019 | ALG_AEAD_AES_256_CCM_8 |
| 13 | ALG_AES_BLOCK_128_CBC_NOPAD |
| 22 | ALG_AES_CBC_ISO9797_M1 |
| 23 | ALG_AES_CBC_ISO9797_M2 |
| 24 | ALG_AES_CBC_PKCS5 |

## 9.7	senv:rngType

The values in Table 9.7-1 are defined:

Table 9.7-1: rngType defined values

| Value | Meaning |
| --- | --- |
| 1 | pseudo RNG |
| 2 | True (physical) RNG |

## 9.8	senv:hashAlgorithm

The values in Table 9.8-1 are defined:

Table 9.8-1: hashAlgorithm defined values

| Value | Meaning |
| --- | --- |
| 4 | SHA256 |
| 5 | SHA384 |
| 6 | SHA512 |

NOTE:	These values were taken from the JavaCard API.

## 9.9	senv:signatureAlgorithm

The values in Table 9.9-1 are defined:

NOTE:	These values were taken from the JavaCard API.

Table 9.9-1: signatureAlgorithm defined values

| Value | Meaning |
| --- | --- |
| 49 | ALG_AES_CMAC_128 |
| 18 | ALG_AES_MAC_128_NOPAD |
| 33 | ALG_ECDSA_SHA_256 |
| 34 | ALG_ECDSA_SHA_384 |
| 38 | ALG_ECDSA_SHA_512 |
| 25 | ALG_HMAC_SHA_256 |
| 26 | ALG_HMAC_SHA_384 |
| 27 | ALG_HMAC_SHA_512 |

## 9.10	senv:connectionTypeID

The values in Table 9.10-1 are defined:

Table 9.10-1: connectionTypeID defined values

| Value | Meaning |
| --- | --- |
| 1 | TLS |
| 2 | DTLS |
| 3 | SMS |
| 4 | E2EKey |

# 10	Short Name definitions for the Mcs reference point

### 10.1	Short Names for Mcs specific resource attributes

The mapping between the full names and their shortened form is given in the following subclauses.

These names are case-sensitive. A oneM2M implementation shall use the letter casing given in these clauses.

In protocol bindings, resource attributes names shall be translated into short names shown in table 10.1-1.

Table 10.1-1: Mcs Resource attribute short names

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| SEType | SE | seT |
| securityLevel | SE | seL |
| rebootType | SEReboot | rbT |
| cipherLabel | algorithmSpecificParameter | Clab |
| cipherAlgorithm | cipher | Calg |
| rngType | rand | rgT |
| hashAlgorithm | hash | Halg |
| signatureAlgorithm | signature | Salg |
| connectionType | secureConnection | cnT |

### 10.2	Short Names for Mcs specific resource types

In protocol bindings resource type names shall be translated into short names of Table 10.2-1.

Table 10.2-1: Mcs Resource type short names

| Resource Type Name | Short Name |
| --- | --- |
| SE | Senv |
| SEReboot | Srbt |
| sensitiveDataObject | Sdo |
| cipher | Cph |
| encrypt | Enc |
| decrypt | Dec |
| generateKey | gnK |
| algorithmSpecificParameter | algP |
| rand | Rnd |
| generateRand | gnR |
| hash | Hsh |
| calculateHash | cHsh |
| signature | Sgn |
| calculateSignature | cSgn |
| verifySignature | vSgn |
| secureConnection | Ssc |
| connectionInstance | Isc |
| connect | cnt |
| send | snd |
| identity | Sidn |
| authenticate | Sauth |

### -----------------------End of change 6-------------------------------------------