| Input Contribution |
| --- |
| Meeting ID* | SEC 35 |
| Title:* | Dynamic Access Control Polies |
| Source:* | Flynn Bob, Convida Wireless, Flynn.Bob@convidawireless.com |
| Date:* | 2018-05-13 |
| Input related to* | TS-0050 v0.3.0 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

TR-0050 Atribute Based Access Control Policy

New Issues

### -----------------------Start of change 1-------------------------------------------

### 6.2.3	Key Issue #1.3: Non-Originator Context

#### 6.2.3.1	Key issue details

Editor's Note: This clause will describe the key issue.

Current access control policies depend on the context of the requestor/originator.  For example, one might give authorization to access the door lock if the request comes from an originator when the originator is located close to the house.  Some interesting scenarios can be developed using the context of entities other than the originator.  For example, authorization to access the door lock can be granted only if the home owner is not home.

#### 6.2.3.2	Potential security requirements

Editor's Note: This clause will describe the potential requirements arising from the key issue.

When granting access to an originator the oneM2M System should consider factors or conditions other than just the state of the originator request message. It could also look at the location of another “entity” or the state of some other device.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of new text 2-------------------------------------------

### 6.2.4	Key Issue #1.4: Propagate ACPs

#### 6.2.4.1	Key issue details

Editor's Note: This clause will describe the key issue.

When adding new devices such as sensors or actuators, it should not be difficult to integrate those devices into the applications that manage the systems that those devices are becoming a part of.  For example, adding a new smart lock should be simple to integrate into the smart home application that each family member uses to manage devices within the home. If the lock is located in the main entrance, all members of the family should be able to control the smart lock, however if the lock is located in the garage, the children may not be authorized to access the smart lock. These different authorizations should be easy to configure by considering the context of the configuration of the smart lock.

#### 6.2.4.2	Potential security requirements

Editor's Note: This clause will describe the potential requirements arising from the key issue.

When new resources are created there should be a mechanism to apply default policies other than just assigning authorizations to the originator.  For example, in my home, I want all access to all devices.  However, when a new device registers to the CSE, until my “AE-ID” is added to the resource only the application that created the resource has access to the resources (or ALL entities have access).

### -----------------------End of new text 2-------------------------------------------

### -----------------------Start of new text 3-------------------------------------------

### 6.2.5	Key Issue #1.5: ACPs with limited usage configurations

#### 6.2.5.1	Key issue details

Editor's Note: This clause will describe the key issue.

Access control policies are generally given with “unlimited” usage, meaning that if the policy grants a permission to perform an operation, that operation can be performed as often as desired by the originator that has the permission. It could be desired to allow a more limited policy.  For example, a permission may allow an originator to unlock a door 2 times per day.

#### 6.2.5.2	Potential security requirements

Editor's Note: This clause will describe the potential requirements arising from the key issue.

The oneM2M system should allow configurable limits to the ACP such as a “count”. The CSE should check the “count” before allowing access and then modify the remaining “count” after granting access to an originator. This could limit based on the number of accesses, the amount of data allowed to be accessed, etc.

### -----------------------End of new text 3-------------------------------------------