| Input Contribution |
| --- |
| Meeting ID* | TP#37 |
| Title:* | TR-0050 ABAC Policy Language Model |
| Source:* | Wei Zhou, Datang, zhouwei@catt.cn Yang Liu, CAICT, liuyang7@caict.ac.cn |
| Date:* | 2018-09-17 |
| Input related to* | WI-0077 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TR-0055 Attribute Based Access Control Policy, V0_4_0 |
| Decision requested or recommendation:* | Approve the proposed text into the TR. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This contribution proposes a language model for ABAC policy.

### -----------------------Start of change 1---------------------------------------------

### 6.3.x	Solution #1.y: ABAC Policy Language Model

#### 6.3.x.1	Introduction

The solution provides a language model of the ABAC policy.

#### 6.3.x.2	Solution details

##### 6.3.x.2.1	Policy Language Model

The ABAC policy language model is shown in figure 6.3.x.2-1. The main components of the model are:

Rule primitive,

Rule,

Policy,

Policy set.

These are described in the following sub-clauses.

Figure 6.3.x.2-1: ABAC policy language model

##### 6.3.x.2.2	Rule Primitive

A rule primitive is the most elementary unit of policy. It consists of 3 components:

Operand 1: It can be a single value, or multiple values of the same type, or represented by a function that can get the values at runtime.

Operand 2: It can be a single value, or multiple values of the same type, or represented by a function that can get the values at runtime. The data type of operand 1 and operand 2 should be the same.

Operator: It is a logical operator or a set operator. Logical operator performs logical comparison operation on operand 1 and operand 2, for example, greater than, less than, equal to, and so on. Set operator performs a set comparison operation on operand 1 and operand 2. For example, operand 1 is equal to operand 2, operand 1 is included in operand 2, and so on.

The output of a rule primitive is TRUE or FALSE.

##### 6.3.x.2.3	Rule

A rule is the basic element for evaluating an access request. The main components of a rule are:

A rule constraint: It contains a set of rule primitives. These primitives represent the set of requests to which the rule is intended to apply in the form of a logical expression on attributes in the request. The relation between the primitives could be ‘AND’ and/or ‘OR’.

A condition: It contains a set of rule primitives that represents a Boolean expression that refines the applicability of the rule beyond the predicates implied by rule constraint. Condition may be absent. If it is exist, the associated rule is applicable only when the condition evaluates to TRUE.

An effect: It indicates the consequence of a rule when the rule evaluates to TRUE. Two values are allowed: "Permit" and "Deny".

The output of a rule is "Permit", "Deny" or “Not applicable”.

##### 6.3.x.2.4	Policy

A policy combines multiple rules. The main components of a policy are:

Applicable subjects: Specify the access requesters that apply to this policy.

Applicable resources: Specify the resources that apply to this policy.

A set of rules: Rules are described above.

Rule combining algorithm: Define a procedure for arriving at an authorization decision given the individual results of evaluation of a set of rules.

The output of a policy is "Permit", "Deny" or “Not applicable”.

##### 6.3.x.2.5	Policy Set

A policy set combines multiple policies. The main components of a policy set are:

Applicable subjects: Specify the access requesters that apply to this policy set.

Applicable resources: Specify the resources that apply to this access control policy set.

A set of policies: Policies are described above.

Policy combining algorithm: Define a procedure for arriving at an authorization decision given the individual results of evaluation of a set of policies.

The output of a policy set is "Permit", "Deny" or “Not applicable”.

#### 6.3.x.3	Evaluation

Editor's Note: This clause will contain a variety of evaluations of this solution.

<Text>

### -----------------------End of change 1---------------------------------------------