| Work Item |
| --- |
| Work Item Title:* | oneM2M Interoperability Testing |
| Document Number* | WI-0022 Interoperability_Testing |
| Supporting Members or Partner type 2* | KETI, KCA, NEC, InterDigital |
| Date:* | 2015-03-26 |
| Abstract:* | Proposes a work item to produce an Interoperability Testing Specification of the oneM2M primitives defined in TS-0001 and TS-0004 |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

Title

Interoperability Test Specification(s)

Output

Technical Specifications:

- TS-0013 - Interoperability Testing

Impact

Impact on other Technical Specifications and Technical Reports

No strong direct impact is expected on other Technical Specifications and/or Reports, as most of the work will be performed in a new Technical Specification.

This work is likely to result in direct feedback to the existing Technical Specifications, and possibly even in Change Requests to these deliverables.

Impact on other oneM2M Work Items;

None expected.

Scope

The specification will address the testing of these primitives on the oneM2M interfaces as specified in TS-0001 and TS-0004. The purpose of the interoperability testing is to prove end-to-end functionality between Application Entities and Common Service Entities over the Mca and Mcc reference points

The testing is intended to address the access to resources on local CSE and/or remote CSE.

Although the primitives are defined to be independent of the transport protocol, the tests produced will be run between entities supporting the same protocol binding on each tested interface. This means that the testing needs to be developped based on a dedicated transport protocol.

For this reason, the current proposal is to produce an interoperability Test Specification considering each transport protocol binding .

Testing best practise recommends that interoperability tests are written including some conformance checks on lower protocol, allowing a better debugging. Considering each binding in the Test specification will allow using this test methodology.

In an initial phase of this WI – which is expected to complete within 2 meeting cycles – the limitation of the scope of testing shall be defined. As part of this initial phase, the relevant test configurations of the architecture entities will be selected.The next phase will be to define the individual test descriptions.

It is intended that each test description covers a specific functionality (eg: create a container) that can be tested independently of other functionalities.

Since the test descriptions are only coverying interoperability, it cannot be assumed that conformance with the oneM2M specification is guaranteed.

Informative example

An example of Test Description for container creation on Mca (HTTP and CoAP):

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_07 |
| Objective: | AE creates a container resource in registrar CSE via a container Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> |
| 2 | Check Mca | Primitive | Sent CREATE request contains To: <CSEBase>/<AE>?rty=container Fr: AE-ID Cn: container resource <container> to be created |
|  |  | HTTP | Sent POST request contains Request URI <CSEBase>/<AE>?rty=container Host : Registrar CSE Payload: container resource <container> to be created Content-Type= media-type |
|  |  | CoAP | Sent POST request contains Code = 2(POST) Uri-Path: <CSEBase> Uri-Path: <AE>?rty=container Payload: container resource <container> to be created Content Type option |
|  |  | MQTT | TBD |
| 3 |  | Verify | Check if possible that the <container> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive | Registrar sends response containing: To: AE-ID Fr: CSE-ID Cn: Created <container> |
|  |  | HTTP | Registrar sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container> Payload: Created <container> |
|  |  | CoAP | Registrar sends response containing: Code = 2.01 (2001 Created) Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <contaner> The same Message ID as that of the previous request |
|  |  | MQTT | TBD |
| 5 |  | Verify | AE indicates successful operation |
| 6 |  |  | Repeat step 1-5 creating container resource with short lifetime |
| 7 |  |  | Check the created resource is removed after the expiry of its lifetime |

Schedule

Provide the schedule of tasks to be performed;

| Doc Type | Spec Number | Title | Milestone dates | Primary Responsible | Notes |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |
| TS | 0013 | Interoperability Testing | TP#15 | TP#18 | TP#21 | TP#22 | WG TST |  |

Supporters

KETI, KCA, NEC, InterDigital

Work Item Rapporteurs.

Laurent Velez (ETSI)

History

| Document history |
| --- |
| V0.0.1 | 14 Nov 2014 | Initial proposal |
| V1.0.0 | 19 November 2014 | Uploaded to portal as a permanent document – WI-0022 |
| V1.1.0 | 2 February 2015 | Changed names and numbers of the produced Technical Specifications |
| V1.2.0 | 27 March 2015 | Merged the three deliverables. |