| Work Item |
| --- |
| Work Item Title:* | Interworking with 3GPP Rel-13 MTC feature |
| Document Number* | WI-00xx-3GPP_Rel13_IWK-V1_0_0 |
| Supporting Members or Partner type 2* | Intel, AT&T, ZTE, Telecom Italia, Sierra Wireless?, NEC?, Interdigital?, Huawei?, Alcatel-Lucent?, LG electronics? |
| Date:* | 2015-05-19 |
| Abstract:* | This Work Item is intended to produce a interworking specification between oneM2M IN/MN CSEs and 3GPP Service Capability exposure function (SCEF) defined in 3GPP TS 23.682. |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

Title

Interworking with 3GPP Rel-13 MTC features

Output

A new Technical Report (TR) will be generated to study and analyse interworking options and will identify potential areas of standardization in existing specifications.

Depending on the conclusion of TR, Change Requests to following specification may be needed:

- the Technical Specification TS-0001 on Functional Architecture

Impact

Impact on other Technical Specifications and Technical Reports

See the above paragraph.

Impact on other oneM2M Work Items

None

Scope

As part of Rel-13 work on MTC features, 3GPP has defined the architecture for service capability exposure. In the enhanced 3GPP network architecture, Service Capability Exposure Function (SCEF) provides a means to securely expose the services and capabilities provided by 3GPP network interfaces to Applications (AS) as shown in Figure 1 below. Please refer TS 23.682 for futher details.

Figure 1:  3GPP architecture for Service Capability Exposure [cf. TS 23.682]

3GPP has also defined other features in Rel-13, summarized under their LS to oneM2M (cf. S2-151514).

The objective of this work item is to study interworking architecture options between oneM2M architecture and 3GPP Rel-13 architecture for Service Capability Exposure as defined in TS 23.682.

Different deployment scenarios where SCEF is controlled by MNO vs when it is hosted by M2M Service Provider or hosted by a 3rd party service provider will be considered.

Differnet architecure options will be considerd including the following:

- The SCEF is part of the IN CSE i.e. oneM2M CSEs interfacing directly to 3GPP network

- The IN CSE connected to the SCEF using APIs defined by other SDOs (e.g. NetAPI defined by OMA)

Schedule

| Doc Type | Spec Number | Title | Milestone dates | Primary Responsible | Notes |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |
| TR | TR-000x | 3GPP Rel-13 Interworking | TP#17 | n/a | TP#21 | TP#22 | WG2 |  |
| CRs | TS-0001 | Functional Architecture | TP#22 | n/a | TP#23 | TP#23 | WG2 |  |

Supporters

Intel, AT&T, ZTE, Telecom Italia, Sierra Wireless?, NEC?, Interdigital?, Huawei?, Alcatel-Lucent?, LG electronics?

Work Item Rapporteurs

TBD

History

| Document history |
| --- |
| V1.0.0 | 19 May 2015 | Initial proposal |

# Comments

Needs to be updated with oneM2M document# once SA2 LS is received by oneM2M