| Work Item |
| --- |
| Work Item Title:* | DDS usage in oneM2M system |
| Document Number* |  |
| Supporting Members or Partner type 2* | KETI, Huawei, Hitachi, China Unicom |
| Date:* | 2016-05-01 |
| Abstract:* | This WI is to investigate and enable the usage of DDS in the oneM2M system. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

1	Title (Acronym)

DDS usage in oneM2M system

2	Justification

DDS can be found in applications ranging from large navy ships to single embedded sensor applications. It is deployed in healthcare devices, unmanned systems such as UAV’s, financial banking applications, asset tracking solutions, remote diagnostic monitoring for power substations and many other types of applications. DDS also supports real-time audio and video transmission which is used in many fields, such as security, entertainment, and communication. The typical use of DDS is for low latency and highly deterministic communications between devices. See further detail about DDS protocol on clause 6.8 of TR-0009 V.0.7.0.

The Purpose of oneM2M is to specify and promote an M2M Common Service Layer, so from the high level point of view, the intended areas of DDS matches the target market of oneM2M

From the technical point of view, DDS can meet some of the existing oneM2M requirements, for example:

- The oneM2M System shall support the ability for single or multiple M2M Applications to interact with a single or multiple M2M Devices/Gateways (application in the device/gateway) (OSR-009). (the many to many communication of DDS)

- In automated production with utilization of information and communication technology, behaviours of devices are controlled according to sensor values. In order to achieve adequate control, real-time Ethernet , with which sensors and devices are connected through controllers, are required to provide real-time transmission and a high-level of reliability. (DDS can provide real-time communication)

- The gateway shall be able to collect data from the field area network (e.g. industrial bus systems) according to the data collection policy stored in the gateway. (DDS has MultiTopic and ContentFilteredTopic which allow for content-based subscriptions )

- The data collection policy shall be manageable (configured, updated, deleted..) by M2M Applications on the M2M service platform. (DDS has large number of configuration parameters and QoS policies)

- The oneM2M system shall be able to transmit data according to priority (CRPR-003). (DDS has the transport priority policy)

For the above reasons, it is necessary for the oneM2M system to support DDS protocol and further it is worth to study how the existing DDS subsystems can be integrated into the oneM2M system.

3	Intended Output

| Tick all the appropriate cases |  |
| --- | --- |
| x | Change request(s) to existing Technical Specification(s) |
|  | Change request(s) to existing Technical Reports(s) |
| x | New Normative Technical Specifications(s) |
| x | New Permanent Technical Reports(s) |
|  | New Temporary Technical Reports(s) |

4	Impact

It is anticipated that there will be change requests to TS-0001, TS-0004.

5	Scope

The objective of this work item is to study and specify how the advantage of the DDS protocol can be used in the oneM2M system to enhance the oneM2M platform perception of the whole system data capability, and further how the existing DDS subsystem can be integrated into the oneM2M system.

The scope of this Work Item includes (not limited to the items below):

Transporting oneM2M messages across DDS protocol:

  - Specifying the binding of Mca and Mcc primitives to DDS in a new TS; and

  - Identifying any changes that might be needed to TS-0001 and TS-0001.

Centralized management of DDS topics, QoS policies and the publish/subscribe relations:

  - Specifying the centralized management mechanisms in a new TS; and

  - Identifying any changes that might be needed to TS-0001 and TS-0001.

[Secondary] Study the solution of how the DDS subsystem can be integrated into the oneM2M system and the DDS data space can be accessed by the oneM2M enabled application.

This specification is depending on Service Layer Core protocol specification (TS-0004) for data types.

6	Schedule and impacted specifications

Provide the schedule of tasks to be performed;

| New Specifications (if any) |
| --- |
| Document Type | Document Number* | Title | Schedule (TP No.) | Lead WG | Impacted WGs | Comments |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |  |
| TS | TBD | DDS protocol binding | TP 24 | TP 30 | TP 31 | TP 32 | PRO | ARC |  |
| TR | TBD | Integration of DDS subsystem | TP 24 | TP 27 | TP 28 | TP 28 | REQ ARC | PRO |  |

* Optional for first versions (i.e. before it will be assigned by the secretariat)

| CRs to existing specifications (if any) |
| --- |
| Impacted TS/TR | CR number (when known) | Subject of the CR | Approved at plenary# | Impacted WGs | Comments |
| TS-0001 | TBD | Functional Architecture changes for DDS binding | TP30 | ARC |  |
| TS-0004 | TBD | Service Layer Core Protocol changes for DDS binding | TP32 | PRO |  |
| TS-0002 | TBD | Requirements | TP27 | REQ |  |

7	Work Item Rapporteur(s)

Sungchan Choi, sungchan.keti@gmail.com

Jessie, lijing80@huawei.com

8	History

| Document history |
| --- |
| V.0.0.1 | 15 May 2016 | Initial proposal |

-------------------------------