| Work Item PROPOSAL |
| --- |
| Work Item Title:* | Semantic Support Enhancements |
| Document Number* | WI-xxxx (oneM2M Release- 3, WI-Track 1) |
| Supporting Members or Partner type 2* | NEC (ETSI), NEC (TTC), |
| Date:* | 2016-07-18 |
| Abstract:* | This work item completes and extends the WI on Abstraction & Semantics Capability Enablement (WI-0005) of Release-2 |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

Title

Semantic Support Enhancements.

Output

“Technical Report 0007 - Study on Abstraction and Semantics Enablement”.

A separate TS to TS-0001 should be considered to contain normative work

Impact

Impact on other Technical Specifications and Technical Reports

Impact is foreseen on the design of oneM2M architecture, interface and/or procedures .

The specific TS/TR that might be impacted, are:

“Technical Specification 0001 – M2M Architecture”,

“Technical Specification 0011 – Common Terminology”

“Technical Specification 0012 – Base ontology”

“Technical Specification 0004 – Service Layer Core Protocol”

Impact on other oneM2M Work Items

The impacted WIs are WI-xxxx( Generic Interworking Enhancements), other WIs may be impacted.

Scope

The scope of this WI includes:

Enhancements:

Table 5: Semantics Query Requirements

| QRY-001 | The oneM2M System shall provide capabilities to discover M2M Resources based on semantic descriptions. | Implemented in Rel-2 |
| --- | --- | --- |

Implement:

Table 7: Semantics Reasoning Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| RES-001 | The oneM2M System shall be able to update ontologies as a result of the ontology reasoning. | Not Implemented |
| RES-002 | The oneM2M System shall be able to support semantic reasoning e.g. ontology reasoning or semantic rule-based reasoning. | Not Implemented |
| RES-003 | The oneM2M System shall be able to support adding and updating semantic information based on semantic reasoning. | Not Implemented |

Partly Implement (details TBD):

Table 3: Ontology Requirements

| Requirement ID | Description | Release |
| --- | --- | --- |
| ONT-001 | The M2M System shall support a standardized format for the rules/policies used to define service logic. | Not implemented |
| ONT-002 | The M2M System shall support modelling semantic descriptions of Things (including relationships among them) by using ontologies. | Implemented in Rel-2 |
| ONT-003 | The M2M System shall support a common modeling language for ontologies (e.g. OWL). | Implemented in Rel-2 |
| ONT-004 | The M2M System should be able to provide translation capabilities from different modeling languages for ontologies to the language adopted by oneM2M if the expressiveness of the imported ontology allows. | Not implemented |
| ONT-005 | The M2M System shall provide the capability to retrieve semantic descriptions and ontologies stored outside of the M2M System. | Not implemented |
| ONT-006 | The M2M System shall provide support for linking ontologies defined in the context of the M2M System with ontologies defined outside this context. | Not implemented |
| ONT-007 | The M2M System shall be able to support extending ontologies in the M2M System. | Targeted for Release 2 Not implemented |
| ONT-008 | The M2M System shall be able to use ontologies that contain concepts representing aspects (e.g. a room) that are not represented by resources of the M2M System. | Implemented in Rel-2 |
| ONT-009 | The M2M System shall be able to re-use common ontologies (e.g., location, time ontologies, etc.) which are commonly used in M2M Applications. | Targeted for Release 2 Not implemented |
| ONT-010 | The M2M System shall be able to support simultaneous usage of multiple ontologies for the same M2M resource. | Implemented in Rel-2 |
| ONT-011 | The M2M System shall provide the capability for making ontology available in the M2M System, e.g. through announcement. | Targeted for Release 2 Not implemented |
| ONT-012 | The M2M System shall be able to support mechanisms to import external ontologies into the M2M System. | Implemented in Rel-2 Not implemented |
| ONT-013 | The M2M System shall be able to support update of ontologies. | Targeted for Release 2 Not implemented |
| ONT-014 | The M2M System shall enable functions for data conversion based on ontologies. | Targeted for Release 2Not Implemented |
| ONT-015 | The M2M System shall be able to model devices based on ontologies which may be available outside the M2M System (e.g. HGI device template). | Implemented in Rel-2 |
| ONT-016 | The M2M System shall support storage, management and discovery of ontologies. | Not Implemented |
| ONT-017 | The oneM2M System shall support a semantic relation (“Is Paired To”) between two M2M Devices. | Not Implemented |

Schedule

The proposed schedule is shown the following table:

| Doc Type | Spec Number | Title | Milestone dates | Primary Responsible | Notes |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |
| TR | 0007 | Study of Abstraction and Semantics Enablements | TP#25 |  |  |  | WG5 |  |
| TS | 0001 | Functional Architecture |  |  |  |  | WG2 |  |
| TS | 0003 | oneM2M Security Solutions |  |  |  |  | WG4 |  |
| TS | 0004 (and related protocol bindings) | Service Layer Core Protocol | TP#20 | N/A | TP#22 | TP#23 | WG3 |  |

Supporters

NEC (ETSI), NEC (TTC),

Work Item Rapporteurs.

Martin Bauer, NEC

History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Document history |
| --- |
| V1.0 | 01 March 2013 | Work Item agreed TP#3 (oneM2M-TP-2013-0212R02) |
| V1.1 | June 2013 | Revised Agreed-, Freeze- and Approval dates. |
| V1.2 | October 2013 | Revised Change Control-, Freeze- and Approval dates. |
| V1.3 | March 2015 | Revised to include normative work in oneM2M Rel.-2. Uploaded to WPM area of the portal following approval at TP17 |
| V3.0 | July 2016 |  |

# Comments

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0521R01

REQ-2015-0609