| Work Item |
| --- |
| Work Item Title:* | Industrial Domain Enablement |
| Document Number* | WI-0028-Industrial Domain Enablement V2.0.0 |
| Supporting Members or Partner type 2* | Hitachi, Huawei, KDDI, Telecom Itallia SpA, NTT, NEC, InterDigital, KETI, Federal Network Agency (BNetzA) |
| Date:* | 2016-07-07 |
| Abstract:* | This work item shall produce a technical report analyzing the requirements from industrial scenarios and continue normative work for industrial domain enablement in oneM2M future releases. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Copyright statement

No part may be reproduced except as authorized by written permission.

The copyright and the foregoing restriction extend to reproduction in all media.

All rights reserved.

1	Title (Acronym)

Industrial Domain Enablement

2	Justification

Since industrial application is under pressures of efficiency, flexibility, safety, and so on, utilizing oneM2M standardized technology is expected to be desirable.

3	Intended Output

| Tick all the appropriate cases |  |
| --- | --- |
| X | Change request(s) to existing Technical Specification(s) |
| X | Change request(s) to existing Technical Reports(s) |
|  | New Normative Technical Specifications(s) |
| X | New Permanent Technical Reports(s) |
|  | New Temporary Technical Reports(s) |

4	Impact

4.1	oneM2M Work Items

WI-0001 oneM2M Requirements

WI-0039 oneM2M Architecture

WI-0015 oneM2M Use Case Continuation

WI-0005 oneM2M Abstraction and Semantics Capability Enablement

5	Scope

Industrial domain is expected to be able to improve efficiency and flexibility by utilizing ICT technology: collecting data from devices in multiple factories, analyzing them, and applying the analysis results to decisions. So, it is desirable to utilize oneM2M standardized technology in the industrial domain.  To better understand the special requirements to support the operations of the industrial environment, it is desirable to conduct studies on various functionalities that are keen to support this purpose so as to identify necessary technical works to enhance the future oneM2M specifications.  This work item is intended to study such functionalities and the results of that study will be presented in a Technical Report.

Initially, the targeted functionalities to be studied include:

(1)	 Balancing of availability/processing of data:

This functionality will provide basis to select an optimized solution dealing with data collection complexity and the processing means between an “intra factory” and an “inter factories” environments.

(2)	 Data processing model between real-time operating environments through a remote server:

Many devices in a factory work autonomously and communicate with each other (e.g. over high speed industry buses) in a real-time fashion. However, a remote server (e.g. a server in the Cloud) can be used to support analytical work off-line in an inter-factories environment. The present work item will study how a remote server service can be provided to support these devices in factories.

(3)	Reliability of data transmission/aggregation.

In factory applications, the quality of the manufacturing process is highly depending on the accuracy of the data, which can be greatly affected with the reliability of the communications among devices and the server. So, means of monitoring the data flow and integrity is needed in order to keep the manufacturing work effectively.

After the concluded study work in TR-0018 “Industrial Domain Enablement” during oneM2M release 2, the work item needs to be enhanced to include normative work in future releases of oneM2M specifications.

Abstraction and semantics are required by industrial applications similarly with the home domain especially for semantical interoperability and data analytics, such as the industrial elements of diverse types are abstracted in machine-interpretable languages for solving tasks autonomously, as well as alert data is reported not only to avoid an individual accident but also to provide a “industrial alert repository” based on semantic annotation.

Continuation of industrial use cases for describing semantic applications will be contributed to TR-0018 (as CRs). Some of the general concepts, which are defined by the industrial domain ontology but could also be utilized in other domains, will be taken into account to extend the “TS-0012 Base Ontology” (as CRs) for semantic enablement. Additionally, an additional TR (Industrial Domain Information Model) that defines an Abstract Information Model for the physical elements in the industrial domain might also be developed. The definition of the Abstract Information Model will be based on data models that currently exist in the industrial domain (e.g. the defined information model from OPC-UA which has been adopted by many industry market leaders).

6	Schedule and impacted specifications

Provide the schedule of tasks to be performed;

| New Specifications (if any) |
| --- |
| Document Type | Document Number* | Title | Schedule (TP No.) | Lead WG | Impacted WGs | Comments |
|  |  |  | Start | Change Control | Freeze | Approval |  |  |  |
| TR | 0018 | Industrial Domain Enablement | TP16 | TP20 | TP20 | TP21 | WG1 | WG2 WG3WG4WG5 |  |
| TR | xxxx | Industrial Domain Information Model | TP24 | TP26 | TP26 | TP27 | WG5 |  |  |

* Optional for first versions (i.e. before it will be assigned by the secretariat)

NOTE: The schedule of the intended TR “Industrial Domain Information Model” would need more discussion in WG5 since the work shall be done after the agreement of introducing the use cases related to semantic applications.

| CRs to existing specifications (if any) |
| --- |
| Impacted TS/TR | CR number (when known) | Subject of the CR | Approved at plenary# | Impacted WGs | Comments |
| TS-0002 | REQ-2015-0546R01 | Requirements to support integrity of data collection monitoring | REQ16.2 | WG1 |  |
| TS-0002 | REQ-2015-0550R03 | Requirements to support integrity of data collection monitoring | REQ17 | WG1 |  |
| TS-0002 | REQ-2015-0553R02 | Requirements to support the use case “on-demand data collection for factories” | REQ17 | WG1 |  |
| TS-0002 | REQ-2015-0583R01 | Requirements to support the use case “Data Process for Inter-factory manufacturing” | REQ17.1 | WG1 |  |
| TS-0002 | REQ-2015-0601R01 | Requirements to support use case “real-time data collection” | REQ18 | WG1 |  |
| TS-0002 | REQ-2015-0604R02 | Requirements to support the use case “Data encryption in industrial domain” | REQ18 | WG1 |  |
| TS-0001 | CRs to TS-0001 | Architecture impact from industrial domain enablement |  | WG2 |  |
| TS-0004 | CRs to TS-0004 | Protocol impact from industrial domain enablement |  | WG3 |  |
| TR-0018 | CRs to TR-0018 | Add additional use cases describing semantic applications from the industrial domain | REQ25 | WG1 WG5 |  |
| TS-0012 | CRs to TS-0012 | Base ontology extension from industrial domain ontology | MAS26 | WG5 |  |

7	Work Item Rapporteur(s)

Miao Jiang, Hitachi (China) Research &Development Corporation (CCSA) .

8	History

| Document history |
| --- |
| V1.0.0 | 23 January 2015 | For information |
| V1.1.0 | 27 March 2015 | Removing checkbox from the cover sheet and adding co-rapporteurs |
| V1.2.0 | 20 May 2015 | Revised schedule and rapporteurs |
| V1.3.0 | 20 July 2015 | Adding a supporter and revising rapporteurs |
| V1.4.0 | 03 Sep 2015 | Revising impacted TR, TS, and WG, and updating template |
| V1.4.1 | 09 Sep 2015 | Adding a supporter |
|  | 15 September 2015 | Uploaded to the Portal following approval of TP-2015-0817R01 |
| V2.0.0 | 07 July 2016 | Scope extension |

-------------------------------