| CHANGE REQUEST |
| --- |
| Meeting ID:* | REQ 30 |
| Source:* | Catalina Mladin, Convida, Mladin.Catalina@convidawireless.comKenichi Yamamoto, KDDI, kc-yamamoto@kddi.com |
| Date:* | 2017-07-10 |
| Reason for Change/s:* | TS002 new reqs from TR-0026, not implemented |
| CR against: Release* | Release 3 |
| CR against: WI* | Active MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision) Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0002 V 3.0.0 |
| Clauses * |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |

| Impacted other TS/TR(s) | TR-0026 |
| --- | --- |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This document proposes to move requirements pertaining to Vehicular Domain from TR-0026 clause 7 to TS-0002.

This is aimed at capturing requirements identified in the Vehicle Domain WI to be covered in future releases. The inclusion of these requiremenmts into TS-0002 was postponed at TP#29, in order to allow for re-wording.

Note: For re-wording of the first requirement below:

DTG = Digital Tachograph ( a device fitted to a vehicle that digitally records its speed and distance, together with the driver's activity selected from a choice of modes)

TS-0026 clause 6.4 excerpt for clarification:

“DTG-based fleet management service” is the fleet management services utilizing DTG data and related service, to facilitate extensive service features of fleet management.

DTG provides vehicle data such as driving speed, RPM (Revolution Per Minute), brake’s status, and mileage, etc.

DTG data management service, based on M2M gateway and DTG data management server, reports and manages DTG data in real-time to store it in the memory of M2M device in vehicle at a certain rate (i.e. one second in this case) to submit it to the national authority or transfer it to central office managing the data in a server.

The fleet management service utilizing the above mentioned service functionality provides advanced service features such as the precise quest of vehicles based on location and the tracking of cargo along with the route of the carrier vehicle, by means of the capability of remote monitoring and control of vehicle status provided by the DTG data management service.

### -----------------------Start of Change 1 -------------------------------------------

| OSR-yy3 | The oneM2M System shall enable provisioning, installation, configuration and registration methods of field devices for different management systems (e.g. allowing different entities to own and manage the device) or application systems (e.g. allowing different entities to utilise the device data). | future releases? |
| --- | --- | --- |
| OSR-yy8 | The oneM2M System shall enable registrations to include information identifing the peer entites, and related information (e.g. management privilege, subscription etc.), necessary for establishment of the respective peer relationships. | future releases? |
| OSR-yy9 | The oneM2M System shall enable registrations using a complete set of information context for the peer entities (termed "full registrations"). | future releases? |
| OSR-y10 | The oneM2M System shall enable registrations using only a subset of information context for the peer entities (termed "lightweight registration"). | future releases? |
| OSR-y11 | The oneM2M System shall enable "lightweight registrations" instances with different entities, which pertain to a common peer entity, to use different sets of information about the common peer entity as needed. | future releases? |
| OSR-y12 | The oneM2M System shall enable correlation of the "full registration" and the "lightweight registration" instances pertaining to a common peer entity. | future releases? |
| OSR-y13 | The oneM2M System shall enable differentiation of the "full registrations" and the "lightweight registrations" instances pertaining to a common peer entity. | future releases? |

### -----------------------End of Change 1 ---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause?