## Slide 1: ETSI STF 555 Study of use cases and communications involving IoT devices in emergency situations
18.02.2019
Samir Medjiah, STF expert
oneM2M TP#39,
February 18, 2019

## Slide 2: Content
  Objective & presentation of the STF
  Current status
  Use cases and potential requirements
  oneM2M liaison

## Slide 3: Objectives
  The purpose of STF 555 is to deliver a Technical Report to prepare the requirements for communications involving IoT devices in all types of emergency situations. This includes the use of IoT devices to enhance:
    Emergency calling, e.g. between individuals and emergency authorities/organisations, between emergency authorities/organisations, and between individuals;
    Mission critical communications within emergency services/public safety organisations, e.g. between public safety officers and control centres, between the control centres of different public safety organisations, and between individual public safety officers;
    Public Warning System type communications from authorities to the general public.

## Slide 4: Project Description
  Deliverable : ETSI TR 103 582: Study of use cases and communications involving IoT devices in provision of emergency situations
  Experts
  Steering Committee
    Daniel Voisard, Ofcom
    Cristina Lumbreras, EENA
    Chantal Bonardi, ETSI
  Related TBs
    ETSI TC SmartM2M, TC TCCE, TC SmartBAN, and if possible, oneM2M, 3GPP (SA1, SA4 and SA6)
Expert | Organization
Craig Bishop | Bishop Communications Ltd
Anton Donner | Ingenieurbüro Donner
Ban Al-Bakri | MeadowCom
Samir Medjiah | LAAS-CNRS / Netellany SASU
Michelle Wetterwald (STF leader) | Netellany SASU / FBConsulting

## Slide 5: Project Description
  Schedule
    The STF started on June 25, 2018

## Slide 6: Activities and achievements at this point
  STF web page at: https://portal.etsi.org//STF/STFs/STFHomePages/STF555
  Liaison statement (EMTEL(18)000026) sent by SC EMTEL to the related standardisation bodies on August 2, 2018 to inform them about the start of the STF and its scope
  Draft versions :
    V0.2.0 of TR 103 582 with the results of Task 2 (state of the art) is available as an SC EMTEL draft
    V0.3.0 with use cases descriptions (Task 3) is available as an SC EMTEL draft
    V0.4.0 with identification of points of failure and a first list of requirements (Task 4) is available as an SC EMTEL draft
  Final draft will be available for approval by SC EMTEL on 15.04.2019

## Slide 7: List of use cases
  EC1: Automatic direct emergency call from IoT device
  EC2: IoT device provides additional information to an emergency call
  MC1: IoT-based mission critical communications
  MC2: Mission critical logistics support
  MC3: Emergency services teams accessing pre-deployed IoT devices
  PWS1: Warning sent by IoT device to citizens
  AE1: IoT communication with priority handling to prevent emergency situation
  AE2: IoT-based action following public warning system message reception
Notes: The STF has analysed and described various situations where IoT devices and systems would improve the support of such situations by responders, e.g. Automatic direct emergency call from IoT device, IoT-based mission critical communications, Mission critical logistics support.
Some situations could even only rely on device to device communications, for example IoT-based action following public warning system message reception, where an IoT device could take action on another system automatically, preventing a further disaster (e.g. stopping a train in case of an earthquake).

## Slide 8: Example Use Case: MC1: IoT-based mission critical communications

## Slide 9: Example Use Case: AE2: IoT-based action following PWS message reception

## Slide 10: Potential points of failure (extracted examples)
  Summary of points of failure in all domains
    IoT device failure (battery failure, physical damage, etc.)
    Call failure (network failure, protocol incompatibility, improper configuration, improper PSAP selection, etc.)
    False alarm (hacked or faulty IoT device, misinterpreting of environment data, etc.)
    Redundant alarm detection
    Network congestion
    Message is not comprehensive or cannot be understood
    Emergency services are not able to obtain the IoT device data because the IoT service platform is not available
    Intentional denial-of-service attacks or jamming.
    IoT device is not able to exchange data with applications, service platforms because they were produced by different providers (lack of interoperability)
    etc.

## Slide 11: Recommendations of requirements
  For every domain, 5 knowledge areas have been identified :
    Usage & maintenance
    Interoperability
    Networks and connectivity
    Data exchange at service and application level
    Security

## Slide 12: Recommendations of requirements (extracted examples)
  Interoperability
    Emergency Calling domain
      PSAPs / ECCs should support the reception of emergency a data message from an IoT device (i.e. a one-shot emergency data message with no Callback).
      Emergency data from an authorized IoT device should be in a format that is understandable by the PSAP.
    Mission Critical Communication domain
      All IoT devices to be used for mission critical applications should have passed some sort of "interoperability certification" to ensure that devices from different vendors can communicate over networks from other vendors with each other.
      Syntax and semantics of data contributing to the Common operating Picture (COP) should be standardised. This includes IoT data.
    Public Warning System domain
      An IoT device acting in PWS should be able to understand PWS as standardised for different regulations.
      An IoT device acting in PWS should support the format of the connected devices to be able to convey the information (i.e. video, voice, text, etc.).
    Automated Emergency Response domain
      IoT devices should be able to support automated emergency response priority service.

## Slide 13: Recommendations of requirements (extracted examples)
  Data exchange at service and application level
    Emergency Calling domain
      EC-enabled IoT devices should support the sending of an emergency data message
    Mission Critical Communication domain
      All (IoT) devices and the on/off-network should support time synchronisation and should assign time stamps to data when/where appropriate.
      IoT devices should be able to trigger other IoT devices (e.g., smoke detector turns on a camera).
    Public Warning System domain
      PWS message content should be comprehensive, this may include different languages, icons, text, etc. Comprehensive PWS message is used to identify the warning message and to enable the IoT device to take the required action if instructed by the PWS message.
      The IoT service platform and the IoT device should identify PWS message duplication and suppress them.
      The IoT service platform and IoT device should forward the PWS message, if instructed to do so and if its capability allows.
    Automated Emergency Response domain
      An AE-enabled IoT device should support the sending and receiving of the automated emergency response server information.

## Slide 14: oneM2M liaison
  Final draft approval by SC EMTEL is before next oneM2M TP (#40)
    Pre-final stable draft will be sent in a LS from SC EMTEL for comments and suggestions around 15.03.2019
    Need for feedback by oneM2M community before 07.04.2019
    Final draft will be available for approval by SC EMTEL on 15.04.2019

## Slide 15: Contact details
Thank you for your attention. Questions?
Samir Medjiah
STF 555 member LAAS-CNRS / Netellany Email: samir.medjiah@laas.fr Samir.medjiah@gmail.com
STF web page: https://portal.etsi.org//STF/STFs/STFHomePages/STF555