| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST#15 |
| Title:* | Definition of test related terms |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Huawei, Yinjiaxin@huawei.com |
| Date:* | 2015-1-9 |
| Abstract:* | The contribution proposes new definitions to the TS0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS0013 |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## 3.1	Definitions

Test Suite: A Test Suite is a collection of Test Cases. It’s used to test if the Tested Entity has specified behaviour to perform certain functionalities.

Test Case: A Test Case is a sequence of Test Steps in a specified order to test if the reaction of Tested Entity could match the Expected Output. A Test Case has an explicit purpose.

Test Step: A Test Step is one step of the Test Case to fulfil the Test Case. It could be a one time message exchange or one internal change of the state.

Test Sequence: A Test Sequence is a sequence of Test Steps in a specified order.

Test Requirements: A Test Requirement stems from requirements in oneM2M. The Test Requirement describes one intended purpose of the test work. It shall be covered by at least one of the Test Cases.

Tested Entity: The entity that is been tested. The Tested Entity may be AE or CSE.

Preamble: A Test Case may have several preambles which serves as pre-conditions that need to be satisfied by the Tested Entity before the execution of the Test Sequence.

Postamble: A Test Case may have several Postambles after the execution of Test Sequence. The Postamble are to restore the Test Entity’s state if needed.

Observation Point: The point to inspect the behaviour of the Tested Entity during testing. The output inspected from the Observation Point is to be compared with the Expected Output.

Control Point: The point to trigger the reaction of the Test Entity. It may be the interface to send request to the Test Entity.

Tester: The equipment or facility that helps the testing work to the Tested Entity.

Expected Output: After a series of Test Steps, the output that is regarded to be correct according to the definition in oneM2M standard.

Supporting Layer: The supporting layer is transport layer of the primitives between Tester, Observation Point and Control Point when performing test. It could be HTTP, CoAP or MQTT according to the primitive binding method. It could also be any proprietary method the deliver the primitive which is out of scope of the current TS.