| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Testing configurations new organization |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-02-19 |
| Abstract:* | The contribution proposes a new organization of testing configurations to make them more coherent with oneM2M architecture and provides requried multi hops testing configurations. |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes a new organization of testing configurations to make them more coherent with neM2M architecture and provides requried multi hops testing configurations.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# 7	Configuration

## 7.1	Test Configuration

This section defines the different test configurations.

### No hop

### M2M_CFG_01

AE manages resources on registrar CSE (Hosting CSE)

oneM2M entities model

Relationship supported by oneM2M node types

| AE | Registrar-CSE |
| --- | --- |
| ASN-AE | ASN-CSE |
| MN-AE | MN-CSE |
| IN-AE | IN-CSE |
| ADN-AE | IN-CSE |
| ADN-AE | MN-CSE |

### Single hop

### M2M_CFG_02

oneM2M entities model

Relationship supported by oneM2M node types

| Registree-CSE | Registrar-CSE |
| --- | --- |
| ASN-CSE | IN-CSE |
| ASN-CSE | MN-CSE |
| MN-CSE | MN-CSE |
| MN-CSE | IN-CSE |

### M2M_CFG_03

AE manages resources on remote CSE

oneM2M entities model

Relationship supported by oneM2M node types

| AE | Registrar-CSE | Hosting-CSE |
| --- | --- | --- |
| ASN-AE | ASN-CSE | IN-CSE |
| ASN-AE | ASN-CSE | MN-CSE |
| ADN-AE | ASN-CSE | IN-CSE |
| ADN-AE | ASN-CSE | MN-CSE |
| MN-AE | MN-CSE | IN-CSE |
| MN-AE | MN-CSE | MN-CSE |
| IN-AE | IN-CSE | MN-CSE |
| IN-AE | IN-CSE | ASN-CSE |

Editor’s Note: The table is currently not an exhaustive list of all the possible relationships. How to clearly describe the relationship is FFS.

### M2M_CFG_04

oneM2M entities model

Relationship supported by oneM2M node types

| AE1 | CSE1 | CSE2 | AE2 |
| --- | --- | --- | --- |
| ADN-AE | MN-CSE | IN-CSE | IN-AE |
| MN-AE | MN-CSE | IN-CSE | IN-AE |
| ASN-AE | ASN-CSE | IN-CSE | IN-AE |
| ASN-AE | ASN-CSE | MN-CSE | MN-AE |
| MN-AE | MN-CSE | MN-CSE | MN-AE |

Editor’s Note: The table is currently not an exhaustive list of all the possible relationships. How to clearly describe the relationship is FFS.

### Multi hops

### M2M_CFG_05

Relationship supported by oneM2M node types

| Rgistrar CSE | Transit CSE | Hosting CSE |
| --- | --- | --- |
| ASN-CSE | MN-CSE | IN-CSE |
| MN-CSE | MN-CSE | IN-CSE |
| ASN-CSE | MN-CSE | MN-CSE |
| MN-CSE | MN-CSE | MN-CSE |

Editor’s Note: The table is currently not an exhaustive list of all the possible relationships. How to clearly describe the relationship is FFS.

### M2M_CFG_06

Relationship supported by oneM2M node types

| AE1 | Rgistrar CSE | Transit CSE | Hosting CSE |
| --- | --- | --- | --- |
| ADN-AE | MN-CSE | MN-CSE | IN-CSE |
| MN-AE | MN-CSE | MN-CSE | IN-CSE |
| ASN-AE | ASN-CSE | MN-CSE | IN-CSE |
| ASN-AE | ASN-CSE | MN-CSE | MN-CSE |
| MN-AE | MN-CSE | MN-CSE | MN-CSE |

Editor’s Note: The table is currently not an exhaustive list of all the possible relationships. How to clearly describe the relationship is FFS.

### M2M_CFG_07

Relationship supported by oneM2M node types

| AE1 | Rgistrar CSE | Transit CSE | Hosting CSE | AE2 |
| --- | --- | --- | --- | --- |
| ADN-AE | MN-CSE | MN-CSE | IN-CSE | IN-AE |
| MN-AE | MN-CSE | MN-CSE | IN-CSE | IN-AE |
| ASN-AE | ASN-CSE | MN-CSE | IN-CSE | IN-AE |
| ASN-AE | ASN-CSE | MN-CSE | MN-CSE | MN-AE |
| MN-AE | MN-CSE | MN-CSE | MN-CSE | MN-AE |

Editor’s Note: The table is currently not an exhaustive list of all the possible relationships. How to clearly describe the relationship is FFS.

## 7.2	Resources Request examples

In order to ease test setup and execution of the tests, some resource request example may be provided to the users.

# 8	Test Descriptions

Editor’s Note: The content of this section can be modified according to the progress of this TS.

Editor’s Note: The Test Descriptions defined in this clause serves as an example purpose for the skeleton of the specification. The details of the content need to be further investigated.

## No hop configuration testing

### remoteCSE Management

#### remoteCSE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | Registree CSE registers to Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.1 [2] 7.3.3.2.1 |
| Pre-test conditions: | Void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Registree CSE is requested to send a remoteCSE Create request to register to the Registrar CSE |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Content Type option Payload: <remoteCSE> resource |
|  | 3 | Check | Check if possible that the remoteCSE resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/ <remoteCSE> Payload: created <remoteCSE> resource |
|  | 5 | Check | Check if possible that the remoteCSE resource is created in registree CSE. |
|  | 6 | Verify | Registree CSE and Registrar CSE indicate successful operation |

#### remoteCSE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | Registree CSE retrieve remoteCSE resource from Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.2 [2] 7.3.3.2.2 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Registree CSE is requested to send a remoteCSE Retrieve request to the Registrar CSE |
|  | 2 | Check (Mca) | Sent GET request contains Request method = GET Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Content Type option Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 (OK) Payload: <remoteCSE> resource |
|  | 4 | Verify | Registree CSE indicates successful operation |

#### remoteCSE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | MN-CSE registers to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.3 [2] 7.3.3.2.3 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Content Type option Payload: modified < remoteCSE> resource |
|  | 3 | Check | Check if possible that the remoteCSE resource has been updated in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Content-Location <RegistrarCSE>/ <remoteCSE> Payload: updated < remoteCSE > resource |
|  | 5 |  | Check if possible that the remoteCSE resource is also updated in registree CSE. |
|  | 6 | Verify | Registree CSE and Registrar CSE indicate successful operation |

#### remoteCSE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_04 |
| Objective: | MN-CSE cancels registration to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.4 [2] 7.3.3.2.4 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
|  | 2 | Check (Mca) | Sent DELETE request contains Request method = DELETE Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  | 4 |  | Check if possible that the remoteCSE resource has been removed in registrar CSE. |
|  | 5 |  | Check if possible that the remoteCSE resource is also removed in registree CSE. |
|  | 6 | Verify | Registree CSE and Registrar CSE indicate successful operation |

## Single Hop configuration testing

### CSEBase Management

#### CSEBase Retrieve on Mca

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_05 |
| Objective: | AE retrieves the CSEBase resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.3.2 [2] 7.3.2 |
| Pre-test conditions: | CSEBase resource has been automatically created in CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a retrieve Request (GET) to CSE |
|  | 2 | Check (Mca) | Sent GET request contains Request method = GET Request URI <CSEBase> Host : registrar CSE Content Type option Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Payload: <CSEBase> resource |
|  | 4 | Verify | AE indicates successful operation |

#### CSEBase Retrieve on Mcc

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_06 |
| Objective: | Remote CSE retrieves the CSEBase resource |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.3.2 [2] 7.3.2 |
| Pre-test conditions: | CSEBase resource has been automatically created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Remote CSE is requested to send a retrieve Request (GET) to registrar CSE |
|  | 2 | Check (Mca) | Sent GET request contains Request method = GET Request URI <CSEBase> Host : registrar CSE Content Type option Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Payload: <CSEBase> resource |
|  | 4 | Verify | Remote CSE indicates successful operation |

### Application Entity Registration

#### AE Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_07 |
| Objective: | AE registers to its registrar CSE via an AE Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.1 [2] 7.3.4.2.1 |
| Pre-test conditions: | Void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a AE Create request to register to the Registrar CSE |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>/<AE> Host : Registrar CSE Content Type option Payload: <AE> resource to be created |
|  | 3 | Check | Check if possible that the <AE> resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/<AE> Payload: created <AE> resource |
|  | 5 | Verify | AE indicates successful operation |

#### AE Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_08 |
| Objective: | AE retrieves <AE> resource via an AE Retrieve Request (GET) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.2 [2] 7.3.4.2.2 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an application Retrieve Request (GET) |
|  | 2 | Check (Mca) | Sent GET request contains Request method = GET Request URI : <CSEBase>/<AE> Host : registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code =200 Payload: <AE> resource |
|  | 4 | Verify | AE indicates successful operation |

#### AE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_09 |
| Objective: | AE updates attribute in <AE> resource via an AE Update Request (PUT) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.3 [2] 7.3.4.2.3 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Update Request (PUT) |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI : <CSEBase>/<AE> Host : registrar CSE Payload: modified <AE> resource |
|  | 3 | Check | Check if possible that the <AE> resource has been updated in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: updated <AE> resource |
|  | 5 | Verify | AE indicates successful operation |

#### AE Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_10 |
| Objective: | AE de-registers by deleting <AE> resource via an AE Delete Request (DELETE) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.4 [2] 7.3.4.2.4 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Delete Request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request method = DELETE Request URI : <CSEBase>/<AE> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  | 4 | Check | Check if possible that the <AE> resource has been removed in registrar CSE. |
|  | 5 | Verify | AE indicates successful operation |

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_11 |
| Objective: | AE creates a container ressource in registrar CSE via a container Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Create Request (POST) to create container <container> |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: container resource <container> to be created |
|  | 3 | Check | Check if possible that the <container> resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar sends response containing: Code = 200 Content-Location : <CSEBase> /<AE>/<container> Payload: Created <container> |
|  | 5 | Verify | AE indicates successful operation |
|  | 6 |  | Repeat step 1-5 creating container resource with short lifetime |
|  | 7 |  | Check the created resource is removed after the expiry of its lifetime |

#### Container Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_12 |
| Objective: | AE retrieves information of a container resource via a container Retrieve Request (GET) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | A container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Retrieve Request (GET) for resource <container> |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase>/<AE>/<container> Host : Registar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: <container> resource |
|  | 4 | Verify | AE indicates successful operation |

#### Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_13 |
| Objective: | AE updates attribute in application resource via a container Update Request (PUT) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | a container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an container Update Request (PUT) to update the lifetime of the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: modified <container> resource |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: Updated <container> resource |
|  | 4 | Verify | AE indicates successful operation |

#### Container Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_14 |
| Objective: | AE deletes a specific container ressource via a container Delete Request (DELETE) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.4 [2] 7.3.5.2.4 |
| Pre-test conditions: | AE has created a container resource <container> in application <AE> on the Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an Container Delete Request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registar CSE sends response containing: Code = 200 Payload: empty |
|  | 4 | Check | Check if possible that the <container > resource has been removed in registrar CSE. |
|  | 5 | Verify | AE indicates successful operation |

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_15 |
| Objective: | AE adds a contentInstance resource <contentInstance> to a specific container in Registrar CSE via a contentInstance Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a contentInstance Create Request (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <CSEBase>/ <AE>/<container> /<contentInstance> Host : Registrar CSE Payload: ContentInstance resource <contentInstance> to be created |
|  | 3 | Check | Check if possible that the <contentInstance> resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-Location : CSEBase>/ <AE>/<container> /<contentInstance> Payload: <contentInstance> resource |
|  | 5 | Verify | AE indicates successful operation |

#### ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_16 |
| Objective: | AE retrieves information of a contentInstance resource via a container Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE AE has created a contentInstance resource <contentInstance> residing under the <container> resource. |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | App is requested to send a containerRetrieveRequest (GET) for retrieving the attributes/meta-data and the opaque data of a <contentInstance> resource |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase>/ <AE>/<container> /<contentInstance> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: <contentInstance> resource |
|  | 4 | Verify | AE indicates successful operation |
|  | 5 |  | Repeat steps 1-4 using <latest> instead of <contentInstance> to get the latest contentInstance. |
|  | 6 |  | Repeat steps 1-4 using <oldest> instead of <contentInstance> to get the oldest contentInstance. |

#### Content Instance Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_17 |
| Objective: | AE deletes contentInstance resource via a container Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.4 [2] 7.3.6.2.4 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE AE has created a contentInstance resource <contentInstance> residing under the <container> resource. |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a contentInstance Delete Request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request URI <CSEBase>/ <AE>/<container> /<contentInstance> Host : registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: empty |
|  | 4 | Check | Check if possible that the <contentInstance> resource has been removed in registrar CSE. |
|  | 5 | Verify | AE indicates successful operation |

### Discovery

#### Discovery of all resources

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_18 |
| Objective: | AE discovers resources residing in Registrar CSE |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to initiate a procedure in order to discover resources under resource /discovery located in Registrar CSE |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase>/discovery Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: Discovery resource including references to all resources residing in Registrar CSE |
|  | 4 | Verify | AE indicates successful operation |

#### Discovery with Filter Criteria

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_19 |
| Objective: | AE discovers resources residing in Registrar CSE using specific Filter criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE with labels =key1 |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a Discovery procedure in order to discover resources under a known resource /discovery located in Registrar CSE |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase >/discovery?labels=key1 Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: Discovery resource including references to <AE> |
|  | 4 | Verify | AE indicates successful operation |

#### Discovery with limit condition

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_20 |
| Objective: | AE discovers resources residing in Registrar CSE limiting the number of matching resources to the specified value. |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | App is requested to send a DiscoveryRetrieveRequest in order to discover resources under resource /discovery located in localCSE |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase >/discovery?limit =2 Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload Payload: Trunked Discovery resource including only 2 resource references |
|  | 4 | Verify | AE indicates successful operation |

#### Discovery with multiple parameters

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_21 |
| Objective: | AE discovers resources residing in Registrar CSE using multiple Filter Criteria |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.6 [2] 7.2.3.13 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE with labels=key1 and labels =key2 |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | App is requested to send a Discovery procedure in order to discover resources under resource <discovery> located in Registrar CSE |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase>/<discovery>?labels =key1 &labels=key2&sizeBelow=1& filterUsage =discovery Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: Discovery resource including a reference to <AE> |
|  | 4 | Verify | AE indicates successful operation |

### Subscription Management

#### Subscription Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_22 |
| Objective: | AE creates a subscription to Application Entity resource via subscription Create Request (POST) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.2 [2] 7.3.7.2 |
| Pre-test conditions: | App has created an application resource <app> on local SCL App has created a container resource <container> on local SCL |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | App is requested to send a subscriptionCreateRequest (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: subscription <subscription> resource to be created |
|  | 3 | Check | Check if possible that the <subscription> resource is created in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container>/ <subscription> Payload: Created < subscription > resource |
|  | 5 | Verify | AE indicates successful operation |

#### Subscription Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_23 |
| Objective: | AE retrieves information about a subscription via subscription Retrieve Request (GET), such as expirationTime, labels, etc… |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.3 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a subscription Retrieve Request (GET) for retrieving information about a subscription <subscription> |
|  | 2 | Check (Mca) | Sent GET request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: <subscription> resource |
|  | 4 | Verify | AE indicates successful operation |

#### Subscription Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_24 |
| Objective: | AE updates information about a subscription via subscription Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.4 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a subscription Retrieve Request (PUT) to update the lifetime of the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: Modified <subscription> resource |
|  | 3 | Check | Check if possible that the <subscription> resource is updated in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: Modified <subscription> resource |
|  | 5 | Verify | AE indicates successful operation |

#### Subscription Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_25 |
| Objective: | AE cancels subscription via an subscription Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.5 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | App is requested to send a subscriptionDeleteRequest |
|  | 2 | Check (Mca) | Sent DELETE request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Payload: Empty |
|  | 3 | Check (Mca) | SCL sends response containing: Code = 204 Payload: Empty |
|  | 4 | Check | Check if possible that the <subscription> resource has been removed in registrar CSE. |
|  | 5 | Verify | AE indicates successful operation |

### accessControlPolicy Management

#### accessControlPolicy Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_26 |
| Objective: | AE creates an accessControlPolicy resource |
| Configuration: | M2M_CFG_01, |
| References: | [1] 10.2.21.1 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an accessControlPolicy Create Request (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI <CSEBase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: application resource <accessControlPolicy> to be created |
|  | 3 | Check | Check if possible that the <accessControlPolicy> resource is created in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<AE>/<accessControlPolicy> Payload: created <accessControlPolicy> resource |
|  | 5 | Verify | AE indicates successful operation |

#### accessControlPolicy Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_27 |
| Objective: | AE retrieves accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.2 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a accessControlPolicy Retrieve request (GET) |
|  | 2 | Check (Mca) | Sent GET request contains Request method = GET Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code =200 Payload: <accessControlPolicy> resource |
|  | 4 | Verify | AE indicates successful operation |

#### accessControlPolicy Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_28 |
| Objective: | AE updates attribute in accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.3 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an accessControlPolicy Update request (PUT) |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Payload: modified <accessControlPolicy>resource |
|  | 3 | Check | Check if possible that the <accessControlPolicy> resource is updated in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: updated <accessControlPolicy> resource |
|  | 5 | Verify | AE indicates successful operation |

#### accessControlPolicy Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_29 |
| Objective: | AE deletes accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.4 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an accessControlPolicy Delete request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request method DELETE Request URI <CSEBase>/<AE>/ <accessControlPolicy> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  | 4 | Check | Check if possible that the <accessControlPolicy> resource has been removed in registrar CSE. |
|  | 5 | Verify | App indicates successful operation |

#### Unauthorized operation (Insufficient Access Rights)

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_30 |
| Objective: | AE delete request is rejected due to accessControlPolicy |
| Configuration: | M2M_CFG_01 |
| References: | [1] [2] ] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource < acp1> under <AE> on Registrar CSE, which forbids to delete container AE has created a container resource <container> in application <AE>, using the access right <acp1> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Delete Request (DELETE) for resource <container> |
|  | 2 | Check (Mca) | Sent DELETE request contains Request URI <CSEBase>/ <AE>/<container> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 403 (Forbidden operation) Payload: ??? |
|  | 4 | Check | Check if possible that the <container> resource has not been removed in registrar CSE. |
|  | 5 | Verify | AE indicates unsuccessful operation (Delete error – no privilege) |

### Group Management

#### Group Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_31 |
| Objective: | AE creates a group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.2 [2] 7.3.12.2.1 |
| Pre-test conditions: | void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a group Create Request (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI <CSEBase>/<group> Host : Registrar CSE Payload: Group resource <group> to be created |
|  | 3 | Check | Check if possible that the <group> resource is created in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<group> Payload: created <group> resource representation |
|  | 5 | Verify | AE indicates successful operation |

#### Group Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_32 |
| Objective: | AE retrieves group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.3 [2] 7.3.12.2.2 |
| Pre-test conditions: | AE has created a Group resource <group> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a group Retrieve Request (GET) |
|  | 2 | Check (Mca) | Sent GET request contains Request method = GET Request URI <CSEBase>/<group> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code =200 Payload: <group> resource representation |
|  | 4 | Verify | AE indicates successful operation |

#### Group Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_33 |
| Objective: | AE updates attribute in group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.4 [2] 7.3.12.2.3 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a group Update Request (PUT) |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI <CSEBase>/<group> Host : Registrar CSE Payload: modified group resource |
|  | 3 | Check | Check if possible that the <group> resource is updated in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: updated <group> resource representation |
|  | 5 | Verify | AE indicates successful operation |

#### Group Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_34 |
| Objective: | AE deletes group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.5 [2] 7.3.12.2.4 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a group Delete Request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request method = DELETE Request URI <CSEBase>/<group> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Payload: empty |
|  | 4 | Check | Check if possible that the <group> resource is deleted in Registrar CSE. |
|  | 5 | Verify | AE indicates successful operation |

# Proforma copyright release text block

This text box shall immediately follow after the heading of an element (i.e. clause or annex) containing a proforma or template which is intended to be copied by the user. Such an element shall always start on a new page.

Notwithstanding the provisions of the copyright clause related to the text of the present document, oneM2M grants that users of the present document may freely reproduce the <proformatype> proforma in this {clause|annex} so that it can be used for its intended purposes and may further publish the completed <proformatype>.

<PAGE BREAK>

## Annexes

Each annex shall start on a new page (insert a page break between annexes A and B, annexes B and C, etc.).

Use the Heading 9 style for the title and the Normal style for the text.

Annex A (Normative): Title of annex (style H9)

Editor’s note : as agreed at the TST#15 meeting, the Test description template is put in Annex of  the TS-0013

A.1	Test Description definition

A "Test Description" (TD) is a well detailed description of a process that pretends to test one or more functionalities of an implementation. Applying to interoperability testing, these testing objectives address the interoperable functionalities between two or more vendor implementations.

In order to ensure the correct execution of an interoperability test, the following information should be provided by the test description:

- The proper configuration of the vendor implementations.

- The availability of additional equipment (protocol monitors, functional equipment, …) requires to achieve the correct behaviour of the vendor implementations.

- The correct initial conditions.

- The correct sequence of the test events and test results.

TDs are based on the test scenarios.

In order to facilitate the specification of test cases an interoperability test description should include as a minimum the following fields as indicated table 1.

Table 1: Interoperability test description

| Identifier | a unique test description ID |
| --- | --- |
| Objective | a concise summary of the test which should reflect the purpose of the test and enable readers to easily distinguish this test from any other test in the document |
| References | a list of references to the base specification section(s), use case(s), requirement(s), TP(s) which are either used in the test or define the functionality being tested |
| Applicability | a list of features and capabilities which are required to be supported by the SUT in order to execute this test (e.g. if this list contains an optional feature to be supported, then the test is optional) |
| Configuration or Architecture | a list of all required equipment for testing and possibly also including a (reference to) an illustration of a test architecture or test configuration |
| Pre-Test Conditions | a list of test specific pre-conditions that need to be met by the System under test (SUT) including information about equipment configuration, i.e. precise description of the initial state of the SUT required to start executing the test sequence |
| Test Sequence | an ordered list of equipment operation and observations. The test sequence may contain also the conformance checks as part of the observations |

Example of oneM2M Test Descriptions

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_P2P_12 |
| Objective: | AE retrieves information of a container resource via a container Retrieve Request (GET) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.2 [2] 7.3.5.2.2 |
| Pre-test conditions: | A container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Retrieve Request (GET) for resource <container> |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase>/<AE>/<container> Host : Registar CSE Payload: empty |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Payload: <container> resource |
|  | 4 | Verify | AE indicates successful operation |

Types of events:

A stimulus corresponds to an event that enforces an EUT to proceed with a specific protocol action, like sending a message for instance.

A verify consists of verifying that the EUT behaves according to the expected behaviour (for instance the EUT behaviour shows that it receives the expected message).

A configure corresponds to an action to modify the EUT configuration.

A check ensures the receipt of protocol messages on reference points, with valid content. This "check" event type corresponds to the interoperability testing with conformance check method.

<PAGE BREAK>

Annex <B>(Informative/Normative): Remove Informative or Normative as appropriateTitle of annex (style H9)

<Text>

B.1	First clause of the annex (style H1)

<Text>

B.1.1	First subdivided clause of the annex (style H2)

<Text>

<PAGE BREAK>

The following text is to be used when appropriate:

Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

<Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

# History

This clause shall be the last one in the document and list the main phases (all additional information will be removed at the publication stage).

| Publication history |
| --- |
| V1.1.1 | <dd-Mmm-yyyy> | <Milestone> |

| Draft history (to be removed on publication) |
| --- |
| V.0.0.1 | 12 January 2015 | Rapporteur Input – Draft Skeleton |
| V.0.0.2 | 28 January 2015 | Implements the agreed contributions from TP#15 TST-2015-0012R02-TS-0013-skeleton TST-2015-0013R01-Interoperability_Test_Description_template TST-2015-0016R03-Interoperability_Test_Descriptions_input |

============== == End of  1st Part: Proposed Test Descriptions ==================