| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Single hop CSEBase management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-02-19 |
| Abstract:* | The contribution proposes some Interoperability Test Descriptions for Single hop CSEBase management to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some test descriptions about Multi-Hop CSEBase resource management, to be included into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

Editor’s Note: The content of this section can be modified according to the progress of this TS.

## Single Hop configuration testing

### CSEBase Management

#### CSEBase Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | AE retrieves a remote CSEBase resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.3.2 [2] 7.3.3.2.2 |
| Pre-test conditions: | void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a CSEBase Retrieve Request (GET) for resource <CSEBase> in remoteCSE |
|  | 2 | Check (Mca) | Sent GET request contains Request URI <CSEBase> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mcc) | Forwarded GET request contains Request URI <CSEBase> Host : remote CSE Payload: empty |
|  | 4 | Check (Mcc) | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <CSEBase> resource |
|  | 5 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 200 Payload: <CSEBase> resource |
|  | 6 | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================