| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Single hop ContentInstance management |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-03-04 |
| Abstract:* | The contribution proposes some Interoperability Test Descriptions for Single hop contentInstance management to be added to TS-0013 |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some test descriptions about Multi-Hop contentInstance resource management, to be included into the TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

Editor’s Note: The content of this section can be modified according to the progress of this TS.

## Single Hop configuration testing

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_06 |
| Objective: | AE creates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.2 [2] 7.3.7.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <Container> has been created in <AE> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a ContentInstance Create Request (POST) to create a ContentInstance <ContentInstance> on remote CSE. |
|  | 2 | Check (Mca) | Sent POST request contains Request URI : <remoteCSE>/<AE>/<Container> ?rty=contentInstance Host : Registrar CSE Payload: resource <ContentInstance> to be created |
|  | 3 | Check (Mcc) | Forwarded POST request contains Request URI : <remoteCSE>/<AE>/<Container>?rty=contentInstance Host : remote CSE Payload: resource <ContentInstance> to be created |
|  | 4 | Check | Check if possible that the < ContentInstance > resource is created in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<Container>/<ContentInstance> Payload: Created <ContentInstance> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<Container>/<ContentInstance> Payload: Created < ContentInstance > (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |
|  | 8 |  | Repeat step 1-7 creating ContentInstance resource with short lifetime |
|  | 9 |  | Check the created resource is removed after the expiry of its lifetime |

#### ContentInstance Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_07 |
| Objective: | AE retrieves a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.3 [2] 7.3.7.2.2 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <Container> has been created in <AE> Resource <ContentInstance> has been created in <Container> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a ContentInstance Retrieve Request (GET) for resource < ContentInstance > |
|  | 2 | Check (Mca) | Sent GET request contains Request URI : <remoteCSE>/<AE>/<Container>/<ContentInstance> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mcc) | Forwarded GET request contains Request URI <remoteCSE>/<AE>/<Container>/<ContentInstance> Host : remote CSE Payload: empty |
|  | 4 | Check (Mcc) | Remote CSE sends response to Registrar CSE containing: Code = 200 Payload: <ContentInstance> resource |
|  | 5 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 200 Payload: <ContentInstance> resource |
|  | 6 | Verify | AE indicates successful operation |

#### ContentInstance Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_08 |
| Objective: | AE updates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.4 [2] 7.3.7.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <Container> has been created in <AE> Resource <ContentInstance> has been created in <Container> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a ContentInstance Update Request (PUT) to update the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI : <remoteCSE>/<AE>/<Container>/<ContentInstance> Host : Registrar CSE Payload: modified <ContentInstance> resource |
|  | 3 | Check (Mcc) | Forwarded PUT request contains Request URI : <remoteCSE>/<AE>/<Container>/<ContentInstance> Host : remote CSE Payload: modified <ContentInstance> resource <ContentInstance> |
|  | 4 | Check | Check if possible that the <ContentInstance> resource is updated in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: modified <ContentInstance> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE sends response to AE containing: Code = 200 Payload: modified <ContentInstance> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |

#### ContentInstance Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_09 |
| Objective: | AE deletes a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.5 [2] 7.3.7.2.4 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <Container> has been created in <AE> Resource <ContentInstance> has been created in <Container> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a ContentInstance Delete Request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request URI : <remoteCSE>/<AE>/<Container>/<ContentInstance> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mcc) | Forwarded DELETE request contains Request URI : <remoteCSE>/<AE>/<Container>/<ContentInstance> Host : Remote CSE Payload: empty |
|  | 4 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  | 5 | Check (Mca) | Registrar CSE Forwards response to AE containing: Code = 200 Payload: empty |
|  | 6 | Check | Check if possible that the <ContentInstance> resource is deleted in remote CSE. |
|  | 7 | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================