| Input Contribution |
| --- |
| Meeting ID* | TP16 |
| Title:* | AE Announcement Tests |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@InterDigital.com Dale Seed, InterDigital, Dale.Seed@InterDigital.com |
| Uploaded Date:* | 2015-03-15 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some Interoperability Test Descriptions for AE announcement procedures to be added to TS-0013 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution consists of some AE Announce test descriptions to be included into TS-0013.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# Test Descriptions

Editor’s Note: The content of this section can be modified according to the progress of this TS.

## Single Hop configuration testing

### AE Announce

#### AE Create with announceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE creates a AE resource and announces it to a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Create Request (POST) to register to the Registrar-CSE and announce on the Hosting-CSE. |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <Registrar-CSE>?rty=AE Host : Registrar CSE Payload: resource <AE> to be created (payload includes announeTo attribute with value <Hosting-CSE> and announcedAttribute with value of <announcable attribute> |
|  | 3 | Check (Mcc) | Send POST request contains Request URI <Hosting-CSE>?rty=AEAnnc Host : Hosting-CSE Payload: Resource <AEAnnc> to be created with <announcable attribute> |
|  | 4 | Check | Check if possible that the <AEAnnc> resource is created in Hosting-CSE with the <announcable attribute> |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<AEAnnc> Payload: Created <AEAnnc> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE responds to AE containing: containing: Code = 201 Content-Location : < Registrar-CSE >/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |
|  | 8 |  | Repeat step 1-7 creating AE resource with short lifetime |
|  | 9 |  | Check the created resource is removed after the expiry of its lifetime |

#### AE Retrieve Announced Resource Information

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE retrieves announced resource information |
| Configuration: | M2M_CFG_04 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | CSE1 is registered to CSE2 Resource <AE1> has been created on CSE1 Resource <AE1Annc> has been created in CSE2 |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE2 is requested to send a AE Retrieve Request (GET) for resource <AE1Annc> |
|  | 2 | Check (Mca) | Sent GET request contains Request URI < CSE2>/<AE1annc> Host : CSE2 Payload: empty |
|  | 3 | Check (Mca) | CSE2 sends response to AE2 containing: Code = 200 Payload: <AEannc> resource |
|  | 4 | Verify | AE2 indicates successful operation |
|  | 5 | Stimulus | AE2 is requested to send a AE2 Retrieve Request (GET) for resource <AE1Annc> with Result Content set to “original-resource” |
|  | 6 | Check (Mca) | AE2 sends GET request containing: Request URI <CSE2>/<AEannc> Result Content “original-resource” Host : CSE2 Payload: empty |
|  | 7 | Check (Mcc) | CSE2 forwards GET request to CSE1 containing: Request URI <CSE1>/<AE1> Host : CSE1 Payload: empty |
|  | 8 | Check (Mcc) | CSE1 sends response to CSE2 containing: Code = 200 Payload: <AE1> resource |
|  | 9 | Check (Mca) | CSE2 forwards response to AE2 containing: Code = 200 Payload: <AE1> resource |
|  | 10 | Verify | AE indicates successful operation |

#### AE Update AnnounceTo Attribute

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE announces itself to a remote CSE by updating announceTo resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE Resource <AE> has been created on Registrar-CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Update Request (PUT) to update the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI <Registrar-CSE>?rty=AE Host : Registrar CSE Payload: resource <AE> containing announceTo attribute with value <Hosting-CSE> |
|  | 3 | Check (Mcc) | Send POST request contains Request URI <Hosting-CSE>?rty=AEAnnc Host : Hosting-CSE Payload: Resource <AEAnnc> to be created |
|  | 4 | Check | Check if possible that the <AEAnnc> resource is created in Hosting-CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<AEAnnc> Payload: Created <AEAnnc> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <AE> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |
|  | 8 | Stimulus | AE is requested to send an AE Update Request (PUT) to update the resource. |
|  | 9 | Check (Mca) | Sent PUT request contains Request URI <Registrar-CSE>?rty=AE Host : Registrar CSE Payload: resource <AE> containing announceTo attribute with value empty |
|  | 10 | Check (Mcc) | Send DELETE request contains Request URI <Hosting-CSE>?rty=AEAnnc Host : Hosting-CSE Payload: empty |
|  | 11 | Check | Check if possible that the <AEAnnc> resource is deleted in Hosting-CSE. |
|  | 12 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 201 Payload: empty |
|  | 13 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 200 Payload: modified <AE> (assigned and/or modified attributes) |
|  | 14 | Verify | AE indicates successful operation |

#### AE Delete AnnounceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE deletes an AE resource and de-announces it from a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE Resource <AE> has been created on Registrar-CSE Resource <AEAnnc> has been created in Hosting-CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Delete Request (DELETE) |
|  | 2 | Check (Mca) | Sent DELETE request contains Request URI <Registrar-CSE>/<AE> Host : Registrar CSE Payload: empty |
|  | 3 | Check (Mcc) | Sent DELETE request contains Request URI < Hosting-CSE >/<AEannc> Host : Hosting-CSE Payload: empty |
|  | 4 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 200 Payload: empty |
|  | 5 | Check (Mca) | Registrar CSE sends response to AE containing: Code = 200 Payload: empty |
|  | 6 | Check | Check if possible that the <AEannc> resource is deleted in Hosting-CSE and <AE> resource is deleted in Registrar-CSE |
|  | 7 | Verify | AE indicates successful operation |

================ End of  1st Part: Proposed Test Descriptions ==================