| Input Contribution |
| --- |
| Meeting ID* | TST#16 |
| Title:* | TS-0015-Conformance test architecture |
| Source:* | Laurent Velez, ETSI, Laurent.velez@etsi.org |
| Uploaded Date:* | 2015-03-12 |
| Document(s) Impacted* | TS-0015 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

1.	Introduction

The contribution proposes some text for the clause 6.2 (Test Architecture) of conformance testing section of the TS-0015 Testing framework. It provides conformance test methodology steps as the selection of the IUT and the identification of reference points.

2.	Proposal

===== Start of 1st Part: Reference=====

## 2.1	Normative references

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001 "Functional Architecture" V1.6.1

===== End of 1st Part: Reference =====

===== Start of 2nd Part: Test Architecture =====

## 6.2	Test Architecture

### 6.2.1	Selection of Implementation Under Test

#### 6.2.1.1	Definition

The "Implementation Under Test" (IUT) is a protocol implementation considered as an object for testing. This means that the test process will focus on verifying the compliance of this protocol implementation (IUT) with requirements set up in the related base standard. An IUT normally is implemented in a "System Under Test" (SUT). For testing, a SUT is connected to a test system over at least a single interface. Such an interface is identified as "Reference Point" (RP) in the present document. Further details on RPs are presented in clause 6.2.2.

NOTE:	Other interfaces between the test system and the IUT may be used to control the behaviour of the IUT during the test process.

IUTs normally are entities of a protocol architecture for a specific communication protocol located in an OSI layer. Figure 1 shows a complete view of communication layer for oneM2M domain. Further details are presented in the following clauses.

Figure 1: Examples of IUTs in the oneM2M reference architecture

#### 6.2.1.2	oneM2M Service Layer Communication

Table 1 shows the IUTs for oneM2M reference architecture as defined in [1].

Table 1. IUTs for oneM2M

| IUT (node) | Entities | Interfaces | Notes |
| --- | --- | --- | --- |
| ASN | Application Entity (AE) | Mca |  |
|  | Common Services Entity (CSE) | Mca, Mcc, Mcn |  |
| ADN | Application Entity (AE) | Mca |  |
| MN | Application Entity (AE) | Mca |  |
|  | Common Services Entity (CSE) | Mca, Mcc, Mcn |  |
| IN | Application Entity (AE) | Mca |  |
|  | Common Services Entity (CSE) | Mca, Mcc, Mcn, Mcc’, Mch |  |
| Any of above | Network Services Entity (NSE) | Mcn |  |

Table 1 needs to be amended in the following cases:

A new node or entity is defined on the base specifications.

A new interface is defined on the base specifications between any of the existing nodes or entities.

### 6.2.2	Identification of the Reference Points

This clause illustrates candidate reference points (RPs) where test systems can be connected in order to test conformance of oneM2M protocols (IUTs) with oneM2M base standards.

Table 2. RPs for oneM2M

| RP Identifier | RP Type | oneM2M node-entity | oneM2M node-entity | Network |
| --- | --- | --- | --- | --- |
| RP-oneM2M-1 | Mca | ASN-AE | ASN-CSE |  |
| RP-oneM2M-2 | Mca | MN-AE | MN-CSE |  |
| RP-oneM2M-3 | Mca | IN-AE | IN-CSE |  |
| RP-oneM2M-4 | Mca | ADN-AE | IN-CSE |  |
| RP-oneM2M-5 | Mca | ADN-AE | MN-CSE |  |
| RP-oneM2M-6 | Mcc | ASN-CSE | IN-CSE |  |
| RP-oneM2M-7 | Mcc | ASN-CSE | MN-CSE |  |
| RP-oneM2M-8 | Mcc | MN-CSE | MN-CSE |  |
| RP-oneM2M-9 | Mcc | MN-CSE | IN-CSE |  |
| RP-oneM2M-10 | Mcn | ASN-CSE | NSE |  |
| RP-oneM2M-11 | Mcn | MN-CSE | NSE |  |
| RP-oneM2M-12 | Mcn | IN-CSE | NSE |  |
| RP-oneM2M-13 | Mcc’ | IN-CSE | IN-CSE’ |  |
| RP-oneM2M-14 | Mch | IN-CSE | Charging Server |  |

===== End of 2nd Part: Test Architecture =====