| Input Contribution |
| --- |
| Meeting ID* | TST#16 |
| Title:* | TS-0015-IXIT |
| Source:* | Laurent Velez, ETSI, Laurent.velez@etsi.org |
| Uploaded Date:* | 2015-03-13 |
| Document(s) Impacted* | TS-0015 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* |  |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

## 1.	Introduction

The contribution proposes some text for the clause 6.3 (Development of Conformance Test) of conformance testing section of the TS-0015 Testing framework. It contains descriptions IXIT document required for the development of Conformance Testing in oneM2M methodology

## 2.	Proposal

===== Start of 1st Part: Definitions =====

## 3.1	Definitions

Implementation eXtra Information for Testing (IXIT): checklist which contains or references all of the information (in addition to that given in the ICS) related to the IUT and its testing environment, which will enable the test laboratory to run an appropriate test suite against the IUT

IXIT proforma: document, in the form of a questionnaire, which when completed for an implementation or system, becomes an IXIT.

===== End of 1st Part: Definitions =====

===== Start of 2nd Part: IXIT =====

### 6.3.4	Implementation eXtra Information for Testing (IXIT)

The ICS contains base specification dependent information. To derive executable tests this is insufficient; also information about the IUT and its environment shall be supplied. Such information is called Implementation eXtra Information for Testing (IXIT).

An IXIT proforma identifies which ICS items are to be tested and which parameters to be instantiated for the TSS&TP being developed. The production of a IXIT Proforma is specified in ISO/IEC 9646-6 [i.2]. A supplier, providing an IUT for conformance testing, is required to complete a IXIT proforma, which contains additional questions that need to be answered in order to  turn on/off the "switches" and identify Means of Testing for a particular Implementation Under Test (IUT).

The IXIT may contain address information of the IUT, or parameter and timer values which are necessary for the execution of the test suite. The IXIT information , is supplied by the supplier of the IUT to the testing laboratory. To guide production of the IXIT the testing laboratory provides an IXIT proforma.

The selected and implemented test cases with parameter values according to the IXIT form the executable test suite, which are executed on a test system. The testing laboratory uses the IXIT values stated in the IXIT proforma for executing test cases according to the capabilities of the Implementation Under Test. Supported values are given as a single value or a range depending on the nature of the parameter.

===== End of 2nd Part: IXIT =====