| CHANGE REQUEST |
| --- |
| Meeting:* | TST 16 |
| Source:* | ETSI |
| Date:* | 2015-03-26 |
| Contact:* | Laurent Velez, ETSI, Laurent.velez@etsi.org |
| Reason for Change/s:* | To add the mandatory Content-type header for POST/PUT when missing and set it to proper media-type |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0013 V0.0.3 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

According to TS-0009-HTTP_Protocol_Binding-V1_0_1 , in clause 6.4.3 :

Any HTTP request or response containing message-body shall include the Content-type header set to one of ”application/xml”, “application/json”, ”application/vnd.onem2m-res+xml”, “application/vnd.onem2m-res+json”, “application/vnd.onem2m-ntfy+xml” , “application/vnd.onem2m-ntfy+json”, “application/vnd.onem2m-attrs+xml” , “application/vnd.onem2m-attrs+json”.

So, this CR proposes to add the mandatory Content-type header to all POST/PUT request and responses containing message body of the TS-0013.

To be generic in each related test desciption, the proposed value of the content-type is : “proper media-type”.

### -----------------------Start of change 1-------------------------------------------

#### AE Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_03 |
| Objective: | AE registers to its registrar CSE via an AE Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.1 [2] 7.3.4.2.1 |
| Pre-test conditions: | Void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a AE Create request to register to the Registrar CSE |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>?rty=AE Host : Registrar CSE Content-type: proper media-type Payload: <AE> resource to be created |
|  | 3 | Check | Check if possible that the <AE> resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/<AE> Content-type: proper media-type Payload: created <AE> resource |
|  | 5 | Verify | AE indicates successful operation |

#### AE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_05 |
| Objective: | AE updates attribute in <AE> resource via an AE Update Request (PUT) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.3 [2] 7.3.4.2.3 |
| Pre-test conditions: | AE has created a resource <AE> on registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Update Request (PUT) |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI : <CSEBase>/<AE> Host : registrar CSE Content-type: proper media-type Payload: modified <AE> resource |
|  | 3 | Check | Check if possible that the <AE> resource has been updated in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-type: proper media-type Payload: updated <AE> resource |
|  | 5 | Verify | AE indicates successful operation |

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_07 |
| Objective: | AE creates a container resource in registrar CSE via a container Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Create Request (POST) to create container <container> |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <CSEBase>/<AE>?rty=container Host : Registrar CSE Content-type: proper media-type Payload: container resource <container> to be created |
|  | 3 | Check | Check if possible that the <container> resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container> Content-type: proper media-type Payload: Created <container> |
|  | 5 | Verify | AE indicates successful operation |
|  | 6 |  | Repeat step 1-5 creating container resource with short lifetime |
|  | 7 |  | Check the created resource is removed after the expiry of its lifetime |

#### 8.1.3.3	Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_09 |
| Objective: | AE updates attribute in application resource via a container Update Request (PUT) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | a container resource <container> has been created in application <AE> on the Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an container Update Request (PUT) to update the lifetime of the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI <CSEBase>/<AE>/<container> Host : Registrar CSE Content-type: proper media-type Payload: modified <container> resource |
|  | 3 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-type: proper media-type Payload: Updated <container> resource |
|  | 4 | Verify | AE indicates successful operation |

#### 8.1.4.1	ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_11 |
| Objective: | AE adds a contentInstance resource <contentInstance> to a specific container in Registrar CSE via a contentInstance Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a contentInstance Create Request (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <CSEBase>/<AE>/<container> ?rty=contentInstance Host : Registrar CSE Content-type: proper media-type Payload: ContentInstance resource <contentInstance> to be created |
|  | 3 | Check | Check if possible that the <contentInstance> resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-Location : CSEBase>/<AE>/<container> /<contentInstance> Content-type: proper media-type Payload: <contentInstance> resource |
|  | 5 | Verify | AE indicates successful operation |

#### 8.1.6.1	Subscription Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_18 |
| Objective: | AE creates a subscription to Application Entity resource via subscription Create Request (POST) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.2 [2] 7.3.7.2 |
| Pre-test conditions: | App has created an application resource <app> on local SCL App has created a container resource <container> on local SCL |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | App is requested to send a subscriptionCreateRequest (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request URI: <CSEBase>/<AE>/<container> ?rty=subscription Host : Registrar CSE Content-type: proper media-type Payload: subscription <subscription> resource to be created |
|  | 3 | Check | Check if possible that the <subscription> resource is created in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container>/ <subscription> Content-type: proper media-type Payload: Created < subscription > resource |
|  | 5 | Verify | AE indicates successful operation |

#### 8.1.6.3	Subscription Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_20 |
| Objective: | AE updates information about a subscription via subscription Retrieve Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.4 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created a container resource <container> on Registrar CSE AE has created a subscription resource <subscription> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a subscription Retrieve Request (PUT) to update the lifetime of the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI: <CSEBase>/<AE>/<container>/<subscription> Host : Registrar CSE Content-type: proper media-type Payload: Modified <subscription> resource |
|  | 3 | Check | Check if possible that the <subscription> resource is updated in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-type: proper media-type Payload: Modified <subscription> resource |
|  | 5 | Verify | AE indicates successful operation |

#### 8.1.7.1	accessControlPolicy Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_22 |
| Objective: | AE creates an accessControlPolicy resource |
| Configuration: | M2M_CFG_01, |
| References: | [1] 10.2.21.1 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an accessControlPolicy Create Request (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI <CSEBase>/<AE>?rty= accessControlPolicy Host : Registrar CSE Content-type: proper media-type Payload: application resource <accessControlPolicy> to be created |
|  | 3 | Check | Check if possible that the <accessControlPolicy> resource is created in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<AE>/<accessControlPolicy> Content-type: proper media-type Payload: created <accessControlPolicy> resource |
|  | 5 | Verify | AE indicates successful operation |

#### 8.1.7.3	accessControlPolicy Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_24 |
| Objective: | AE updates attribute in accessControlPolicy resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.21.3 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE AE has created an accessControlPolicy resource <accessControlPolicy> under <AE> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an accessControlPolicy Update request (PUT) |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI <CSEbase>/<AE>/<accessControlPolicy> Host : Registrar CSE Content-type: proper media-type Payload: modified <accessControlPolicy>resource |
|  | 3 | Check | Check if possible that the <accessControlPolicy> resource is updated in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-type: proper media-type Payload: updated <accessControlPolicy> resource |
|  | 5 | Verify | AE indicates successful operation |

#### 8.1.8.1	Group Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_27 |
| Objective: | AE creates a group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.2 [2] 7.3.12.2.1 |
| Pre-test conditions: | void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a group Create Request (POST) |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI <CSEBase>?rty=group Host : Registrar CSE Content-type: proper media-type Payload: Group resource <group> to be created |
|  | 3 | Check | Check if possible that the <group> resource is created in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<group> Content-type: proper media-type Payload: created <group> resource representation |
|  | 5 | Verify | AE indicates successful operation |

#### 8.1.8.3	Group Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_29 |
| Objective: | AE updates attribute in group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.4 [2] 7.3.12.2.3 |
| Pre-test conditions: | AE has created a group resource <group> on Registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a group Update Request (PUT) |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI <CSEBase>/<group> Host : Registrar CSE Content-type: proper media-type Payload: modified group resource |
|  | 3 | Check | Check if possible that the <group> resource is updated in Registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Code = 200 Content-type: proper media-type Payload: updated <group> resource representation |
|  | 5 | Verify | AE indicates successful operation |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 8.2.1.1	remoteCSE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | Registree CSE registers to Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.1 [2] 7.3.3.2.1 |
| Pre-test conditions: | Void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Registree CSE is requested to send a remoteCSE Create request to register to the Registrar CSE |
|  | 2 | Check (Mca) | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>?rty=remoteCSE Host : Registrar CSE Content-type: proper media-type Payload: <remoteCSE> resource |
|  | 3 | Check | Check if possible that the remoteCSE resource is created in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/ <remoteCSE> Content-type: proper media-type Payload: created <remoteCSE> resource |
|  | 5 | Check | Check if possible that the remoteCSE resource is created in registree CSE. |
|  | 6 | Verify | Registree CSE and Registrar CSE indicate successful operation |

#### 8.2.1.3	remoteCSE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_03 |
| Objective: | MN-CSE registers to IN-CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.3 [2] 7.3.3.2.3 |
| Pre-test conditions: | <remoteCSE> resource has been created in registrar CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | Registree CSE is requested to send a remoteCSE Update request to the Registrar CSE |
|  | 2 | Check (Mca) | Sent PUT request contains Request method = PUT Request URI: <RegistrarCSE>/<remoteCSE> Host : Registrar CSE Content-type: proper media-type Payload: modified <remoteCSE> resource |
|  | 3 | Check | Check if possible that the remoteCSE resource has been updated in registrar CSE. |
|  | 4 | Check (Mca) | Registrar CSE sends response containing: Status Code = 200 Content-Location <RegistrarCSE>/<remoteCSE> Content-type: proper media-type Payload: updated <remoteCSE> resource |
|  | 5 |  | Check if possible that the remoteCSE resource is also updated in registree CSE. |
|  | 6 | Verify | Registree CSE and Registrar CSE indicate successful operation |

#### 8.2.2.1	AE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | AE creates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.1.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | void |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Create Request (POST) to create an AE <AE> on remote CSE. |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <remoteCSE>?rty=AE Host : Registrar CSE Content-type: proper media-type Payload: resource <AE> to be created |
|  | 3 | Check (Mcc) | Forwarded POST request contains Request URI <remoteCSE>?rty=AE Host : remote CSE Content-type: proper media-type Payload: Resource <AE> to be created |
|  | 4 | Check | Check if possible that the <AE> resource is created in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE> Content-type: proper media-type Payload: Created <AE> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AE> Content-type: proper media-type Payload: Created <AE> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |
|  | 8 |  | Repeat step 1-7 creating AE resource with short lifetime |
|  | 9 |  | Check the created resource is removed after the expiry of its lifetime |

#### 8.2.2.3	AE Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_04 |
| Objective: | AE updates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send an AE Update Request (PUT) to update the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI <remoteCSE>/<AE> Host : Registrar CSE Content-type: proper media-type Payload: modified <AE> resource |
|  | 3 | Check (Mcc) | Forwarded PUT request contains Request URI < remoteCSE >/<AE> Host : remote CSE Content-type: proper media-type Payload: modified <AE>resource |
|  | 4 | Check | Check if possible that the <AE> resource is updated in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 200 Content-type: proper media-type Payload: modified <AE> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 200 Content-type: proper media-type Payload: modified <AE> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |

#### 8.2.3.1	Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | AE creates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Create Request (POST) to create container <container> on remote CSE. |
|  | 2 | Check (Mca) | Sent POST request contains Request URI <remoteCSE>/<AE>?rty=container Host : Registrar CSE Content-type: proper media-type Payload: resource <container> to be created |
|  | 3 | Check (Mcc) | Forwarded POST request contains Request URI <remoteCSE>/<AE>?rty=container Host : remote CSE Content-type: proper media-type Payload: resource <container> to be created |
|  | 4 | Check | Check if possible that the <container> resource is created in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to Registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Content-type: proper media-type Payload: Created <container> resource (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Content-type: proper media-type Payload: Created <container> resource (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |
|  | 8 |  | Repeat step 1-7 creating container resource with short lifetime |
|  | 9 |  | Check the created resource is removed after the expiry of its lifetime |

#### 8.2.3.3	Container Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_03 |
| Objective: | AE updates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.3 [2] 7.3.5.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in < AE> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a container Update Request (PUT) to update the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI <remoteCSE>/<AE>/<container> Host : Registrar CSE Content-type: proper media-type Payload: modified resource <container> |
|  | 3 | Check (Mcc) | Forwarded PUT request contains Request URI <remoteCSE>/<AE>/<container> Host : remote CSE Content-type: proper media-type Payload: modified <container> resource |
|  | 4 | Check | Check if possible that the <container> resource is updated in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to Registrar CSE containing: Code = 200 Content-type: proper media-type Payload: modified <container> resource (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 200 Content-type: proper media-type Payload: modified <container> resource (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |

#### 8.2.4.1	ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_06 |
| Objective: | AE creates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.2 [2] 7.3.7.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a ContentInstance Create Request (POST) to create a ContentInstance <contentInstance> on remote CSE. |
|  | 2 | Check (Mca) | Sent POST request contains Request URI : <remoteCSE>/<AE>/<container> ?rty=contentInstance Host : Registrar CSE Content-type: proper media-type Payload: resource <contentInstance> to be created |
|  | 3 | Check (Mcc) | Forwarded POST request contains Request URI : <remoteCSE>/<AE>/<container>?rty=contentInstance Host : remote CSE Content-type: proper media-type Payload: resource <contentInstance> to be created |
|  | 4 | Check | Check if possible that the <ContentInstance> resource is created in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Content-type: proper media-type Payload: Created <contentInstance> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Content-type: proper media-type Payload: Created <ContentInstance> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |
|  | 8 |  | Repeat step 1-7 creating ContentInstance resource with short lifetime |
|  | 9 |  | Check the created resource is removed after the expiry of its lifetime |

#### 8.2.4.3	ContentInstance Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_MH_08 |
| Objective: | AE updates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.4 [2] 7.3.7.2.3 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> Resource <contentInstance> has been created in <container> |
| Test Sequence: | Step | Type | Description |
|  | 1 | Stimulus | AE is requested to send a ContentInstance Update Request (PUT) to update the resource. |
|  | 2 | Check (Mca) | Sent PUT request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : Registrar CSE Content-type: proper media-type Payload: modified <contentInstance> resource |
|  | 3 | Check (Mcc) | Forwarded PUT request contains Request URI : <remoteCSE>/<AE>/<container>/<contentInstance> Host : remote CSE Content-type: proper media-type Payload: modified <contentInstance> resource <contentInstance> |
|  | 4 | Check | Check if possible that the <contentInstance> resource is updated in remote CSE. |
|  | 5 | Check (Mcc) | Remote CSE sends response to registrar CSE containing: Code = 200 Content-type: proper media-type Payload: modified <contentInstance> (assigned and/or modified attributes) |
|  | 6 | Check (Mca) | Registrar CSE sends response to AE containing: Code = 200 Content-type: proper media-type Payload: modified <contentInstance> (assigned and/or modified attributes) |
|  | 7 | Verify | AE indicates successful operation |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?