| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Set resource type number for creation |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-04-09 |
| Abstract:* | Replace resource type name with resource type number in creation request |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes to replace resource type name with resource type number in creation request

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

# 8	Test Descriptions

Editor’s Note: The content of this section can be modified according to the progress of this TS.

## No Hop configuration testing

### Application Entity Registration

#### AE Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_03 |
| Objective: | AE registers to its registrar CSE via an AE Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.1.1 [2] 7.3.4.2.1 |
| Pre-test conditions: | Void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a AE Create request to register to the Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>?rty=2 Host : Registrar CSE Content Type option Payload: <AE> resource to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <AE> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/<AE> Payload: created <AE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================

============== == Start of  2st Part: Proposed Test Descriptions ==================

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_07 |
| Objective: | AE creates a container resource in registrar CSE via a container Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> |
| 2 | Check Mca | Primitive | Sent CREATE request contains To: <CSEBase>/<AE>?rty=container Fr: AE-ID Cn: container resource <container> to be created |
|  |  | HTTP | Sent POST request contains Request URI <CSEBase>/<AE>?rty=3 Host : Registrar CSE Payload: container resource <container> to be created Content-Type= media-type |
|  |  | CoAP | Sent POST request contains Code = 2(POST) Uri-Path: <CSEBase> Uri-Path: <AE>?rty=container Payload: container resource <container> to be created Content Type option |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <container> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive | Registrar sends response containing: To: AE-ID Fr: CSE-ID Cn: Created <container> |
|  |  | HTTP | Registrar sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container> Payload: Created <container> |
|  |  | CoAP | Registrar sends response containing: Code = 2.01 (2001 Created) Location-Path: <CSEBase> Location-Path: <AE> Location-Path: <container> The same Message ID as that of the previous request |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |
| 6 |  |  | Repeat step 1-5 creating container resource with short lifetime |
| 7 |  |  | Check the created resource is removed after the expiry of its lifetime |

============== == End of  2st Part: Proposed Test Descriptions ==================

============== == Start of  3st Part: Proposed Test Descriptions ==================

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_11 |
| Objective: | AE adds a contentInstance resource <contentInstance> to a specific container in Registrar CSE via a contentInstance Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.19.2 [2] 7.3.6.2.1 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on registrar CSE AE has created a container resource <container> in <AE> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a contentInstance Create Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <CSEBase>/<AE>/<container>?rty=4 Host : Registrar CSE Payload: ContentInstance resource <contentInstance> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <contentInstance> resource is created in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : CSEBase>/<AE>/<container>/<contentInstance> Payload: <contentInstance> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

============== == End of  3st Part: Proposed Test Descriptions ==================

============== == Start of  4st Part: Proposed Test Descriptions ==================

### Subscription Management

#### Subscription Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_18 |
| Objective: | AE creates a subscription to Application Entity resource via subscription Create Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.11.2 [2] 7.3.7.2 |
| Pre-test conditions: | AE has created an application resource <AE> on registrar CSE AE has created a container resource <container> on registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a subscriptionCreateRequest |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI: <CSEBase>/<AE>/<container> ?rty=23 Host : Registrar CSE Payload: subscription <subscription> resource to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <subscription> resource is created in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/<container>/ <subscription> Payload: Created < subscription > resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

============== == End of  4st Part: Proposed Test Descriptions ==================

============== == Start of  5st Part: Proposed Test Descriptions ==================

### accessControlPolicy Management

#### accessControlPolicy Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_22 |
| Objective: | AE creates an accessControlPolicy resource |
| Configuration: | M2M_CFG_01, |
| References: | [1] 10.2.21.1 [2] 7.3.1.2 |
| Pre-test conditions: | AE has created an Application Entity resource <AE> on Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an accessControlPolicy Create Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI <CSEBase>/<AE>?rty=1 Host : Registrar CSE Payload: application resource <accessControlPolicy> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <accessControlPolicy> resource is created in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<AE>/<accessControlPolicy> Payload: created <accessControlPolicy> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

============== == End of  5st Part: Proposed Test Descriptions ==================

============== == Start of  6st Part: Proposed Test Descriptions ==================

### Group Management

#### Group Resource creation

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_NH_27 |
| Objective: | AE creates a group resource |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.7.2 [2] 7.3.12.2.1 |
| Pre-test conditions: | void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a group Create Request |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI <CSEBase>?rty=9 Host : Registrar CSE Payload: Group resource <group> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <group> resource is created in Registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 Content-Location : <CSEBase>/<group> Payload: created <group> resource representation |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

============== == End of  6st Part: Proposed Test Descriptions ==================

============== == Start of  7st Part: Proposed Test Descriptions ==================

## Single hop configuration testing

### remoteCSE Management

#### remoteCSE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | Registree CSE registers to Registrar CSE |
| Configuration: | M2M_CFG_02 |
| References: | [1] 10.2.2.1 [2] 7.3.3.2.1 |
| Pre-test conditions: | Void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | Registree CSE is requested to send a remoteCSE Create request to register to the Registrar CSE |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <RegistrarCSE>?rty=16 Host : Registrar CSE Content Type option Payload: <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the remoteCSE resource is created in registrar CSE. |
| 4 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response containing: Status Code = 200 (OK) Content-Location : <RegistrarCSE>/ <remoteCSE> Payload: created <remoteCSE> resource |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 5 |  | Verify | Check if possible that the remoteCSE resource is created in registree CSE. |
| 6 |  | Verify | Registree CSE and Registrar CSE indicate successful operation |

============== == End of  7st Part: Proposed Test Descriptions ==================

============== == Start of  8st Part: Proposed Test Descriptions ==================

### AE Management

#### AE Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_02 |
| Objective: | AE creates a remote AE resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.1.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | void |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an AE Create Request to create an AE <AE> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <remoteCSE>?rty=2 Host : Registrar CSE Payload: resource <AE> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI <remoteCSE>?rty=2 Host : remote CSE Payload: Resource <AE> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <AE> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: containing: Code = 201 Content-Location : <remoteCSE>/<AE> Payload: Created <AE> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
|  |  |  | Repeat step 1-7 creating AE resource with short lifetime |
|  |  |  | Check the created resource is removed after the expiry of its lifetime |

============== == End of  8st Part: Proposed Test Descriptions ==================

============== == Start of  9st Part: Proposed Test Descriptions ==================

### Container Management

#### Container Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_01 |
| Objective: | AE creates a remote container resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.4.1 [2] 7.3.5.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request to create container <container> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <remoteCSE>/<AE>?rty=3 Host : Registrar CSE Payload: resource <container> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI <remoteCSE>/<AE>?rty=3 Host : remote CSE Payload: resource <container> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <container> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to Registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container> Payload: Created <container> resource (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 9 |  | Verify | Check the created resource is removed after the expiry of its lifetime |

============== == End of  9st Part: Proposed Test Descriptions ==================

============== == Start of  10st Part: Proposed Test Descriptions ==================

### ContentInstance Management

#### ContentInstance Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_06 |
| Objective: | AE creates a remote ContentInstance resource |
| Configuration: | M2M_CFG_03 |
| References: | [1] 10.2.19.2 [2] 7.3.7.2.1 |
| Pre-test conditions: | Resource <AE> has been created in remote CSE Resource <container> has been created in <AE> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a ContentInstance Create Request to create a ContentInstance <contentInstance> on remote CSE. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI : <remoteCSE>/<AE>/<container> ?rty=4 Host : Registrar CSE Payload: resource <contentInstance> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Forwarded POST request contains Request URI : <remoteCSE>/<AE>/<container>?rty=4 Host : remote CSE Payload: resource <contentInstance> to be created |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <ContentInstance> resource is created in remote CSE. |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Payload: Created <contentInstance> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE forwards response to AE containing: Code = 201 Content-Location : <remoteCSE>/<AE>/<container>/<contentInstance> Payload: Created <ContentInstance> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating ContentInstance resource with short lifetime |
| 9 |  | Verify | Check the created resource is removed after the expiry of its lifetime |

============== == End of  10st Part: Proposed Test Descriptions ==================

============== == Start of  11st Part: Proposed Test Descriptions ==================

### Container Announce

#### Container Create with announceTo

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_SH_XX |
| Objective: | AE creates a container resource and announces it to a remote CSE |
| Configuration: | M2M_CFG_03 |
| References: | [1] 9.6.26, 10.2.18 [2] 7.2.3.9 |
| Pre-test conditions: | Registrar-CSE is registered to Hosting-CSE AE is registered to Registrar-CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a container Create Request and announce the container |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request URI <Registrar-CSE>?rty=3 Host : Registrar CSE Payload: resource <container> to be created (payload includes announeTo attribute with value <Hosting-CSE> and announcedAttribute with value of <announcable attribute> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 3 | Check Mcc | Primitive |  |
|  |  | HTTP | Send POST request contains Request URI <Hosting-CSE>?rty=10003 Host : Hosting-CSE Payload: Resource <containerAnnc> to be created with <announcable attribute> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the <containerAnnc> resource is created in Hosting-CSE with the <announcable attribute> |
| 5 | Check Mcc | Primitive |  |
|  |  | HTTP | Remote CSE sends response to registrar CSE containing: Code = 201 Content-Location : <Hosting-CSE>/<containerAnnc> Payload: Created <containerAnnc> |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE responds to AE containing: Code = 201 Content-Location : < Registrar-CSE >/<container> Payload: Created <container> (assigned and/or modified attributes) |
|  |  | CoAP |  |
|  |  | MQTT |  |
| 7 |  | Verify | AE indicates successful operation |
| 8 |  |  | Repeat step 1-7 creating container resource with short lifetime |
| 9 |  | Verify | Check the created resource is removed after the expiry of its lifetime. Check that the announced resource is removed after the expiry of its lifetime. |

============== == End of  11st Part: Proposed Test Descriptions ==================