| Input Contribution |
| --- |
| Meeting ID* | TST 16.3 |
| Title:* | ICS Proforma Annex |
| Source:* | Laurent Velez, ETSI, laurent.velez@etsi.org |
| Uploaded Date:* | 2015-04-28 |
| Document(s) Impacted* | TS-0017 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0017 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Header

Text here.

- Introduction

This contribution consists of definition and proforma to be added in the Annex A of  TS-0017 (Implementation Conformance Statements V0_0_1).

- Proposal

============== == Start of  1st Part: Proposed Annex A ==================

Annex A (Informative): ICS Proforma

A.1	Guidance for completing the ICS proforma

A.1.1	Purposes and structure

The purpose of this ICS proforma is to provide a mechanism whereby a supplier of an implementation of the

requirements defined in TS-0001 [1] may provide information about the implementation in a standardized manner.

The ICS proforma is subdivided into clauses for the following categories of information:

- guidance for completing the ICS proforma;

- identification of the implementation;

- identification of the TS-0001 [1];

- global statement of conformance;

- ICS proforma tables.

A.1.2	Abbreviations and conventions

The ICS proforma contained in this annex is comprised of information in tabular form in accordance with the guidelines

presented in ISO/IEC 9646-7 [3].

Item column

The item column contains a number which identifies the item in the table.

Item description column

The item description column describes in free text each respective item (e.g. parameters, timers, etc.). It implicitly

means "is <item description> supported by the implementation?".

Reference column

The reference column gives reference to the relevant sections in core specifications.

Status column

The various status used in this annex are in accordance with the rules in table A.1.

Table A.1: Key to status codes

| Status code | Status name | Meaning |
| --- | --- | --- |
| m | mandatory | The capability shall be supported. It is a static view of the fact that the conformance requirements related to the capability in the reference specification are mandatory requirements. This does not mean that a given behaviour shall always be observed (this would be a dynamic view), but that it shall be observed when the implementation is placed in conditions where the conformance requirements from the reference specification compel it to do so. For instance, if the support for a parameter in a sent PDU is mandatory, it does not mean that it shall always be present, but that it shall be present according to the description of the behaviour in the reference specification (dynamic conformance requirement). |
| o | optional | The capability may or may not be supported. It is an implementation choice. |
| n/a | not applicable | It is impossible to use the capability. No answer in the support column is required. |
| c.<integer> | conditional | The requirement on the capability ("m", "o", "n/a") depends on the support of other optional or conditional items. <integer> is the identifier of the conditional expression. |
| o.<integer> | qualified optional | For mutually exclusive or selectable options from a set. <integer> is the identifier of the group of options, and the logic of selection of the options. |

Mnemonic column

The Mnemonic column contains mnemonic identifiers for each item.

Support column

The support column shall be filled in by the supplier of the implementation. The following common notations, defined in ISO/IEC 9646-7 [3], are used for the support column:

Y or y	supported by the implementation

N or n	not supported by the implementation

N/A, n/a or - 	no answer required (allowed only if the status is N/A, directly or after evaluation of a conditional status)

References to items

For each possible item answer (answer in the support column) within the ICS proforma there exists a unique reference, used, for example, in the conditional expressions. It is defined as the table identifier, followed by a solidus character "/", followed by the item number in the table.

EXAMPLE1:	A.5/4 is the reference to the answer of item 4 in table A.5.

EXAMPLE 2: 	A.6/3b is the reference to the second answer (i.e. in the second support column) of item 3 in

table 6 of annex A.

Values allowed column

The values allowed column contains the type, the list, the range, or the length of values allowed. The following

notations are used:

- range of values: 			<min value> .. <max value>

example:			 5 .. 20

- list of values: 				<value1>, <value2>, ..., <valueN>

example: 			2 ,4 ,6 ,8, 9

example: 			'1101'B, '1011'B, '1111'B

example: 			'0A'H, '34'H, '2F'H

- list of named values: 	<name1>(<val1>), <name2>(<val2>), ..., <nameN>(<valN>)

example: 			reject(1), accept(2)

- length: 					size (<min size> .. <max size>)

example: 			size (1 .. 8)

Values supported column

The values supported column shall be filled in by the supplier of the implementation. In this column, the values or the

ranges of values supported by the implementation shall be indicated.

Prerequisite line

A prerequisite line takes the form: Prerequisite: <predicate>.

A prerequisite line after a clause or table title indicates that the whole clause or the whole table is not required to be

completed if the predicate is FALSE.

A.1.3	Instructions for completing the ICS proforma

The supplier of the implementation shall complete the ICS proforma in each of the spaces provided. In particular, an

explicit answer shall be entered, in each of the support or supported column boxes provided, using the notation

described in clause A.1.2.

If necessary, the supplier may provide additional comments in space at the bottom of the tables or separately.

More detailed instructions are given at the beginning of the different clauses of the ICS proforma.

A.2	Identification of the implementation

A.2.1	Introduction

Identification of the Implementation Under Test (IUT) and the system in which it resides (the System Under Test

(SUT)) should be filled in so as to provide as much detail as possible regarding version numbers and configuration

options.

The product supplier information and client information should both be filled in if they are different.

A person who can answer queries regarding information supplied in the ICS should be named as the contact person.

A.2.2	Date of the statement

.........................................................................................................................................................................................

A.2.3	Implementation Under Test (IUT) identification

IUT name:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

IUT version:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

A.2.4	System Under Test (SUT) identification

SUT name:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

Hardware configuration:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

.........................................................................................................................................................................................

Operating system:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

A.2.5	Product supplier

Name:

.........................................................................................................................................................................................

Address:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

.........................................................................................................................................................................................

Telephone number:

.........................................................................................................................................................................................

Facsimile number:

.........................................................................................................................................................................................

E-mail address:

.........................................................................................................................................................................................

Additional information:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

.........................................................................................................................................................................................

A.2.6	Client (if different from product supplier)

Name:

.........................................................................................................................................................................................

Address:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

.........................................................................................................................................................................................

Telephone number:

.........................................................................................................................................................................................

Facsimile number:

.........................................................................................................................................................................................

E-mail address:

.........................................................................................................................................................................................

Additional information:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

A.2.7	ICS contact person

(A person to contact if there are any queries concerning the content of the ICS)

Name:

.........................................................................................................................................................................................

Telephone number:

.........................................................................................................................................................................................

Facsimile number:

.........................................................................................................................................................................................

E-mail address:

.........................................................................................................................................................................................

Additional information:

.........................................................................................................................................................................................

.........................................................................................................................................................................................

.........................................................................................................................................................................................

A.3	Identification of the reference specifications

This ICS proforma applies to the following standard:

[1]			TS-0001 :" Functional Architecture V1_6_1

[2]			TS-0004 :" Service Layer Core Protocol V1_0_1

A.4	Global statement of conformance

Are all mandatory capabilities implemented? (Yes/No) .....................

NOTE: Answering "No" to this question indicates non-conformance to the oneM2M standard specification.

Non-supported mandatory capabilities are to be identified in the ICS, with an explanation of why theimplementation is non-conforming, on pages attached to the ICS proforma.

A.5	Tables

Editor note: the following tables are there for example only and should be replaced by proper ones.

A.5.1 Roles

The supplier of the implementation shall state the support of type of the implementation according to the following

station type, in table A.1.

Editor note: Example 1

Table A.x: oneM2M Node type

| Item | Type | Mnemonic | Reference | Status | Support |
| --- | --- | --- | --- | --- | --- |
| 1 | ADN |  |  |  |  |
| 2 | ASN |  |  |  |  |
| 3 | MN-CSE |  |  |  |  |
| 4 | IN-CSE |  |  |  |  |

Editor note: Example 2

Table A.x: Parameter support

| Item | Parameters | Reference | Status | Support | Value Allowed | Value Supported |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | xxx | Annex A | m |  | Integer |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |

============== == End of  1st Part: Proposed Annex A ==================