| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TST |
| Title:* | Test non blocking synchronous requests |
| Source:* | LAAS-CNRS |
| Contact: | ben.alaya@laas.fr |
| Date:* | 2015-05-03 |
| Abstract:* | Testing of non blocking synchronous requests for retrieve, create, update and delete operations. |
| Agenda Item:* | TBD |
| Work item(s): | WI0022 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the proposed text into TS-0013 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes Testing of non blocking synchronous requests for retrieve, create, update and delete operations.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## Non blocking configuration testing

### Synchronous request

#### Resource Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE retrieves a resource using non blocking synchronous request |
| Configuration: |  |
| References: |  |
| Pre-test conditions: | AE has created a <Resource> resource on registrar CSE located on <CSEBase>/<Resource> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous request to <CSEBase> to retrieve the <Resource> resource |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <CSEBase>/<Resource>?rt=nonBlockingRequestSynch Host : registrar CSE |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Resource> Uri-Query: rt=nonBlockingRequestSynch |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : registrar CSE |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: resource with the parameter "requestStatus" set to "COMPLETED" and the "operationResult" parameter containing the <Resource> resource. |
|  |  | CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 Payload: <Request> resource with the parameter "requestStatus" set to "COMPLETED" and the "operationResult" parameter containing the <Resource> resource. |
|  |  | MQTT |  |
| 8 |  | Verify | AE indicates successful operation |

#### Resource Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE creates a resource using non blocking synchronous request. |
| Configuration: |  |
| References: |  |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous create request to <CSEBase> to create the <Resource> resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase>?rt=nonBlockingRequestSynch&rty=ResourceTypeNum Host : registrar CSE |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rt=nonBlockingRequestSynch Uri-Query: rty=ResourceTypeNum |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : registrar CSE |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: resource with the parameter "requestStatus" set to "COMPLETED" and the "operationResult" parameter containing the created<Resource> resource. |
|  |  | CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 Payload: <Request> resource with the parameter "requestStatus" set to "COMPLETED" and the "operationResult" parameter containing the created <Resource> resource. |
|  |  | MQTT |  |
| 8 |  | Verify | AE indicates successful operation |

#### Resource Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE updates a resource using non blocking synchronous request. |
| Configuration: |  |
| References: |  |
| Pre-test conditions: | AE has created a <Resource> resource on registrar CSE located on <CSEBase>/<Resource> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous update request to <CSEBase> to update the <Resource> resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent PUT request contains Request method = PUT Request URI: <CSEBase>?rt=nonBlockingRequestSynch Host : registrar CSE |
|  |  | CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Resource> Uri-Query: rt=nonBlockingRequestSynch |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : registrar CSE |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: resource with the parameter "requestStatus" set to "COMPLETED" and the "operationResult" parameter containing the updated <Resource> resource. |
|  |  | CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 Payload: <Request> resource with the parameter "requestStatus" set to "COMPLETED" and the "operationResult" parameter containing the updated <Resource> resource. |
|  |  | MQTT |  |
| 8 |  | Verify | AE indicates successful operation |

#### Resource Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE deletes a resource using non blocking synchronous request. |
| Configuration: |  |
| References: |  |
| Pre-test conditions: | AE has created a <Resource> resource on registrar CSE located on <CSEBase>/<Resource> |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a non blocking synchronous delete request to delete the <Resource> resource. |
| 2 | Check Mca | Primitive |  |
|  |  | HTTP | Sent DELETE request contains Request method = DELETE Request URI: <CSEBase>?rt=nonBlockingRequestSynch Host : registrar CSE |
|  |  | CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <Resource> Uri-Query: rt=nonBlockingRequestSynch |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Status Code = 202 Payload: Reference to the created <Request> resource |
|  |  | CoAP | Registrar CSE creates an inernal <Request> resource and sends acknowledgement response containing: Response Code = None Payload <Request> reference |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  | Stimulus | AE is requested to wait then send a retrieve request to <Request> reference |
| 6 | Check Mca | Primitive |  |
|  |  | HTTP | Sent GET request contains Request method = GET Request URI: <Request> reference Host : registrar CSE |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <Request> reference |
|  |  | MQTT |  |
| 7 | Check Mca | Primitive |  |
|  |  | HTTP | Registrar CSE sends response to AE containing: Code = 200 Payload: resource with the parameter "requestStatus" set to "COMPLETED". |
|  |  | CoAP | Registrar CSE sends response to AE containing: Response Code= 2.05 Payload: <Request> resource with the parameter "requestStatus" set to "COMPLETED" . |
|  |  | MQTT |  |
| 8 |  | Verify | AE indicates successful operation |

============== == End of  1st Part: Proposed Test Descriptions ==================