| Input Contribution |
| --- |
| Meeting ID* | TP17 |
| Title:* | Polling Channel Tests |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@InterDigital.com Dale Seed, InterDigital, Dale.Seed@InterDigital.com |
| Uploaded Date:* | 2015-03-15 |
| Document(s) Impacted* | TS-0013 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some Interoperability Test Descriptions for PollingChannel and PollingChannelURI resource procedures to be added to TS-0013 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes testing of polling channel resource management requests for create, retrieve, update and delete operations of the <pollingChannel> resource as well as Long Polling retrieve operations.

The clause numbers and the TD identifier names in the following proposal may change when included in to TS-0013.

- Proposal

============== == Start of  1st Part: Proposed Test Descriptions ==================

## No Hop configuration testing

### PollingChannel Management

#### PollingChannel Create

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE creates a <pollingChannel> resource in registrar CSE via a Create Request |
| Configuration: |  |
| References: | [1] 10.2.13.2 [2] 7.3.21.2.1 |
| Pre-test conditions: |  |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a pollingChannel Create Request to create < pollingChannel > |
| 2 | Check Mca | Primitive | Sent CREATE request contains To: <CSEBase>/<AE> ResourceType=pollingChannel Fr: AE-ID Cn: <pollingChannel> resource to be created |
|  |  | HTTP | Sent POST request contains Request method = POST Request URI: <CSEBase>?rty=15 Host : registrar CSE Payload: < pollingChannel > resource |
|  |  | CoAP | Sent POST request contains Method: 0.02 (POST) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Query: rty=15 Payload: < pollingChannel > resource |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the < pollingChannel > resource is created in Registrar CSE. |
| 7 | Check Mca | Primitive | Sent CREATE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: Created <pollingChannel> |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Content-Location : <CSEBase>/<AE>/< pollingChannel > Payload: Created < pollingChannel > |
|  |  | CoAP | Registrar CSE sends response containing: Response Code = 2.01 Location-Path: <CSEBase> Location-Path: <AE> Location-Path: < pollingChannel > |
|  |  | MQTT |  |
| 8 |  | Verify | Registrar CSE indicates successful operation |

#### PollingChannel Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE retrieves information of a pollingChannel resource via a Retrieve Request (GET) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.3 [2] 7.3.21.2.2 |
| Pre-test conditions: | A pollingChannel resource < pollingChannel > has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a pollingChannel Retrieve Request for < pollingChannel > |
| 2 | Check Mca | Primitive | Sent RETRIEVE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<pollingChannel> Host : Registar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <pollingChannel> |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive | Sent RETRIEVE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: <pollingChannel> resource |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: <pollingChannel> resource |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: <pollingChannel> resource |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |

#### pollingChannel Update

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE updates attribute in pollingChannel resource via a Update Request (PUT) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.4 [2] 7.3.21.2.3 |
| Pre-test conditions: | a pollingChannel resource < pollingChannel > has been created in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an pollingChannel Update Request to update the lifetime of the resource. |
| 2 | Check Mca | Primitive | Sent UPDATE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID Response Statuse Code : OK Cn: <pollingChannel> resource to be updated |
|  |  | HTTP | Sent PUT request contains Request URI <CSEBase>/<AE>/<pollingChannel> Host : Registrar CSE Payload: modified <pollingChannel> resource |
|  |  | CoAP | Sent PUT request contains Method: 0.03 (PUT) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: <pollingChannel> Payload: <pollingChannel> resource updated |
|  |  | MQTT |  |
| 3 |  | Verify | Check if possible that the <pollingChannel> resource has been updated in registrar CSE. |
| 4 | Check Mca | Primitive | Sent UPDATE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: <pollingChannel> resource |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Updated <pollingChannel> resource |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | MQTT |  |
| 5 |  | Verify | AE indicates successful operation |

#### pollingChannel Delete

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE deletes a pollingChannel resource via a Delete Request |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.5 [2] 7.3.21.2.4 |
| Pre-test conditions: | AE has created a pollingChannel resource < pollingChannel > in application <AE> on the Registrar CSE |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send an pollingChannel Delete Request |
| 2 | Check Mca | Primitive | Sent DELETE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID |
|  |  | HTTP | Sent DELETE request contains Request URI <CSEBase>/<AE>/< pollingChannel > Host : Registrar CSE Payload: empty |
|  |  | CoAP | Sent DELETE request contains Method: 0.04 (DELETE) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: < pollingChannel > |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive | Sent DELETE request contains To: <CSEBase>/<AE>/<pollingChannel> Fr: AE-ID Response Statuse Code : OK |
|  |  | HTTP | Registar CSE sends response containing: Code = 200 Payload: empty |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 |
|  |  | MQTT |  |
| 4 |  | Verify | Check if possible that the < pollingChannel > resource has been removed in registrar CSE. |
| 5 |  | Verify | AE indicates successful operation |

#### Long Polling on a PollingChannel Retrieve

| Interoperability Test Description |
| --- |
| Identifier: | TD_M2M_XX |
| Objective: | AE retrieves information of a pollingChannel resource via a Retrieve Request (GET) |
| Configuration: | M2M_CFG_01 |
| References: | [1] 10.2.13.7 [2] 7.3.22.2.2 |
| Pre-test conditions: | A pollingChannel resource < pollingChannel > has been created in application <AE> on the Registrar CSE A subscription to a <container> resource has been created using the <pollingChannel> as a notificationURI in the subscription. A single <contentInstance> resource is created in the subscribed to resource. |
| Test Sequence |
| Step | RP | Type | Description |
| 1 |  | Stimulus | AE is requested to send a pollingChannelURI Retrieve Request for <pollingChannelURI> |
| 2 | Check Mca | Primitive | Sent RETRIEVE request contains To: <CSEBase>/<AE>/<pollingChannel>/pollingChannelURI Fr: AE-ID |
|  |  | HTTP | Sent GET request contains Request URI <CSEBase>/<AE>/<pollingChannel>/pollingChannelURI Host : Registar CSE Payload: empty |
|  |  | CoAP | Sent GET request contains Method: 0.01 (GET) Uri-Host: Registrar CSE host Uri-Port: Registrar CSE port Uri-Path: <CSEBase> Uri-Path: <AE> Uri-Path: < pollingChannel > URI-Path: pollingChannelURI |
|  |  | MQTT |  |
| 3 | Check Mca | Primitive | Sent RETRIEVE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : OK Cn: pending Notification request |
|  |  | HTTP | Registrar CSE sends response containing: Code = 200 Payload: Response primitive with Content set with Notification request |
|  |  | CoAP | Registrar sends response containing: Response Code = 2.05 Payload: Response primitive with Content set with Notification request |
|  |  | MQTT |  |
| 4 |  | Verify | AE indicates successful operation |
| 5 |  |  | Repeat steps 1-2. There is no pending request. When the Request Expiration Timestamp expires Registrar sends response indicating “REQUEST_TIMEOUT” |
| 6 | Check Mca | Primitive | Sent RETRIEVE response contains To: AE-ID Fr: CSE-ID Response Statuse Code : REQUEST_TIMEOUT |
|  |  | HTTP | Registrar CSE sends response containing: Code = 408 |
|  |  | CoAP | Registrar sends response containing: Response Code = 4.04 oneM2M-RSC = 4008 |
|  |  | MQTT |  |

============== == End of  1st Part: Proposed Test Descriptions ==================